Source	MARKET NEWS
Date	05/03/2017
Time	05:18:17 AM

Company	 Sage Gold Inc.
Title	Grade Thickness 
Model High Grade Zones Clavos





    CDNX Symbol: SGX











Press Release





SAGE GOLD INC ("SGX-V")
- Grade Thickness Model-High Grade Zones-Clavos

Sage Gold Inc. (the "Company") has completed a Grade times
Thickness model for the Clavos gold deposit located 32 kms east north
east in the prolific East Timmins Gold Camp. The purpose of this
analysis is to determine plunge trends for the higher grade gold
mineralization within the Clavos gold system. An outcome of this work
is that a number of high grade intersections are proximal to primary
structures below the 300 metre level controlling the lens geometry.
These uncut assays in these intersections were drilled by Kinross and
previously reported by United Tex Sol Mines Inc. and include the
following as reported in press releases:

KC 99-131- 94.6g/t over 9.6 metres uncut - (press release
September 21, 1999)

KC 99-137- 61.59g/t over 3 metres uncut (press release November
17, 1999)

KC 99- 155W- 85.15g/t over 3.2 metres uncut (press release March
2, 2000)

These holes are assumed to be reported as drill core lengths.

The development of the grade thickness model as detailed below has
led to a re-interpretation of the potential plunge directions and
controls on the gold mineralization at Clavos. The majority of the
higher grade composites occur below the 300 meter level below and
adjacent to the mine infrastructure. The intersection of the high angle
back thrust faults with the low angle imbricate thrust faults are
within reach of drill stations on the 225, 285 and 300 levels. The
model also provides vectors to potential new gold plunge directions
higher in the Clavos deposit such as at the 100 metre east level.
Underground definition drilling will commence on May 7th on the 100
metre east level. Further underground drilling will follow from the 225
level to fill in up plunge from KC99-137 and from the 285 and 300
levels to test up plunge from KC99-131 and 155W.

Nigel Lees, President and CEO commented, "This modeling will
provide Sage with the analytical framework to more precisely target
underground definition, exploration and resource drilling. The exercise
of plotting grade times width across the Clavos deposit has yielded
higher grade plunge trends that will potentially outline additional
resources. We are looking forward to the commencement of our
underground drill program and expect to be drilling these higher grade
zones next month."

Sage has recently completed a compilation of the surface and
diamond drilling assay database focusing on the gold mineralization by
computing composite weighted average grades over core lengths for the
major gold zones specified in the 2012 NI 43-101 resource estimation
report as well as sub-zones not included in this report. The drill
database includes holes which have been previously disclosed by
previous operators such as those quoted above and holes which are in
the drill database. This data comprised 569 surface diamond drill holes
for all of the Clavos area drilling totalling 126,894 m for an average
drill hole length of 225 m. A total of 837 underground drill holes with
a combined length of 64,225 m and an average length of 77 m were also
provided. The Clavos area drilling spans a strike length of 3.3 km
covered by 171 geological cross-sections spaced from 15 metres to 30
metres apart. A total of 30,836 surface drilling assays and 13,912
underground drilling assays.

GRADE / THICKNESS CALCULATIONS

Composite intervals were based on a minimum cut-off grade of 2.75
g/t over a minimum true width of 1.2 metres. Grade capping was set at
90 g/t affecting 29 assays. An allowance of 2 metres for internal
dilution was employed factoring in the stockwork and replacement
veining style of gold mineralization. True widths were calculated by
applying a 30% correction factor to the assay core lengths.

A total of 499 grade (grams) / true width (m) composites were
manually calculated from the surface drilling database. The composites
having a grams x m product greater than 30 total 46.

A typical example of some of the high grade composites are the
historic holes KC99-131, 155W, KC00-176 and 159 which were drilled by
Kinross exploring the property in 1999 and 2000. Please note that drill
holes KC99-131,137,155W as originally reported above have been cut to
90g/t and are reported as true widths.

The table below is a sampling of some of the higher grade
composites.

TABLE: SELECTED COMPOSITES CUT TO 90 GRAMS

//st

HOLE_ID        FROM     TO       GRADE (G) CUT      TRUE WIDTH (M)   G X M
90 G

CL_KC99-131    341      350.6    30.5               7.38             225

CL_KC00-176    327.2    333.95   34.78              5.19             181

CL_KC00-159    298.5    306.5    24.26              6.15             149

CL_KC99-137    409.13   411.13   30.83              2.31             71

CL_KC99-155W   650.8    655      17.91              3.23             58

//et

A total of 515 grade (grams) / true width (m) composites were
manually calculated from the underground drilling database. The
composites having a grams x m product greater than 30 total 70. Refer
to the Sage website - www.sagegoldinc.com - longitudinal plot of the
grade thickness model.

MODELING PARAMETERS

Since the four major mineralized vein systems are stratabound in
nature and located proximal to the steeply dipping Pipestone Thrust
Fault, a longitudinal projection of the centroids of the composite
intervals for each hole was projected to a vertical WEST/ EAST plane.
The grade estimation parameters employed a search radius of 60 metres
selecting 13 nearest grade composite by Inverse Distance Squared method
in 3D, then plotting and contouring the values on a 2D longitudinal
section where the drill holes pierce the section. The G X M product was
contoured in colour ranges set at 5 to 8; 8 to 13; 13 to 21; 21 to 34;
34 to 55; 55 to 89; ) 89.

INTERPRETATION

The grade / thickness geological model reveals six major
structures cross-cutting the main mine stratigraphy and the Pipestone
Thrust Fault. The orientation and arrangement of these structures also
displays a remarkable symmetry with structural lineaments interpreted
from airborne magnetics. In a regional context, four of these arcuate
structures exhibit the habit of imbricate thrust faults facing to the
southeast. They conform with right lateral strike-slip deformation
during the later stages of the D2 deformation compressional juxtaposing
the Kidd-Munro ultramafic assemblage with the Davidson-Tisdale felsic
volcanics. The imbricate thrust faults have orientations varying from
55 degrees to 70 degrees and transect the grade / thickness model at
shallow angles to the west. A conjugate series of four back thrust
faults with orientations at Az 150 degrees steeply crosscut the
longitudinal section facing to the east. These faults served as
important fluid corridors enhancing gold enrichment processes.

The geological, modeling computations and interpretations of this
news release has been reviewed and approved by Sage's consulting
geologist, Peter Hubacheck, P. Geo, who is a Qualified Person ("QP") as
defined in National Instrument 43-101. Len MacKenzie, P.Geo. guided the
geologic modeling of the grade / thickness exercise.

About Sage Gold

The Company is a mineral exploration and development company which
has primary interests in near-term production and exploration
properties in Ontario. Its main properties are the Clavos Gold
property, 100% owned, in Timmins and the 100% owned Onaman property and
other exploration properties in the Beardmore-Geraldton Gold Camp.
Technical reports and information relating to the properties can be
obtained from the System for Electronic Document Analysis and Retrieval
(SEDAR) website at www.sedar.com and www.sagegoldinc.com.

Sage currently plans to complete a reserve estimate and a
pre-feasibility study on the Clavos property. In the event that a
production decision is made that is not based on a feasibility study of
mineral reserves demonstrating economic and technical viability
prepared in accordance with National Instrument 43-101, readers are
cautioned that there is increased uncertainty and higher risk of
economic and technical failure associated with such a production
decision.

CAUTIONARY STATEMENT: Neither the TSX Venture Exchange nor its
Regulation Services Provider (as that term is defined in the policies
of the TSX Venture Exchange) accepts responsibility for the adequacy or
accuracy of this release. This news release may contain forward looking
information and the Company cautions readers that forward looking
information is based on certain assumptions and risk factors that could
cause actual results to differ materially from the expectations of the
Company included in this news release. This news release includes
certain "forward-looking statements", which often, but not always, can
be identified by the use of words such as "believes", "anticipates",
"expects", "estimates", "may", "could", "would", "will", or "plan".
These statements are based on information currently available to the
Company and the Company provides no assurance that actual results will
meet management's expectations. Forward-looking statements include
estimates and statements with respect to the Company's future plans,
objectives or goals, to the effect that the Company or management
expects a stated condition or result to occur.

Since forward-looking statements are based on assumptions and
address future events and conditions, by their very nature they involve
inherent risks and uncertainties. Actual results relating to, among
other things, results of exploration, metallurgical processing, project
development, reclamation and capital costs of the Company's mineral
properties, and the Company's financial condition and prospects, could
differ materially from those currently anticipated in such statements
for many reasons such as, but are not limited to: failure to identify
mineral resources; failure to convert estimated mineral resources to
reserves; the preliminary nature of metallurgical test results; delays
in obtaining or failures to obtain required governmental, environmental
or other project approvals; political risks; uncertainties relating to
the availability and costs of financing needed in the future; changes
in equity markets, inflation, changes in exchange rates; fluctuations
in commodity prices; delays in the development of projects; capital and
operating costs varying significantly from estimates and the other
risks involved in the mineral exploration and development industry; and
those risks set out in the Company's public documents filed on SEDAR.
This list is not exhaustive of the factors that may affect any of the
Company's forward-looking statements. These and other factors should be
considered carefully and readers should not place undue reliance on the
Company's forward-looking statements. Although the Company believes
that the assumptions and factors used in preparing the forward-looking
information in this news release are reasonable, undue reliance should
not be placed on such information, which only applies as of the date of
this news release, and no assurance can be given that such events will
occur in the disclosed time frames or at all. The Company disclaims any
intention or obligation to update or revise any forward-looking
information, whether as a result of new information, future events or
otherwise, other than as required by law.

Shares 68,486,783
TSX Venture closing price for SGX-V
Date: 2017/05/02
Closing Price: 0.18

TEL:  416-204-3170  Nigel Lees, President and CEO
Sage Gold Inc.
EMAIL:  nlees@sagegoldinc.com
INTERNET:  www.sagegoldinc.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1712200009TS11712200786-05155420170503