Source	MARKET NEWS
Date	05/03/2017
Time	05:09:17 AM

Company	 Tinka Resources Limited
Title	Extends High 
Grade Zinc Mineralization at South





    CDNX Symbol: TK











Press Release





TINKA RESOURCES LTD ("TK-V;TKRFF-0")
- Extends High Grade Zinc Mineralization at South Ayawilca

Tinka Resources Limited ("Tinka" or the "Company") is pleased to
announce results from four new drill holes at its 100%-owned Ayawilca
zinc project in central Peru.  Three holes were drilled into the new
discovery area at South Ayawilca, with one drilled at West Ayawilca.
These new results confirm high grade zinc mineralization at South
Ayawilca is associated with gently dipping massive to semi-massive
sulphide replacements of carbonate and clastic sediments.  Hole A17-061
is approximately 80 metres off-section from holes A17-056 and A17-057
(April 3, 2017, TK press release).  Zinc mineralization is all sulphide
(sphalerite, marmatite) accompanied by minor galena and iron sulphides.


We have now released results for six of the planned 25 to 30 holes
in the 2017 drill program.  Three drill rigs are currently turning at
South Ayawilca, with an additional rig to be mobilized to test the Zone
3 area shortly.

Key Highlights:

Hole A17-061 (South Ayawilca):

//st

* 18.6 metres at 10.4 % zinc & 52 g/t silver from 184.0 metres depth
(includes 3.1 metres no recovery assigned a zero grade), including:
* 2.6 metres at 23.6 % zinc, 2.4 % lead & 192 g/t silver from 196.2.0
metres depth; and

* 13.4 metres at 18.7 % zinc, 57 g/t silver & 463 g/t indium from 220.0
metres depth, including:
* 7.9 metres at 29.3 % zinc, 71 g/t silver & 719 g/t indium from 224.1
metres depth; and

* 1.8 metres at 37.0 % zinc, 85 g/t silver & 808 g/t indium from 265.0
metres depth.

//et

Hole A17-060 (South Ayawilca):

//st

* 4.5 metres at 15.0 % zinc, 20 g/t silver & 383 g/t indium from 275.0
metres depth; and
* 30.5 metres at 3.4% zinc & 10 g/t silver from 298.0 metres depth,
including:
* 8.6 metres at 5.1 % zinc & 11 g/t silver from 303.4 metres depth.

//et

Hole A17-056A (continuation of A17-056):

//st

* 4.1 metres at 18.6 % zinc, 27 g/t silver & 224 g/t indium from 309.0
metres depth, including:
* 2.6 metres at 27.3 % zinc, 38 g/t silver & 336 g/t indium from 310.5
metres depth.

//et

Hole A17-058 (West Ayawilca):

//st

* 4.2 metres at 20.2 % zinc, 4.2 % lead & 329 g/t silver from 103.5
metres depth (vein);
* Abandoned at 301 metres prior to target depth.

//et

Dr. Graham Carman, Tinkas President and CEO, stated: "This set of
drill results continues to show significant thicknesses of high grade
zinc mineralization at South Ayawilca, as we step out from the recent
discovery holes.  The zinc bodies dip gently to the south, with the
thicker zones of mineralization lying between two interpreted
west-dipping northeast-trending faults approximately 250 metres apart,
appearing to thicken towards the north. These structures were likely
important conduits for the zinc mineralization.  The mineralization at
South Ayawilca remains open along strike in both directions (see Figure
1 & Figure 2). At West Ayawilca, additional holes are required to fully
test the extensions with more holes planned."Dr. Carman continued,
"Drilling continues with three rigs at South Ayawilca, focusing on
expanding the new zinc discovery to the northeast towards the Central
Ayawilca resource, and to provide confidence of continuity of
mineralization. While our resource expansion drilling continues at
Ayawilca, we are also looking forward to commencing the drilling at
Zone 3."

True thicknesses of the zinc intersections are estimated to be at
least 85% of the downhole thickness, except where otherwise noted in
Table 1. All significant results of the 2017 program are summarized in
Table 1 with the strongest zinc intercepts in bold text.

Table 1.  Summary of 2017 Drill Results

//st

Drill hole From m To m   Interval Zn %  Pb   Ag   Indium Reported
m              %    g/t  g/t

A17-056 1  90.30  90.65  0.35     29.0  0.4  82   443    April 3 '17

And        113.00 113.40 0.40     31.2  0.0  85   759    April 3 '17

And        126.00 189.90 63.90    5.6   0.1  17   29     March 6 '17

Including  127.50 145.40 17.90    11.6  0.2  36   20     March 6 '17

Including  127.50 133.30 5.80     22.5  0.3  77   50     March 6 '17

And        199.20 204.70 5.50     5.8   0.1  6    38     April 3 '17

And        228.50 233.70 5.20     12.9  0.0  11   162    March 6 '17

And        242.00 293.90 51.90    10.1  0.1  624  233    April 3 '17

Including  279.00 293.90 14.90    20.6  0.2  1524 441    April 3 '17

Including  279.00 285.40 6.40     37.5  0.4  301  916    April 3 '17

A17-056A   286.50 296.00 9.50     9.3   0.3  19   88     here

And        309.00 313.10 4.10     18.6  0.1  27   224    here

Including  310.50 313.10 2.60     27.3  0.1  38   336    here

A17-057    84.90  86.35  1.45     24.8  0.0  62   157    April 3 '17

And        143.70 144.50 0.80     40.4  0.1  138  261    April 3 '17

And        157.60 197.70 40.10    9.1   0.2  22   168    April 3 '17

Including  168.20 177.80 9.60     16.8  0.1  22   299    April 3 '17

And        227.15 234.90 7.75     3.5   0.2  21   85     April 3 '17

And        264.00 279.30 15.30    20.0  2.5  102  263    April 3 '17

including  265.75 269.00 3.25     34.5  2.1  96   196    April 3 '17

including  272.50 277.70 5.20     32.5  1.3  69   639    April 3 '17

A17-058    103.50 107.70 4.205    20.2  4.2  3294 15     here

and        133.25 134.35 1.105    30.3  3.2  500  61     here

Hole did not reach target, lost at 301 metres depth in
sandstone
A17-059    results awaited

A17-060    262.40 264.40 2.00     14.8  0.0  35   1178   here

and        275.00 279.50 4.50     15.0  0.0  20   383    here

and        298.00 328.50 30.52    3.4   0.2  10   38     here

including  303.40 312.00 8.60     5.1   0.1  11   6      here

A17-061    122.70 150.50 27.80    4.4   0.1  18   24     here

including  145.70 147.50 1.805    27.2  0.0  32   157    here

and        184.00 202.60 18.63    10.4  0.5  52   59     here

including  196.20 198.80 2.60     23.6  2.4  192  19     here

including  201.90 202.60 0.70     28.7  3.6  202  41     here

and        220.00 233.40 13.40    18.7  0.9  57   463    here

including  224.10 230.00 7.90     29.3  0.8  71   719    here

and        265.00 266.80 1.80     37.0  0.2  85   808    here

1 hole lost at 293.9 metres; wedged and completed as A17-056A to 376
metres depth

2 includes 0.6 m with no core recovery from 315.2 to 315.8 m; this
interval was given a zero grade

3 includes 3.1 m with no core recovery from 198.8 to 201.9 m; this
interval was given a zero grade

4 includes a silver assay cut at 1000 g/t

5 high grade vein intercepts with variable true thicknesses

Note: Assays are calculated using a zinc only cut off grade of 2% over 6
metres

//et

Notes on sampling and assaying:Drill holes are diamond HQ or NQ
size core holes with recoveries generally above 80% and often close to
100%. The drill core is marked up, logged, and photographed on site.
The cores are cut in half at the Company's core storage facility, with
half-cores stored as a future reference.  Half-core is bagged on
average over 1 to 2 metre composite intervals and sent to ALS
laboratory in Lima, an ISO 9001:2000-registered laboratory, for assay
in batches.  Standards and blanks are inserted into each batch prior to
departure from Tinka's core storage facilities.  At the laboratory
samples are dried, crushed to 100% passing 2mm, then 500 grams
pulverized for multi-element analysis by ICP (MS) using multi-acid
digestion. Samples assaying over 1% zinc, lead, or copper are
re-assayed using precise ore-grade AAS techniques.

Table 2.  Summary of Drill Collar Information

//st

Drill Hole WGS84East WGS84North Total Elevation Azimuth Dip
depth (m)
(m)

A17-056    333046    8845062    293.9 4201      300     -75

A17-056A   333046    8845062    376.4 4201      300     -75

A17-057    333046    8845062    477.0 4201      300     -55

A17-058    332557    8845657    301.0 4305      040     -82

A17-059    332840    8845192    248.9 4202      120     -85

A17-060    333174    8845005    358.4 4220      300     -70

A17-061    333058    8844996    326.9 4190      290     -67

//et

Figure 1.   Simplified cross section of holes A17-056, A17-057 &
A17-060 (looking northeast)

Figure 2.   Map of 2017 Ayawilca drill program on airborne RTP
magnetics (red = magnetic sources)

The qualified person, Dr. Graham Carman, Tinka's President and
CEO, and a Fellow of the Australasian Institute of Mining and
Metallurgy, has reviewed and verified the technical contents of this
release.

On behalf of the Board,

"Graham Carman"Dr. Graham Carman, President & CEO

About Tinka Resources LimitedTinka is an exploration and
development company with its flagship property being the 100%-owned
Ayawilca carbonate replacement deposit (CRD) in the zinc-lead-silver
belt of central Peru, 200 kilometres northeast of Lima. The Ayawilca
Zinc Zone has an Inferred Mineral Resource of 18.8 Mt at 5.9 % zinc,
0.2 % lead, 15 g/t silver & 74 g/t indium, and a Tin Zone Inferred
Mineral Resource of 5.4 Mt at 0.76 % tin, 0.31 % copper & 18 g/t
silver. Both resources are open for expansion (May 25, 2016). The
Silver Zone at Colquipucro, 2 km north of the Zinc Zone, has an
Indicated Mineral Resource of 2.9 Mt at 112 g/t silver for 10.4 Moz
silver and an Inferred Mineral Resource of 2.2 Mt at 105g/t silver for
7.5 Moz silver hosted by oxidized lenses between the surface and 80
metres depth (Feb. 26, 2015).

Forward Looking Statements: Certain information in this news
release contains forward-looking statements and forward-looking
information within the meaning of applicable securities laws
(collectively "forward-looking statements").  All statements, other
than statements of historical fact are forward-looking statements.
Forward-looking statements are based on the beliefs and expectations of
Tinka as well as assumptions made by and information currently
available to Tinka's management.  Such statements reflect the current
risks, uncertainties and assumptions related to certain factors
including, without limitations, drilling results, the Company's
expectations regarding mineral resource calculations, capital and other
costs varying significantly from estimates, production rates varying
from estimates, changes in world metal markets, changes in equity
markets, uncertainties relating to the availability and costs of
financing needed in the future, equipment failure, unexpected
geological conditions, imprecision in resource estimates or metal
recoveries, success of future development initiatives, competition,
operating performance, environmental and safety risks, delays in
obtaining or failure to obtain necessary permits and approvals from
local authorities, community agreements and relations, and other
development and operating risks. Should any one or more of these risks
or uncertainties materialize, or should any underlying assumptions
prove incorrect, actual results may vary materially from those
described herein.  Although Tinka believes that assumptions inherent in
the forward-looking statements are reasonable, forward-looking
statements are not guarantees of future performance and accordingly
undue reliance should not be put on such statements due to the inherent
uncertainty therein. Except as may be required by applicable securities
laws, Tinka disclaims any intent or obligation to update any
forward-looking statement.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release

Contact Information:

For further information:  Investor Information: www.tinkaresources.com, Rob
Bruggeman, 1.416.884.3556, rbruggeman@tinkaresources.com; Company Contact:
Mariana Bermudez, 1.604.699.0202, info@tinkaresources.com

RELATED LINKS
www.tinkaresources.com
______________________________
_______________________________________________
TSX Venture closing price for TK-V
Date: 2017/05/02
Closing Price: 0.75
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1712200004TS11712200720-05063520170503