Source	MARKET NEWS
Date	05/08/2017
Time	06:01:23 AM

Company	 Azimut Exploration Inc.
Title	Identifies a Significant and Continuous Gravity





    CDNX Symbol: AZM











Press Release





Identifies a Significant and Continuous Gravity Anomaly over a HighGrade 
Chromite Zone at Eastmain West (Cr, PGE, Ni) --->@NEWS RELEASE
AZIMUT EXPLORATION INC ("AZM-V;AZMTF-0")
- Identifies a Significant and Continuous Gravity Anomaly
- over a High-Grade Chromite Zone at Eastmain West (Cr, PGE, Ni)

Azimut Exploration Inc. ("Azimut") is pleased to report the
results of a recent ground-based gravity survey on its 100%-owned
Eastmain West Property in the James Bay region of Quebec. A linear
gravity anomaly has been defined along the entire length of a 1.2 km by
900 m grid on the central part of a 4-km-long ultramafic-mafic horizon.
The gravity anomaly is spatially associated to the high-grade Dominic
Prospect, where channel sampling recently yielded 17.21% Cr2O3 over
7.54 m including 33.2% Cr2O3 over 3.55 m (see press release of January
19, 2017). The next phase of work will consist of diamond drilling to
determine the chromite potential of the anomaly.

The residual gravity anomaly is 1.2 km long and up to 200 m wide,
and remains open to the north and south. According to the
interpretation of a property-scale airborne magnetic and
electromagnetic survey, the position of the gravity anomaly is
stratigraphically high in the intrusion and favourable for chromite
sills.

Inversion modelling was performed to construct subsurface 3D
models of possible causative bodies to explain the gravity anomaly. The
results suggest a body of significant strike, generally more developed
at depth, below 50 m. It could reflect a subvertically dipping chromite
body of substantial size, or disseminations or thin interdigitations of
chromite within high-density host rocks (dunite, harzburgite).

The gravity method is a proven geophysical tool for delineating
the footprints of major chromite deposits in the Ring of Fire in
Northern Ontario. As an example, a strong gravity anomaly marks the
1,400-m strike length of the Big Daddy deposit owned by Noront
Resources Ltd and KWG Resources Inc. (measured and indicated resource
of 29.1 Mt at 31.7% Cr2O3, inferred resource of 3.4 Mt at 28.1% Cr2O3)
(from public data). The geological context and chromite mineralization
of the Eastmain West Property share many features with the Ring of Fire
chromite-bearing intrusions, as highlighted by several independent
studies (e.g., Geological Survey of Canada Open File 7856, 2015). In
addition to chromite, the geological setting of the Eastmain West
Property has significant potential for massive sulphide Ni-Cu-PGE
mineralization.

The Eastmain West Property covers 66 claims with a surface area of
35 km2. Situated in the Province of Quebec, recognized as one of the
best mining jurisdictions worldwide, the project is close to major
infrastructure (permanent roads, power lines, airports), 45 km
northeast of the municipality of Nemaska, and would have access to
seaborne shipping via James Bay.

This project complements Azimut's strategic gold position in the
James Bay region, which comprises 15 properties. Four of the Company's
gold projects are active partnerships with Goldcorp Inc., Hecla Mining
Company, Eastmain Resources Ltd and Everton Resources Inc., and four
others are part of a regional Strategic Alliance with SOQUEM covering
176,300 km2.

The geophysical survey was performed by Geosig Inc., a geophysical
consulting firm based in the city of Quebec. Modelling and
interpretation was conducted by Jeremy S. Brett, Senior Geophysical
Consultant at MPH Consulting Limited of Toronto.

This press release was prepared by geologist Jean-Marc Lulin,
acting as Azimut's Qualified Person under National Instrument 43-101.

Azimut is a mineral exploration company with a core business
centred on target generation and concurrent partnership development.
Targets are identified using advanced processing of large geoscientific
databases, enhanced by extensive exploration know-how. Azimut holds a
strategic position for gold and base metals in Quebec. The Company has
45.4 million shares outstanding.

Jean-Marc Lulin, President and CEO, Tel.: (450) 646-3015, Fax:
(450) 646-3045, info@azimut-exploration.com, www.azimut-exploration.com

______________________________
_______________________________________________
TSX Venture closing price for AZM-V
Date: 2017/05/05
Closing Price: 0.33
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1712700016TS11712701040-06002320170508