Source	CANADA NEWSWIRE
Date	05/08/2017
Time	03:33:05 AM

Company	 Azimut Exploration Inc.
Title	Azimut identifies a significant and continuous gravity anomaly over a
high-grade chromite zone at Eastmain West (Cr, PGE, Ni)





    CDNX Symbol: AZM











Press Release




" BC-Azimut-EastmainWest   05-08 0606
News release via CNW Telbec, Montreal 514-878-2520 -ME-

Attention Business Editors:
^Azimut identifies a significant and continuous gravity anomaly over a
high-grade chromite zone at Eastmain West (Cr, PGE, Ni)@

Symbol: AZM.TSX Venture
LONGUEUIL, QC, May 8, 2017 /CNW Telbec/ - Azimut Exploration Inc.
("Azimut") (TSXV: AZM) is pleased to report the results of a recent
ground-based gravity survey on its 100%-owned Eastmain West Property in the
James Bay region of Quebec. A linear gravity anomaly has been defined along
the entire length of a 1.2 km by 900 m grid on the central part of a 4-km-long
ultramafic-mafic horizon. The gravity anomaly is spatially associated to the
high-grade Dominic Prospect, where channel sampling recently yielded 17.21%
Cr2O3 over 7.54 m including 33.2% Cr2O3 over 3.55 m (see press release of
January 19, 2017). The next phase of work will consist of diamond drilling to
determine the chromite potential of the anomaly.
The residual gravity anomaly is 1.2 km long and up to 200 m wide, and
remains open to the north and south. According to the interpretation of a
property-scale airborne magnetic and electromagnetic survey, the position of
the gravity anomaly is stratigraphically high in the intrusion and favourable
for chromite sills.
Inversion modelling was performed to construct subsurface 3D models of
possible causative bodies to explain the gravity anomaly. The results suggest
a body of significant strike, generally more developed at depth, below 50 m.
It could reflect a subvertically dipping chromite body of substantial size, or
disseminations or thin interdigitations of chromite within high-density host
rocks (dunite, harzburgite).
The gravity method is a proven geophysical tool for delineating the
footprints of major chromite deposits in the Ring of Fire in Northern Ontario.
As an example, a strong gravity anomaly marks the 1,400-m strike length of the
Big Daddy deposit owned by Noront Resources Ltd and KWG Resources Inc.
(measured and indicated resource of 29.1 Mt at 31.7% Cr2O3, inferred resource
of 3.4 Mt at 28.1% Cr2O3) (from public data). The geological context and
chromite mineralization of the Eastmain West Property share many features with
the Ring of Fire chromite-bearing intrusions, as highlighted by several
independent studies (e.g., Geological Survey of Canada Open File 7856, 2015).
In addition to chromite, the geological setting of the Eastmain West Property
has significant potential for massive sulphide Ni-Cu-PGE mineralization.
The Eastmain West Property covers 66 claims with a surface area of 35
km2. Situated in the Province of Quebec, recognized as one of the best mining
jurisdictions worldwide, the project is close to major infrastructure
(permanent roads, power lines, airports), 45 km northeast of the municipality
of Nemaska, and would have access to seaborne shipping via James Bay.
This project complements Azimut's strategic gold position in the James
Bay region, which comprises 15 properties. Four of the Company's gold projects
are active partnerships with Goldcorp Inc., Hecla Mining Company, Eastmain
Resources Ltd and Everton Resources Inc., and four others are part of a
regional Strategic Alliance with SOQUEM covering 176,300 km2.
The geophysical survey was performed by Geosig Inc., a geophysical
consulting firm based in the city of Quebec. Modelling and interpretation was
conducted by Jeremy S. Brett, Senior Geophysical Consultant at MPH Consulting
Limited of Toronto.
This press release was prepared by geologist Jean-Marc Lulin, acting as
Azimut's Qualified Person under National Instrument 43-101.
Azimut is a mineral exploration company with a core business centred on
target generation and concurrent partnership development. Targets are
identified using advanced processing of large geoscientific databases,
enhanced by extensive exploration know-how. Azimut holds a strategic position
for gold and base metals in Quebec. The Company has 45.4 million shares
outstanding.

SOURCE Azimut Exploration Inc.



View original content:
http://www.newswire.ca/en/releases/archive/May2017/08/c7802.html

-0-                           05/08/2017
/For further information: Jean-Marc Lulin, President and CEO, Tel.: (450)
646-3015, Fax: (450) 646-3045, info(at)azimut-exploration.com,
www.azimut-exploration.com/
/Web Site: http://www.azimut-exploration.com /
(AZM.)

CO:  Azimut Exploration Inc.
ST:  Quebec
IN:  MNG
SU:  SVY

-30-