Source	MARKET NEWS
Date	05/10/2017
Time	06:34:48 AM

Company	 Broadway Gold Mining Ltd.
Title	Continued Drill Success At Madison Underground:





    CDNX Symbol: BRD











Press Release





Continued Drill Success At Madison Underground: --->@NEWS RELEASE
BROADWAY GOLD MINING LTD ("BRD-V;BDWYF-0")
- Continued Drill Success At Madison Underground:
- 41.6 G/t Gold Over 11 Meters

Broadway Gold Mining Ltd. ("Broadway" or the "Company") is pleased
to announce additional high-grade gold results and provide a geophysics
and drilling update from underground exploration at its 100%-owned
Madison copper-gold project in the historic Butte-Anaconda mining
region of Montana.

Further to our May 3, 2017 press release in which the Company
announced over 30 meters of 24.5 grams per tonne gold (g/t Au) in
UG17-05, we are pleased to report assay highlights from the second
hole, U17-06:

//st

* 41.6 g/t Au over 11 meters.
* 0.9 meter intercepts ranging from 8.69 to 90.1 g/tAu.
* Seven of the 12 samples returned values in excess of 34.3 g/tAu.

//et

Highlights

//st

* New high-grade massive sulphide target has been confirmed by both
underground and surface drilling and remains open to depth.
* Geophysics show new zones exist as extensions of prior trial mining
work.
* The massive sulphide and garnet epidote zone continues to display
consistent gold concentrations over 7.5 to 30-meter widths.
* Five underground holes and 13 surface holes are in assay process to be
released near term.
* Rehabilitated underground workings, infrastructure, heavy equipment and
Small Miners Exclusion Permit will allow for near-term evaluation of
high-grade bulk sampling.

//et

"Drilling continues to return excellent results, and we are seeing
consistency of grades across our target zones at Madison. The strong
correlation between assay results and geophysics is also extremely
encouraging," said Duane Parnham, President and CEO for Broadway
Mining. "Mineralization remains open at depth, and we look forward to
reporting additional results from underground and surface drilling."

Geophysical contractor Peter E. Walcott & Associates recently
completed a Mise ala Masse electrical geophysical survey to trace the
location, shape and extent of the massive sulphide zone intersected in
the underground drilling, utilizing access through hole UG17-06. The
survey confirmed the ovoid cylindrical shaped of the sulphide body and
its western plunge to depth. Additional Mise ala Masse surveying is
planned as additional holes are drilled into the massive sulphide.

Recently completed surface drill hole C17-20 successfully tested
the down dip extension on the massive sulfide 41 metres below the 600
level. Parallel to its short axis, it intersected a zone of massive
sulphides between 146.1 and 153.8 metres. True width of this
intersection has not yet been determined. Broadway cautions investors
these are visible observations of the core mineralization and assay
results have not yet been received from the laboratory.

Time Domain Pulse electromagnetics (EM) was also completed over a
number of the shallower geophysical targets identified in the earlier
IP survey (see press release dated March 8, 2017). A number of these
anomalies were further substantiated and are currently being
prioritized for follow-up drilling. In addition, Peter E. Walcott and
Associates is currently expanding the earlier IP survey to cover the
newly acquired contiguous claim blocks to the south and west (see news
release dated March 29, 2017).

Assay Results Summary

//st
-------------------------------------------------
Hole               From         To       Interval  Copper (%)     Gold

(ft)   (m)  (ft)   (m)  (ft)   (m)            (g/t)
(oz/t)
---------------------------------------------------------------------------
-
U17-06             27    8.2   63   19.2   36   11.0    0.384   41.65  1.21
---------------------------------------------------------------------------
-
including  30    9.1   45   13.7   15    4.6    0.271   51.84  1.51
---------------------------------------------------------------------------
-
including  57   17.4   60   18.3    3    0.9    0.368   90.1   2.63
---------------------------------------------------------------------------
-
//et

True width is estimated at 70 percent core length

The complete assay results for the intervals, accompanying drill
plan and geophysical plot can be found on the current exploration page
of the Company's website.

U17-06 was drilled on an azimuth of 231 degrees at a dip of -25
degrees, parallel to the longer axis of the steeply dipping ovoid
cylindrical massive sulfide body plunging near vertical at 15 degrees
south-southwest and measuring roughly 30 meters by 16.5 meters on the
600 level, and containing massive sulphides with pyrite, pyrrhotite and
chalcopyrite. The U17-06 intersection is on the southeast edge of the
sulfide as shown on the drilling plan and consisted of massive sulfide
inter-fingered with epidote-garnet skarn. Mineralization is described
as 5% to 30% pyrite and 1% to 3% chalcopyrite.

All analyses were completed at the North Vancouver ALS Minerals
laboratory, an ISO/IEC 17025:2005 certified facility. Broadway is
utilizing a program of third-party standards and blanks inserted at
regular intervals through the sample stream as its QA/QC program.
Groundhog Mining of Dillon, Montana is the contractor performing the
underground drilling program. AK Drilling, Inc. of Butte, Montana is
the contractor performing the surface drilling programs.

Sample Preparation and Quality Control

Supervision, organization and splitting of drilling core samples
were undertaken by company personnel. Samples were collected at 0.9
metre intervals from half core samples. Samples were catalogued by
Broadway geologists and stored in a secure location. Certified
reference standards were placed in the sample stream of each drill hole
at random intervals. Blank material was also inserted at random
intervals. Samples were packed into rice bags, zap strapped and
securely stored until they were turned over to the local trucking
company for transport to the ALS Minerals Laboratory in North
Vancouver, BC.

Laboratory Quality Assurance/Quality Control

Quality control samples from the lab include numerous control
blanks, duplicates and standards. Reference standards used include
OREAS-904, OREAS-45b, OGGeo08 and PGMS25. No issues were noted with
analytical accuracy or precision.

Assay Techniques

Three different assay procedures were designed by ALS Minerals for
the samples, based on the presence of copper sulfides or oxides, and
native copper. The standard assay procedure of Au-ICP21 and Cu-ICP61
was applied to most of the samples. Au-ICP21 is a 30 gram fire assay
with an ICP-AES finish. ICP61 is a 4 acid digestion of a one gram
sample with an ICP finish. Samples with visible copper mineralization
received a Cu-OG62 copper analysis, a four acid digestion of a 0.5
grams sample with ICP-AES finish. OG62 has a copper range from 0.001 to
40%, while the ICP61 analysis has a copper maximum range of 10,000 ppm.
Samples with visible native copper received a duplicate Cu-ICP61
analysis followed by a duplicate Cu-OG62 analysis that included a
WSH-22 procedure where the pulverizers are cleaned with barren material
after every sample. Over-limit copper values from the ICP61 analyses
received an OG62 procedure to determine the final Cu grade.

Qualified Person

R. Tim Henneberry, P.Geo., a Director of Broadway and a Qualified
Person as defined by NI 43-101, has reviewed and approved the technical
information contained in this news release.

About Broadway Gold Mining Ltd.

Broadway Gold Mining Ltd. is a resource company focused on
development-stage projects with advanced exploration potential. The
company owns a 100% interest in the Madison copper-gold project located
in the Butte-Anaconda mining region of Montana, USA. The Madison
project is permitted for exploration and contains a past-producing
underground mine that Broadway has refurbished. While actively
expanding known copper and gold zones that remain open for development
in the mine's perimeter, the company's exploration program has
identified new anomalies across its extensive land package that provide
compelling drill targets that are believed to be associated with
large-scale porphyry mineralization.

Neither the TSX Venture Exchange Inc. nor its regulation services
provider (as that term is defined in the policies of The TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

For more information:
Duane Parnham
President and CEO
Broadway Gold Mining
1-800-680-0661
info@broadwaymining.com
www.broadwaymining.com

Media:
Adam Bello
Primoris Group Inc.
+1 416.489.0092
media@primorisgroup.com
______________________________________
_______________________________________________
TSX Venture closing price for BRD-V
Date: 2017/05/09
Closing Price: 0.65
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1712900012TS11712901286-06305120170510