Source	MARKET NEWS
Date	05/10/2017
Time	06:28:49 AM

Company	 Sage Gold Inc.
Title	Clavos Drill 
Results New Gold Zone





    CDNX Symbol: SGX











Press Release





SAGE GOLD INC ("SGX-V;SGGDF-0")
- Clavos Drill Results - New Gold Zone

Sage Gold Inc. 'Sage' has completed the surface drilling program at
its Clavos gold property located 32 kms east north east of Timmins,
Ontario in the prolific East Timmins Gold Camp.

The drill program has yielded three important results; the
continuity of gold mineralization across the gap between the main mine
zone and the 960 zone, the discovery of a new gold zone (Sediment 2
zone CL 17-07 4.09g/t over 4.2 metres) 100 metres south of the existing
sediment zone and the Footwall intersection in CL-17-08 of 5.15g/t over
3.9 metres. The intersection in hole CL-17-08 opens up approximately
300 metres of strike length of potential mineralization west of the
western end of the 150m west level in the upper part of the existing
mine workings.

DRILLING RESULTS

//st
---------------------------------------------------------------------------
-
HOLE_ID                         EASTING NORTHING ELEVATION   AZ  DIP
LENGTH
---------------------------------------------------------------------------
-
CL-17-01                         514765  5384659       280  180  -55
266
---------------------------------------------------------------------------
-
CL-17-01
---------------------------------------------------------------------------
-
CL-17-02                         514645  5384682       282  180  -57
347
---------------------------------------------------------------------------
-
CL-17-02
---------------------------------------------------------------------------
-
CL-17-03                         514585  5384669       278  180  -59
386
---------------------------------------------------------------------------
-
CL-17-03
---------------------------------------------------------------------------
-
CL-17-04                         514705  5384454       274  360  -62
284
---------------------------------------------------------------------------
-
CL-17-05                         514525  5384399       273  360  -55
374
---------------------------------------------------------------------------
-
CL-17-05
---------------------------------------------------------------------------
-
CL-17-06                         514437  5384683       279  180  -65
372
---------------------------------------------------------------------------
-
CL-17-07                         514484  5384681       277  180  -65
387
---------------------------------------------------------------------------
-
CL-17-07
---------------------------------------------------------------------------
-
CL-17-08                         512515  5384678       273  360  -55
188
---------------------------------------------------------------------------
-
CL-17-09                         512456  5384697       273  360  -55
269
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
AVG
TRUE
HOLE_ID                           FROM     TO        ZONE    GRADE
WIDTH
---------------------------------------------------------------------------
-
CL-17-01                         163.5  164.8     CONTACT     1.69
0.9
---------------------------------------------------------------------------
-
CL-17-01                         174.5  177.3  SEDIMENT 1     3.36
2.0
---------------------------------------------------------------------------
-
CL-17-02                           149 152.05    FOOTWALL     4.32
2.1
---------------------------------------------------------------------------
-
CL-17-02                           228  229.8     CONTACT    16.76
1.3
---------------------------------------------------------------------------
-
CL-17-03                         181.6  182.6 HANGINGWALL     3.32
0.7
---------------------------------------------------------------------------
-
CL-17-03                         197.4  199.4     CONTACT     4.93
1.4
---------------------------------------------------------------------------
-
CL-17-04                         191.4  192.4 HANGINGWALL     1.59
0.7
---------------------------------------------------------------------------
-
CL-17-05                        341.65 343.15  SEDIMENT 1     3.12
1.1
---------------------------------------------------------------------------
-
CL-17-05                        364.75  366.5     CONTACT     2.56
1.2
---------------------------------------------------------------------------
-
CL-17-06                           258  263.5     CONTACT     4.43
2.8
---------------------------------------------------------------------------
-
CL-17-07                           268    269     CONTACT     3.89
0.7
---------------------------------------------------------------------------
-
CL-17-07                           375    381  SEDIMENT 2     4.09
4.2
---------------------------------------------------------------------------
-
CL-17-08                           144  149.5    FOOTWALL     5.15
3.9
---------------------------------------------------------------------------
-
CL-17-09                            91   96.7     CONTACT     1.83
4.0
---------------------------------------------------------------------------
-
//et

All drill intersections are based on calculated true widths

Nigel Lees, President and CEO commented: "The surface drill
program has been successful in establishing a mineralized corridor from
section 514425E, the 'Main Zone' to the western end of the 960 zone,
the 'Gap', and in locating new mineralized intersections in holes
CL-17-08 and CL-17-09 west of the 150 metre west level (mine
elevation). The results of the eastern drilling now open up the
possibility of driving further east off the 285 level (mine elevation)
through mineralized material out to the 960 zone and potentially
further east. It is interesting to note that Kinross (KC99-148)
intersected 8.78g/t over 3.5 metres in the Contact zone roughly
coincident with the Contact zone mineralization in CL-17-07. The
"Sediment 2" intersection in CL-17-07 represents the first significant
mineralization in the new sediment zone. The Sediment 2 zone was
encountered in CL17-01 and 02 with anomalous gold mineralization."

The program consisted of 2,873 metres of surface diamond
drilling involving 9 drill holes completed from January 23rd to April
7th. Seven holes were drilled east of the existing mine infrastructure
and west of the 960 zone. Two holes were drilled west of the existing
mine infrastructure.

The Contact Zone which demarcates the Pipestone Thrust Fault
juxtaposing the Kidd-Munro Group ultramafics to the north and the
Porcupine Group sediments to the south, has been intersected in four
drill holes over a strike length of 330 metres.

The weighted average grade of the composite intervals vary from
16.76 g/t over 1.8 metres returned from drill hole CL-17-02 and 4.43
g/t over 4 metres returned from drill hole CL-17-06.

Hole Cl-17-07 has intersected a new "Sediment Zone" located 100
metres to the south of the Pipestone Thrust Fault returning 4.09 g/t
over 6 metres.

Drill holes CL-17- 08 and 09 intersected significant
mineralization at the Footwall Zone and Contact Zone establishing
continuity along the 150 metre level (mine elevation).

The current program's objective was to test a 340 metre gap
between the existing underground infrastructure and the 960 Zone from
section 514435E and 514765E. Seven holes targeted a shallow plunging
flexure proximal to offsetting structures possibly controlling gold,
arsenopyrite, pyrite quartz vein mineralization located in the altered
ultramafics and porphyries flanking the Porcupine Group sediments
demarked by the Pipestone Fault structure. A systematic drill hole
spacing of 60 meters was employed to define the plunge orientation of
some of the high-grade shoots located within the existing mine
infrastructure.

These holes were also positioned between two major structures
transecting the Pipestone Fault at 514300E and 514700E disrupting the
horizontal continuity of four gold bearing zone. The orientation in
plan view of these cross-cutting structures are at Az 330 and Az 055
identified by airborne magnetics. Both structures are now interpreted
to be a high angle back thrust dipping to the east and low angle thrust
fault dipping to the west evident on the recently completed grade /
thickness longitudinal model.

Follow-up infill drilling at 30 metre spacing is warranted to
define the extent of the Contact Zone Between sections 514300E and
514700E.

QA/QC Program Protocols

Sage Gold Inc. has implemented a rigorous QA/QC program using
best practice principles which are being applied to the
sampling/analysis of the drill core and complies with National
Instrument 43-101 requirements for the Clavos property. The NQ core is
delivered to the secure core shack facility on site by Crites Drilling
personnel and/or Sage personnel. Prior to splitting, and core logging,
all drill core is photographed. Core logging is focused on identifying
the type and style of mineralization recording structure, lithology
contacts, and alteration including quartz veining % and total sulphide
%. Core splitting is done with a diamond core saw and 1/2 of the drill
core is submitted to ALS Global Laboratories based in Timmins, an
accredited laboratory for analysis. The remainder of the core is stored
at the Clavos Mine Property. All samples are shipped in sealed rice
bags with numbered security tags and transported in a company truck
from the property to ALS Global Laboratories preparation lab in
Timmins, ON.

Sage routinely inserts certified standards, blanks and field
duplicate samples into the sample stream such that every 20 sample
batch contains a blank and standard. The sample preparation procedures
for drill core samples consist of crushing the samples to 70% minus 9
mesh (2mm), pulverizing a 500g sub-sample to 85% minus 200 mesh (75um),
and analyzed by standard fire assay (FA) method using a 50 gram sample
with AA finish and any samples assaying greater than 10 g/t Au are
re-analyzed using a gravimetric finish. For mineralized zone intervals
where visible gold is observed to be present, samples are submitted for
analysis using the metallic screen method where the entire half core is
crushed, pulped and screened to 100 mesh. The screen coarse and fine
fractions are analyzed by fire assay (FA) method with a gravimetric
finish and the total assay result is calculated.

The geotechnical content of this news release has been reviewed
and approved by Sage's consulting geologist, Peter Hubacheck, P. Geo,
who is a Qualified Person ("QP") as defined in National Instrument
43-101.

Sage currently plans to complete a reserve estimate and a
prefeasibility study regarding the Clavos project. In the event that a
production decision is made that is not based on a feasibility study of
mineral reserves demonstrating economic and technical viability
prepared in accordance with National Instrument 43-101, readers are
cautioned that there is increased uncertainty and higher risk of
economic and technical failure associated with such production
decisions.

About Sage Gold

The Company is a mineral exploration and development company
which has primary interests in near-term production and exploration
properties in Ontario. Its main properties are the Clavos Gold
property, 100% owned, in Timmins and the 100% owned Onaman property and
other exploration properties in the Beardmore-Geraldton Gold Camp.
Technical reports and information relating to the properties can be
obtained from the System for Electronic Document Analysis and Retrieval
(SEDAR) website at www.sedar.com and www.sagegoldinc.com.

CAUTIONARY STATEMENT: Neither the TSX Venture Exchange nor its
Regulation Services Provider (as that term is defined in the policies
of the TSX Venture Exchange) accepts responsibility for the adequacy or
accuracy of this release. This news release may contain forward looking
information and the Company cautions readers that forward looking
information is based on certain assumptions and risk factors that could
cause actual results to differ materially from the expectations of the
Company included in this news release. This news release includes
certain "forward-looking statements", which often, but not always, can
be identified by the use of words such as "believes", "anticipates",
"expects", "estimates", "may", "could", "would", "will", or "plan".
These statements are based on information currently available to the
Company and the Company provides no assurance that actual results will
meet management's expectations. Forward-looking statements include
estimates and statements with respect to the Company's future plans,
objectives or goals, to the effect that the Company or management
expects a stated condition or result to occur. Since forward-looking
statements are based on assumptions and address future events and
conditions, by their very nature they involve inherent risks and
uncertainties.             Actual results relating to, among other
things, results of exploration, metallurgical processing, project
development, reclamation and capital costs of the Company's mineral
properties, and the Company's financial condition and prospects, could
differ materially from those currently anticipated in such statements
for many reasons such as, but are not limited to: failure to identify
mineral resources; failure to convert estimated mineral resources to
reserves; the preliminary nature of metallurgical test results; delays
in obtaining or failures to obtain required governmental, environmental
or other project approvals; political risks; uncertainties relating to
the availability and costs of financing needed in the future; changes
in equity markets, inflation, changes in exchange rates; fluctuations
in commodity prices; delays in the development of projects; capital and
operating costs varying significantly from estimates and the other
risks involved in the mineral exploration and development industry; and
those risks set out in the Company's public documents filed on SEDAR.
This list is not exhaustive of the factors that may affect any of the
Company's forward-looking statements. These and other factors should be
considered carefully and readers should not place undue reliance on the
Company's forward-looking statements. Although the Company believes
that the assumptions and factors used in preparing the forward-looking
information in this news release are reasonable, undue reliance should
not be placed on such information, which only applies as of the date of
this news release, and no assurance can be given that such events willoccur in 
the disclosed time frames or at all. The Company disclaims any
intention or obligation to update or revise any forward-looking
information, whether as a result of new information, future events or
otherwise, other than as required by law.

Nigel Lees
President and CEO
416-204-3170
nlees@sagegoldinc.com
______________________________________
_______________________________________________
TSX Venture closing price for SGX-V
Date: 2017/05/09
Closing Price: 0.18
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1712900011TS11712901252-06252420170510