Source	CANADA NEWSWIRE
Date	05/15/2017
Time	05:33:56 AM

Company	 Marlin Gold Mining Ltd.
Title	Marlin Gold Intersects 1.56 g/t AuEq (0.83 g/t Au and 116 g/t Ag) over
102.5 Meters at the Commonwealth Project





    CDNX Symbol: MLN











Press Release




" BC-Marlin-Commenwealth   05-15 1583
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Marlin Gold Intersects 1.56 g/t AuEq (0.83 g/t Au and 116 g/t Ag) over
102.5 Meters at the Commonwealth Project@

/NOT FOR DISTRIBUTION TO U.S. NEWSWIRE SERVICES OR FOR RELEASE OR
DISSEMINATION DIRECTLY, OR INDIRECTLY, IN WHOLE OR IN PART, IN OR INTO THE
UNITED STATES/
VANCOUVER, May 15, 2017 /CNW/ - Marlin Gold Mining Ltd. (TSX-V: MLN)
("Marlin" or the "Company") is pleased to report drilling results from its
wholly owned Commonwealth silver and gold project in Cochise County, Arizona
(the "Commonwealth Project").
Core hole 17CDDH26 intersected 1.56 g/t gold equivalent (0.83 g/t Au and
116 g/t Ag) using a 160:1 silver to gold ratio ("AuEq") over 102.5 meters
(57.4 meters estimated true width). The hole was programmed as a twin to
reverse circulation ("RC") hole E-9, drilled by DRX Inc. ("DRX") 6.5 meters
away nearly 30 years ago. The grade x thickness profile of 17CDDH26 was over
2.5 times that of the 1980's RC hole.
Fourteen of Marlin's 27 core holes completed to date were programmed to
confirm results of adjacent historic RC holes. Most core holes yielded results
similar to the historic RC holes but importantly, several modern holes yielded
significant intercepts far greater than the neighboring RC holes. Additional
twin holes are being evaluated to confirm that a significant positive
reconciliation between core and RC drilling exists. This is an important
exercise as all historic RC holes were used in the calculation of the resource
estimate in the April 2014 NI 43-101 Technical Report and Preliminary Economic
Assessment.
Click HERE for a histogram comparing the individual gold and silver
assays of core hole 17CDDH26 with that of DRX's E-9 RC hole assays.
It should also be noted that 17CDDH26 is the highest grade x thickness
intercept in Commonwealth's 45-year drilling database, surpassing that of
17CDDH10, which hit 2.12 g/t AuEq over 55 meters (33 meters estimated true
width). As is the case with 17CDDH26, the only existing drill data near
17CDDH10 was that of historic RC holes (see press release dated February 2,
2017).
Akiba Leisman, Executive Chairman and Interim CEO of Marlin states that,
"the significance of 17CDDH26 cannot be overstated. We hit 1.56 g/t gold
equivalent over an estimated 57.4 meters true width, and only 9.5 meters from
surface. This is in an open pit and potentially heap leachable project. The
positive reconciliation that we see in hole 17CDDH26, and other twin holes
drilled to date, is hinting that the historic RC holes are potentially
underestimating grade, which if proven true, may have a positive impact on the
economics of the Commonwealth Project."
Additionally, core hole 17CDDH25 was designed to test the down-dip
extension of the Footwall Zone. We are pleased to report that 17CDDH25 hit two
significant intercepts in the down-dip extension of the Footwall Zone, both of
which are interpreted to be true widths, of 0.98 g/t AuEq over 11.4 meters and
1.04 g/t AuEq over 16.5 meters.
Click HERE for a cross section that highlights drill hole 17CDDH25.
All holes drilled to date have been in oxide mineralization, which can
potentially be recovered through a heap leach process.
See below for a summary table of newly released drill holes. Intercepts
in bold intersected the Footwall Zone.

Drill Hole(1) From (m)     To (m)      Length (m)  AuEq (g/t)(2)   Au 
(g/t)       Ag (g/t)
------------  -------      -----       ---------   -------------   
--------       --------

17CDDH25                      108.70      153.00           44.30            
1.08         0.64    71

including(3)      111.28      120.00            8.72            2.60         
1.54   170

and                           184.60      195.95           11.35            
0.98         0.94     6

and                           201.55      218.00           16.45            
1.04         0.98    10
---                           ------      ------           -----            
----         ----   ---

17CDDH26(4)                     9.54      112.00          102.46            
1.56         0.83   116

including(3)        9.54       28.00           18.46            2.10         
0.95   191

including(3)       48.00       68.00           20.00            2.60         
1.29   203

including(3)       75.89       92.60           16.71            2.60         
1.87   123

and                           118.00      124.00            6.00            
0.56         0.25    50

and                           166.00      172.25            6.25            
0.48         0.47     2
---                           ------      ------            ----            
----         ----   ---

17CDDH27                       27.00       33.00            6.00            
1.02         0.30   115

and                            40.00       48.00            8.00            
0.70         0.27    69

and                            64.00       96.00           32.00            
0.44         0.26    29

and                           101.35      107.70            6.35            
0.91         0.75    26
---                           ------      ------            ----            
----         ----   ---
(1)    Significant intercept defined as
a minimum assay of 0.3 g/t
AuEq over a minimum 6-meter
interval with no more than 2
meters of internal dilution
below 0.3 g/t AuEq.

(2)    Gold equivalent ("AuEq") values
at a silver to gold ratio of
160:1.

(3)    Significant internal intercept
defined as a minimum assay of
2.0 g/t AuEq over a minimum
6-meter interval with no more
than 2 meters of internal
dilution below 0.5 g/t AuEq.

(4)    Significant intercept criteria
for hole 17CDDH26 was modified
from all previously reported
drill holes to properly account
for the length of the intercept
from 9.54 to 112.00 meters.
For this intercept, a single
4-meter zone of internal
dilution of 0.246 g/t AuEq,
below the cutoff grade of 0.300
g/t AuEq, was included in the
reported intercept.  All other
criteria remained the same.
Dr. Matthew D. Gray. C.P.G., of Resource Geosciences Incorporated, a
Qualified Person under the definitions of CSA NI 43-101, implemented and
supervised industry standard QA/QC protocols for the Commonwealth Project
drill sampling program including insertion of duplicate and reference standard
samples. Dr. Gray has verified the reliability of the drill sampling results
reported in this press release.
Notes on Sampling and Assaying
Drill core was continuously sampled from inception to termination of the
drill hole. Sample intervals were typically two meters. All drill holes were
started as large diameter PQ (8.5cm) core holes, and were reduced to HQ
(6.35cm) only where drilling conditions required. Geologic and geotechnical
data was captured into a digital database, core was photographed, then one
half split of the core was collected for analysis and one half was retained in
the core library. Samples were kept in a secured logging and storage facility
until such time that they were received on site by representatives of Skyline
Assayers and Laboratories ("Skyline"). Sample preparation and analysis of
pulps was done in the Tucson, Arizona facilities of Skyline. Gold was analyzed
by standard fire assay fusion, 30 gram aliquot, AAS finish, with samples
reporting greater than 10 grams per tonne gold re-assayed by fire assay fusion
with gravimetric finish. Controls samples consisting of duplicates, standards,
and blanks were inserted into the sample stream and analytical results of
control samples confirmed reliability of the assay data.
About Marlin Gold
Marlin is a growth-oriented gold and silver mining company focused on the
Americas. The company owns two properties located in Sinaloa, Mexico and
Arizona, USA and a portfolio of royalties. Marlin's priority is to advance its
properties toward commercial production and enhance shareholder value through
the growth of its wholly owned subsidiary, Sailfish Royalty Corp. Marlin is
backed by a well-funded investor with a successful track record in the
resources sector. The La Trinidad Mine in Sinaloa, Mexico declared commercial
production on November 1, 2014 and is one of the highest-grade open pit heap
leach gold mines in Mexico. A NI 43-101 mineral resource estimate and
preliminary economic assessment for the La Trinidad Mine and Commonwealth
Project can be found at www.sedar.com or at www.marlingold.com.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
the term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary statement regarding forward?looking information
This news release contains 'forward-looking statements' within the
meaning of applicable securities laws. Forward-looking statements are
statements that are not historical facts and are generally, but not always,
identified by words such as the following: expects, plans, anticipates,
believes, intends, estimates, projects, assumes, potential and similar
expressions. Forward-looking statements also include reference to events or
conditions that will, would, may, could or should occur, including, without
limitation, the intended use of proceeds. These forward-looking statements are
necessarily based upon a number of estimates and assumptions that, while based
on management's expectations and considered reasonable at the time they are
made, are inherently subject to a variety of risks and uncertainties which
could cause actual events or results to differ materially from those reflected
in the forward-looking statements, including, without limitation: the risk
that the anticipated effects of the equity financing may not result in the
outcomes predicted by management, uncertainties related to raising sufficient
financing to fund planned work in a timely manner and on acceptable terms;
changes in planned work resulting from logistical, technical or other factors;
the possibility that results of work will not fulfill projections/expectations
and realize the perceived potential of the Company's projects; uncertainties
involved in the interpretation of drilling results and other tests and the
estimation of gold resources; risk of accidents, equipment breakdowns and
labour disputes or other unanticipated difficulties or interruptions; the
possibility of environmental issues at the Company's projects; the possibility
of cost overruns or unanticipated expenses in work programs; the need to
obtain permits and comply with environmental laws and regulations and other
government requirements; fluctuations in the price of gold and other risks and
uncertainties, including those described in the Company's current Annual
Information Form filed on SEDAR at www.sedar.com. As a result, readers are
cautioned not to place undue reliance on these forward-looking statements. The
forward-looking statements contained in this news release are made as of the
date of this release. Unless required by law, Marlin has no intention to and
assumes no obligation to update or revise any forward-looking statements,
whether as a result of new information, future events or otherwise.
NOT FOR DISTRIBUTION TO U.S. NEWSWIRE SERVICES OR FOR RELEASE OR
DISSEMINATION DIRECTLY, OR INDIRECTLY, IN WHOLE OR IN PART, IN OR INTO THE
UNITED STATES
SOURCE Marlin Gold Mining Ltd.



View original content with multimedia:
http://www.newswire.ca/en/releases/archive/May2017/15/c8220.html

-0-                           05/15/2017
/For further information: Akiba Leisman, Executive Chairman and Interim
CEO, Marlin Gold Mining Ltd., Telephone: 203-862-7059, E-mail:
aleisman(at)marlingold.com/
/Web Site: http://www.marlingold.com /
(MLN.)

CO:  Marlin Gold Mining Ltd.
ST:  British Columbia
IN:  MNG
SU:

-30-