Source	Marketwire
Date	05/15/2017
Time	05:00:58 AM

Company	 SALAZAR RESOURCES LIMITED
Title	Salazar Cuts 16.60 Metres (15.60m True) Averaging 3.66 g/t Gold, 117.40 
g/t Silver, 4.88% Copper, 5.36% Zinc Northeast of the El Domo Deposit at Its 
Curipamba Project





    CDNX Symbol: SRL











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Salazar Resources Limited

TSX VENTURE SYMBOL: SRL
FRANKFURT SYMBOL: CCG

May 15, 2017

Salazar Cuts 16.60 Metres (15.60m True) Averaging 3.66 g/t Gold, 117.40 g/t 
Silver, 4.88% Copper, 5.36% Zinc Northeast of the El Domo Deposit at Its 
Curipamba Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 15, 2017) - Salazar Resources 
Limited (TSX VENTURE:SRL)(FRANKFURT:CCG) ("Salazar" or the "Company") is 
pleased to report results from the additional six holes (1,888 meters) of the 
phase V diamond drill program in progress on the Company's 100-per-cent owned 
(21,500 ha) Curipamba volcanogenic massive sulphide (VMS) project in Ecuador. 
These holes represent new exploratory drilling and were not included in the 
latest El Domo resource estimate which was released on January 16th, 2015.

HIGHLIGHTS:

/T/

Hole CURI-224
-  16.60 metres (15.60m true) averaging 3.66 g/t gold, 117.40 g/t silver,
4.88% copper, 5.36% zinc,
Including:
6.35 metres (5.97m true) averaging 7.72 g/t gold, 180.05 g/t silver, 2.28%
copper, 8.24% zinc, and
6.50 metres (6.11m true) averaging 1.32 g/t gold, 99.22 g/t silver, 8.89%
copper, 4.48% zinc

/T/

PROGRAM RESULTS

The Company has now drilled 5,251.05 meters as part of the Phase V drilling 
program which encompassed 40 holes (10,000 meters) designed to further expand 
the El Domo volcanogenic massive sulphide ("VMS") deposit and explore its 
margins, as well as to test geophysical anomalies and surface showings (Figure 
1). The latest six holes (1,888 metres) (Table 1) were drilled as part of this 
program. It is anticipated that the drill program will be completed by the 
third quarter of this year.

CURI-224 intersected 16.60 meters (15.60 meters true width) of massive and 
semi-massive chalcopyrite-sphalerite-pyrite grading 3.66 g/t gold, 117.40 g/t 
silver, 4.88% copper, 5.36% zinc beneath an andesite sill that occurs in the 
vicinity of the hole (Figure1). The intersection in CURI-224 is located 
approximately 120 meters east of the intersection in CURI-173 (2.74 meters 
averaging 0.677 g/t gold, 6.5 g/t silver, 0.39% copper and 0.37% zinc) and 75 
meters south from CURI-198 (7.40 meters averaging 2.498 g/t gold, 74.61 g/t 
silver, 3.45% copper and 5.07% zinc; see News Release of August 27, 2012). The 
mineralization in CURI-187, CURI-198 and CURI-224 is currently interpreted to 
be part of a separate zone of mineralization. The intercept in CURI-224 is 
gold-rich; the top of the mineralization grades 7.72 g/t gold over 6.35m 
(225.40 - 231.75m). Further drilling is planned to test this area.

Fredy Salazar, President and CEO, commented: "We are thrilled with the recent 
results from hole CURI-224 located in the north east of the El Domo resource. 
The mineralization encountered is thicker and of better grade to the last hole 
drilled in this area: CURI-198. This new intersection indicates significant 
potential for finding thicker mineralization in the north-east area of El Domo 
resource which will increase the size and quality of the resource. So far we 
are very satisfied with the results to date from this Phase V drilling program 
and will continue working to expand the resource."

The latest six holes (1,888 metres) (Table 1) were drilled as part of the 
planned 40-hole (10,000 meters) drill program that is designed to further 
expand the El Domo volcanogenic massive sulphide ("VMS") deposit and explore 
its margins, as well as to test geophysical anomalies and surface showings 
(Figure 1). It is anticipated that the drill program will be complete by the 
third quarter of this year.

Holes CURI-219 and CURI-221 were drilled west of the El Domo deposit to further 
test the area of the CURI-213 (which intersected two zones of mineralization: 
4.14 meters (true width) averaging 1.01 g/t gold, 16.78 g/t silver, 0.67% 
copper, 0.95% lead and 4.77% zinc, and 29.37 metres (true width) averaging 0.5 
g/t gold, 77.93 g/t silver, 0.17% copper, 0.17% copper and 0.89% zinc (See News 
Release of March 23, 2017). CURI-219 and CURI- 221 were collared approximately 
350 metres west of El Domo deposit and 50 meters north and south from the 
CURI-213 respectively. No significant mineralization was encountered and no 
further drilling is planned in this area.

Hole CURI-220 was drilled vertically from the same collar as the CURI-218 (See 
News Release of March 23, 2017). CURI-220 did not encounter significant 
mineralization, however, the horizontal separation between CURI-220 and the 
mineralization in CURI-218 is estimated to be approximately 138 metres. The 
eastern limit of the mineralization intersected in CURI-218 remains to be 
established. As well, the mineralization in CURI-218 remains open to the north 
and south.

Hole CURI-222, drilled steeply due east from the same platform as CURI-224, 
intersected 2.66 meters averaging 0.13 g/t gold, 5.56 g/t silver, 0.31% copper 
and 1.15% zinc.

Holes CURI-223 was drilled vertically 50 meters north from the historic hole 
CURI-155 which cut two mineralized zones with gold and silver values and 
anomalous zinc and copper values (see News Release of January 26, 2012). 
CURI-223 encountered similar lithology to that in CURI-155 with one interval 
grading 3.61 meters of 0.77 g/t gold, 37.54 g/t silver, 0.15% copper and 1.68% 
zinc.

TABLE 1

/T/

----------------------------------------------------------------------------
Elev                         Depth
Hole ID               East      North      (m)       Azimuth    Dip      (m)
----------------------------------------------------------------------------
CURI-219          694567.2  9855144.9   829.73    90 degrees    -65   317.70
----------------------------------------------------------------------------
CURI-220          695565.2  9855188.9  1097.34   270 degrees    -90   401.50
----------------------------------------------------------------------------
CURI-221          694532.4  9855052.2   861.18    90 degrees    -75   290.75
----------------------------------------------------------------------------
CURI-222          695488.6  9855540.9  1027.06    90 degrees    -87   302.70
----------------------------------------------------------------------------
CURI-223          695743.3  9855201.3  1083.91     0 degrees    -90   311.70
----------------------------------------------------------------------------
CURI-224          695488.6  9855540.9  1027.06   260 degrees    -70   263.70
----------------------------------------------------------------------------

/T/

PSAD_1956_UTM_Zone_17S

To view Figure 1, El Domo Deposit - Pierce Point Map, please visit the 
following link: http://media3.marketwire.com/docs/srl0515fig1.pdf.

TABLE 2

SIGNIFICANT INTERSECTIONS

/T/

----------------------------------------------------------------------------
From      To  Width    Au       Ag    Cu    Pb    Zn
Hole ID                  (m)     (m)    (m)  (g/t)   (g/t)   (%)   (%)   (%)
----------------------------------------------------------------------------
CURI-219             No significant mineralization encountered in this hole,
located 50m north from CURI-213
----------------------------------------------------------------------------
CURI-220             No significant mineralization encountered in this hole,
located 138m east from CURI-218
----------------------------------------------------------------------------
CURI-221              218.75  221.95    3.2      -       -  0.16     -  1.46
----------------------------------------------------------------------------
234.35  235.95    1.6   0.14    10.3  0.11  0.88  1.26
----------------------------------------------------------------------------
CURI-222              224.28  226.94   2.15   0.13    5.56  0.31  0.11  1.15
----------------------------------------------------------------------------
CURI-223               220.9  224.51   3.61   0.77   37.54  0.15   0.7  1.68
----------------------------------------------------------------------------
CURI-224               225.4     242   16.6   3.66   117.4  4.88  0.44  5.36
----------------------------------------------------------------------------
including   225.4  231.75   6.35   7.72  180.05  2.28  1.13  8.24
----------------------------------------------------------------------------
including  234.05  240.55    6.5   1.32   99.22  8.89  0.01  4.48
----------------------------------------------------------------------------

/T/

Widths presented in Table 2 are downhole core lengths. Where possible, true 
width estimates are noted in the text. A rigorous chain-of-custody and quality 
assurance/quality control program that included the insertion of certified 
standard control samples and blanks, and re-analysis of samples with high 
levels(overlimit) of gold, copper and zinc, was applied to the NQ-diameter, 
rock-sawn half-core samples. All samples were analyzed by Inspectorate Services 
Peru S.A.C. (Bureau Veritas), a certified ISO 17025 and ISO 9001:2000 
laboratory.

As part of the program's sample quality assurance, twin samples were taken on 
the CURI-224. The samples were part of a Brecciated Dacite and gave the 
following results:

/T/

----------------------------------------------------------------------------
Au       Ag       Cu       Pb       Zn
Sample #           Top   Bottom    (g/t)    (g/t)    (ppm)    (ppm)    (ppm)
----------------------------------------------------------------------------
170422          242.00   243.45    0.219     7.90     2186       31     2199
----------------------------------------------------------------------------
170423          242.00   243.45    0.232     7.80     1371       31     1758
----------------------------------------------------------------------------

/T/

The scientific and technical information contained in this news release has 
been reviewed and approved by Kieran Downes, Ph.D., P.Geo. a Qualified Person 
as defined by National Instrument 43-101.

ON BEHALF OF THE BOARD OF SALAZAR RESOURCES LIMITED

Fredy Salazar, President & CEO

Salazar Resources Limited

Salazar Resources Ltd. is a publicly-listed (TSX VENTURE:SRL) mineral resource 
company engaged in the exploration and development of new highly prospective 
areas in Ecuador. Led by a senior Ecuadorian management team and most notably 
by its namesake Fredy Salazar, this team has been instrumental in other major 
discoveries throughout Ecuador, including Aurelian's Fruta Del Norte discovery, 
IAMGold's Quimsacocha Deposit, Mozo Deposit, Ex Newmont's Cangrejos Project and 
International Minerals Rio Blanco and Gaby Deposit. Being an Ecuadorian based 
company gives the Company a strategic advantage enabling the Company to 
complete exploration at a rapid pace. With an excellent property portfolio (4 
projects - 36,269 hectares), good geopolitical positioning and a number of 
strategic corporate and financial partnerships, Salazar has positioned itself 
to be a strategic player in Ecuador.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

This press release contains "forward -looking information" within the meaning 
of applicable Canadian securities laws. All statements included herein, other 
than statements of historical fact, are forward-looking information and such 
information involves various risks and uncertainties. Forward-looking 
information herein includes, but is not limited to, statements that address 
activities, events or developments that the Company expects or anticipates will 
or may occur in the future, including such things as the execution of the Phase 
V drilling program. Such forward-looking information is based on a number of 
material factors and assumptions. Although the Company has attempted to 
identify important factors that could cause actual actions, events or results 
to differ materially from those described in forward-looking information, there 
may be other factors that cause actions, events or results not to be as 
anticipated, estimated or intended. There can be no assurance that such 
information will prove to be accurate, and actual results and future events 
could differ materially from those anticipated in such information. A 
description of assumptions used to develop such forward-looking information and 
a description of risk factors that may cause actual results to differ 
materially from forward-looking information can be found in the Company's 
disclosure documents on the SEDAR website at www.sedar.com. Accordingly, 
readers should not place undue reliance on forward -looking information. The 
Company does not undertake to update any forward-looking information except in 
accordance with applicable securities laws.

- 30 -

CONTACT INFO:

Salazar Resources Ltd.
ir@salazarresources.com
www.salazarresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=593178417


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Salazar Resources Limited

TSX VENTURE SYMBOL: SRL
FRANKFURT SYMBOL: CCG

May 15, 2017

Salazar Cuts 16.60 Metres (15.60m True) Averaging 3.66 g/t Gold, 117.40 g/t 
Silver, 4.88% Copper, 5.36% Zinc Northeast of the El Domo Deposit at Its 
Curipamba Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 15, 2017) - Salazar Resources 
Limited (TSX VENTURE:SRL)(FRANKFURT:CCG) ("Salazar" or the "Company") is 
pleased to report results from the additional six holes (1,888 meters) of the 
phase V diamond drill program in progress on the Company's 100-per-cent owned 
(21,500 ha) Curipamba volcanogenic massive sulphide (VMS) project in Ecuador. 
These holes represent new exploratory drilling and were not included in the 
latest El Domo resource estimate which was released on January 16th, 2015.

HIGHLIGHTS:

/T/

Hole CURI-224
-  16.60 metres (15.60m true) averaging 3.66 g/t gold, 117.40 g/t silver,
4.88% copper, 5.36% zinc,
Including:
6.35 metres (5.97m true) averaging 7.72 g/t gold, 180.05 g/t silver, 2.28%
copper, 8.24% zinc, and
6.50 metres (6.11m true) averaging 1.32 g/t gold, 99.22 g/t silver, 8.89%
copper, 4.48% zinc

/T/

PROGRAM RESULTS

The Company has now drilled 5,251.05 meters as part of the Phase V drilling 
program which encompassed 40 holes (10,000 meters) designed to further expand 
the El Domo volcanogenic massive sulphide ("VMS") deposit and explore its 
margins, as well as to test geophysical anomalies and surface showings (Figure 
1). The latest six holes (1,888 metres) (Table 1) were drilled as part of this 
program. It is anticipated that the drill program will be completed by the 
third quarter of this year.

CURI-224 intersected 16.60 meters (15.60 meters true width) of massive and 
semi-massive chalcopyrite-sphalerite-pyrite grading 3.66 g/t gold, 117.40 g/t 
silver, 4.88% copper, 5.36% zinc beneath an andesite sill that occurs in the 
vicinity of the hole (Figure1). The intersection in CURI-224 is located 
approximately 120 meters east of the intersection in CURI-173 (2.74 meters 
averaging 0.677 g/t gold, 6.5 g/t silver, 0.39% copper and 0.37% zinc) and 75 
meters south from CURI-198 (7.40 meters averaging 2.498 g/t gold, 74.61 g/t 
silver, 3.45% copper and 5.07% zinc; see News Release of August 27, 2012). The 
mineralization in CURI-187, CURI-198 and CURI-224 is currently interpreted to 
be part of a separate zone of mineralization. The intercept in CURI-224 is 
gold-rich; the top of the mineralization grades 7.72 g/t gold over 6.35m 
(225.40 - 231.75m). Further drilling is planned to test this area.

Fredy Salazar, President and CEO, commented: "We are thrilled with the recent 
results from hole CURI-224 located in the north east of the El Domo resource. 
The mineralization encountered is thicker and of better grade to the last hole 
drilled in this area: CURI-198. This new intersection indicates significant 
potential for finding thicker mineralization in the north-east area of El Domo 
resource which will increase the size and quality of the resource. So far we 
are very satisfied with the results to date from this Phase V drilling program 
and will continue working to expand the resource."

The latest six holes (1,888 metres) (Table 1) were drilled as part of the 
planned 40-hole (10,000 meters) drill program that is designed to further 
expand the El Domo volcanogenic massive sulphide ("VMS") deposit and explore 
its margins, as well as to test geophysical anomalies and surface showings 
(Figure 1). It is anticipated that the drill program will be complete by the 
third quarter of this year.

Holes CURI-219 and CURI-221 were drilled west of the El Domo deposit to further 
test the area of the CURI-213 (which intersected two zones of mineralization: 
4.14 meters (true width) averaging 1.01 g/t gold, 16.78 g/t silver, 0.67% 
copper, 0.95% lead and 4.77% zinc, and 29.37 metres (true width) averaging 0.5 
g/t gold, 77.93 g/t silver, 0.17% copper, 0.17% copper and 0.89% zinc (See News 
Release of March 23, 2017). CURI-219 and CURI- 221 were collared approximately 
350 metres west of El Domo deposit and 50 meters north and south from the 
CURI-213 respectively. No significant mineralization was encountered and no 
further drilling is planned in this area.

Hole CURI-220 was drilled vertically from the same collar as the CURI-218 (See 
News Release of March 23, 2017). CURI-220 did not encounter significant 
mineralization, however, the horizontal separation between CURI-220 and the 
mineralization in CURI-218 is estimated to be approximately 138 metres. The 
eastern limit of the mineralization intersected in CURI-218 remains to be 
established. As well, the mineralization in CURI-218 remains open to the north 
and south.

Hole CURI-222, drilled steeply due east from the same platform as CURI-224, 
intersected 2.66 meters averaging 0.13 g/t gold, 5.56 g/t silver, 0.31% copper 
and 1.15% zinc.

Holes CURI-223 was drilled vertically 50 meters north from the historic hole 
CURI-155 which cut two mineralized zones with gold and silver values and 
anomalous zinc and copper values (see News Release of January 26, 2012). 
CURI-223 encountered similar lithology to that in CURI-155 with one interval 
grading 3.61 meters of 0.77 g/t gold, 37.54 g/t silver, 0.15% copper and 1.68% 
zinc.

TABLE 1

/T/

----------------------------------------------------------------------------
Elev                         Depth
Hole ID               East      North      (m)       Azimuth    Dip      (m)
----------------------------------------------------------------------------
CURI-219          694567.2  9855144.9   829.73    90 degrees    -65   317.70
----------------------------------------------------------------------------
CURI-220          695565.2  9855188.9  1097.34   270 degrees    -90   401.50
----------------------------------------------------------------------------
CURI-221          694532.4  9855052.2   861.18    90 degrees    -75   290.75
----------------------------------------------------------------------------
CURI-222          695488.6  9855540.9  1027.06    90 degrees    -87   302.70
----------------------------------------------------------------------------
CURI-223          695743.3  9855201.3  1083.91     0 degrees    -90   311.70
----------------------------------------------------------------------------
CURI-224          695488.6  9855540.9  1027.06   260 degrees    -70   263.70
----------------------------------------------------------------------------

/T/

PSAD_1956_UTM_Zone_17S

To view Figure 1, El Domo Deposit - Pierce Point Map, please visit the 
following link: http://media3.marketwire.com/docs/srl0515fig1.pdf.

TABLE 2

SIGNIFICANT INTERSECTIONS

/T/

----------------------------------------------------------------------------
From      To  Width    Au       Ag    Cu    Pb    Zn
Hole ID                  (m)     (m)    (m)  (g/t)   (g/t)   (%)   (%)   (%)
----------------------------------------------------------------------------
CURI-219             No significant mineralization encountered in this hole,
located 50m north from CURI-213
----------------------------------------------------------------------------
CURI-220             No significant mineralization encountered in this hole,
located 138m east from CURI-218
----------------------------------------------------------------------------
CURI-221              218.75  221.95    3.2      -       -  0.16     -  1.46
----------------------------------------------------------------------------
234.35  235.95    1.6   0.14    10.3  0.11  0.88  1.26
----------------------------------------------------------------------------
CURI-222              224.28  226.94   2.15   0.13    5.56  0.31  0.11  1.15
----------------------------------------------------------------------------
CURI-223               220.9  224.51   3.61   0.77   37.54  0.15   0.7  1.68
----------------------------------------------------------------------------
CURI-224               225.4     242   16.6   3.66   117.4  4.88  0.44  5.36
----------------------------------------------------------------------------
including   225.4  231.75   6.35   7.72  180.05  2.28  1.13  8.24
----------------------------------------------------------------------------
including  234.05  240.55    6.5   1.32   99.22  8.89  0.01  4.48
----------------------------------------------------------------------------

/T/

Widths presented in Table 2 are downhole core lengths. Where possible, true 
width estimates are noted in the text. A rigorous chain-of-custody and quality 
assurance/quality control program that included the insertion of certified 
standard control samples and blanks, and re-analysis of samples with high 
levels(overlimit) of gold, copper and zinc, was applied to the NQ-diameter, 
rock-sawn half-core samples. All samples were analyzed by Inspectorate Services 
Peru S.A.C. (Bureau Veritas), a certified ISO 17025 and ISO 9001:2000 
laboratory.

As part of the program's sample quality assurance, twin samples were taken on 
the CURI-224. The samples were part of a Brecciated Dacite and gave the 
following results:

/T/

----------------------------------------------------------------------------
Au       Ag       Cu       Pb       Zn
Sample #           Top   Bottom    (g/t)    (g/t)    (ppm)    (ppm)    (ppm)
----------------------------------------------------------------------------
170422          242.00   243.45    0.219     7.90     2186       31     2199
----------------------------------------------------------------------------
170423          242.00   243.45    0.232     7.80     1371       31     1758
----------------------------------------------------------------------------

/T/

The scientific and technical information contained in this news release has 
been reviewed and approved by Kieran Downes, Ph.D., P.Geo. a Qualified Person 
as defined by National Instrument 43-101.

ON BEHALF OF THE BOARD OF SALAZAR RESOURCES LIMITED

Fredy Salazar, President & CEO

Salazar Resources Limited

Salazar Resources Ltd. is a publicly-listed (TSX VENTURE:SRL) mineral resource 
company engaged in the exploration and development of new highly prospective 
areas in Ecuador. Led by a senior Ecuadorian management team and most notably 
by its namesake Fredy Salazar, this team has been instrumental in other major 
discoveries throughout Ecuador, including Aurelian's Fruta Del Norte discovery, 
IAMGold's Quimsacocha Deposit, Mozo Deposit, Ex Newmont's Cangrejos Project and 
International Minerals Rio Blanco and Gaby Deposit. Being an Ecuadorian based 
company gives the Company a strategic advantage enabling the Company to 
complete exploration at a rapid pace. With an excellent property portfolio (4 
projects - 36,269 hectares), good geopolitical positioning and a number of 
strategic corporate and financial partnerships, Salazar has positioned itself 
to be a strategic player in Ecuador.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

This press release contains "forward -looking information" within the meaning 
of applicable Canadian securities laws. All statements included herein, other 
than statements of historical fact, are forward-looking information and such 
information involves various risks and uncertainties. Forward-looking 
information herein includes, but is not limited to, statements that address 
activities, events or developments that the Company expects or anticipates will 
or may occur in the future, including such things as the execution of the Phase 
V drilling program. Such forward-looking information is based on a number of 
material factors and assumptions. Although the Company has attempted to 
identify important factors that could cause actual actions, events or results 
to differ materially from those described in forward-looking information, there 
may be other factors that cause actions, events or results not to be as 
anticipated, estimated or intended. There can be no assurance that such 
information will prove to be accurate, and actual results and future events 
could differ materially from those anticipated in such information. A 
description of assumptions used to develop such forward-looking information and 
a description of risk factors that may cause actual results to differ 
materially from forward-looking information can be found in the Company's 
disclosure documents on the SEDAR website at www.sedar.com. Accordingly, 
readers should not place undue reliance on forward -looking information. The 
Company does not undertake to update any forward-looking information except in 
accordance with applicable securities laws.

- 30 -

CONTACT INFO:

Salazar Resources Ltd.
ir@salazarresources.com
www.salazarresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=593178417