Source	Marketwire
Date	05/17/2017
Time	09:01:38 PM

Company	 ML GOLD CORP.
Title	ML Gold Updates Palmetto Gold Drilling and Pinnacle Reef Deep Sensing 
Geophysics Program





    CDNX Symbol: MLG











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: ML Gold Corp.

TSX VENTURE SYMBOL: MLG
FRANKFURT SYMBOL: XOVN.F

May 18, 2017

ML Gold Updates Palmetto Gold Drilling and Pinnacle Reef Deep Sensing 
Geophysics Program


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 18, 2017) - ML Gold Corp. (TSX 
VENTURE:MLG)(FRANKFURT:XOVN.F) ("ML Gold" or the "Company") is pleased to 
provide an update on the Palmetto Gold Project in Nevada, USA, and the renamed 
Pinnacle Reef Copper-Gold Project (formerly called the Later) in British 
Columbia.

At the Palmetto Project:

The phase I drilling program is continuing with 13 drill holes completed to 
date and another two holes recently added to the program. The primary purpose 
of the program is to confirm and expand the 3D model being used to calculate a 
maiden gold resource at Palmetto.

ML Gold's team is on-site, logging, preparing and shipping drill samples to 
Reno, Nevada for initial analysis before being sent to Vancouver, Canada, for 
the final multi-element analysis. To date ML Gold has received and released 
assay results for one complete hole of the program, see Company release dated 
May 4, 2017. Additional results are pending.

Based on gold mineralization in quartz veining observed in the recent RC holes 
(PAL-17R07 & PAL-1708) within the Northwest Zone, the Company sees potential to 
focus on this quickly expanding area in a phase II program. The Northwest Zone 
has been overlooked in the past due to a focus on the high grades within the 
Discovery Zone. There is significant potential to expand the Northwest Zone as 
it remains open both east and west, and appears to be widening to the west. 
Contingent on the NI 43-101 technical report and concurrent resource estimate 
being conducted, the Company will fully evaluate the phase II program which 
could begin as early as September 2017.

At the Pinnacle Reef Project (formerly the Later):

In January, 2017, ML Gold identified a large (2 kilometre wide) donut shaped 
Induced Polarization "IP" anomaly representative of a pyritic halo on the 
Pinnacle Reef Project in North central British Columbia (previously reported in 
News Release dated January 19, 2017). To follow up, the Company implemented a 
deep sensing IP program in early April, 2017 to search for a source or "feeder 
zone" for the mineralization observed on the margin of the anomaly. This most 
recent survey has identified a "pipe like" conductive structure going to the 
bottom of the IP survey limits (approximately 700 metres deep) located in the 
southern portion of the "donut".

The new deep sensing IP survey confirms that the widely dispersed near surface 
high chargeability donut is related to a single deep seeded structure, and 
clearly identifies a central area of anomalous chargeability which was not 
previously known. Since highly mineralized rocks are often related to increased 
fracture permeability (clay minerals and stockwork veins) with higher water 
content, it is likely that the conductivity anomaly at the centre of the large 
chargeability halo could be representing a massive porphyry pipe approximately 
500 metres wide. It is also possible, based on the geometry of the 
chargeability distribution, that the anomalous copper-gold mineralization 
encountered in historic drilling and as previously released (News release 
January 19, 2017), is a distal expression of a high grade copper-gold core that 
has never been tested due to glacial till surface cover. A 3D image of the 
inverted IP data showing the target area and location of aforementioned 
historic drilling is available at 
www.mlgoldcorp.com/index.php/projects/pinnacle-reef.

The Pinnacle Reef property is located within the prolific Quesnel Terrane in 
Central BC, consists of 24 mineral claims covering approximately 6,684 
hectares, is accessible by vehicle year round and lies within 50 km of 
hydroelectric power and railway. ML Gold can earn up to a 70% interest in the 
Property over a five year period by completing certain work commitments and 
making certain cash and share payments to Pacific Empire Minerals Corp. over 
the term of the option.

Adrian Smith, President of ML Gold commented, "We are pleased to see the 
Palmetto Project advancing as planned, and are on track to produce the first 
ever resource estimate on the Property. We are equally thrilled to see strong 
geophysical evidence at Pinnacle Reef, supporting previous interpretations and 
narrowing down what has become the best porphyry target I have seen in BC."

The Company also reports that Martin Burian has resigned as the CFO of the 
Company. Brian Morrison, a current director, has been appointed the new CFO.

Adrian Smith, P.Geo., is the qualified person for the Company as that term is 
defined in National Instrument 43-101, and has supervised the technical 
information presented within this news release.

ABOUT ML GOLD CORP.

ML Gold Corp. is a Canadian listed Company, focused on creating shareholder 
value through discoveries and strategic development of mineral properties in 
Canada and the United States.

For additional information please visit the Company's website at 
www.mlgoldcorp.com.

ML GOLD CORP.

Andrew Bowering, Chairman

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

This news release may contain certain "Forward-Looking Statements" within the 
meaning of the United States Private Securities Litigation Reform Act of 1995 
and applicable Canadian securities laws. When or if used in this news release, 
the words "anticipate", "believe", "estimate", "expect", "target, "plan", 
"forecast", "may", "schedule" and similar words or expressions identify 
forward-looking statements or information. These forward-looking statements or 
information may relate to future prices of commodities, accuracy of mineral or 
resource exploration activity, reserves or resources, regulatory or government 
requirements or approvals, the reliability of third party information, 
continued access to mineral properties or infrastructure, currency risks 
including the exchange rate of US$ for CDN$, changes in exploration costs and 
government royalties or taxes in Canada, the United States or other 
jurisdictions and other factors or information. Such statements represent the 
Company's current views with respect to future events and are necessarily based 
upon a number of assumptions and estimates that, while considered reasonable by 
the Company, are inherently subject to significant business, economic, 
competitive, political and social risks, contingencies and uncertainties. Many 
factors, both known and unknown, could cause results, performance or 
achievements to be materially different from the results, performance or 
achievements that are or may be expressed or implied by such forward-looking 
statements. The Company does not intend, and does not assume any obligation, to 
update these forward-looking statements or information to reflect changes in 
assumptions or changes in circumstances or any other events affections such 
statements and information other than as required by applicable laws, rules and 
regulations.

- 30 -

CONTACT INFO:

ML Gold Corp.
Investor Relations
(604) 669-2279
info@mlgoldcorp.com
www.mlgoldcorp.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=593550541