Source	Marketwire
Date	05/23/2017
Time	04:01:06 AM

Company	 ANFIELD GOLD CORP.
Title	Anfield Gold Announces Positive Metallurgy Results





    CDNX Symbol: ANF











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Anfield Gold Corp.

TSX VENTURE SYMBOL: ANF

May 23, 2017

Anfield Gold Announces Positive Metallurgy Results


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 23, 2017) - Anfield Gold Corp. 
("Anfield" or "Company") (TSX VENTURE:ANF) is pleased to announce the results 
from its last round of metallurgical testing for the Coringa Project ("Coringa" 
or "Project"). The results were positive, demonstrating recoveries of 98% gold 
and 61% silver.

These results were achieved by testing a master composite representing 
mineralized material from the Meio and Serra zones of the Project using gravity 
concentration followed by carbon-in-leach ("CIL") cyanidation of the gravity 
tails. The master composite was a 50/50 blend of mineralized material from each 
zone that utilized core from 19 out of the 229 drill holes that have been 
completed across both zones. The master composite also responded very well to 
whole ore cyanidation with gold extraction rates similar to those obtained by 
gravity concentration followed by CIL cyanidation; however, whole ore 
cyanidation was shown to have 9% lower silver recoveries.

Anfield anticipates using gravity concentration followed by CIL cyanidation of 
gravity tails in the final flow sheet for the Project's feasibility study, 
expected in July 2017.

The metallurgical testing was undertaken by C.H. Plenge & CIA S.A. ("C.H. 
Plenge") at its laboratory in Lima, Peru. C.H. Plenge is not related to Anfield.

Permitting and Project Activity Update

On May 10, 2017, Anfield received formal consent for the Project from the 
Instituto Nacional de Colonizacao e Reforma Agraria ("INCRA"). INCRA's consent 
was required by the Secretaria de Estado de Meio Ambiente e Sustentabilidade 
("SEMAS") as a pre-requirement to issuance of permits for the commencement of 
construction and operations at Coringa. Anfield continues to engage with SEMAS 
as the agency works to finalize and issue the required permits.

Pre-construction activities at Coringa continue to advance, with the latest 
developments listed below:

/T/

--  The mine camp is complete and has been upgraded to accommodate over 200
staff during operations.
--  Security fencing around the perimeter of the camp areas has been
completed.
--  Groundwater supply for the camps domestic water needs has been
identified and tested.
--  Mine design, planning and scheduling work based on the updated mineral
resource estimate (May 3, 2017 news release) is being developed for
incorporation into the feasibility study.
--  Site wide hydrological and geochemical modeling will be completed by the
end of May.
--  All field and laboratory investigation programs in support of the design
of the process plant and related infrastructure, tailings storage
facility and mine workings have been completed.
--  Feasibility level tailings storage facility design and scheduling have
been completed.
--  Detailed project engineering and cost estimation is approximately 50%
complete.


/T/

Quality Assurance and Quality Control

All Anfield sample assay results have been monitored through a quality control 
/ quality assurance ("QA/QC") program including the insertion of blind 
standards, blanks and the reanalysis of duplicate samples. The results of the 
QA/QC program and the resampling program indicate that the sample database is 
of sufficient accuracy and precision.

Qualified Persons

Nelson King, SME Registered Member and Metallurgical Consultant to Anfield, is 
a Qualified Person as defined by National Instrument 43-101 Standards of 
Disclosure for Mineral Projects. Mr. King has assisted Anfield in the 
development and direction of the metallurgical testing program for the Project, 
has visited C.H. Plenge's laboratory in Lima to observe the testing program, 
and has reviewed and approved the content of this press release relating to the 
metallurgical testing. Mr. King also verified the results of the metallurgical 
testing.

About Anfield Gold

Anfield Gold Corp. (TSX VENTURE:ANF) is a Vancouver, Canada based precious 
metal exploration and development company focused on the development of the 
Coringa Project located in Para State, Brazil. Anfield's strategic plan also 
includes the acquisition of other gold projects with the goal of becoming a 
mid-tier gold mining company.

Further details are available on the Company's website at 
https://anfieldgold.com

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

Certain statements and information herein, including all statements that are 
not historical facts, contain forward-looking statements and forward-looking 
information within the meaning of applicable securities laws. Often, but not 
always, forward-looking statements can be identified by the use of words such 
as "plans," "intends," "will" "are expected" or variations of such words and 
phrases. Forward looking statements or information in this press release 
include, but are not limited to, the rate of ore recovery at the Project, the 
preparation of, and timing to completion of, a feasibility study for the 
Project; Anfield's strategic plan to acquire other gold projects with the goal 
of becoming a mid-tier gold mining company, timing to completion of 
pre-construction activities and plan to use gravity concentration followed by 
CIL cyanidation of gravity tails. In making the forward-looking statements in 
this release, Anfield has applied certain factors and assumptions that are 
based on information currently available to Anfield as well as Anfield's 
current beliefs and assumptions (including Anfield's belief in the accuracy of 
the mineral resource estimate). Although Anfield considers these beliefs and 
assumptions to be reasonable based on information currently available to it, 
they may prove to be incorrect, and the forward-looking statements in this 
release are subject to numerous risks, uncertainties and other factors that may 
cause future results to differ materially from those expressed or implied in 
such forward-looking statements. Such risk factors include, among others, 
additional drilling and exploration may determine that there is no potentially 
viable mine plan for the Project, risks associated with the business of 
Anfield, risks related to reliance on technical information provided by 
Magellan Minerals Ltd. as related to the Project; risks relating to exploration 
and potential development of the Company's projects;
risks related to obtaining the permits and approvals necessary to develop and 
commission the Project on terms that are acceptable to Anfield; risks related 
to Anfield identifying suitable acquisition targets; business and economic 
conditions in the mining industry generally; the supply and demand for labour 
and other project inputs; prices for commodities to be produced and changes in 
commodity prices; changes in interest and currency exchange rates; risks 
relating to unanticipated operational difficulties (including failure of plant, 
equipment or processes to operate in accordance with specifications or 
expectations, cost escalation, unavailability of materials and equipment, 
government action or delays in the receipt of government approvals, industrial 
disturbances or other job action, and unanticipated events related to health, 
safety and environmental matters); risks relating to adverse weather 
conditions; political risk and social unrest; changes in general economic 
conditions or conditions in the financial markets; and changes to business and 
economic conditions in the mining industry generally. Although Anfield has 
attempted to identify important factors that could cause actual results to 
differ materially from those contained in forward-looking information, there 
may be other factors that cause results not to be as anticipated, estimated or 
intended. There can be no assurance that such information will prove to be 
accurate, as actual results and future events could differ materially from 
those anticipated in such statements. Accordingly, readers should not place 
undue reliance on forward-looking information. Anfield does not undertake to 
update any forward-looking information, except in accordance with applicable 
securities laws.

- 30 -

CONTACT INFO:

Anfield Gold Corp.
Scott Hicks
604  646-1884
Fax: 604  687-7041
www.anfieldgold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=593692544