Source	MARKET NEWS
Date	05/23/2017
Time	08:06:46 AM

Company	 Silver Range Resources Ltd.
Title	Programs Underway In Nevada





    CDNX Symbol: SNG











Press Release





Programs Underway In Nevada --->@NEWS RELEASE
SILVER RANGE RESOURCES LTD ("SNG-V;SLRRF-0")
- Programs Underway In Nevada

Silver Range Resources Ltd. ("Silver Range") is pleased to provide
an update on exploration programs underway in Nevada.

In early April, Silver Range mobilized geological crews to explore
six properties and conduct a reconnaissance project. Following
completion in early May, a geophysical crew was mobilized to complete
surveys on five properties. This work is being conducted on the
following projects:

Gold Chief

Gold Chief is a structurally controlled, carbonate-hosted gold
target north of Caliente in eastern Nevada. Documented historical
production from the Gold Chief Mine on the property includes 5225 t @
6.18 g/t Au (1913-1914). Recent sampling by Silver Range of wall rock
in a collapsed stope returned 4 m @ 1.93 g/t Au including 1 m @ 4.58
g/t Au. Silver Range conducted additional sampling, hyperspectral
alteration mapping and soil geochemical surveys in April and in June
will conduct a three dimensional (3D) induced polarization (IP) survey
over 2 km of favourable structure and stratigraphy centred on the Gold
Chief Mine. The survey is designed to detect additional sulphide
mineralization along the Stampede Detachment Fault and an associated
lateral ramp fault.

Skylight

Skylight is in the Royston Hills, 60 kilometres northwest of
Tonopah in central Nevada. The property is underlain by mid-Tertiary
silicic ash flow tuffs and ignimbrites and Triassic metasediments and
is centred on four large silica caps covering an area of 700 metres (m)
by 450 m. Historical surface sampling in the area by Rimfire Minerals
Corporation and Newmont Mining reportedly returned surface gold samples
to 2.04 g/t Au. The property was drilled in 2007 with 4 of 7 holes
reportedly intersecting "anomalous gold and silver" and a best
announced intersection of 1.766 g/t Au over 3.05 m. Silver Range
conducted mapping, sampling and hyperspectral alteration mapping on the
property in April and will conduct a 3D IP survey centred on the silica
caps in June. The objective of this work is to locate prospective
targets by defining the architecture of the epithermal system.

Strongbox

Strongbox is located north of Beatty near the California - Nevada
border. The property covers widespread orogenic or intrusion related,
structurally controlled mineralization centred on Tule Canyon, a
past-producing placer wash. There is evidence of modern placer and
underground mining in the area and sampling by Silver Range has
returned grab sample results up to 27.1 g/t Au. In April, Silver Range
conducted sampling, geochemical surveys and geological mapping of
surface exposures and underground workings. In May, a geophysical
survey crew mobilized to the property to conduct horizontal loop
electromagnetic (HLEM) and total magnetic field surveys to map the
structures hosting the mineralization.

Enigma

The Enigma Property is located east of Yerington in the Wilson
Mining District and hosts orogenic-style gold mineralization in a
series of laterally extensive fault-controlled quartz veins. Initial
sampling by Silver Range returned grab sample values of up to 73.3 g/t
Au from 12 samples. Geological mapping, soil geochemical surveys and
hyperspectral alteration mapping were completed on the property in
April. Horizontal loop electromagnetic (HLEM) and total magnetic field
surveys will be conducted later this month to map the structures
hosting the mineralization.

Stinson

The Stinson Property covers the Ben Hur and Stinson Mines
approximately 35 kilometres north of Ely. Structurally controlled gold
mineralization is hosted in quartzite at Ben Hur and in carbonates at
Stinson. Initial sampling by Silver Range in 2016 returned gold
analyses up to 51.2 g/t Au. Additional sampling, surface and
underground geological mapping and hyperspectral alteration mapping was
conducted at the Ben Hur Mine in April.

Hunter

The Hunter Property adjoins Eurasian Minerals Golden Sunrise
(French Bullion) property in White Pine County, north of Ely. The
property covers Middle Devonian to Mississippian carbonate and shale
stratigraphy prospective to host Carlin-style mineralization.
Mineralized jasperoid in shaft dumps was sampled by the Nevada Bureau
of Mines and Geology and reportedly returned analyses of up to 2.8 ppm
Au. Silver Range conducted additional sampling on the property in April
to locate additional mineralization of this tenor.

Road Gold

Road Gold is north of Luning and adjacent to the Isabella Pearl
Mine, currently being developed by Gold Resource Corp. The property
covers vein hosted and disseminated gold, silver and copper
mineralization. Recent historic sampling has returned up to 5.88 g/t
Au, 332 g/t Ag and 3.9% Cu. Silver Range intends to conduct IP surveys
south of the most significant showings on the property in a pediment
covered area.

A video presentation describing several of Silver Range's Nevada
projects including Gold Chief and Strongbox can be found at
www.silverrangeresources.com.

Technical information in this news release has been approved by
Mike Power, M.Sc., P.Geo., CPG, President and CEO of Silver Range
Resources Ltd. and a Qualified Person for the purposes of National
Instrument 43-101. Historical sampling results and production summaries
reported in this press release with the exception of results at the
Road Gold Property cannot be independently verified.

Silver Range is a precious metals prospect generator working in
Nunavut, the Northwest Territories and Nevada. The company is actively
seeking joint venture partners to explore the assets in its portfolio.

ON BEHALF OF SILVER RANGE RESOURCES LTD.

"Mike Power"

President, C.E.O. & Director

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release may contain forward looking statements based on
assumptions and judgments of management regarding future events or
results that may prove to be inaccurate as a result of exploration and
other risk factors beyond its control, and actual results may differ
materially from the expected results.

Contact Information:

For further information concerning Silver Range or its exploration projects
please contact:

Investor Inquiries
Richard Drechsler
Vice-President, Communications
Tel: (604) 687-2522
NA Toll-Free: (888) 688-2522
rdrechsler@silverrangeresources.com
http://www.silverrangeresources.com
______________________________
_______________________________________________
TSX Venture closing price for SNG-V
Date: 2017/05/18
Closing Price: 0.25
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1714200037TS11714201813-08050320170523