Source	Marketwire
Date	05/24/2017
Time	05:01:09 AM

Company	 ATLANTIC GOLD CORPORATION
Title	Atlantic Gold Reports Additional Results from the Resource Definition 
Drill Programs at Fifteen Mile Stream and Cochrane Hill





    CDNX Symbol: AGB











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Atlantic Gold Corporation

TSX VENTURE SYMBOL: AGB

May 24, 2017

Atlantic Gold Reports Additional Results from the Resource Definition Drill 
Programs at Fifteen Mile Stream and Cochrane Hill


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 24, 2017) -

HIGHLIGHTS:

Fifteen Mile Stream: 36m @ 2.33 g/t from 112m, 16m @ 2.47g/t from 9.5m, 22m @ 
1.86 g/t from 108m

Cochrane Hill: 18m @ 1.66 g/t from 65m, 13m @ 2.22g/t from 198m, 5m @ 5.50g/t 
from 48m

IDENTIFYING EXTENSIVE BROAD ZONES OF SHALLOW MINERALIZATION AT FIFTEEN MILE 
STREAM

DEPTH EXTENSIONS AT COCHRANE HILL

Atlantic Gold Corporation (TSX VENTURE:AGB) ("Atlantic" or the "Company") is 
pleased to report assay results received from drilling programs on the Fifteen 
Mile Stream and Cochrane Hill gold deposits where resource definition drilling 
on 25m x 20m centres is underway with the objective of upgrading resources to 
measured and indicated categories.

In particular, it is noted that assay results are now being returned from those 
holes at Fifteen Mile Stream drilled through the core of the anticline, and 
these are indicating considerable widths of attractive grades. Total widths of 
significantly mineralized intervals intersected in hole FMS-17-124 (see table 
below) aggregate to 78m @ 1.75g/t and in hole FMS-17-113, to 60m @ 1.73g/t. 
Previously reported holes from this same locale, FMS-17-104 and FMS-17-090, had 
recorded aggregated significantly mineralized intervals of 88m @ 1.79g/t and 
36.5m @ 4.12g/t respectively.

The Company plans to use the results from the drill programs to undertake 
further analysis to determine the economic viability of the above-noted 
deposits which would include analysis of the economics of processing these 
deposits at the Moose River Consolidated ("MRC") processing facility by way of 
a Pre-Feasibility Study.

New assay results from the two drilling programs are reported as follows:

/T/

1.  FIFTEEN MILE STREAM

/T/

Fifteen Mile Stream is located approximately 57km northeast of the central 
milling facility at Touquoy and is readily accessible by highway. Fifteen Mile 
Stream's current inferred mineral resources stand at 11.72 million tonnes at 
1.55 g/t Au for 584,000 oz. New assay results reported herein are from a 
further 14 holes of the ongoing resource definition diamond drilling program. 
At this time 177 holes for 21,387 of the planned 25,000m have now been drilled 
and three drilling rigs are presently operating on the property with completion 
expected in a week's time.

Drilling Results:

The additional assay drill results continue to reflect those grades, widths and 
geometry of gold mineralization documented from the 1980s and 2011 drilling 
programs which support the current inferred resource estimate (see below). 
Mineralization occurs within argillites, greywackes and bedding-parallel quartz 
veins across the hinge zone and limbs of the E-W trending Fifteen Mile Stream 
(FMS) Anticline. The northern limb of the anticline dips moderately north, with 
the southern limb vertical to overturned (generally steeply north dipping). All 
holes are therefore declined to the south at various dips and hence true widths 
vary (see assay table below) depending on which limb of the anticline is 
intersected, and also depending on hole dip. Free gold is commonly observed, 
and in association with pyrrhotite and arsenopyrite.

Results are now being returned from a suite of holes drilled across the hinge 
zone of the anticline in the central part of the main Egerton MacLean zone, 
where drill access had previously been impeded owing to the location of certain 
wetlands. Apart from holes previously noted (FMS-17-090 and 104), attention is 
drawn here to new holes FMS-17-113 and 124 where appreciably mineralized 
intervals combine to down-hole widths of up to 78m. As well as the northern and 
southern limbs of the anticline, the central core or hinge zone of the 
anticline is now being shown to be well mineralized.

These shallow and widespread mineralized intersections across the limbs and 
core of this sub-horizontal anticlinal hinge zone are considered to be highly 
encouraging in the context of potential open pit extraction.

The accompanying cross sections and drilling progress plan can be viewed here:
http://file.marketwire.com/release/atfmsd0523.pdf

Results subsequent of those previously released are tabulated below. Previous 
results can be found here: February 10, 2017, March 1, 2017, March 16, 2017, 
April 3, 2017 and May 1, 2017.

/T/

----------------------------------------------------------------------------
Depth
Hole id       East        North         Dip          Az.          (m)


----------------------------------------------------------------------------
FMS-17-094         13500        10080          -60          175          122
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-109         13475        10020          -60          175           41
----------------------------------------------------------------------------
FMS-17-110         13650        10140          -60          175           80
----------------------------------------------------------------------------
FMS-17-112         13625        10160          -45          175          110
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-113         13425        10160          -60          175          230
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
(incl.
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-114         13450        10220          -80          175          200
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-115         13450        10220          -70          175          188
----------------------------------------------------------------------------
FMS-17-116         13450        10220          -60          175          134
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-117         13475        10235          -65          175          203
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-118         13475        10235          -55          175          209
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-119         13475        10235          -45          175          251
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-120         13400        10220          -80          175          152
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-122         13400        10220          -70          175          140
----------------------------------------------------------------------------
FMS-17-124         13450        10200          -55          175          242
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Significant Intervals
Hole id       (greater than or equal to0.5g/t Au and up to 3m internal
dilution)
-----------------------------------------------------------------
From          To         Width     Approx. true    Grade
(m)          (m)          (m)       width (m)     (g/t Au)
----------------------------------------------------------------------------
FMS-17-094      9.5          25.5          16           14          2.47
----------------------------------------------------------------------------
and      43           45           2            2           2.12
----------------------------------------------------------------------------
and      64           84           20           16          0.97
----------------------------------------------------------------------------
and      88           99           11           9           2.55
----------------------------------------------------------------------------
and     103          104           1            1           4.35
----------------------------------------------------------------------------
FMS-17-109       34           41           7            6          0.95!
----------------------------------------------------------------------------
FMS-17-110       58           64           6            5           0.64
----------------------------------------------------------------------------
FMS-17-112       40           41           1            1           15.3
----------------------------------------------------------------------------
and      64           74           10           10          0.84
----------------------------------------------------------------------------
FMS-17-113       20           21           1            1          13.85
----------------------------------------------------------------------------
and      46           59           13           13          0.95
----------------------------------------------------------------------------
and      68           91           23           23          1.39
----------------------------------------------------------------------------
and     114          121           7            7           4.90
----------------------------------------------------------------------------
(incl.     114          115           1            1          32.0)
----------------------------------------------------------------------------
and     131          139           8            7           0.75
----------------------------------------------------------------------------
and     176          185           9            7           2.12
----------------------------------------------------------------------------
FMS-17-114      115          116           1            1           3.01
----------------------------------------------------------------------------
and     121          134           13           11          0.64
----------------------------------------------------------------------------
FMS-17-115      103          125           22           20          0.75
----------------------------------------------------------------------------
FMS-17-116       95          100           5            5           1.73
----------------------------------------------------------------------------
and     105          120           15           15          1.03    
----------------------------------------------------------------------------
FMS-17-117      105          109           4            4           1.39
----------------------------------------------------------------------------
and     117          118           1            1           45.6
----------------------------------------------------------------------------
and     126          138           12           12          1.05
----------------------------------------------------------------------------
and     148          159           11           11          0.94
----------------------------------------------------------------------------
FMS-17-118      112          148           36           36          2.33
----------------------------------------------------------------------------
and     160          161           1            1           8.67
----------------------------------------------------------------------------
FMS-17-119      109          111           2            2           4.16
----------------------------------------------------------------------------
and     117          152           35           35          1.12
----------------------------------------------------------------------------
and     179          184           5            5           1.44
----------------------------------------------------------------------------
and     205          213           8            8           0.63
----------------------------------------------------------------------------
and     225          232           7            6           0.66
----------------------------------------------------------------------------
FMS-17-120       69           70           1            1           8.57
----------------------------------------------------------------------------
and     117          129           12           12          0.73
----------------------------------------------------------------------------
FMS-17-122      106          112           6            6           0.65
----------------------------------------------------------------------------
FMS-17-124       49           50           1            1           7.56
----------------------------------------------------------------------------
and      80          104           24           24          1.59
----------------------------------------------------------------------------
and     108          130           22           22          1.86
----------------------------------------------------------------------------
and     135          138           3            3           3.30
----------------------------------------------------------------------------
and     142          148           6            5           3.19
----------------------------------------------------------------------------
and     205          228           23           21          1.22
----------------------------------------------------------------------------

/T/

True width of the mineralization varies according to the dip of the enclosing 
stratigraphy and declination of the relevant drill hole. It is therefore noted 
for each intersection in the table above. Particularly in the Egerton-Maclean 
zone hole collars are necessarily located to minimise, though not entirely 
avoid, ingress to wetland areas and as a result hole declinations are adjusted 
to compensate for collar positioning. In many cases holes are drilled at 
different declinations from the same site. Sample distribution is not 
materially compromised.

The current resource estimate for Fifteen Mile Stream is as follows:

/T/

----------------------------------------------------------------------------
Category         Tonnes           Grade            Contained Au
(millions)       (g/t) Au         (oz.)
----------------------------------------------------------------------------
FIFTEEN MILE STREAM
----------------------------------------------------------------------------
Inferred Resource      11.72             1.55           584,000
----------------------------------------------------------------------------
Resources that are not reserves do not have demonstrated economic viability
----------------------------------------------------------------------------

/T/

The Mineral Resource estimate for Fifteen Mile Stream is quoted at a cut-off 
grade of 0.5g/t. It has an effective date of February 16, 2015 and was prepared 
as part of a technical report in accordance with NI 43-101 by Mr. Neil 
Schofield, a principal of FSSI (Australia) Pty Ltd, released on April 2, 2015 
on SEDAR.

/T/

2.  COCHRANE HILL

/T/

The Cochrane Hill Gold deposit is located within trucking distance 
(approximately 80km) to the central milling facility at Touquoy and is readily 
accessible by highway (based on a Preliminary Economic Assessment dated October 
14, 2014 prepared by Moose Mountain Technical Services). Mineral resources at 
Cochrane Hill currently comprise indicated resources of 4.5 million tonnes at 
1.8g/t Au for 251,000 oz. and inferred resources of 5.6 million tonnes at 1.6 
g/t Au for 298,000 oz.

New assay results reported herein are from a further 29 holes of the resource 
definition diamond drilling program. This program was completed at the end of 
April with a total of 177 holes for 26,575m having been drilled. The latter 
phase of the program targeted potential extensions of mineralization to the 
west of the main body of mineralization within an area of shallow wetland where 
particular regulatory approval was required, and west of the step out holes on 
section 2775E across highway #7. Nine additional holes were also drilled to 
test for depth extensions beneath the last, deepest, encouraging intersection 
on each of nine cross-sections east of 3000E. Examples of these deeper 
intersections from previously reported holes are 30m @ 2.61g/t (CH-16-126), 18m 
@ 2.52g/t (CH-16-052) and 11m @ 3.41g/t (CH-16-102).

Drilling Results:

These new assay results come largely from the wetland area to the west of the 
main body of mineralization and where the geometry of the mineralization 
continues to be fairly predictable and continuous, as a reasonably discrete, 
tabular, 70 degrees north-dipping zone having a true width of approximately 
15-20m in this area. Mineralization appears to be attenuating west of the 
highway #7 (around 2750E) though more assays here are pending. Mineralization, 
although narrowing, remains open to the east (east of 3500E).

The accompanying cross section and drill progress plan can be viewed here: 
http://file.marketwire.com/release/atchd0523.pdf

Results subsequent to those previously released are tabulated below. Previous 
results can be found here: Dec 6, 2016, Jan 3, 2017, Jan 11,2017, Feb 2, 2017 
and May 1, 2017.

/T/

----------------------------------------------------------------------------
Depth
Hole id     Easting      Northing       Dip          Az.          (m)


----------------------------------------------------------------------------
CH-17-143           2900         3100          -70          171          170
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-146           2900         3100          -60          171          142
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-147           2925         3220          -60          171          281
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-148           2900         3100          -45          171          112
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-149           2925         3200          -60          171          260
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-150           2900         3070          -45          171           70
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-151           2925         3180          -60          171          230
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-152           3450         3100          -45          171          101
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-153           2950         3080          -70          171          122
----------------------------------------------------------------------------
CH-17-154           3475         3109          -45          171          110
----------------------------------------------------------------------------
CH-17-156           2950         3080          -60          171          100
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-157           3500         3090          -45          171           92
----------------------------------------------------------------------------
CH-17-162           2950         3050          -45          171           52
----------------------------------------------------------------------------
CH-17-163           2747         3150          -45          171          170
----------------------------------------------------------------------------
CH-17-164           2875         3100          -70          171          172
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-165           2675         3120          -70          171          191
----------------------------------------------------------------------------
CH-17-166           2775         3170          -60          171          212
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-167           2700         3110          -60          171          152
----------------------------------------------------------------------------
CH-17-168           2775         3070          -45          171           71
----------------------------------------------------------------------------
(incl.
----------------------------------------------------------------------------
CH-17-169           2725         3090          -60          171          131
----------------------------------------------------------------------------
CH-17-170           2725         3110          -60          171          152
----------------------------------------------------------------------------
CH-17-173           2700         3150          -60          171          190
----------------------------------------------------------------------------
CH-17-174           2875         3100          -45          171          133
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
(incl.
----------------------------------------------------------------------------
CH-17-176           2723         3070          -60          171          110
----------------------------------------------------------------------------
CH-17-177           2725         3050          -60          171           90
----------------------------------------------------------------------------
CH-17-178           2875         3070          -45          171           
82----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-180           2700         3070          -60          171          110
----------------------------------------------------------------------------
CH-17-181           2825         3100          -70          171          151
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-196           3000         3082          -60          171          101
----------------------------------------------------------------------------
(incl.
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
TOTAL                                  177 holes completed for:       26,575
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Significant Intervals
Hole id                  (greater than or equal to0.5g/t Au and up to 3m
internal dilution)
-----------------------------------------------------------------
From          To         Width        Grade
(m)          (m)          (m)        (g/t Au)
----------------------------------------------------------------------------
CH-17-143                          67           81           14     1.23
----------------------------------------------------------------------------
and                        90           92            2     2.67
----------------------------------------------------------------------------
and                       109          113            4     0.80
----------------------------------------------------------------------------
CH-17-146                          22           23            1   4.19(i)
----------------------------------------------------------------------------
and                        69           70            1     8.01
----------------------------------------------------------------------------
and                        80           82            2     4.40
----------------------------------------------------------------------------
CH-17-147                         161          162            1   4.82(i)
----------------------------------------------------------------------------
and                       183          187            4     2.00


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Atlantic Gold Corporation

TSX VENTURE SYMBOL: AGB

May 24, 2017

Atlantic Gold Reports Additional Results from the Resource Definition Drill 
Programs at Fifteen Mile Stream and Cochrane Hill


VANCOUVER, BRITISH COLUMBIA--(Marketwired - May 24, 2017) -

HIGHLIGHTS:

Fifteen Mile Stream: 36m @ 2.33 g/t from 112m, 16m @ 2.47g/t from 9.5m, 22m @ 
1.86 g/t from 108m

Cochrane Hill: 18m @ 1.66 g/t from 65m, 13m @ 2.22g/t from 198m, 5m @ 5.50g/t 
from 48m

IDENTIFYING EXTENSIVE BROAD ZONES OF SHALLOW MINERALIZATION AT FIFTEEN MILE 
STREAM

DEPTH EXTENSIONS AT COCHRANE HILL

Atlantic Gold Corporation (TSX VENTURE:AGB) ("Atlantic" or the "Company") is 
pleased to report assay results received from drilling programs on the Fifteen 
Mile Stream and Cochrane Hill gold deposits where resource definition drilling 
on 25m x 20m centres is underway with the objective of upgrading resources to 
measured and indicated categories.

In particular, it is noted that assay results are now being returned from those 
holes at Fifteen Mile Stream drilled through the core of the anticline, and 
these are indicating considerable widths of attractive grades. Total widths of 
significantly mineralized intervals intersected in hole FMS-17-124 (see table 
below) aggregate to 78m @ 1.75g/t and in hole FMS-17-113, to 60m @ 1.73g/t. 
Previously reported holes from this same locale, FMS-17-104 and FMS-17-090, had 
recorded aggregated significantly mineralized intervals of 88m @ 1.79g/t and 
36.5m @ 4.12g/t respectively.

The Company plans to use the results from the drill programs to undertake 
further analysis to determine the economic viability of the above-noted 
deposits which would include analysis of the economics of processing these 
deposits at the Moose River Consolidated ("MRC") processing facility by way of 
a Pre-Feasibility Study.

New assay results from the two drilling programs are reported as follows:

/T/

1.  FIFTEEN MILE STREAM

/T/

Fifteen Mile Stream is located approximately 57km northeast of the central 
milling facility at Touquoy and is readily accessible by highway. Fifteen Mile 
Stream's current inferred mineral resources stand at 11.72 million tonnes at 
1.55 g/t Au for 584,000 oz. New assay results reported herein are from a 
further 14 holes of the ongoing resource definition diamond drilling program. 
At this time 177 holes for 21,387 of the planned 25,000m have now been drilled 
and three drilling rigs are presently operating on the property with completion 
expected in a week's time.

Drilling Results:

The additional assay drill results continue to reflect those grades, widths and 
geometry of gold mineralization documented from the 1980s and 2011 drilling 
programs which support the current inferred resource estimate (see below). 
Mineralization occurs within argillites, greywackes and bedding-parallel quartz 
veins across the hinge zone and limbs of the E-W trending Fifteen Mile Stream 
(FMS) Anticline. The northern limb of the anticline dips moderately north, with 
the southern limb vertical to overturned (generally steeply north dipping). All 
holes are therefore declined to the south at various dips and hence true widths 
vary (see assay table below) depending on which limb of the anticline is 
intersected, and also depending on hole dip. Free gold is commonly observed, 
and in association with pyrrhotite and arsenopyrite.

Results are now being returned from a suite of holes drilled across the hinge 
zone of the anticline in the central part of the main Egerton MacLean zone, 
where drill access had previously been impeded owing to the location of certain 
wetlands. Apart from holes previously noted (FMS-17-090 and 104), attention is 
drawn here to new holes FMS-17-113 and 124 where appreciably mineralized 
intervals combine to down-hole widths of up to 78m. As well as the northern and 
southern limbs of the anticline, the central core or hinge zone of the 
anticline is now being shown to be well mineralized.

These shallow and widespread mineralized intersections across the limbs and 
core of this sub-horizontal anticlinal hinge zone are considered to be highly 
encouraging in the context of potential open pit extraction.

The accompanying cross sections and drilling progress plan can be viewed here:
http://file.marketwire.com/release/atfmsd0523.pdf

Results subsequent of those previously released are tabulated below. Previous 
results can be found here: February 10, 2017, March 1, 2017, March 16, 2017, 
April 3, 2017 and May 1, 2017.

/T/

----------------------------------------------------------------------------
Depth
Hole id       East        North         Dip          Az.          (m)


----------------------------------------------------------------------------
FMS-17-094         13500        10080          -60          175          122
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-109         13475        10020          -60          175           41
----------------------------------------------------------------------------
FMS-17-110         13650        10140          -60          175           80
----------------------------------------------------------------------------
FMS-17-112         13625        10160          -45          175          110
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-113         13425        10160          -60          175          230
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
(incl.
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-114         13450        10220          -80          175          200
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-115         13450        10220          -70          175          188
----------------------------------------------------------------------------
FMS-17-116         13450        10220          -60          175          134
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-117         13475        10235          -65          175          203
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-118         13475        10235          -55          175          209
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-119         13475        10235          -45          175          251
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-120         13400        10220          -80          175          152
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
FMS-17-122         13400        10220          -70          175          140
----------------------------------------------------------------------------
FMS-17-124         13450        10200          -55          175          242
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Significant Intervals
Hole id       (greater than or equal to0.5g/t Au and up to 3m internal
dilution)
-----------------------------------------------------------------
From          To         Width     Approx. true    Grade
(m)          (m)          (m)       width (m)     (g/t Au)
----------------------------------------------------------------------------
FMS-17-094      9.5          25.5          16           14          2.47
----------------------------------------------------------------------------
and      43           45           2            2           2.12
----------------------------------------------------------------------------
and      64           84           20           16          0.97
----------------------------------------------------------------------------
and      88           99           11           9           2.55
----------------------------------------------------------------------------
and     103          104           1            1           4.35
----------------------------------------------------------------------------
FMS-17-109       34           41           7            6          0.95!
----------------------------------------------------------------------------
FMS-17-110       58           64           6            5           0.64
----------------------------------------------------------------------------
FMS-17-112       40           41           1            1           15.3
----------------------------------------------------------------------------
and      64           74           10           10          0.84
----------------------------------------------------------------------------
FMS-17-113       20           21           1            1          13.85
----------------------------------------------------------------------------
and      46           59           13           13          0.95
----------------------------------------------------------------------------
and      68           91           23           23          1.39
----------------------------------------------------------------------------
and     114          121           7            7           4.90
----------------------------------------------------------------------------
(incl.     114          115           1            1          32.0)
----------------------------------------------------------------------------
and     131          139           8            7           0.75
----------------------------------------------------------------------------
and     176          185           9            7           2.12
----------------------------------------------------------------------------
FMS-17-114      115          116           1            1           3.01
----------------------------------------------------------------------------
and     121          134           13           11          0.64
----------------------------------------------------------------------------
FMS-17-115      103          125           22           20          0.75
----------------------------------------------------------------------------
FMS-17-116       95          100           5            5           1.73
----------------------------------------------------------------------------
and     105          120           15           15          1.03    
----------------------------------------------------------------------------
FMS-17-117      105          109           4            4           1.39
----------------------------------------------------------------------------
and     117          118           1            1           45.6
----------------------------------------------------------------------------
and     126          138           12           12          1.05
----------------------------------------------------------------------------
and     148          159           11           11          0.94
----------------------------------------------------------------------------
FMS-17-118      112          148           36           36          2.33
----------------------------------------------------------------------------
and     160          161           1            1           8.67
----------------------------------------------------------------------------
FMS-17-119      109          111           2            2           4.16
----------------------------------------------------------------------------
and     117          152           35           35          1.12
----------------------------------------------------------------------------
and     179          184           5            5           1.44
----------------------------------------------------------------------------
and     205          213           8            8           0.63
----------------------------------------------------------------------------
and     225          232           7            6           0.66
----------------------------------------------------------------------------
FMS-17-120       69           70           1            1           8.57
----------------------------------------------------------------------------
and     117          129           12           12          0.73
----------------------------------------------------------------------------
FMS-17-122      106          112           6            6           0.65
----------------------------------------------------------------------------
FMS-17-124       49           50           1            1           7.56
----------------------------------------------------------------------------
and      80          104           24           24          1.59
----------------------------------------------------------------------------
and     108          130           22           22          1.86
----------------------------------------------------------------------------
and     135          138           3            3           3.30
----------------------------------------------------------------------------
and     142          148           6            5           3.19
----------------------------------------------------------------------------
and     205          228           23           21          1.22
----------------------------------------------------------------------------

/T/

True width of the mineralization varies according to the dip of the enclosing 
stratigraphy and declination of the relevant drill hole. It is therefore noted 
for each intersection in the table above. Particularly in the Egerton-Maclean 
zone hole collars are necessarily located to minimise, though not entirely 
avoid, ingress to wetland areas and as a result hole declinations are adjusted 
to compensate for collar positioning. In many cases holes are drilled at 
different declinations from the same site. Sample distribution is not 
materially compromised.

The current resource estimate for Fifteen Mile Stream is as follows:

/T/

----------------------------------------------------------------------------
Category         Tonnes           Grade            Contained Au
(millions)       (g/t) Au         (oz.)
----------------------------------------------------------------------------
FIFTEEN MILE STREAM
----------------------------------------------------------------------------
Inferred Resource      11.72             1.55           584,000
----------------------------------------------------------------------------
Resources that are not reserves do not have demonstrated economic viability
----------------------------------------------------------------------------

/T/

The Mineral Resource estimate for Fifteen Mile Stream is quoted at a cut-off 
grade of 0.5g/t. It has an effective date of February 16, 2015 and was prepared 
as part of a technical report in accordance with NI 43-101 by Mr. Neil 
Schofield, a principal of FSSI (Australia) Pty Ltd, released on April 2, 2015 
on SEDAR.

/T/

2.  COCHRANE HILL

/T/

The Cochrane Hill Gold deposit is located within trucking distance 
(approximately 80km) to the central milling facility at Touquoy and is readily 
accessible by highway (based on a Preliminary Economic Assessment dated October 
14, 2014 prepared by Moose Mountain Technical Services). Mineral resources at 
Cochrane Hill currently comprise indicated resources of 4.5 million tonnes at 
1.8g/t Au for 251,000 oz. and inferred resources of 5.6 million tonnes at 1.6 
g/t Au for 298,000 oz.

New assay results reported herein are from a further 29 holes of the resource 
definition diamond drilling program. This program was completed at the end of 
April with a total of 177 holes for 26,575m having been drilled. The latter 
phase of the program targeted potential extensions of mineralization to the 
west of the main body of mineralization within an area of shallow wetland where 
particular regulatory approval was required, and west of the step out holes on 
section 2775E across highway #7. Nine additional holes were also drilled to 
test for depth extensions beneath the last, deepest, encouraging intersection 
on each of nine cross-sections east of 3000E. Examples of these deeper 
intersections from previously reported holes are 30m @ 2.61g/t (CH-16-126), 18m 
@ 2.52g/t (CH-16-052) and 11m @ 3.41g/t (CH-16-102).

Drilling Results:

These new assay results come largely from the wetland area to the west of the 
main body of mineralization and where the geometry of the mineralization 
continues to be fairly predictable and continuous, as a reasonably discrete, 
tabular, 70 degrees north-dipping zone having a true width of approximately 
15-20m in this area. Mineralization appears to be attenuating west of the 
highway #7 (around 2750E) though more assays here are pending. Mineralization, 
although narrowing, remains open to the east (east of 3500E).

The accompanying cross section and drill progress plan can be viewed here: 
http://file.marketwire.com/release/atchd0523.pdf

Results subsequent to those previously released are tabulated below. Previous 
results can be found here: Dec 6, 2016, Jan 3, 2017, Jan 11,2017, Feb 2, 2017 
and May 1, 2017.

/T/

----------------------------------------------------------------------------
Depth
Hole id     Easting      Northing       Dip          Az.          (m)


----------------------------------------------------------------------------
CH-17-143           2900         3100          -70          171          170
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-146           2900         3100          -60          171          142
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-147           2925         3220          -60          171          281
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-148           2900         3100          -45          171          112
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-149           2925         3200          -60          171          260
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-150           2900         3070          -45          171           70
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-151           2925         3180          -60          171          230
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-152           3450         3100          -45          171          101
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-153           2950         3080          -70          171          122
----------------------------------------------------------------------------
CH-17-154           3475         3109          -45          171          110
----------------------------------------------------------------------------
CH-17-156           2950         3080          -60          171          100
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-157           3500         3090          -45          171           92
----------------------------------------------------------------------------
CH-17-162           2950         3050          -45          171           52
----------------------------------------------------------------------------
CH-17-163           2747         3150          -45          171          170
----------------------------------------------------------------------------
CH-17-164           2875         3100          -70          171          172
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-165           2675         3120          -70          171          191
----------------------------------------------------------------------------
CH-17-166           2775         3170          -60          171          212
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-167           2700         3110          -60          171          152
----------------------------------------------------------------------------
CH-17-168           2775         3070          -45          171           71
----------------------------------------------------------------------------
(incl.
----------------------------------------------------------------------------
CH-17-169           2725         3090          -60          171          131
----------------------------------------------------------------------------
CH-17-170           2725         3110          -60          171          152
----------------------------------------------------------------------------
CH-17-173           2700         3150          -60          171          190
----------------------------------------------------------------------------
CH-17-174           2875         3100          -45          171          133
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
(incl.
----------------------------------------------------------------------------
CH-17-176           2723         3070          -60          171          110
----------------------------------------------------------------------------
CH-17-177           2725         3050          -60          171           90
----------------------------------------------------------------------------
CH-17-178           2875         3070          -45          171           
82----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-180           2700         3070          -60          171          110
----------------------------------------------------------------------------
CH-17-181           2825         3100          -70          171          151
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
CH-17-196           3000         3082          -60          171          101
----------------------------------------------------------------------------
(incl.
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
and
----------------------------------------------------------------------------
TOTAL                                  177 holes completed for:       26,575
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Significant Intervals
Hole id                  (greater than or equal to0.5g/t Au and up to 3m
internal dilution)
-----------------------------------------------------------------
From          To         Width        Grade
(m)          (m)          (m)        (g/t Au)
----------------------------------------------------------------------------
CH-17-143                          67           81           14     1.23
----------------------------------------------------------------------------
and                        90           92            2     2.67
----------------------------------------------------------------------------
and                       109          113            4     0.80
----------------------------------------------------------------------------
CH-17-146                          22           23            1   4.19(i)
----------------------------------------------------------------------------
and                        69           70            1     8.01
----------------------------------------------------------------------------
and                        80           82            2     4.40
----------------------------------------------------------------------------
CH-17-147                         161          162            1   4.82(i)
----------------------------------------------------------------------------
and                       183          187            4     2.00
----------------------------------------------------------------------------
and                       197          209           12     0.60
----------------------------------------------------------------------------
and                       229          234            5     1.11
----------------------------------------------------------------------------
CH-17-148                          18           19            1   33.5(i)
----------------------------------------------------------------------------
and                        49           55            6     0.65
----------------------------------------------------------------------------
and                        82           83            1     4.16
----------------------------------------------------------------------------
CH-17-149                         178          182            4     1.28
----------------------------------------------------------------------------
and                       198          211           13     2.22
----------------------------------------------------------------------------
CH-17-150                          27           28            1     5.10
----------------------------------------------------------------------------
and                        35           36            1     32.8
----------------------------------------------------------------------------
CH-17-151                         125          126            1   3.41(i)
----------------------------------------------------------------------------
and                       174          184           10     1.33
----------------------------------------------------------------------------
CH-17-152                          38           39            1     4.02
----------------------------------------------------------------------------
and                        54           63            9   0.83(i)
----------------------------------------------------------------------------
and                        72           82           10     2.06
----------------------------------------------------------------------------
CH-17-153                          14           15            1   3.31(i)
----------------------------------------------------------------------------
CH-17-154                          77           84            7     0.77
----------------------------------------------------------------------------
CH-17-156                           4            5            1     4.61
----------------------------------------------------------------------------
and                        31           39            8     1.02
----------------------------------------------------------------------------
and                        44           65          21`     0.95
----------------------------------------------------------------------------
and                        69           74            5     2.85
----------------------------------------------------------------------------
CH-17-157                          69           75            6     1.90
----------------------------------------------------------------------------
CH-17-162                          18           26            8     1.94
----------------------------------------------------------------------------
CH-17-163                         128          129            1    10.90
----------------------------------------------------------------------------
CH-17-164                          65           83           18     1.66
----------------------------------------------------------------------------
and                        88           92            4     0.80
----------------------------------------------------------------------------
and                       132          135            3     2.96
----------------------------------------------------------------------------
CH-17-165                          43           44            1   7.07(i)
----------------------------------------------------------------------------
CH-17-166                         133          134            1     5.81
----------------------------------------------------------------------------
and                       142          148            6     1.58
----------------------------------------------------------------------------
CH-17-167                                                           NSA
----------------------------------------------------------------------------
CH-17-168                          17           22            5   9.44(i)
----------------------------------------------------------------------------
(incl.                        21           22            1   42.0)(i)
----------------------------------------------------------------------------
CH-17-169                          39           40            1     6.51
----------------------------------------------------------------------------
CH-17-170                                                           NSA
----------------------------------------------------------------------------
CH-17-173                         129          131            2     1.66
----------------------------------------------------------------------------
CH-17-174                          47           56            9     0.38
----------------------------------------------------------------------------
and                        60           65            5     3.40
----------------------------------------------------------------------------
and                        75           80            5     5.04
----------------------------------------------------------------------------
(incl.                        75           76            1    23.3)
----------------------------------------------------------------------------
CH-17-176                          30           31            1   5.29(i)
----------------------------------------------------------------------------
CH-17-177                                                           NSA
----------------------------------------------------------------------------
CH-17-178                          21           24            3     1.31
----------------------------------------------------------------------------
and                        38           39            1     4.00
----------------------------------------------------------------------------
and                        48           53            5     5.50
----------------------------------------------------------------------------
CH-17-180                                                           NSA
----------------------------------------------------------------------------
CH-17-181                          73           85           12     0.47
----------------------------------------------------------------------------
and                       128          129           1`    14.35
----------------------------------------------------------------------------
CH-17-196                          38           42            4     7.80
----------------------------------------------------------------------------
(incl.                             38           39            1    28.0)
----------------------------------------------------------------------------
and                        49           55            6     0.48
----------------------------------------------------------------------------
and                        83           85            2     2.59
----------------------------------------------------------------------------
TOTAL                   metres       END OF CURRENT PROGRAM
----------------------------------------------------------------------------

/T/

(i)Wholly or partly includes 50g fire assay on pulverised whole-sample. All 
other assays are screen fire assays.

True width of the mineralization is approximately 75-85% of the down-hole width 
depending on dip of the drill hole.

The current resource estimate for Cochrane Hill is tabulated below:

/T/

----------------------------------------------------------------------------
Category         Tonnes           Grade            Contained
(millions)       (g/t) Au         Au (oz.)
----------------------------------------------------------------------------
COCHRANE HILL
----------------------------------------------------------------------------
Indicated               4.5              1.8            251,000
Resource
----------------------------------------------------------------------------
Inferred Resource       5.6              1.6            298,000
----------------------------------------------------------------------------
Resources that are not reserves do not have demonstrated economic viability
----------------------------------------------------------------------------

/T/

The Mineral Resource estimate for Cochrane Hill is quoted at a cut-off grade of 
0.5g/t. It has an effective date of August 1, 2014 and was prepared as part of 
a technical report in accordance with NI 43-101 by Mr. Neil Schofield, a 
principal of FSSI (Australia) Pty Ltd, released on August 14, 2014 on SEDAR.

Technical Disclosure

Fifteen Mile Stream

At Fifteen Mile Stream all assays are 50g charge fire assays conducted on 
whole-sample pulverized 1m samples of sawn, half NQ core with 1-in-10 duplicate 
assays and insertion of standards and blind blanks. Sample preparation and 
assaying is conducted at the Sudbury and Vancouver laboratories of ALS Canada 
Ltd, an entity having no other relationship with the Company. Core recovery is 
estimated for each metre and averages greater than 97%, excluding occasional 
voids, usually less than 2m, representing historic underground workings. Wing 
samples to voids may be less than 1m to re-establish routine sampling on 1m 
intervals. Drill core in the hangingwall of the northern limb of the anticline 
where adjacent historic holes very clearly indicate this upper stratigraphy to 
be barren may not be sampled and assayed. Standards, blanks and duplicate assay 
results are acceptable.

Cochrane Hill

All core drilled at Cochrane Hill is assayed. All assays have been conducted on 
1m whole-sampled pulverized samples of sawn, half NQ core and, where 
mineralization is expected, assayed by total sample screen fire assay with 2x 
fines fire assays, and insertion of standards and blind blanks. Sample 
preparation and assaying is conducted at the Sudbury and Vancouver laboratories 
of ALS Canada Ltd, an entity having no other relationship with the Company. In 
the hangingwall and footwall of expected mineralization samples are assayed by 
50g charge fire assay with any mineralized samples (generally greater than 
0.5g/t), and adjacent samples as appropriate, returned for screen fire assay. 
With almost 600 such fire assayed samples having now also been screen fire 
assayed it is apparent that correlation of these duplicate assay results is 
sufficiently close to warrant ongoing assaying by fire assay alone. This 
methodology will apply to samples from the final 28 drill holes. Core recovery 
is estimated for each metre and averages greater than 98%. Standards and blanks 
assay results are acceptable.
Results and updates from this drilling program will be reported progressively.

Wally Bucknell, Director of Exploration to the Company and a Qualified Person 
as defined by National Instrument 43-101 ("NI 43-101") has reviewed and 
approved the contents of this news release.

Further updates will be provided in due course and as new results come to hand.

On behalf of the Board of Directors,

Steven Dean, Chairman and Chief Executive Officer

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Forward-Looking Statements:

This release contains certain "forward looking statements" and certain 
"forward-looking information" as defined under applicable Canadian and U.S. 
securities laws. Forward-looking statements and information can generally be 
identified by the use of forward-looking terminology such as "may", "will", 
"expect", "intend", "estimate", "anticipate", "believe", "continue", "plans" or 
similar terminology. Forward-looking statements and information are not 
historical facts, are made as of the date of this press release, and include, 
but are not limited to, statements regarding discussions of future plans, 
guidance, projections, objectives, estimates and forecasts and statements as to 
management's expectations with respect to, among other things, the activities 
contemplated in this news release and the timing and receipt of requisite 
regulatory, and shareholder approvals in respect thereof. Forward-looking 
statements in this news release include, without limitation, statements related 
to proposed exploration and development programs, grade and tonnage of material 
and resource estimates. These forward looking statements involve numerous risks 
and uncertainties and actual results may vary. Important factors that may cause 
actual results to vary include without limitation, the timing and receipt of 
certain approvals, changes in commodity and power prices, changes in interest 
and currency exchange rates, risks inherent in exploration estimates and 
results, timing and success, inaccurate geological and metallurgical 
assumptions (including with respect to the size, grade and recoverability of 
mineral reserves and resources), changes in development or mining plans due to 
changes in logistical, technical or other factors, unanticipated operational 
difficulties (including failure of plant, equipment or processes to operate in 
accordance with specifications, cost escalation, unavailability of materials, 
equipment and third party contractors, delays in the receipt of government 
approvals, industrial disturbances or other job action, and unanticipated 
events related to health, safety and environmental matters), political risk, 
social unrest, and changes in general economic conditions or conditions in the 
financial markets. In making the forward-looking statements in this press 
release, the Company has applied several material assumptions, including 
without limitation, the assumptions that:
(1) market fundamentals will result in sustained gold demand and prices; (2) 
the receipt of any necessary approvals and consents in connection with the 
development of any properties; (3) the availability of financing on suitable 
terms for the development, construction and continued operation of any mineral 
properties; and (4) sustained commodity prices such that any properties put 
into operation remain economically viable. Information concerning mineral 
reserve and mineral resource estimates also may be considered forward-looking 
statements, as such information constitutes a prediction of what mineralization 
might be found to be present if and when a project is actually developed. 
Certain of the risks and assumptions are described in more detail in the 
Company's audited financial statements and MD&A for the year ended December 31, 
2016 on the SEDAR website at www.sedar.com. The actual results or performance 
by the Company could differ materially from those expressed in, or implied by, 
any forward-looking statements relating to those matters. Accordingly, no 
assurances can be given that any of the events anticipated by the 
forward-looking statements will transpire or occur, or if any of them do so, 
what impact they will have on the results of operations or financial condition 
of the Company. Except as required by law, the Company is under no obligation, 
and expressly disclaim any obligation, to update, alter or otherwise revise any 
forward-looking statement, whether written or oral, that may be made from time 
to time, whether as a result of new information, future events or otherwise, 
except as may be required under applicable securities laws.

- 30 -

CONTACT INFO:

Maryse Belanger
COO
+1 604 689-5564
www.atlanticgoldcorporation.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=593841594