Source	MARKET NEWS
Date	05/24/2017
Time	06:19:06 AM

Company	 Pinecrest Resources Ltd.
Title	Drill 
Program At Its 100% Owned Enchi Gold Proje





    CDNX Symbol: PCR











Press Release





PINECREST RESOURCES LTD ("PCR-V")
- Drill Program At Its 100% Owned Enchi Gold Project, Ghana

Pinecrest Resources Ltd. (the "Company" or "Pinecrest") is pleased
to announce a 3,000 metre Reverse Circulation ("RC") drill program
planned to commence during Q3, 2017 on the 100% owned Enchi Gold
Project ("Enchi or the Project"), located in Southwest Ghana, a region
well-known for prolific gold production. The region hosts numerous
historical and current operating open pit and underground gold mines
located along strike to the northeast of the Project. All figures are
in United States dollars, unless otherwise stated.

Highlights

//st

* Pinecrest to initiate RC drilling program on shallow extensions of the
existing, one million ounce, heap leach, Inferred gold resource (37.36 Mt
@ 0.9 g/t) at Enchi
* Planned work program includes 3,000 meters in 27 RC drill holes
* Past work at Enchi has included extensive RC and diamond drilling (52,385
m in 646 holes), resource estimation and a Preliminary Economic
Assessment ("PEA") study (Pre-Tax NPV 5%: $102 million using $1,300/oz
gold)
* The Enchi gold deposit remains open for further resource expansion along
strike and to depth. Numerous, additional high priority gold targets
exist on the 568 km2 property

//et

Ryan King, President of Pinecrest, commented: "Pinecrest is pleased
to be advancing the Company's logistically sound Enchi Gold Project.
The Enchi gold deposit covers 40 km of the prolific Bibiani Shear Zone
that host the Chirano gold mine operated by Kinross Gold Corporation
located 70 km northwest of the Project. The Enchi deposit is open along
strike and to depth with the 2017 drill program focussed on testing
potential deposit extensions and high priority targets generated by
previous exploration and drilling."

The Enchi Gold Project is road accessible, is on the Ghanaian
power grid and is situated along the eastern margin of the Sefwi gold
belt that hosts multi-million ounce producing mines such as the Chirano
Gold Mine and past producing Bibiani Gold Mine. Enchi includes six
prospecting licenses within a total 568km2 land package. Previous work
carried out on the project has included: RC and diamond drilling
(52,385 m), airborne surveys, soil samples and trenching from numerous
targets which resulted in an Inferred Resource Estimates and a
Preliminary Economic Assessment conducted on three main gold zones
(Boin, Nyam and Sewum). All zones within the Inferred Resource are open
for expansion down dip and along strike, particularly the Boin zone
that has undrilled internal gaps in the well-defined structure of up to
400 metres in strike length. Additional new high priority targets
include Boin Northwest and Kojina Hill both located within 10 km of the
main Boin zone where previous work completed includes trenching and
drilling.

Enchi Gold Project Preliminary Economic Assessment Highlights

A NI 43-101 compliant Preliminary Economic Assessment (the "PEA"
or the "Study") was prepared by WSP Canada Inc. ("WSP") using a base
case Inferred Mineral Resource of 1.07 million ounces (oz) of gold
(37.3 million tonnes grading 0.9 gram of gold per tonne (g/t Au), at a
cut-off of 0.5 g/t Au). The PEA contemplated an owner operated, open
pit, heap leach operation processing 3.0 million tonnes per year
(Mtpy). Using a base case gold price of $1,300/oz, the Study shows that
the Project has net Pre-Tax cash flow of $145 million, a Pre-Tax Net
Present Value (NPV) at 5% discount rate of $102 million and an Internal
Rate of Return (IRR) of 34%. (See news release linked here dated June
29, 2015 for full details and Technical Report filed on Sedar under
Pinecrest Resources Ltd.)

Base Case $1,300/oz gold price

//st

Average Mined Gold Grade (g/t)                           0.91

Processing Rate (Mtpy)                                   3.0

Mine Life (years)                                        8.7

Life-of-Mine (LOM) Strip Ratio                           3.16:1

IRR Pre-Tax (%)                                          34

NPV Pre-Tax (5% Discount Rate) (US$ Million)             102

IRR After-Tax (%)                                        25

NPV After-Tax (5% Discount Rate) (US$ Million)           62

Initial Capital Cost (US$ Million)                       84

LOM Sustaining Capital Cost (US$ Million)                39

Payback (Pre-Tax) (years)                                2.8

Payback (After-Tax) (years)                              3.4

LOM Cash Costs (US$/oz)                                  802

Metallurgical Recoveries (oxide/transition/sulphide %)   75/75/73

Total Recovered Gold (oz)                                538,450

Average Annual Gold Production (oz)                      61,749

Peak Annual Gold Production (oz)                         76,210

//et

The PEA is preliminary in nature, and it includes inferred mineral
resources that are considered too speculative geologically to have the
economic considerations applied to them that would enable them to be
categorized as mineral reserves. There is no certainty that the
preliminary economic assessment will be realized. Numbers may not add
exactly due to rounding. Cash cost includes all operating costs,
royalties, refining charges, environmental monitoring, tenure fees as
well as general and administration costs. Cash cost excludes any
capital cost, either initial or sustaining and closure and remediation
costs. Mineral resources that are not mineral reserves do not have
demonstrated economic viability.

Financial Models

The financial models were completed using a base case gold price
of US$1,300 per ounce. The Base Case Pre-Tax economic evaluation has an
IRR of 34%, payback of capital in 2.8 years and a pre-tax NPV of $102
million at a discount rate of 5%.

Table 1 Pre-Tax Financial Model Sensitivity Analysis

//st

Units    Metal Price Scenarios

(Base Case)

Gold      US$/oz   1,200                   1,250   1,300         1,350

NPV, 5%   M US$    62.5                    82.5    101.9         122.5

Payback   Years    3.4                     3.0     2.8           2.7

IRR       %        24                      29      34            39

//et

The Pre-Tax financial model includes: an initial capital cost of
$72.7 million, a contingency of $11.8 million (20% of direct costs);
sustaining capital of $38.6 million including a contingency of $5.3
million and reclamation and closure costs of $18.3 million. The
Financial Model was completed on a 100% Project ownership basis and
includes a 5% NSR to the Ghanaian Government and a 2% NSR to Red Back
Mining Ghana, a subsidiary of Kinross. The After-Tax financial model
includes a 35% corporate tax, demonstrating a base case NPV of $62
million at a discount rate of 5%. The Government of Ghana have the
right to a 10% free carry interest in the Project.

The PEA was based on the July 15, 2014 NI 43-101 Inferred Mineral
Resource estimate prepared by WSP and using a 0.5 g/t cut-off (see
Table 2 for details).

Table 2 Enchi Gold Project - Inferred Mineral Resource (0.5 g/t
Cut-Off)

//st

Cut-off    Zone    Tonnes       Grade      Contained Gold

Au (g/t)                        Au (g/t)   (ounces)

0.5        Boin    15,872,000   0.96       489,892

0.5        Nyam    5,350,000    0.96       165,129

0.5        Sewum   16,135,000   0.82       423,676

TOTAL   37,357,000   0.90       1,078,697

//et

//st

* CIM definition standards were followed for the resource estimate.
* The 2014 resource models used ordinary kriging (OK) grade estimation
within a three-dimensional block model with mineralized zones defined by
wireframed solids.
* A base cut-off grade of 0.5 g/t Au was used for reporting resources with
a capping of gold grades at 18 g/t.
* A US$1,300/ounce gold price, open pit with heap leach operation was used
to determine the cut-off grade.
* A density of 2.45 g/cm3 was applied.
* Numbers may not add exactly due to rounding.
* Mineral Resources that are not mineral reserves do not have economic
viability

//et

The 2014 Mineral Resource estimate was based on 52,385 metres of
diamond and RC drilling in 646 holes as well as data from 102 surface
trenches totalling 13,799 metres. The drilling is generally spaced at
25 to 50 metre intervals.

The 2017 Enchi Drill Program

The 2017 RC drill program will include approximately 27 holes
totalling 3,000 metres of infill, step out and exploration drilling on
the Boin and Sewum Zones and two new zones outside of the maiden
Inferred Resource Boin northwest and Kojina Hill both representing high
priority targets based on geological, geochemical and geophysical
surface work and previous drilling.

BOIN NORTHWEST ('NW") TARGET

The Boin NW target is located approximately 1000 metres northwest
of the main Boin zone and importantly not currently included in the NI
43-101 Inferred Resource Estimate or PEA. Previous trenching
intersected 26 metres grading 0.61 g/t Au and 40 metres grading 0.54
g/t Au including 10m at 1.64 g/t Au. Past limited drilling intersected
23m at 0.43 g/t Au and 39m at 0.43 g/t Au within the near surface
oxidized material.

KOJINA HILL TARGET

Kojina Hill is located approximately 400 metres northwest of the
Nyam Zone and was not included in the previous NI 43-101 Inferred
Resource Estimate. Previous drilling highlights from only 8 drill holes
included near surface intercepts of: 42 metres grading 1.68 g/t Au and
17 metres grading 0.94 g/t Au.

Mr. Gregory Smith, P.Geo, the Vice-President of Exploration of the
Company, is the Qualified Person as defined by NI 43-101, and is
responsible for the accuracy of the technical data and information
contained in this news release.

Subject to regulatory approval, the Company has granted 250,000
stock options to a consultant of the Company. The options are at an
exercise price of $0.53 per share and valid for a period of five years
from the date of grant and have vesting provisions.

About Pinecrest Resources

Pinecrest engages principally in the acquisition, advancement and
development of precious metal properties with the Company's primary
focus being the 100% owned Enchi Gold Project located in Southwest
Ghana. Major shareholders of Pinecrest include Kinross Gold
Corporation, Management and Directors.

Pinecrest Resources Ltd.

Ryan King, President & Director

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Cautionary Note Regarding Forward Looking Statements

This news release contains certain forward-looking statements, Any
statements that express or involve discussions with respect to
predictions, expectations, beliefs, plans, projections, objectives,
assumptions or future events or performance (often, but not always,
using words or phrases such as "expects" or does not expect", "is
expected", anticipates" or "does not anticipate" "plans", "estimates"
or "intends" or stating that certain actions, events or results " may",
"could", "would", "might" or "will" be taken, occur or be achieved) are
not statements of historical fact and may be "forward-looking
statements". Forward-looking statements are subject to a variety of
risks and uncertainties which could cause actual events or results to
materially differ from those reflected in the forward-looking
statements.

Safe Harbor Statement under the United States Private Securities
Litigation Reform Act of 1995: Except for the statements of historical
fact contained herein, the information presented constitutes
"forward-looking statements" within the meaning of the Private
Securities Litigation Reform Act of 1995. Such forward-looking
statements including but not limited to those with respect to the price
of gold, potential mineralization, reserve and resource determination,
exploration results, and future plans and objectives of the Company
involve known and unknown risks, uncertainties and other factors which
may cause the actual results, performance or achievement of the Company
to be materially different from any future results, performance or
achievements expressed or implied by such forward-looking statements.
There can be no assurance that such statements will prove to be
accurate as actual results and future events could differ materially
from those anticipated in such statements. Accordingly, readers should
not place undue reliance on forward-looking statements.


























TSX Venture closing price for PCR-V
Date: 2017/05/23
Closing Price: 0.53

TEL:  604 628-1012   Ryan King, President & Director
Internet: www.pinecrestresources.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1714300021TS11714301207-06165620170524