Source	MARKET NEWS
Date	05/17/2018
Time	08:31:50 AM

Company	 Thunderstruck Resources Ltd.
Title	Field Work Advances Multiple Precious and Base M





    CDNX Symbol: AWE











Press Release




[200/News Release]AWEVTHUNDERSTRUCK RESOURCES LTDMAY 17 2018  08:30 AM
Field Work Advances Multiple Precious and Base Metals Targets --->@NEWS 
RELEASE
THUNDERSTRUCK RESOURCES LTD ("AWE-V;THURF-0")
- Field Work Advances Multiple Precious and Base Metals Targets

Thunderstruck Resources Ltd. (The "Company" or "Thunderstruck")
is pleased to announce that field operations are well underway on its
100% owned high grade zinc, copper and gold assets in Viti Levu, Fiji.
The present work is building on extensive prior results that point to
the potential for large mineralized systems.

"Our exploration season is now in full swing, and we have
initiated multiple exploration activities across all of our four
primary assets," commented Thunderstruck's President and CEO Bryce
Bradley.

"A detailed mapping program of Rama Creek has begun which will
follow up on the recent Senikura gold zone discovered nearby.
Concurrently, road building into Rama Creek should be completed by the
end of May, making it easier to get larger rigs onto the property later
in the season. In addition, preliminary mineralogical tests from our
Wainaleka VMS project indicate great potential to produce zinc and
copper concentrates via conventional flotation, which is a critical
precursor to mine development."

"Elsewhere, further work on our high-grade Liwa Creek gold
prospect will begin shortly, and we'll be giving all of our zinc,
copper and gold assets much deserved attention this season, with plenty
of news flow forthcoming. This is the first year that Thunderstruck has
had the entire land package under its control and can meaningfully
advance the various targets. The enthusiasm around this program has
prompted investors to request a private placement, at above market,
which we have agreed to."

RAMA CREEK COPPER-GOLD PORPHYRY AND SENIKURA GOLD ZONE

During December 2017, field crews carried out a soil program to
determine the limits of the broad copper-gold (Cu-Au) mineralized
porphyry intrusive at Rama Creek. Originally discovered by Anglo
American in the 1970s, subsequent work, including drilling and
trenching, outlined a broad porphyry system. The recent work was
successful in establishing a framework of porphyry hydrothermal
alteration zonation that is helping to understand the geometry of the
system and will serve as a vector to define the core of the mineralized
system.

Field crews collected a total of 112 ridge-and-spur auger soil
samples that were subsequently submitted for gold and multi-element
geochemical and TerraSpec(r) Short Wave Infrared (SWIR) spectral
analysis. Of the 112 auger soil geochemical samples collected over the
interpreted extent of the Rama Creek Porphyry, a total of 18 samples
returned greater than 50 parts-per-billion (ppb) Au and up to 0.76
grams-per-tonne (g/t) Au; and a total of 31 samples returned greater
than 500 parts-per-million (ppm) Cu and up to 0.56% Cu. In conjunction
with a previous 126 targeted auger soils collected by the Company, an
18-sample subset of which yielded an average of 0.27% Cu and 0.15 g/t
Au (see the Company's March 1, 2018 News Release), the current soil
samples define an approximately 1,000 x 600 metre (m) greater than 200
ppm Cu in soil anomaly containing a northwest elongate 500 x 300 m
greater than 50 ppb Au in soil geochemical response coincident with the
inferred centre of the Rama Creek intrusion (Figures 1 and 2).

Figure 1: 2017 Soil Geochemical Results (Copper) and SWIR Interpretation

To view an enhanced version of Figure 1 please visit:
https://orders.newsfilecorp.com/files/2901/34716_Figure1_Rama_Soils_Cu.jpg

Figure 2: 2017 Soil Geochemical Results (Gold) and SWIR Interpretation

To view an enhanced version of Figure 2, please visit:
https://orders.newsfilecorp.com/files/2901/34716_Figure2_Rama_Soils_Au.jpg

TerraSpec(r) SWIR spectral analyses define a sericite (white mica)
alteration halo that is coincident with the plus-200 ppm Cu in soil
geochemical anomaly. The plus-50 ppb Au geochemical target is
associated with a northwest elongate magnesium-chlorite spectral
response. Gold in soils exceeding 100 ppb (six samples in total) are
coincident with a 300 x 200 m area of higher-temperature potassic
(magnesium-iron chlorite + biotite) alteration containing historic
Australian Anglo American Ltd (Anglo) diamond drill hole "DDH1" that
returned a 244-metre interval between depths of 6 and 250 m averaging
0.22% Cu, ending in mineralization (Figures 1 and 2).

Interpretation

The results of the soil geochemical and SWIR spectral analysis
program were successful in defining a near-surface expression of
porphyry Cu-Au mineralization at Rama Creek. The application of modern
SWIR spectral analysis in particular has added critical evidence of
porphyry hydrothermal alteration zonation comprising distal weak to
moderately chlorite-pyrite altered diorite intrusive and host volcanic
rocks, to pervasive proximal sericite and core zone potassic altered
porphyry intrusive.

The subsurface geometry and depth extent of the Rama Creek Cu-Au
porphyry has not been determined. Historic drilling by Anglo has shown
disseminated Cu-Au mineralization extends to a vertical depth of at
least 250 m, and is open at depth and in all directions.

In addition to the Rama Creek Porphyry Cu-Au target, the recent
soils samples have provided additional resolution on the Company's
emerging Senikura Gold Zone target that returned trench rock channel
sample results averaging 0.96 g/t Au over 11.1 m (38.5 to 49.6 m),
within a broader anomalous gold zone averaging 0.55 g/t Au over 37.6 m
(12 to 49.6 m). At a distance of 700 m to the northwest, a series of 10
auger soils spanning the southwest contact zone of the intrusion
returned anomalous gold values averaging 0.063 g/t Au (63 ppb Au),
including two samples returning 0.1 and 0.2 g/t Au (see the Company's
March 1, 2018 News Release). Together these two gold occurrences define
an apparently northwest trending gold zone along the margin of the Rama
Creek Porphyry that is open to the northwest and southeast into the
headwaters of Senikura Creek.

Moving Forward, the Company has commenced road rehabilitation and
construction to establish vehicle access to the Rama Creek Prospect in
support of 2018 field programs. The present program will include
additional Bulk Leach Extractable Gold (BLEG) stream geochemical
sampling in the headwaters of Rama Creek to the northwest of the Rama
Porphyry and the potential strike extent of Senikura Gold Zone; an
expanded auger soil geochemical program designed to test the southeast
extent of the Senikura Gold Zone; follow-up on an historic Senikura
East gold in soil anomaly located a further 1.5 km to the southeast (12
consecutive 100 m spaced auger soils over 1.2 km returning an average
of 67 ppb Au) (see the Company's March 1, 2018 News Release); detailed
geologic mapping, prospecting; and Induced Polarization (IP) /
Resistivity geophysical surveys towards modelling the subsurface
geometry of disseminated Cu-Au bearing sulphide mineralization and
generation of finalized diamond drill targets.

WAINALEKA ZINC-COPPER VMS

During March 2018, the Company engaged SGS Canada Inc. (SGS) to
complete a QEMSCAN (Quantitative Evaluation of Minerals by Scanning
Microscopy) study on a selection of 10 polished mineralized samples
from the Company's Wainaleka Zn-Cu VMS (Volcanogenic Massive Sulphide)
deposit. The purpose of the QEMSCAN study was to provide information on
modal mineralogy, grain size and to provide a preliminary guidance with
respect to potential metallurgical performance.

QEMSCAN results (Figure 3) for the 10 samples show a range of
sulphide mineral content, with sphalerite, covellite and chalcopyrite
being the main minerals of interest. Other sulphide minerals include
pyrite, bornite, tetrahedrite/tennanite/enargite, and chalcocite.

Figure 3: Wainaleka Zn-Cu VMS Modal Mineral Distributions

To view an enhanced version Figure 3, please visit:
[http://orders.newsfilecorp.com/files/2901/34716_a1526568317844_24.jpg]

The 10 samples contained an average of 26.3% modal sphalerite
(ranging from 0.1% up to 66.5%); an average of 4.2% chalcopyrite
(ranging from 0.1% to 17.9%); and 20.6% pyrite (ranging from 0.9% to
57.7%). Significantly, two samples (RC22 and A0101) collected at a
depth of approximately 131 m within drill hole WLK-11 contained 33.3%
and 21.4% modal covellite.

With respect to grain size and potential floatation metallurgical
performance of the Wainaleka Zn-Cu mineralization, SGS made the
following observations:

//st

* Sequential floatation of copper, then sphalerite into separate
concentrates was recommended as a potential processing option for the
majority of samples.
* High zinc content of two samples (greater than 65%) may make them a good
candidates for pre-concentration using either dense media of gravity
separation.
* Particle size observed is similar to typical VMS deposits, and suggests a
primary grind size of 75 to 100 micron (0.075 to 0.1 mm) should be
targeted.
* With respect to deleterious elements, the observed quantity of
non-sulphide gangue minerals should not negatively affect metallurgy.
Several reagent schemes and processing conditions can be evaluated to
limit recovery of pyrite and arsenic bearing minerals observed in a
minority of samples. In addition possible use of zinc depressants, and
avoiding blending of high covellite and high zinc or zinc-copper material
to limit the potential for high-zinc copper concentrates is suggested.

//et

Interpretation

The Company is encouraged by the results of the preliminary
QEMSCAN &#8206;mineralogical study, which shows the Wainaleka Zn-Cu
mineralization appears to have an overall coarse sulphide distribution,
making it amenable to sequential flotation. Importantly the study
raised the possibility of the creation of a zinc concentrate by
relatively low cost dense-media or gravity process methods.

Other important mineralogical observations that warrant further
study include: the presence of a subset of high modal percent covellite
samples; potential interaction of pyrite in copper primary
mineralization; and the presence of a small percentage of
copper-antimony-arsenic minerals. In future, the Company intends to
investigate various flotation and gravity separation methods, grind
size, and reagent (pyrite and zinc suppressor) combinations on fresh
drill core samples. The QEMSCAN study represents an important step
forward with respect to optimizing subsequent detailed metallurgical
studies.

These results are extremely significant in that they provide to
potential joint venture partners comfort, on an initial basis, that the
material could be processed to produce saleable concentrates.

About the Wainaleka VMS Deposit

During 1977 Australian Anglo American Ltd. (Anglo) completed a 15
hole diamond drill program totaling 1,850 m with holes averaging a
relatively shallow 120 m depth that defined the Wainaleka Zn-Cu VMS
deposit. Drill hole WLK-1A intersected 9.8 m averaging 8.28% Zn and
1.45% Cu; and drill hole WLK-10 returned 14.1m averaging 1.3% Zn and
1.5% Cu within what has been interpreted as a zone of stringer
mineralization. True widths are estimated at 80-100% of the drilled
interval. Geologic mapping indicates 15 km prospective geology strike
length; including 8 more underexplored Zn-Cu VMS prospects.

During 1980, Anglo commissioned Golder Associates to conduct a
review of potential mining scenarios of several Fijian VMS deposits
including Wainaleka*. The study published an historic, uncategorized
resource for the portion of the Wainaleka Deposit that was tested by
the initial drilling of 250,000 tonnes grading 8% Zn and 2% Cu. The
resources are considered historic in nature and do not meet the
criteria for a National Instrument (NI) 43-101 compliant resource of
any category and as such should not be relied upon. Thunderstruck has
been unable to verify these sources of information.

*Source: Golder Associates, Review of the Mining Potential of the
Fijian Kuroko Style Mineral Discoveries, 1980.

Financing

The Company has arranged a non-brokered private placement to raise
up to $150,000 through the sale of up to 1,666,666 units at a price of
$0.09 per unit (the "Financing"). Each unit will comprise one common
share and one share purchase warrant. Each whole warrant will entitle
the holder to purchase a further common share at a price of $0.15 per
share for a period of 36 months from closing. The warrants will be
subject to accelerated exercise provisions such that if the closing
price of Thunderstruck's common shares exceeds $0.25 per share for a
period of 20 consecutive trading days, Thunderstruck may give notice of
the acceleration of the warrants' term to a period of 30 days following
such notice. Proceeds of the Placement will be applied to continuing
operations on the Company's Fiji properties and general working
capital.

About Thunderstruck Resources

Thunderstruck Resources is a Canadian mineral exploration company
that has assembled extensive and highly prospective properties in Fiji
on which recent and previous exploration has confirmed VMS, copper and
precious metals mineralization. The Company provides investors with
exposure to a diverse portfolio of exploration stage projects with
potential for zinc, copper, gold and silver in a politically safe and
stable jurisdiction. Thunderstruck trades on the Toronto Venture
Exchange (TSX-V) under the symbol "AWE".

Qualified Person Statement

Kristopher J. Raffle, P.Geo. (BC) Principal and Consultant of APEX
Geoscience Ltd. of Edmonton, AB, is a qualified person for the project
as defined by National Instrument NI 43-101. Mr. Raffle has reviewed
and approved the portion of the technical content of this news release
as it relates to the Rama Creek and Wainaleka Prospects.

During 2017 all Auger soil samples were submitted to Australian
Laboratory Services Pty. Ltd (ALS) labs for gold and multi-element
geochemical analysis via aqua-regia extraction of a 25 gram (g) sample
with ICP-MS finish. SWIR spectra were analysed by ALS using a
TerraSpec(r) 4 High-Resolution Spectrometer on an approximately 100 g
plus 2 millimetre coarse soil separate. Spectral interpretation was
completed using AusSPec International aiSIRIS(TM) (Spectral InfraRed
Interpretation System) software to produce raw spectral files and
output mineral assemblages and relevant spectral parameters. Auger soil
samples were collected at a maximum depth of 2 m or to refusal. Given
the reconnaissance nature of the samples, Thunderstruck has relied on
the external QA/QC of ALS which included the insertion of insertion of
standard, blank and duplicate samples at a rate of 10% into the sample
stream to confirm the accuracy of the reported results.
QEMSCAN image analysis is able to measure mineralogical
variability based on chemistry at the micrometer-scale. It utilizes
both back-scattered electron (BSE) signal intensity, as well as Energy
Dispersive X-ray Signal (EDS) at each measurement point. QEMSCAN can
map many thousands of particles in a polished section to obtain a
detailed and statistically robust characterization of the minerals
present. It maps the particles based on differences in chemical
analysis and can differentiate amongst the various non-opaque gangue
present in the ore body.

For additional information, please contact:

Bryce Bradley, President, Chief Executive Officer and Director
Telephone: (604) 349-8119 Email: Bryce@thunderstruck.ca

or, visit our website: http://www.thunderstruck.ca

Neither the TSX Venture Exchange Inc. nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release contains certain statements that may be deemed
"forward-looking statements". Although Thunderstruck believes the
expectations expressed in such forward-looking statements are based on
reasonable assumptions, such statements are not guarantees of future
performance and actual results may differ materially from those in
forward looking statements. Forward looking statements are based on the
beliefs, estimates and opinions of Thunderstruck's management on the
date the statements are made. Except as required by law, Thunderstruck
undertakes no obligation to update these forward-looking statements in
the event that management's beliefs, estimates or opinions, or other
factors, should change.

TEL: 604-349-8119    THUNDERSTRUCK RESOURCES LTD
FAX: 778-340-3891
E-mail: Bryce@linxinc.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1813600033TS11813601725-08302420180517