Source	MARKET NEWS
Date	05/10/2018
Time	07:06:58 AM

Company	 Dunnedin Ventures Inc.
Title	Provides 
Update on Ongoing Drilling at Kahuna Pr





    CDNX Symbol: DVI











Press Release





DUNNEDIN VENTURES INC ("DVI-V;OCPFF-0")
- Provides Update on Ongoing Drilling at Kahuna Project
- First Kimberlites Drilled by Company

Dunnedin Ventures Inc. (the "Company" or "Dunnedin") today
provides an update on its ongoing 2018 drill program at its 100% owned
Kahuna project, Nunavut.  The Company has drill-tested five of
approximately 40 targets (13%), with potentially diamond-bearing
kimberlite intercepted at two targets.  Inclement weather limited
drilling and confined operations to the vicinity of the Company's newly
constructed camp and the Company's best kimberlite pipe-type targets
with the highest associated diamond indicator minerals ("DIM") have not
yet been tested. Dunnedin plans to return the property in six to eight
weeks to drill the remaining high priority targets.

Of the five targets drilled, two were high count DIM-in-till
targets, both of which yielded significant extensions to the known
high-grade diamond-bearing PST and 07KD-24 kimberlite dikes.
Concentrated DIMs-in-tills were clearly associated with adjacent
OhmMapper geophysical responses and new kimberlite intercepts,
demonstrating the effectiveness of Dunnedin's targeting methods.

Chris Taylor, Dunnedin's CEO said, "During April drilling, we were
able to show that our DIM-based exploration methods work.  We confirmed
that high concentrations of priority ranked DIMs correlate directly to
new potentially diamond-bearing kimberlite in both areas where tested.
Unusually poor weather only allowed us to test a handful of targets
near our camp, and we are eager to drill our main DIM targets as soon
as field conditions allow. Many of these are associated with kimberlite
pipe-type geophysical signatures and large, high-count DIM trains that
appear highly prospective for new diamond discoveries."

Progress to date includes:

//st

* Completion of 11 Rotary Air Blast ("RAB") drill holes (plus two abandoned
holes), of which eight contain kimberlite intercepts consistent with
vertically dipping kimberlite dikes
* Approximately 400 kg of kimberlitic material has been shipped to CF
Mineral Research Ltd. of Kelowna, BC for diamond and indicator mineral
recovery
* Initial diamond recovery results are expected in approximately eight
weeks
* A 20 person field camp was established south central to the Kahuna
Property to support future exploration programs
* The OhmMapper geophysical technique was employed on the Kahuna property
for the first time and, together with DIM-based exploration methods,
appears to be a highly effective drill targeting technique

//et

Figure 1: Dunnedin 2018 Drilling Update -- 13% of targets drilled
to date. There are multiple targets in each target area.

To view an enhanced version of Figure 1, please visit:
http://orders.newsfilecorp.com/files/3803/34568_a1525921948866_91.jpg

The first of the kimberlites drilled during the program is an
on-strike extension to 07KD-24, an exceptionally diamond bearing
kimberlite dike which historically returned over 305 diamonds including
seven commercial-sized diamonds from a 2.2 kg sample.  Five drill holes
in two locations spaced 100 metres apart were completed across this
target, details of which are provided below.  The drilled strike length
of this body is now 225 metres, and it remains open to extension along
strike and down dip.

Drilling at the second kimberlite target successfully intercepted
the along-strike continuation of the Company's PST kimberlite dike,
which previously returned an average sample grade of 4.02 carats per
tonne from 2.03 tonnes (+0.85 mm), and high quality commercial sized
diamonds during Dunnedin's 2015-2017 work (see news release dated July
25, 2017).  Three drill holes were completed across this target at one
location.  The PST kimberlite's drilled strike length is now
approximately 350 metres, and also remains open along strike and down
dip.

Both PST and 07KD-24 appear to have greater strike extent than was
apparent from past drilling and geophysical surveying.  No resource has
yet been calculated on either target.

Three strong magnetic highs with lower DIM-in-till counts were
also tested and were determined to be caused by magnetic bedrock
formations. Two of these contained significant intervals of silicified,
sulphide-mineralized banded iron formation ("BIF") and are prospective
for gold mineralization similar to the adjacent Meliadine gold project
of Agnico Eagle Mines Ltd. (TSX: AEM).  DIMs at these targets were
likely sourced from undiscovered nearby diamond-bearing kimberlites.

Table 1: Highlighted RAB Drill Intercepts

//st

Drill Hole   Target   Azimuth   Dip   From     To     Interval   Description
Type                     (m)     (m)      (m)        of rock
chips

18-RAB-001    Mag        0      90    21.34   28.96     7.62     Silica and
High                                                sulphide
bearing BIF

18-RAB-002    DIM       300     60    51.82   54.86     3.05     Kimberlite
and gneiss
(07KD-24)

18-RAB-003    DIM       300     50    41.15   44.20     3.05     Kimberlite
and gneiss
(07KD-24)

18-RAB-004    DIM       300     70    65.53   73.15     7.62     Kimberlite
and gneiss
(07KD-24)

18-RAB-005    Mag        0      90    3.05    45.72    42.67     Silica and
High                                                sulphide
bearing BIF

18-RAB-006    Mag        0      90    4.57    38.10    33.53        Mafic
High                                                intrusive

18-RAB-007    DIM       120     60    48.77   51.82     3.05     Kimberlite
and gneiss
(PST)

18-RAB-008    DIM       120     70    71.63   73.15     1.52       Altered
gneiss and
kimberlite
(PST)

18-RAB-009    DIM       120     50    38.10   39.62     1.52     Kimberlite
and gneiss
(PST)

18-RAB-010    DIM       300     70    18.29   22.86     4.57     Kimberlite
and gneiss
(07KD-24)

18-RAB-011    DIM       300     80    68.58   73.15     4.57     Kimberlite
and gneiss
(07KD-24)

//et

RAB drilling is an efficient way to evaluate shallow targets for
diamond content (2018 holes ranged from 27.4 to 83.8 metres in length).
The RAB method produces chips and fine material brought to surface by
pressurized air, drilled in 1.5 metre intervals. As a result,
geological contacts are not distinct and true widths of kimberlite are
unknown at this time. Intercepts reported herein include kimberlite and
country rock that may represent dilution by adjacent country rock,
internal xenoliths or down--hole dilution caused by the RAB drilling
process itself. Over the course of winter RAB drilling, the Company
completed 801.6 metres in 11 drill holes (plus two lost holes). A
summary of drilling is provided as Table 1.

OhmMapper Geophysical Surveying

The majority of kimberlites drilled at the Kahuna project have a
range of magnetic low and moderate magnetic high responses.  The
diamond-bearing kimberlites drilled to date are typically moderate
magnetic highs, and can be difficult to distinguish from background
geology using only magnetic-based geophysical methods.

As part of the winter 2018 program, the Company evaluated ground
electromagnetic responses in key target areas using the Geometrics
OhmMapper Capacitive-Coupled Resistivity System, operated and
post-processed by Aurora Geosciences. Survey results were highly
successful at rapidly illuminating kimberlite dikes and associated
alteration at depth.  This technique has been used by other Canadian
diamond explorers including Kennady Diamonds (recently merged with
Mountain Province Diamonds; TSX: MPDV) as a primary drill hole
targeting tool.  It shows fine-scale resistivity contrasts in the
shallow subsurface and was highly effective showing the location of the
two potentially diamond-bearing kimberlites drilled by Dunnedin during
this program, as shown in Figure 2.

The Company plans to complete additional Ohm Mapper surveys and
test other ground electromagnetic methods in other priority areas. The
combination of DIM-based target identification and resistivity-based
ground geophysics appear to be very effective and complimentary methods
of refining kimberlite targets for future drilling.

Figure 2: OhmMapper Section -- Showing Resistivity Contrast
Between Bedrock and Kimberlite

To view an enhanced version of Figure 2, please visit:
http://orders.newsfilecorp.com/files/3803/34568_a1525921949194_64.jpg

Jeff Ward, P.Geo, Vice President Exploration and a Qualified
Person under National Instrument 43-101, has reviewed and approved the
technical information contained in this release.

For further information please contact Mr. Knox Henderson,
Investor Relations, at 604-551-2360 or khenderson@dunnedinventures.com.


On behalf of the Board of Directors

Dunnedin Ventures Inc.

Chris Taylor Chief Executive Officer

About the Kahuna Project

Dunnedin Ventures Inc. (TSXV: DVI) is a Vancouver-based company
whose primary asset is the 100% owned, advanced-stage Kahuna Diamond
Project in Nunavut which hosts a high-grade, near surface inferred
diamond resource and numerous kimberlite pipe targets.  The Company
holds diamond interest in 1,664 km2 of mineral tenure located 26
kilometers northeast of Rankin Inlet and adjacent to Agnico Eagle's
Meliadine gold mine.  To define and prioritize kimberlite pipe targets
Dunnedin has evaluated an extensive historic data set and recovered
diamonds and indicator minerals from a series of kimberlite and till
samples over three seasons of field work. Working with advisor and
shareholder Dr. Chuck Fipke, the Company has used the same till
sampling and mineral screening protocols employed during Dr. Fipke's
discovery of Canada's first diamond mine at Ekati, N.W.T., but improved
by over 20 years of additional diamond data and experience.  The Kahuna
Diamond Project has an Inferred Resource Estimate of 3,987,000 tonnes
at an average grade of 1.01 carats per tonne, totalling over 4 million
carats of diamonds (+0.85 mm) (see news release dated March 31, 2015).
The largest diamond recovered from the property to date is a 5.43
carat stone from the Kahuna dike which was a piece of a larger diamond
that had been broken during the sample preparation process and was
reconstructed as having an original size of 13.42 carats.  Dunnedin is
backed by a world-renowned team of diamond experts with decades of
combined experience in Arctic exploration and capital markets strength.


Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Statements included in this announcement, including statements
concerning our plans, intentions and expectations, which are not
historical in nature are intended to be, and are hereby identified as,
"forward-looking statements".  Forward-looking statements may be
identified by words including "anticipates", "believes", "intends",
"estimates", "expects" and similar expressions. The Company cautions
readers that forward-looking statements, including without limitation
those relating to the Company's future operations and business
prospects, are subject to certain risks and uncertainties that could
cause actual results to differ materially from those indicated in the
forward-looking statements. Accordingly, readers should not place undue
reliance on forward-looking statements.  Forward-looking statements
contained herein are made as of the date of this news release and the
Company disclaims any obligation to update any forward-looking
statements, except as required by applicable securities laws.

TEL: 604-681-0084    DUNNEDIN VENTURES INC
FAX: 604-681-0094
E-mail: ro@oceanparkventures.ca
Website: http://www.dunnedinventures.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1812900038TS11812901436-07022420180510