Source	MARKET NEWS
Date	05/07/2018
Time	10:12:37 AM

Company	 Westhaven Ventures Inc.
Title	Drills 
17.7 Metres of 3.9 g/t Gold, Including 2.





    CDNX Symbol: WHN











Press Release





WESTHAVEN VENTURES INC ("WHN-V;WTHVF-0")
- Drills 17.7 Metres of 3.9 g/t Gold, Including 2.9 Metres
- of 9.7 g/t Gold at Shovelnose

Westhaven Ventures Inc. is pleased to report partial drill results
from its spring drill campaign on its 18,768 hectare Shovelnose gold
property, located within the prospective Spences Bridge Gold Belt
(SBGB), approximately 30 kilometres south of Merritt, British Columbia.
The drill program is ongoing and consists of 7 holes totaling more than
2,800 metres of diamond drilling.

Drilling Highlights from drill hole SN18-03:

*  (178m - 206.7m) 28.7 meters (m) of 2.6 g/t gold (Au), including

*  (189m - 206.7m) 17.7m grading 3.9 g/t Au which in turn includes

*  (203m - 206.7m) 3.7m grading 6.3 g/t Au and
*  (190m - 192.9m) 2.9m grading 9.7g/t Au.

*Drilling to date is limited so true widths cannot be definitively
determined. However, based on the geology of the vein zone with a
moderate dip to the west, we can estimate true widths at 80%.

Gren Thomas, President & CEO of Westhaven stated, "These initial
results from the spring drilling campaign are very encouraging and
demonstrate higher grade exists at depth, in addition to what's been
found on surface. The South Zone was only discovered at the end of 2017
and has had limited work to date. It is now the priority focus at
Shovelnose and we are confident that similar zones of gold
mineralization will be found elsewhere within this newly discovered
area."

This drill program is following-up on last year's discovery of the
South Zone where two holes in an unexplored area intersected an
auriferous silicified zone. SN17-06 intersected 85m of 0.52 g/t Au.
SN18-03 was drilled as an overcut of SN17-06 and it intersected a zone
of silicification and quartz veining, including metre scale quartz
veins that differentiate this zone from all other zones drilled on
Shovelnose, with vein intersections of up to 8 metres. Exploratory
holes SN18-01 and SN18-02 were drilled 200 metres and 400 metres south
of SN17-06 but failed to intersect the zone.

Thomas goes on to add, "SN18-03 is the most encouraging hole
drilled to date on Shovelnose, where Westhaven has carried out numerous
small drill programs over a period of 8 years and outlined a number of
gold rich zones. The Company is looking forward to receiving the assays
from the remaining four holes as all four holes intersected
silicification and quartz veining at various depths over a strike
length of 200m. A summer drill program will commence in June."

The Spences Bridge Gold Belt (SBGB)

Westhaven owns a 100% interest in over 32,000 hectares within the
prospective SBGB, which is situated within a geological setting similar
to those which host other significant epithermal gold-silver systems.
It is close to existing transportation and infrastructure allowing for
cost-effective exploration. The SBGB is a 110-kilometre
northwest-trending belt of intermediate to felsic volcanic rocks
dominated by the Cretaceous Spences Bridge group. Westhaven has been
working on the SBGB since 2011 and believes these relatively
underexplored volcanic rocks are highly prospective for epithermal
style gold mineralization.

On behalf of the Board of Directors  WESTHAVEN VENTURES INC.

"Gareth Thomas"

Gareth Thomas, Director

About Westhaven Ventures Inc.

Westhaven Ventures Inc. is a Canadian based exploration company
focused on the acquisition and exploration of prospective resource
properties. Westhaven is focused on advancing its Shovelnose, Prospect
Valley and Skoonka gold projects in British Columbia. Westhaven trades
on the TSX Venture Exchange under the ticker symbol WHN. For further
information, please call 604-681-5558 or visit Westhaven's website at
www.westhavenventures.com.

Qualified Person Statement

Peter Fischl, P.Geo., who is a Qualified Person within the context
of National Instrument 43-101, has read and takes responsibility for
this release.

QA/QC

Core samples were prepared using the PREP-31 package in ALS's
Kamloops facility each core sample is crushed to better than 70 %
passing a 2 mm (Tyler 9 mesh, US Std. No.10) screen. A split of 250 g
is taken and pulverized to better than 85 % passing a 75 micron (Tyler
200 mesh, US Std. No. 200) screen. 0.5g of this pulverized split is
digested in aqua regia and analyzed via ICP-MS and ICP-AES (method code
ME-MS41L), which reports a 53-element suite of elements. All results
greater than 100 ppb gold were reanalyzed by ALS using their Fire Assay
with an AAS finish, method code Au-AA23 (30g sample size). All analysis
is conducted in ALS's North Vancouver facility. A QA/QC program
included the lab and field standards inserted every 25 samples.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TEL: 604-681-5558    WESTHAVEN VENTURES INC
FAX: 604-681-5528
E-mail: gthomas@westhavenventures.com
Website: http://www.westhavenventures.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1812600036TS11812602066-10091520180507