Source	MARKET NEWS
Date	05/08/2018
Time	06:00:42 AM

Company	 Terrax Minerals Inc.
Title	Extends 
Crestaurum Zone to 300 Meters Vertical D





    CDNX Symbol: TXR











Press Release





TERRAX MINERALS INC ("TXR-V;TRXXF-0")
- Extends Crestaurum Zone to 300 Meters Vertical Depth,
- Doubling Size of Known Mineralized Structure

TerraX Minerals Inc. is pleased to announce assay results from the
remaining 11 holes drilled at the Yellowknife City Gold project this
winter.  Four of these holes (1,170 m) were drilled on the high-grade
Crestaurum gold bearing structure to test whether gold mineralization
continued to depth.   All four holes hit mineralized structure, with
two holes containing visible gold. All holes intersected significant
gold with selected intervals of:

//st

* 8.84 g/t Au over 2.49 m and 5.38 g/t Au over 0.63 m in hole TCR18-076
* 3.08 g/t Au over 2.80m, and 5.57 g/t Au over 2.06 m, in hole TCR18-078
* 13.30 g/t Au over 1.24 m, and 4.41 g/t Au over 0.80 m, in hole TCR18-079
* 3.86 g/t Au over 0.56 m in hole TCR18-077

//et
The upper portion of the Crestaurum structure has been previously
drilled with 187 drill holes over 1.4 kilometers of strike length, from
surface down to a depth of approximately 100-150 meters depth,
outlining a lode style shear and vein deposit (including 5.00 m @ 62.90
g/t Au, news release October 2, 2013). Although the structure is very
continuous the high grade lodes are more discrete and these initial
widespread deeper holes were designed to intersect structure to
determine whether there was probability of high grade lodes continuing
at depth potentially doubling the size of the mineralized zones.  A
drill hole location map can be found here and a long section of the
Crestaurum main shear are available here.

Joe Campbell, CEO of TerraX, states "This small program of four
holes successfully demonstrated that the Crestaurum zone continues at
depth on multiple surfaces, potentially doubling the size of the zone.
The 300 meter vertical depth tested with these holes is still
considered very shallow for Archean lode gold deposits and
mineralization remains open for further expansion, both along strike
and at depth."

TerraX also tested the Sam Otto west zone, another lode style
shear and vein deposit near TerraX's Sam Otto Main zone (1.90 m @ 13 96
g/t Au, news release May 2, 2017). This drilling included 5 holes
totaling 2,081 m testing strike and depth potential (down to 250 meters
vertical) on this zone. All holes hit gold mineralized structure with
best results of 3.00 g/t Au over 2.69 m in hole TSO18-038, 1.06 g/t Au
over 4.00 m in hole TSO18-041, and 1.32 g/t Au over 2.70 m in hole
TSO18-036. All holes included intersections of 2.0 to 5.6 meters of
0.71 to 0.81 g/t Au. The continuous presence of the gold mineralized
structures that now extend over more than a kilometer of strike and 250
meters of depth, with alteration and mineralization styles like the
high grade zones from the nearby Con and Giant mines, makes this a good
target for continued exploration.

A single hole (TSO18-039, 430 meters) was drilled approximately
500 m south along strike from the Sam Otto Main zone, and 600 meters
north of TSO18-037 (1.92 g/t Au over 11.52 meters, news release Mach 9,
2018). This hole confirmed the continuity of the Sam Otto structure
between the known extents of the Sam Otto Main and Sam Otto South
zones, intersecting a broad zone of deformation and alteration (0.10
g/t Au over 157.75 m) consistent with the Sam Otto style of
mineralization, including multiple 2.50 m - 9.10 m wide zones of 0.35
g/t Au -- 0.82 g/t Au.

All holes were drilled approximately normal to projected strike
and dip of the zones of mineralization and are interpreted to be
approximately 80-95% of true thickness

Tables are available at
https://www.terraxminerals.com/news/2018/terrax-extends-crestaurum-zone-to-
300-meters-vertical-depth-doubling-size-of-known-mineralized-structure/




The 2018 winter drill program at the Yellowknife City Gold project
is now complete.  TerraX drilled 3,681 meters and collected 2,331
samples for assay from the drilling reported here. Results ranged from
below detection to 21.8 g/t Au. Drill hole collar locations were
surveyed to sub-meter accuracy. Down hole surveying was completed on
all holes. TerraX inserts certified standards and blanks into the
sample stream as a check on laboratory QC. Drill core samples are cut
by diamond saw at TerraX's core facilities in Yellowknife.  A halved
core sample is left in the core box. The other half core is sampled and
transported by TerraX personnel in securely sealed bags to ALS Chemex's
(ALS) preparation laboratory in Yellowknife. After sample preparation,
samples are shipped to ALS's Vancouver facility for gold and ICP
analysis. Gold assays of )3 g/t are re-assayed on a 30 gm split by fire
assay with a gravimetric finish. ALS is a certified and accredited
laboratory service. ALS routinely inserts certified gold standards,
blanks and pulp duplicates, and results of all QC samples are reported.


The technical information contained in this news release has been
approved by Joseph Campbell, the Chief Executive Officer of TerraX, who
is a Qualified Person as defined in "National Instrument 43-101,
Standards of Disclosure for Mineral Projects."

About the Yellowknife City Gold Project

The Yellowknife City Gold ("YCG") project encompasses 772 sq km of
contiguous land immediately north, south and east of the City of
Yellowknife in the Northwest Territories. Through a series of
acquisitions, TerraX controls one of the six major high-grade gold
camps in Canada. Being within 10 km of the City of Yellowknife, the YCG
is close to vital infrastructure, including all-season roads, air
transportation, service providers, hydro-electric power and skilled
tradespeople.

The YCG lies on the prolific Yellowknife greenstone belt, covering
70 km of strike length along the main mineralized break in the
Yellowknife gold district, including the southern and northern
extensions of the shear system that hosted the high-grade Con and Giant
gold mines. The project area contains multiple shears that are the
recognized hosts for gold deposits in the Yellowknife gold district,
with innumerable gold showings and recent high-grade drill results that
serve to indicate the project's potential as a world-class gold
district.

For more information on the YCG project, please visit our web site
at www.terraxminerals.com.

On behalf of the Board of Directors

"JOSEPH CAMPBELL"

Joe Campbell
CEO

For more information, please contact:

Samuel Vella Manager of Corporate Communications Phone:
604-689-1749 Toll-Free: 1-855-737-2684 svella@terraxminerals.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release contains forward-looking information, which
involves known and unknown risks, uncertainties and other factors that
may cause actual events to differ materially from current expectation.
Important factors - including the availability of funds, the results of
financing efforts, the completion of due diligence and the results of
exploration activities - that could cause actual results to differ
materially from the Company's expectations are disclosed in the
Company's documents filed from time to time on SEDAR (see
www.sedar.com). Readers are cautioned not to place undue reliance on
these forward-looking statements, which speak only as of the date of
this press release. The company disclaims any intention or obligation,
except to the extent required by law, to update or revise any
forward-looking statements, whether as a result of new information,
events or otherwise.

TEL: 604-689-1749    TERRAX MINERALS INC
FAX: 604-648-8665
E-mail: info@terraxminerals.com
Website: http://www.terraxminerals.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1812700014TS11812701219-05560020180508