Source	MARKET NEWS
Date	05/29/2018
Time	05:54:06 AM

Company	 Radisson Mining Resources Inc.
Title	Intersects 8.7 G/T Gold Over 1.5 Meters 300m Eas





    CDNX Symbol: RDS











Press Release





Intersects 8.7 G/T Gold Over 1.5 Meters 300m East Of The VintageZone 
--->@NEWS RELEASE
RADISSON MINING RESOURCES ("RDS-V;RMRDF-0")
- Intersects 8.7 G/T Gold Over 1.5 Meters 300m East Of The
- Vintage Zone

Radisson Mining Resources Inc. ("Radisson" or the "Company") is
pleased to announce an update of the exploration program underway at
the O'Brien gold project located along the Cadillac Break, halfway
between Rouyn-Noranda and Val-d'Or in Quebec, Canada. Final results
from the 6,000 meters ("m") drill program completed on the Vintage Zone
of the O'Brien gold project are pending.

Following the resource estimate update published for the O'Brien
gold project (See March 20, 2018 Press release), the company announced
the expansion of the drilling program to 11,000 meters with a principal
focus on the F Zone where first two drill holes completed intersected
specs of visible gold.

Press release highlights:

*  Hole OB-18-71 intersected 8.7 g/t Au over 1.5 m, 300 meters
East of the Vintage Zone at vertical depth of 338 m. (See figure 2)

*  2 drill holes that intersected visible gold on the F Zone a few
meters West outside current resources area are currently being assayed
(See figure 1).

*  3 shallow drill holes completed in vertical extension of an
enrichment vector defined on 36E area are currently being assayed. (See
figure 1)

*  Current work will allow the company to define a drill program
below depth of 550 meters where all sectors of the O'Brien gold project
remain open.

F Zone area

The F Zone is contiguous and to the West of 36E area and extends
up to the old O'Brien mine. Results obtained from the 2016-2017
drilling program allowed to define the vertical and lateral extension
of historical mined stopes on the F Zone (See 20.2 g/t Au over 2.5 m
and 11.9 g/t Au over 3 m). Due to lack of 3D information from former
mining infrastructures of the F Zone, this sector was not incorporated
in the resource estimate update published on March 20, 2018. (See
Radisson announces 95% increase in Indicated resources at O'Brien).

Following the resource estimate update, the company started 3D
modelling of former mining infrastructures of the F Zone. The
geological team also established a 4,000 meters drill program with main
objective of building 43-101 compliant resources in a future resource
estimate update for the O'Brien gold project. Four drill holes were
completed therein, including one at the boundary of the 36E area.
Results are currently pending.

Vintage Zone

The Vintage zone is a parallel zone of the O'Brien project located
approximately 85 meters north of the Cadillac Break in the Cadillac
Group of meta-sediments comprising sequence of polymictic conglomerate,
banded iron formation (BIF) and grauwacke. A few mineralized zones
intercepted on Vintage were included in the latest resource estimate.
In parallel, the bulk of current resources on 36E and Kewagama zones
are located in the Piche Group, south of the Cadillac Break. Due to
their proximity all zones could eventually be accessed via same mining
infrastructures.

Drill holes published targeted the eastern extension of the
Vintage Zone. Exploration works completed on the Vintage Zone have
demonstrated the presence of Banded iron formations (BIF) north of the
Larder-Lake-Cadillac Break that could play a significant role for gold
distribution. Radisson is currently developing a litho-structural model
in order to plan future exploration work and increase its geological
knowledge on this area of the O'Brien project.

Drilling results summary on the Vintage Zone

//st

Drill hole   From (m)   To (m)   Length (m)   Grade Au   Interpreted Zone

OB-17-70     -          -        -            NSV        Vintage East

OB-17-71     409.6      411.1    1.5          8.7        Cadillac Wacke

OB-17-72     -          -        -            NSV        Vintage East

//et

**NSV; No significant value

Note; Results are presented as down hole width; true width are
estimated between 55 to 70% of down hole thickness.

All drill cores in this campaign are NQ in size. Assays were
completed on sawn half-cores, with the second half kept for future
reference. The samples were analyzed using standard fire assay
procedures with Atomic Absorption (AA) finish at ALS Laboratory Ltd, in
Val-d'Or, Quebec. Samples yielding a grade higher than 5 g/t were
analyzed a second time by fire assay with gravimetric finish at the
same laboratory. Samples containing visible gold were analyzed with
metallic sieve procedure. Standard reference materials and blank
samples were inserted prior to shipment for quality assurance and
quality control (QA/QC) program.

Qualified Person

Catherine Jalbert, P. Geo, acts as a Qualified Person as defined
in National Instrument 43-101 and has reviewed and approved the
technical information in this press release.

About Radisson Mining Resources Inc.

Radisson is a Quebec-based mineral exploration company. The
O'Brien project, cut by the regional Cadillac Break, is Radisson's
flagship asset. The project hosts the former O'Brien Mine, considered
to have been the Abitibi Greenstone Belt's highest-grade gold producer
during its production (1,197,147 metric tons at 15.25 g/t Au for
587,121 ounces of gold from 1926 to 1957; InnovExplo, April 2015).

For more information on Radisson, visit our website at
www.radissonmining.com.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Forward-Looking Statements: This press release may contain certain
forward-looking information. All statements included herein, including
the scheduled Closing date, but other than statements of historical
fact, is forward-looking information and such information involves
various risks and uncertainties. There can be no assurance that such
information will prove to be accurate, and actual results and future
events could differ materially from those anticipated in such
information. A description of assumptions used to develop such
forward-looking information and a description of risk factors that may
cause actual results to differ materially from forward looking
information can be found in Radisson's disclosure documents on the
SEDAR website at www.sedar.com.

Photos accompanying this announcement are available at



http://www.globenewswire.com/NewsRoom/AttachmentNg/3c28ae5e-3a95-49e8-b426-
ca22c76d2d0e



http://www.globenewswire.com/NewsRoom/AttachmentNg/512a96c5-9a9a-4e2b-830e-

TEL:  (819-763-9969  Hubert Parent-Bouchard, Corporate Development
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1814800027TS11814800938-05514520180529