Source	MARKET NEWS
Date	05/31/2018
Time	06:00:23 AM

Company	 Pure Energy Minerals Limited
Title	Completion of Pilot Plant Basic Design at the Cl





    CDNX Symbol: PE











Press Release





Completion of Pilot Plant Basic Design at the Clayton Valley LithiumProject 
--->@NEWS RELEASE
PURE ENERGY MINERALS LTD ("PE-V;PEMIF-0")
- Completion of Pilot Plant Basic Design at the Clayton Valley
- Lithium Project

Pure Energy Minerals Limited (the "Company" or "Pure Energy") is
pleased to announce the completion of basic design for the pilot plant
at its flagship Clayton Valley Project ("CV Project"). Pure Energy has
been working closely with its engineering providers to achieve the
basic engineering and ensuing final design of the pilot plant. Building
on the work reviewed at an engineering meeting on February 2018 (see
Company news release dated 27 February, 2018), the basic design
includes drafts of process flow diagrams (PFDs), piping and
instrumentation diagrams (P&IDs), specifications, subcontractor scopes,
contracting documents, and facility layouts.

The pilot plant design is being led by Tenova Advanced
Technologies ("TAT") with significant contributions from SUEZ Water
Technologies & Solutions, a business unit of SUEZ Group, and NORAM
Engineering & Constructors (collectively, the "Engineering Team"). The
facility at the CV Project will be the first pilot-scale implementation
of the Tenova Process in the world.

Patrick Highsmith, Pure Energy's CEO, stated, "We are truly
excited to receive the pilot-plant basic design package from the
Engineering Team. The team has made significant progress over the three
months since we last met at TAT's research facility in Israel. The
basic design package represents the culmination of thousands of hours
of engineering effort toward the design of this first-of-its-kind
facility. We are particularly pleased to work with Tenova, SUEZ, and
NORAM, all of whom are world-renowned leaders in their respective
fields. Their support is invaluable to the development and success of
the CV Project."

Completion of the pilot plant basic design is an important
milestone in Pure Energy's development of the CV Project. The Company
plans to build the pilot plant in Nevada to further evaluate the
innovative technology developed by TAT for the extraction of lithium
and production of lithium hydroxide monohydrate at the CV Project (the
"Tenova Process"). Data from a successful pilot plant trial will be
used in the design of a full-scale commercial plant to produce lithium
hydroxide directly from Clayton Valley brine using the Tenova Process.

The Tenova Process flowsheet consists of three distinct sections:
*  Pre-Treatment - LiP(TM): The pre-treatment stage efficiently
removes the alkaline earth elements (Ca, Mg, and Sr) with minimal
lithium loss. This was achieved in the mini-pilot plant test work using
membranes supplied by SUEZ Water Technologies & Solutions;
*  Solvent Extraction - LiSX(TM): The solvent extraction step
incorporates Tenova Pulsed Columns in each of the extraction, scrubbing
and stripping stages to extract the lithium from the brine and
concentrate it into a strip solution. Based on successful mini-pilot
plant test results (see Company's news release dated 13 December,
2016), the LiSX(TM) step is expected to increase the lithium
concentration by a factor of approximately 38 with no measurable
lithium losses;
*  Electrolysis - LiEL(TM): Through electrolysis, the lithium
sulphate produced in the preceding solvent extraction step is
transformed into lithium hydroxide using equipment and a process
designed by NORAM Engineering & Constructors. This step allows for the
direct production of lithium hydroxide monohydrate without having to
first produce lithium carbonate.

The Tenova Process is specifically designed to exclude solar pond
evaporation, increase and accelerate lithium recovery, and reduce the
associated environmental footprint of lithium production. After
successful bench-scale testing, proof-of-concept for the Tenova Process
through mini-pilot plant test work was completed in 2016 at TAT's
Research & Development Center in Israel.

The Engineering Team is committed alongside Pure Energy to the
design, construction, and operation of the pilot plant, as described in
the Memorandum of Understanding ("MOU") between Pure Energy, TAT, and
the rest of the Engineering Team (see Company news release of 11
October, 2017). To date, the Engineering Team has contributed more than
US$600,000 toward the pilot-plant project in the form of in-kind
contributions and discounts.

Quality Assurance

Walter Weinig, Professional Geologist and SME Registered Member
(SME Registered Member # 4168729), is a qualified person as defined by
NI 43-101 and supervised the preparation of the scientific and
technical information that forms the basis for this news release. Mr.
Weinig is not independent of the Company, as he is an officer.

About Pure Energy Minerals Limited

Pure Energy Minerals is a lithium resource developer that is
driven to become a low-cost supplier for the growing lithium battery
industry. Pure Energy's CV Project is located in Esmeralda County,
Nevada, adjacent to the only producing lithium-brine operation in North
America. The CV Project has access to excellent infrastructure and an
experienced workforce in one of the world's premier mining
jurisdictions. The Company is also exploring a new lithium brine
project in the Lithium Triangle of South America, the Terra Cotta
Project ("TC Project"). The TC Project is located on Salar de Pocitos
in Salta, Argentina, where it enjoys some of the best infrastructure
and access of any lithium brine exploration project in Argentina.

On behalf of the Board of Directors,

"Patrick Highsmith"
Chief Executive Officer

Contact Information:

CONTACT:

Pure Energy Minerals Limited (www.pureenergyminerals.com)
Email: info@pureenergyminerals.com
Telephone - 604 608 6611

Cautionary Statements and Forward-Looking Information

The information in this news release contains forward looking
statements that are subject to a number of known and unknown risks,
uncertainties and other factors that may cause actual results to differ
materially from those anticipated in our forward looking statements.
Factors that could cause such differences include: changes in world
commodity markets, equity markets, costs and supply of materials and
equipment relevant to the mining industry, weather or other conditions
that may affect access to the Company's project sites, change in
government and changes to regulations affecting the mining industry.
Forward-looking statements in this release may include statements
regarding future design work on the CV Project, completion of various
engineering studies, construction of a pilot plant, as well as possible
future operations at the CV Project. Although we believe the
expectations reflected in our forward looking statements are
reasonable, results may vary, and we cannot guarantee future results,
levels of activity, performance or achievements.

The Company does not undertake to update any forward-looking
information, except as required by applicable laws.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1815000017TS11815000922-05570720180531