Source	MARKET NEWS
Date	06/04/2018
Time	09:54:54 AM

Company	 Satori Resources Inc.
Title	Metallurgical Test Results Favourable at Tartan





    CDNX Symbol: BUD











Press Release





Metallurgical Test Results Favourable at Tartan and Corporate Update 
--->@NEWS RELEASE
SATORI RESOURCES INC ("BUD-V;STRRF-0")
- Metallurgical Test Results Favourable at Tartan and Corporate Update

Satori Resources Inc. ("Satori" or the "Company") announces that
it has completed an independent metallurgical study, in order to better
understand the inconsistency of recovery rates documented from
production at the Tartan Lake Gold Mine Project in the late 1980's.
The report evidences favourable recovery rates from a significant bulk
sample, which concluded that the Main zone had an overall Au recovery
ranging between 95 and 97%; while the South zone returned Au recovery
values ranging between 91 and 92%.  Management's analysis of this study
is that the historical recoveries would most likely have been related
to either mill design, or mill operation.  Based on this metallurgical
testwork, Satori intends to proceed toward a new optimized mill design
for the Tartan Lake Gold Mine Project.

The test results of metallurgical performance at the Tartan Lake
Gold Mine Project was completed by an independent consultant, Base Met
Labs, using composite samples, one from each of the Main (5.6 g/tonne)
and the South (3.4 g/tonne) Zones. Samples for each of the zones were
selected to provide a composite representation of the possible
lithologic and mineralogic variations within the zone, and to
approximate the calculated resource grade for that zone.

Overall, the zone composites demonstrated excellent gold recovery
at relatively coarse particle size distributions.
Gravity-Floatation-Leach and Gravity-Leach flowsheets were compared for
both composites, and it was found that tests with no floatation stage
performed better than with floatation (due to the rougher floatation
tailings).

The following table from the report indicates a summary of the
metallurgical test results:

//st

Composite Test Schematic Au Recovery - percent               Primary
Grind
m K80
Gravity  Flotation Leach  Overall
(unit)

Main Zone 1    Grav      58.3     38.9      -      97.2      300
Float

3    Grav      54.4     40.4      86.6   89.3      300
Float
Leach

5    Grav Cu   61.8     34.5      -      96.3      300
- Py
Float

6    WOL       -        -         94.3   94.3      300

8    Grav      57.5     -         87.4   94.6      300
Leach

South     2    Grav      40.3     51.8      -      92.1      300
Zone           Float

4    Grav      33.7     60.5      74.3   78.7      300
Float
Leach

7    WOL       -        -         86.1   86.1      300

9    Grav      32.6     -         78.9   85.8      300
Leach

10   Grav      34.4     -         85.5   90.5      225
Leach

11   Grav      45.5     -         89.3   94.2      150
Leach

12   Grav      36.0     -         85.4   90.7      225
Leach

//et

Note: Grav Float Schematic would require cyanidation leaching
which would incur additional gold losses

Test Work Methodology

At a primary grind of 300m K80, gravity concentration followed by
whole ore leaching of the gravity tailings recovered about 94.6 percent
of the gold in the Main Zone Composite, and 85.8 percent of the gold in
the South Zone Composite.

Finer primary grinding was tested on the South Zone to improve
gold performance. At a primary grind of 150m K80, 94.2 percent of the
gold was recovered for the South Zone. This primary grind size is still
considered coarse for whole ore leach processing.

Some of the gold lost in bulk sulphide floatation is thought to be
associated with non-sulphide minerals, which would not be recoverable
to bulk sulphide processing. A gravity-float-leach schematic provides
operating cost savings when leaching requires a very fine particle size
for successful extraction.  This does not seem to be the case for these
sample, particularly the Main Zone.

Copper was measured at low contents in the composites, at about
0.04 percent for both composites. This copper was identified as
chalcopyrite in through bulk mineral analysis. The copper did not have
a negative impact on leaching, likely due to the form of copper and
conditions used.

Primary grind size distribution is a key parameter for successful
gold recovery in cyanidation leaching, as establish for the South Zone
Composite. A variability program assessing the extent of performance
versus primary grind size, across numerous discrete zones of the
deposit is recommended. This would identify the risk and sensitivity to
recovery in the process with fluctuations in feed material. The
variability program should also include Sulphur feed grade assessment,
as fluctuations in feed grade can have a significant influence on both
flotation and cyanide leaching, influencing factors such as mass
recovery in flotation and cyanide and oxygen consumption in leaching.

Peter Karelse P.Geo., registered in the Province of Ontario, a
Geological Consultant, is the qualified person as defined by NI 43-101
responsible for the technical data in this news release.

The Company further announces that due to time constraints, Mr.
Allen Palmiere has submitted his resignation as a member of the board
of directors and as Chief Executive Officer, and that Mr. Bruce Reid
shall fill the vacancy on an interim basis.

ABOUT SATORI RESOURCES INC.

Satori is a Toronto-based mineral exploration and development
company whose primary property is the Tartan Lake Gold Mine Project
(100% interest), located in the prolific Flin Flon mining district, in
Manitoba, Canada. The Tartan Lake Gold Mine had historical high-grade
production of 48,000 ounces of gold between 1987-1989.  The Project
hosts a largely intact 450 tonne per day gold concentrator and related
infrastructure, along with a decline ramp providing access to developed
gold mineralization within the Main and South Zones to a vertical depth
of 320 metres.

FOR FURTHER INFORMATION, PLEASE

Contact Information:

CONTACT:

Ms. Jennifer Boyle
Satori Resources Inc.
jennifer@capexgroupinc.com
416-904-2714

For further information, please visit www.satoriresources.ca.

The TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) does
not accept responsibility for the adequacy or accuracy of this release.


CAUTION REGARDING FORWARD-LOOKING INFORMATION

This news release of Satori contains statements that constitute
"forward-looking statements." Such forward-looking statements involve
known and unknown risks, uncertainties and other factors that may cause
Satori's actual results, performance or achievements, or developments
in the industry to differ materially from the anticipated results,
performance or achievements expressed or implied by such
forward-looking statements.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1815400049TS11815402056-09521720180604