Source	MARKET NEWS
Date	05/25/2018
Time	05:11:39 AM

Company	 Great Bear Resources Ltd.
Title	Drilling Returns High Grade Gold at Dixie Projec





    CDNX Symbol: GBR











Press Release





Drilling Returns High Grade Gold at Dixie Project, Red Lake, Ontario 
--->@NEWS RELEASE
GREAT BEAR RESOURCES LTD ("GBR-V;GTBDF-0")
- Drilling Returns High Grade Gold at Dixie Project, Red Lake, Ontario

Great Bear Resources (the "Company" or "Great Bear"),  today
announced results from the first 5 drill holes of its Phase 2 drill
program at its Dixie project in the Red Lake district of Ontario.  A
total of 15 holes were drilled along 2.3 kilometres strike length of a
prospective geological contact, testing both new and existing gold
targets.  All holes hit the hydrothermal alteration system which is
characterized by varying silicification, sulphide mineralization and
gold content.  Drilling will recommence in June 2018.

Highlights from the first five drill holes include:

//st

* The first "Hinge Zone" drilling by Great Bear intercepted high-grade gold
including 17.18 g/t gold over 1.7 metres, which includes 46.3 g/t gold
over 0.60 metres in drill hole DHZ-002. DHZ-001, drilled 75 metres
vertically above DHZ-002 intersected 10.15 g/t gold over 1.25 metres,
suggesting significant vertical and grade continuity. Oriented core data
suggests that these intercepts are likely from a vein system that is
parallel to historically drilled veins, indicating multiple high-grade
gold veins are present in the Hinge Zone
* A "Hanging Wall Zone" was intercepted parallel to the main Dixie Limb
Zone, returning 12.41 g/t gold over 1.5 metres including 30.20 g/t gold
over 0.55 metres. This adds an additional drill-confirmed high-grade
gold-bearing zone within the primary drill area
* Gold is confirmed at the "South Limb Zone"; DSL-001, Great Bear's first
drill hole into this target intersected a 32-metre-wide zone of quartz
veining and silica/sulphide alteration containing anomalous gold
mineralization which included 5.34 g/t gold over 0.50 metres and 3.47 g/t
gold over 1.0 metre

//et

Chris Taylor, CEO of Great Bear commented, "Our Phase 2 drilling
was ambitiously designed to test the size potential of the Dixie gold
system at shallow depths and along strike, plus a number of new gold
targets.  It was successful on all fronts.  Our drilling has revealed a
regionally-significant gold-bearing hydrothermal system which has now
been drilled along more than 2 kilometres of a favourable geological
contact. The system contains multiple drill-confirmed high-grade gold
zones comparable in width and grade to mined deposits in Red Lake, all
of which are open to extension.  Historical drilling and geophysics
suggest that the primary gold-bearing contact may extend for up to 10
kilometres on the property.  The remaining 7,000 metres of the Phase 2
drill program will include further step-out holes along this contact,
and follow-up delineation drilling of areas with high-grade gold
intercepts at depth."

Table 1: Drill intercept highlights from the first 5 of 15 drill
holes completed during initial Phase 2 drilling.  All interval lengths
are drill indicated and may not represent true thicknesses.

//st

Hole                   From    To (m)    Au     Width    Zone     Comment
(m)              (g/t)    (m)

DHZ-001                140.30   142.15   6.95    1.85     Hinge    visible
gold

including    140.90   142.15   10.15   1.25

and       141.65   142.15   15.10   0.50
including

DHZ-002                198.00   199.70   17.18   1.70     Hinge    visible
gold

including    198.00   199.10   26.41   1.10

and       198.50   199.10   46.30   0.60
including

DL-009                 88.60    96.00    2.59    7.40    Hanging   visible
Wall      gold

including    94.50    96.00    12.41   1.50

and       95.45    96.00    30.20   0.55
including

230.40   234.80   1.96    4.40     Dixie    visible
Limb      gold

including    231.40   232.35   4.04    0.95

DL-010                 234.25   239.00   1.73    4.75     Dixie
Limb

DSL-001                137.10   169.10   0.32    32.00    South    visible
Limb      gold

including    163.75   164.25   5.34    0.50

And       182.00   183.00   3.47    1.00

including    182.00   182.50   4.62    0.50

//et

Hinge Zone

DHZ-001 and DHZ-002 are the first holes drilled into the Hinge
Zone by Great Bear.  They intersected quartz veins with strong
peripheral biotite alteration and both contained high-grade intervals
with visible gold.

This combination of hydrothermal biotite alteration with quartz
vein-hosted high-grade visible gold also occurs at the High Grade Zone
at the Red Lake gold mine operated by Goldcorp (TSX: G). The intercepts
in the two Hinge Zone holes are 75 metres apart (vertically) and remain
open for follow-up drilling.

Hanging Wall Zone

High-grade gold mineralization was encountered in drill hole
DL-009 at the contact between a rhyolite  and tholeiitic basalt, and
occurs approximately 80 meters above (in the hanging wall) of the
primary Dixie Limb contact.  Significant visible gold is observed which
returned 30.20 g/t gold over 0.5 metres, within a broader interval of
2.59 g/t gold over 7.40 metres.  Several historical holes intersected
the same contact (according to historical drill log descriptions),
however not all of the intervals were assayed for gold by past
explorers.  The Company will continue to explore this zone and test
other possible parallel gold zones.

Figure 1: Drill plan showing locations of first 15 holes of the
2018 drill program.  Sub-zones within the Dixie gold system are labeled


To view an enhanced version of Figure 1, please visit:
https://orders.newsfilecorp.com/files/5331/34831_a1527224904927_43.jpg

South Limb Zone

Hole DSL-001 is the first hole drilled by Great Bear into the
interpreted South Limb of an apparent folded duplication of the main
Dixie Limb, as shown on Figure 1.  Observations of a wide silicified
and sulphide-gold bearing interval in DSL-001 suggests that the Dixie
hydrothermal system may be wider in this area, and that significant
gold potential exists at South Limb.
Pending Assays

The Company is awaiting assays from 10 additional drill holes.
These include step out holes along the primary Dixie Limb contact that
increase its drilled strike length from approximately 500 metres to 2.3
kilometres, and additional drill holes into the main Dixie Limb within
the primary drill area.  Results are expected to be received over the
next four weeks, and will be released in batches as processed.  The
Company expects to be drilling again during June.

Drill core was logged and sampled in a secure core storage
facility located in Red Lake Ontario.  Core samples from the program
were cut in half, using a diamond cutting saw, and were sent to
Activation Laboratories Ltd. in Ancaster Ontario, an accredited mineral
analysis laboratory, for analysis.  All samples were analysed for gold
using standard Fire Assay-AA techniques.  Samples returning over 3.0
g/t gold were analysed utilizing standard Fire Assay-Gravimetric
methods. Certified gold reference standards, blanks and field
duplicates were routinely inserted into the sample stream, as part of
Great Bear's quality control/quality assurance program.

About Great Bear

Great Bear is earning a 100% royalty-free interest in the Dixie
property which consists of 7,106 hectares in the Red Lake district
covering a drill and geophysically defined multi-kilometre gold
mineralized structure similar to that hosting other producing gold
mines in the district.  The project has seen over 160 drill holes
to-date and has yielded high grade near-surface gold results including
10.40 m of 16.84 g/t gold.  In addition, Great Bear is also earning a
100% royalty-free interest in its West Madsen properties which total
2,725 hectares and are contiguous with Pure Gold Mining Inc.'s (TSX-V:
PGM) Madsen property.  All of Great Bear's Red Lake projects are
accessible year-round through existing roads.

Mr. R. Bob Singh, P.Geo, Director and VP Exploration for Great
Bear, is the Qualified Person as defined by National Instrument 43-101
responsible for the accuracy of technical information contained in this
news release.

For further information please contact Mr. Chris Taylor, P.Geo,
President and CEO at 604-646-8354, or Mr. Knox Henderson, Investor
Relations, at 604-551-2360.

ON BEHALF OF THE BOARD

"Chris Taylor"

Chris Taylor, President and CEO

Inquiries: Tel: 604-646-8354 Fax: 604-646-4526
info@greatbearresources.ca www.greatbearresources.ca

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

This new release may contain forward-looking statements. These
statements are based on current expectations and assumptions that are
subject to risks and uncertainties. Actual results could differ
materially because of factors discussed in the management discussion
and analysis section of our interim and most recent annual financial
statement or other reports and filings with the TSX Venture Exchange
and applicable Canadian securities regulations. We do not assume any
obligation to update any forward-looking statements.

We seek safe harbor

TEL: 778-327-5799    GREAT BEAR RESOURCES LTD
FAX: 778-327-6675
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1814400001TS11814400366-05094920180525