Source	CANADA NEWSWIRE
Date	06/06/2018
Time	06:03:27 AM

Company	 Marlin Gold Mining Ltd.
Title	Marlin Gold Announces Positive Metallurgical Test Results for the
Commonwealth Project - Supporting Both Heap Leach and Milling Scenarios





    CDNX Symbol: MLN











Press Release




" BC-MLN-PostiveTes-Reslts   06-06 1836
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Marlin Gold Announces Positive Metallurgical Test Results for the
Commonwealth Project - Supporting Both Heap Leach and Milling Scenarios@

VANCOUVER, June 6, 2018 /CNW/ - Marlin Gold Mining Ltd. (TSX-V: MLN)
("Marlin" or the "Company") is pleased to announce that it has received
encouraging preliminary results from the latest metallurgical testing program
being conducted on its wholly owned Commonwealth gold and silver property in
Cochise County, Arizona (the "Commonwealth Project"). The results indicate
that the gold and silver mineralization is amenable to processing by heap
leaching or milling and recovery by industry standard methods.
Akiba Leisman, Executive Chairman and Interim CEO states that, "Over the
past nine months, Marlin has been conducting extensive metallurgical testing
to help define the parameters and process flowsheet for the Commonwealth
Project. The entire resource is in oxidized material, and both heap leach and
milling scenarios were investigated. The results received to date meet or
exceed management's expectations for recoveries and engineering has commenced
to determine the optimal capacity and processing method for the project."
Samples for the metallurgical test program were selected from 26 large
diameter PQ (8.5cm diameter) core holes drilled in 2016 and 2017 along with
various exploration assay rejects to represent 28 variations in the style of
mineralization identified by the exploration work. McClelland Laboratories
Inc. ("MLI") was engaged to conduct a bench scale metallurgical test program
to guide the development of the Commonwealth Project. A series of columns
tests, and cyanidation tests by bottle roll and agitation were carried out to
determine the metallurgical response to heap leaching and a conventional whole
ore milling process. The flowsheets for a mill operation considered
cyanidation with carbon recovery as well as a flotation concentration and
gravity concentration as possible processing options to demonstrate gold and
silver recoveries that can be expected from either a heap leach operation or a
whole ore milling operation.
The test work used a range of size distributions to determine the optimum
crushing and grinding sizes for each of the processing options in conjunction
with testing the metallurgical response of the 28 variations in the style of
mineralization that have been identified by the exploration program to date.
The depth of the samples as well as higher grade mineralization was given
representation in the variability samples to help guide future mine planning
considerations. Composite groupings were defined based on host rock,
alteration, mineralization style and either or both gold and silver assays.
Heap Leaching
Fifty-four column tests have been initiated to test the potential to
apply heap leaching as the process route for the Commonwealth Project.
Although only 11 of the column tests have reached completion and reporting,
the preliminary results to date provide good insight into the results to be
expected from this type of processing.
The average gold recovery after a 75-day leach cycle was 80.4% on all
samples crushed to minus 3/8 inch with recoveries ranging from 83% to 88% on
finer material depending on the style of mineralization. Results indicate
improved extractions with finer crush sizes by as much as 5% to 15%. The main
process consumables range from 1.17 to 3.24 kg/tonne of cyanide and 1.0 to 2.5
kg/tonne of lime. The consumption of cement added to agglomerate the finer
material was 2.0 kg/tonne. The leach cycle times being tested range from 75 to
100 days with up to 175 days to complete the total leach and rinse times
required. The column tests yielded low silver extractions averaging 15.2%.
The Company plans to report on the column test results as soon as the
full test results report is received from MLI.
Whole Ore Cyanidation
A series of bench scale tests were carried out to test the metallurgical
response to a standard gold mill employing cyanidation with recovery of the
gold and silver by carbon in pulp or carbon in leach. This included rolling
bottle testing and agitated leach tests with cyanide and pH adjustment with
lime. As possible variations to whole ore cyanidation, testing of gravity
concentration was carried out as well as flotation concentration to provide
preliminary indications of the probable metallurgical response of all
variations of the processing options. These variations may possibly reduce
grinding costs, reduce consumption of major consumables, and improve overall
metal recoveries as well as guide the final selection of the process
flowsheet.
Bottle roll testing was completed on all composites in a total of 88
tests keeping the cyanide levels and pH constant. The results showed good gold
extractions ranging from 85.7% to 97.2% with silver extractions improved over
the column testing ranging from 19.0% to 55.1%. Historical mineralogical
studies indicated that low silver recovery may be attributed to very fine
silver encapsulated in the silica matrix, very fine silver included in
jarosite and silver contained within manganese oxides. Ultrafine grinding
testing showed improved extractions for both gold and silver but is probably
not economic due to the increased power cost as well and probable increased
reagent costs associated with the finer material that would have to be
handled.
Agitated leach tests were carried out on samples which for the most part
compared with the bottle roll tests and conclusions reached. The leach
kinetics indicated that most of the leachable gold and silver were in solution
after 24 hours supporting the normal design parameters of 36 hours retention
time in a commercial flowsheet. The cyanide consumption ranged from 0.83 to
1.29 kg/tonne with lime requirements at 1.6 to 2.6 kg/tonne. There was an
indication that cyanide consumption was higher on the deeper composites that
were tested.
Analysis for organic carbon as a potential metal loss from solution
showed 0.12% with considerably less in the drill core samples. The exception
to the low levels was in two zones with sedimentary material that will require
closer analysis in the mining plan and any potential inclusions in the
mineralized zones.
Scoping level flotation tests were completed on three higher grade
composites to test the metallurgical response to single stage rougher
flotation. The three composites were ground to 80% passing 100, 150 and 200
mesh (150, 106 and 75 microns). Results indicated that gold recovery to the
flotation concentrate would range from 82.8% to 89.1% while silver recovery
would range from 10.6 % to 54.9%. As with the bottle roll testing, the finer
grind showed improved recoveries of both metals.
The tailings from the flotation circuit were subjected to cyanidation
tests and indicated the overall recovery of gold would be comparable to the
whole ore cyanidation results. This would make the overall process decision on
the inclusion of flotation rest on the operating costs of the two options and
any potential savings that could be achieved with reagents and grinding costs.
The scoping level bench testing of gravity concentration on samples at
80% passing 200 mesh (75 microns) showed 12.2% to 27.7% of the gold and 1.9%
to 11.2% of the silver reporting to a gravity concentrate as expected by the
metallic assay results.
Quality Assurance and Quality Control
All sample preparation, compositing, and test work was performed or
overseen by McClelland Laboratories Inc. in Sparks, Nevada. Their processes
and assaying results met the requirements of the Company and its consultants,
including Sr. Metallurgist Craig L. McKenzie, and are traceable and well
documented.
Qualified Person
Ross MacFarlane P. Eng Watts, Griffis and McOuat Limited, Associate
Metallurgist and Joe Hinzer, P.Geo., the President and Director of Watts,
Griffis and McOuat Limited both independent of Marlin and "Qualified Persons"
under NI 43-101 have reviewed and approved the written scientific and
technical disclosure contained in this presentation.
About Marlin Gold
Marlin is a growth-oriented gold and silver mining company focused on the
Americas. The company owns three properties located in Mexico and the USA and
a portfolio of royalties. Marlin's priority is to profitably operate its La
Trinidad Mine, conduct further exploration on its other projects and enhance
shareholder value through a strategic relationship with Sailfish Royalty Corp.
(TSX-V:FISH). Marlin is backed by a well-funded investor with a successful
track record in the resources sector. The La Trinidad Mine in Sinaloa, Mexico
declared commercial production on November 1, 2014 and is one of the highest
grade open pit heap leach gold mines in Mexico.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
the term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary statement regarding forward?looking information
This news release contains "forward-looking statements" within the
meaning of applicable securities laws. Forward-looking statements are
statements that are not historical facts and are generally, but not always,
identified by words such as the following: expects, plans, anticipates,
believes, intends, estimates, projects, assumes, potential and similar
expressions. Forward-looking statements also include reference to events or
conditions that will, would, may, could or should occur, including, without
limitation statements relating to: the anticipated access to mineralized
material, including any potential mining thereof; the timing and scope of
certain drilling programs; the receipt of assay results; statements regarding
the perceived merit of properties, exploration programs and budgets;
anticipated capital expenditures; mineral resource estimates; timelines;
strategic plans; and other statements that are not statements of fact. These
forward-looking statements are necessarily based upon a number of estimates
and assumptions that are based on management's expectations and considered
reasonable at the time they are made, including among others: that work
proceeds in accordance with the timing and scope anticipated by management and
that anticipated market prices for precious and base metals are achieved.
Investors are cautioned that all forward-looking statements are inherently
subject to a variety of risks and uncertainties which could cause actual
events or results to differ materially from those reflected in the
forward-looking statements, including, without limitation: uncertainties
related to raising sufficient financing to fund planned work in a timely
manner and on acceptable terms; changes in planned work resulting from
logistical, technical or other factors; the possibility that results of work
will not fulfill projections/expectations and realize the perceived potential
of the Company's projects; uncertainties involved in the interpretation of
drilling results and other tests and the estimation of gold resources; risk of
accidents, equipment breakdowns and labour disputes or other unanticipated
difficulties or interruptions; the possibility of environmental issues at the
Company's projects; the possibility of cost overruns or unanticipated expenses
in work programs; the need to obtain permits and comply with environmental
laws and regulations and other government requirements; fluctuations in the
price of gold; and other risks and uncertainties, including those described in
the Company's annual management's discussion and analysis filed on SEDAR at
www.sedar.com. As a result, readers are cautioned not to place undue reliance
on these forward-looking statements. The forward-looking statements contained
in this news release are made as of the date of this release. Unless required
by law, Marlin has no intention to and assumes no obligation to update or
revise any forward-looking statements, whether as a result of new information,
future events or otherwise.
SOURCE Marlin Gold Mining Ltd.



View original content with multimedia:
http://www.newswire.ca/en/releases/archive/June2018/06/c3667.html

-0-                           06/06/2018
/For further information: Akiba Leisman, Executive Chairman and Interim
CEO, Marlin Gold Mining Ltd., Telephone: 203-862-7059, E-mail:
aleisman(at)marlingold.com/
/Web Site: http://www.marlingold.com /
(MLN.)

CO:  Marlin Gold Mining Ltd.
ST:  British Columbia
IN:  MIN
SU:  SVY

-30-