Source	MARKET NEWS
Date	06/06/2018
Time	06:52:07 AM

Company	 Sama Resources Inc./Ressources Sama Inc.
Title	SRG's Maiden 
Resource Estimate for the Gogota Ni





    CDNX Symbol: SME











Press Release





SAMA RESOURCES INC ("SME-V")
- SRG's Maiden Resource Estimate for the Gogota Nickel-Cobalt
- Deposit 44.9Mt @ 1.28% Ni and 0.13% Co

Sama Resources Inc. ("SME" or the "Company") today reports that
SRG Graphite Inc. ("SRG") has today announced the maiden resource
estimate for the SRG 100%-owned Gogota nickel-cobalt deposit located in
the Republic of Guinea. The mineral resource estimate, prepared by
Montreal based Met-Chem, a division of DRA Americas Inc.
("Met-Chem/DRA"), includes a pit-constrained inferred resource of 44.9
million tonnes ("Mt") grading 1.28% nickel ("Ni") for a content of
573,040 tonnes and 0.13% cobalt ("Co") for a content of 59,560 tonnes.
The limonitic portion of the deposit also contains 1,166,200 kilograms
("kg") of scandium ("Sc").

The highlights of the pit constrained estimate are as follows:

*  44.9 Mt of mineralized weathered material (limonite and
saprolite) from surface to 40 meters
*  1.28% Nickel ("Ni"), 0.13% cobalt ("Co"), 29.4g/t scandium
("Sc")
*  38Mt of limonite material grading 0.15% Co for 57,140 t of
in-situ cobalt
*  Preliminary strip ratio of 0.23

Mineral resources were based on 51 vertical drill holes carried
out over the Gogota deposit in 2012-2013. 31 drill holes were drilled
over a 200-meter by 400-meter grid and the remaining 20 were drilled
over a 200-meter by 200-meter grid.  SRG will file a NI 43-101
technical report supporting the mineral resource estimate with SEDAR
within 45 days of the issuance of this press release.

"The Met-Chem/DRA resource estimate demonstrates the exceptional
potential of the Gogota project and reaffirms the tremendous geological
potential in the sub-region" said Dr. Marc-Antoine Audet, Lead
Geologist and Qualified Person ("QP") for SRG and President and CEO of
Sama.

Resource Summary

The mineral resource for the Gogota project incorporates assay
results from 51 vertical diamond drill holes representing 1,361 meters.
800 samples were sent for analysis in 2013 representing 31 drill holes
and the remaining 425 samples representing 20 drill holes were sent for
analysis in 2018 for a total 1,225 samples representing all 51 drill
holes. The maiden resource is established for the weathered profile of
the deposit, from surface to a depth ranging from surface to
approximately 40 meters with an average thickness of 22 meters. The
surface area of the deposits covers 1.96 kilometers-squared.

Core logging and sampling were performed at the SRG's facility in
the village of Gogota. Sample preparation was performed by Veritas
Laboratory in Abidjan, Cote d'Ivoire. Pulp samples were delivered to
Activation Laboratories Ltd. ("ActLab"), Ancaster, Ontario, Canada. All
samples were assayed for nickel, cobalt and all major oxides using
peroxide fusion XRF. Scandium was determined by inductively coupled
plasma optical emission spectrometry.

The estimate was prepared using a block model constrained with 3D
wireframes of the principal mineralized domains. Values for nickel,
cobalt and scandium, were interpolated using inverse-distance ("ID")
interpolation methodologies on 40 x 40 x 2m blocks. A preliminary open
pit optimization algorithm was run on the estimated grade block model
to constrain the resources and to support the Canadian Institute of
Mining, Metallurgy and Petroleum's ("CIM") requirement that mineral
resources have "reasonable prospects for eventual economic extraction."
Only mineralization contained within the preliminary pit shell has been
included in the resource estimate.

The base case mineral resource estimate is summarized in the
following table at a cut-off grade of 0.07% Co in the limonite facies
of the profile and 0.70% Ni in the transition and saprolite layers
together. Sensitivity estimates were conducted at 0.10% Co and 1.0% Ni,
and 0.12% Co and 1.2% Ni in limonite and transition/saprolite
respectively. The resource estimate and sensitivities are established
with data from boreholes drilled in 2012 and 2013.



Base Case Mineral Resources

Table is available at
http://samaresources.com/news/sama-resources-reports-on-srgs-maiden-resourc
e-estimate-for-the-gogota-nickel-cobalt-deposit-44-9mt-1-28-ni-and-0-13-co/


Sensitivity 1: 0.10% Co, 1.0%Ni

Table is available at
http://samaresources.com/news/sama-resources-reports-on-srgs-maiden-resourc
e-estimate-for-the-gogota-nickel-cobalt-deposit-44-9mt-1-28-ni-and-0-13-co/


Notes: 1) CIM definitions (May 10, 2014) observed for
classification of mineral resources. 2) Block bulk densities
interpolated from specific gravity measurements taken from core
samples. 3) Resources are constrained by a Lersch Grossman (LG)
optimized pit shell using MineSight software. 4) Pit shell defined
using 30-degree pit slope, $USD 5.5/lbs Ni, $USD 30/lbs Co, $USD 0.0/g
Sc, $USD 2.00/t mining costs, $USD 43/t processing costs, $USD 3.50/t
G&A and $USD 175/t for concentrate transportation costs. 5) Mineral
resources are not mineral reserves and have no demonstrated economic
viability. The estimate of mineral resources may be materially affected
by mining, processing, metallurgical, infrastructure, economic,
marketing, legal, environmental, social and governmental factors
("Modifying Factors"). 6) Numbers may not add due to rounding. 7)
Effective Date of Resource estimate is June 6th, 2018.

Qualified Person

Met-Chem/DRA's consultant, Schadrac Ibrango, P. Geo was
responsible for estimating the mineral resources and has reviewed and
approved the contents of this press release. Mr. Ibrango is a Qualified
Person ("QP"), independent of SRG Graphite, within the meaning of NI
43-101 - Standards of Disclosure for Mineral Projects of the Canadian
Securities Administrators.

About Sama Resources Inc.

Sama is a Canadian-based mineral exploration and development
company with projects in West Africa. Sama holds a control position in
SRG of 24,658,267 shares representing 36.17% of the issued and
outstanding shares of SRG and is considered an insider for reporting
purposes.

On October 23, 2017, Sama announced that it had entered into a
binding term sheet in view of forming a strategic partnership with HPX
TechCo Inc., for the development of its Cote d'Ivoire Nickel-Copper and
Cobalt project in Cote d'Ivoire, West-Africa. For more information
about Sama, please visit Sama's website at
http://www.samaresources.com.

FOR FURTHER INFORMATION, PLEASE

Contact Information:

CONTACT:

SAMA RESOURCES INC./RESSOURCES SAMA INC. Dr. Marc-Antoine Audet,
President and CEO Tel: (514) 726-4158 OR Mr. Matt Johnston, Corporate
Development Advisor Tel: (604) 443-3835 Toll Free: 1 (877) 792-6688,
Ext. 5

Neither the TSXV nor its Regulation Services Provider (as that
term is defined in the policies of the TSXV) accepts responsibility for
the adequacy or accuracy of this release.

FORWARD LOOKING STATEMENTS

Certain of the statements made and information contained herein
are "forward-looking statements" or "forward-looking information"
within the meaning of Canadian securities legislation. Forward-looking
statements and forward-looking information are subject to a variety of
risks and uncertainties, which could cause actual events or results to
differ from those reflected in the forward-looking statements or
forward-looking information, including, without limitation, the
availability of financing for activities, risks and uncertainties
relating to the interpretation of electrochemical characterization,
drill results and the estimation of mineral resources and reserves, the
geology, grade and continuity of mineral deposits, the possibility that
future exploration, development or mining results will not be
consistent with the Company's expectations, metal price fluctuations,
environmental and regulatory requirements, availability of permits,
escalating costs of remediation and mitigation, risk of title loss, the
effects of accidents, equipment breakdowns, labour disputes or other
unanticipated difficulties with or interruptions in exploration or
development, the potential for delays in exploration or development
activities, the inherent uncertainty of cost estimates and the
potential for unexpected costs and expenses, commodity price
fluctuations, currency fluctuations, expectations and beliefs of
management and other risks and uncertainties.

In addition, forward-looking statements and forward-looking
information are based on various assumptions.  Should one or more of
these risks and uncertainties materialize, or should underlying
assumptions prove incorrect, actual results may vary materially from
those described in forward-looking information or forward-looking
statements.  Accordingly, readers are advised not to place undue
reliance on forward-looking statements or forward-looking information.
Except as required under applicable securities legislation, the
Company undertakes no obligation to publicly update or revise
forward-looking statements or forward-looking information, whether as a
result of new information, future events or otherwise.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1815600026TS11815601234-06504720180606