Source	CANADA NEWSWIRE
Date	06/23/2020
Time	02:13:44 PM

Company	 Minsud Resources Corp.
Title	Minsud announces results of the scout-drilling program at the
Chinchillones Porphyry in the Chita Valley Project, San Juan, Argentina





    CDNX Symbol: MSR











Press Release




" BC-Minsud-Chinchillones   06-23 2017
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.166670:
^Minsud announces results of the scout-drilling program at the
Chinchillones Porphyry in the Chita Valley Project, San Juan, Argentina@

TSX-V: MSR
TORONTO, June 23, 2020 /CNW/ - Minsud Resources Corp. (TSXV: MSR)
("Minsud" or the "Company") is pleased to announce the results of the 6 hole,
3,559 meters scout drilling program completed at the Chinchillones Porphyry
and Epithermal Complex, part of the Chita Valley Project. The exploration
survey was based on the results of the geophysics carried out during December
2019, where a porphyry and epithermal anomalies were identified.
The objective was to determine the possible presence, as the geophysical
and conceptual models indicated, of a porphyry-type system below the Chita
Valley and of an epithermal target hosted in the lithocap cover.
The results of this exploration scout program and the revision of
historical drill results performed in the Chinchillones area, have provided
some intercepts that support the presence at shallow and at down depth level
of a Zn-Pb-Cu-(Ag-Au) polymetallic epithermal system.
Table 1 below highlights the main mineralized intersections near the
surface and in depth with highly anomalous Au-Ag-Cu-Mo-Pb-Zn. Two intrusive
phases have been recognized, a quartz-diorite, cut by an inter mineral dacite
porphyry, both affected by an intensely, widespread, quartz sericite
alteration. B and D porphyry style quartz veins forming strong stockwork, are
present in both lithologies.
Drill hole CHDH20-04 intercepts continuous 739.70 m of a diorite
porphyry. The diorite porphyry is cut by polymetallic epithermal veins and
hydrothermal phreatic breccias mineralized with pyrite, chalcopyrite,
sphalerite, galena and tenantite.
Evidences of secondary enrichment is represented by covelite-digenite in
a partial replacement of chalcopyrite. This mineralized style represents a
telescopic sequence of alteration-mineralization zones, from shallow argillic
and underlying quartz-sericite to deeper chlorite-sericite and minor remnant
potassic of a classic porphyry system type.


Table 1: Chinchillones Diamond Drilling Program - Summary of Analytical Results

---

Hole ID

From

To                  Length                       Au

Ag         Cu       Mo      Pb

Zn

---

(m)

(m)                      (m) ((x))                  g/t

g/t                        %         ppm      ppm     ppm

---

CHDH20-01                              34.00                        
94.00                  60.00                       0.04                       
1.05       0.16%      67       62         21

---

CHDH20-02                              16.00                        
45.00                  29.00                       0.16                      
15.15       0.19%      46      242        604



Incl.                                44.00                        
45.00                   1.00                       0.27                         
66       0.93%      46     2030       4910


86.00                       112.70                  26.70                       
0.37                      64.23       0.45%      69     1055       2847



Incl.                               98.00                       
100.00                   2.00                       1.07                        
262       2.16%      34     2978      14050


44.00                       220.00                 176.00                       
0.12                      16.18       0.17%     109      506       1711



Incl.                                52.00                       
160.00                 108.00                       0.15                      
21.37       0.20%      82      599       2034


87.00                       100.00                  13.00                       
0.42                      84.28       0.64%      44     1659       4300



CHDH20-03
Intercepts hydrothermal pyrite halo


CHDH20-04                              16.00                        
44.00                  28.00                       0.64                      
73.35       0.02%      22     1068        130



Incl.                                32.00                        
40.00                   8.00                       0.61                     
154.25       0.02%      34     2061        149


54.00                       581.50                 527.50                       
0.09                       8.49       0.09%      37     1177       3243



Incl.                                96.00                       
126.00                  30.00                       0.23                      
10.79       0.14%      54      723       3081


260.00                       406.00                 
146.00                       0.12                      12.03       0.09%      
40     1969       5044


634.00                       738.00                 
104.00                       0.02                       8.77       0.29%     
202     1111       3365



CHDH20-05                             154.00                       
174.00                  20.00                       0.13                       
9.43       0.22%      48       93       1534


169.70                       191.00                  
21.30                       0.21                         18       0.33%      
37       95       1325



Incl.                               169.70                       
174.00                   4.30                       0.29                       
35.2       0.63%      20      236       4721


178.00                       191.00                  
13.00                       0.22                      17.58       0.32%      
40       68        540


360.00                       364.00                   
4.00                       0.48                       4.03       0.03%      
28       71        558


581.35                       582.00                   
0.65                       0.21                        9.1       2.60%     
318       11        347



CHDH20-06                              96.00                        
97.00                   1.00                       0.96                      
56.80       1.32%       6     1345       4780

---


168.00                              170.00                         
2.00                   0.18                      12.40                      
0.12%          6      939     3520

---


((x)) Intervals reported in the above table are not true thicknesses
Historical drilling data in the Chinchillones area is shown in Table 2
below and it highlights the most significant intersections of Polymetallic
Au-Ag-Cu-Mo-Pb-Zn grades values.
These results support and are indicative of the high potential of the
polymetallic epithermal Au-Ag-Cu-Pb-Zn trend in the Chinchillones target and
its continuity to the East and Northeast.


Table 2: Chinchillones historical drilling data

---

Hole ID                            From                  To        
Length                           Au                      Ag            
Cu            Mo       Pb        Zn

---

(m)                              (m)                (m) ((x))        
g/t                            g/t                     %             
ppm           ppm      ppm

---

CHS-11-01                                70.00                  74.00         
4.00                           0.13                    12.9           
0.18%             4        50       218

---


119.00                                 142.00                  23.00         
0.02                          10.12                   0.20%              
8            671      2505



151.00                                 168.00                  17.00         
0.02                          19.17                   0.07%              
7           1444      7283

---

CHS-11-03                                12.00                  15.00         
3.00                              0                    3.51           
0.04%             5      1291      3188

---


21.00                                  24.00                   3.00            
0                           4.06                   0.01%             
10            642      1458



38.00                                  45.00                   7.00         
0.11                          14.13                   0.02%              
6           5193     13143



98.00                                 101.00                   3.00         
0.18                          37.47                   0.06%              
3           6479      8590

---

CHS-11-04                                15.00                  21.00         
6.00                           0.02                   16.31           
0.17%             5       258       340

---


35.00                                  45.00                  10.00         
0.02                           5.62                   0.04%              
6            504      1967



57.00                                  72.00                  15.00         
0.07                          30.12                   0.11%              
7            886      4159



125.00                                 130.00                   5.00         
0.26                          52.55                   0.33%              
3            327       807



135.00                                 168.00                  33.00         
0.05                          13.33                   0.05%              
3            605      2021

---

CHS-11-05                                81.00                 104.00        
23.00                           0.07                    8.51           
0.01%             3       546      5604



Incl.                                 100.00                 102.00         
2.00                           0.35                   41.04           
0.01%             3      1135     43658


108.00                 115.00         7.00                           
0.07                   13.53           0.01%             4      1351      4478


135.00                 146.00        11.00                           
0.13                    34.5           0.02%             3      4422     15187



MSA08-A                                 98.00                 129.00        
31.00                           0.01                    0.41           
0.11%           146        14       112

---


136.00                                 149.00                  13.00            
0                           0.06                   0.09%            
158             10       131



167.00                                 180.00                  13.00         
0.03                           1.66                   0.09%            
110             32       208



222.00                                 239.00                  17.00         
0.08                           0.53                   0.19%            
101             39       396



264.00                                 276.00                  12.00         
0.01                           0.07                   0.04%            
184             10       118

---

MSA08-C                                 21.00                  28.00         
7.00                           0.01                    3.24           
0.76%             4       365       307

---


31.00                                  80.00                  49.00         
0.07                          13.82                   0.05%             
16           1884      6960



87.00                                  91.00                   4.00         
0.04                           5.48                   0.01%              
6            230      1210



104.00                                 108.00                   4.00         
0.16                          94.08                   0.24%              
6           4204      5225



127.00                                 133.00                   6.00         
0.18                          90.01                   0.27%              
5           1126      2017



141.00                                 215.00                  74.00         
0.11                          43.83                   0.13%              
8           2565     10286



240.00                                 279.00                  39.00         
0.02                           5.74                   0.02%              
6           1289      4116

---

C-96-01                                 14.00                  22.00         
8.00                            0.1                    5.75           0.00%
No data         1784        61

---

66.00                                  78.00                  12.00         
0.11                           9.52                   0.35%
No data               1292      2557



126.00                                 142.00                  16.00         
0.09                          11.36                   0.08%
No data               1465      7763

---

C-96-02                                 56.00                  74.00        
18.00                           0.07                    4.07           0.03%
No data          882      2547



Incl.                                  56.00                  60.00         
4.00                            0.2                    12.7           0.10%
No data         3113      7230


108.00                 120.00        12.00                           
0.09                    4.52           0.02%
No data          635      2503


C-96-03                                110.00                 120.00        
10.00                           0.21                    6.24           0.65%
No data          146       250


C-96-04                                 32.00                  94.00        
62.00                           0.05                    4.39           0.01%
No data          907      2354



144.00                                 170.00                  26.00         
0.21                          13.38                   0.10%
No data               1707      6656



Incl.                                 160.00                 164.00         
4.00                           0.75                    49.8           0.53%
No data         5808     15056

---


((x)) Intervals reported in the above table are not true thicknesses
Conceptual Geological Model at Chinchillones
The Map 1 below, displays the extension of the polymetallic veins system
(in red lines) open to the East and Northeast configuring a namely "Linked
Area" between Chinchillones and Chita porphyry target that highlights untested
porphyry systems and epithermal polymetallic veins associated.
This recent fieldwork also highlights the potential for a porphyry and
epithermal system at shallow depths and suggests the presence of a long-lived
mineralization system open to the East and linked with the Chita Porphyry,
located 2 km to the East.
As cooling of the intrusive complex progressed at Chinchillones, the
structural and chemical character of the mineralizing environment changed
largely in response to the inflow of meteoric water, represented by near
vertical presence of type D veins and phreatic breccia.
With continued cooling, upper and peripheral zones of late alteration
process and mineralization progressively collapsed inward and downward over
zones of early mineralization, penetrating deeper along continuous vein
structures (East-West structural system) as it is seen at the north and south
border of the Chita valley.
In the last stages, an acid hot-spring sys

" BC-Minsud-Chinchillones   06-23 2017
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.166670:
^Minsud announces results of the scout-drilling program at the
Chinchillones Porphyry in the Chita Valley Project, San Juan, Argentina@

TSX-V: MSR
TORONTO, June 23, 2020 /CNW/ - Minsud Resources Corp. (TSXV: MSR)
("Minsud" or the "Company") is pleased to announce the results of the 6 hole,
3,559 meters scout drilling program completed at the Chinchillones Porphyry
and Epithermal Complex, part of the Chita Valley Project. The exploration
survey was based on the results of the geophysics carried out during December
2019, where a porphyry and epithermal anomalies were identified.
The objective was to determine the possible presence, as the geophysical
and conceptual models indicated, of a porphyry-type system below the Chita
Valley and of an epithermal target hosted in the lithocap cover.
The results of this exploration scout program and the revision of
historical drill results performed in the Chinchillones area, have provided
some intercepts that support the presence at shallow and at down depth level
of a Zn-Pb-Cu-(Ag-Au) polymetallic epithermal system.
Table 1 below highlights the main mineralized intersections near the
surface and in depth with highly anomalous Au-Ag-Cu-Mo-Pb-Zn. Two intrusive
phases have been recognized, a quartz-diorite, cut by an inter mineral dacite
porphyry, both affected by an intensely, widespread, quartz sericite
alteration. B and D porphyry style quartz veins forming strong stockwork, are
present in both lithologies.
Drill hole CHDH20-04 intercepts continuous 739.70 m of a diorite
porphyry. The diorite porphyry is cut by polymetallic epithermal veins and
hydrothermal phreatic breccias mineralized with pyrite, chalcopyrite,
sphalerite, galena and tenantite.
Evidences of secondary enrichment is represented by covelite-digenite in
a partial replacement of chalcopyrite. This mineralized style represents a
telescopic sequence of alteration-mineralization zones, from shallow argillic
and underlying quartz-sericite to deeper chlorite-sericite and minor remnant
potassic of a classic porphyry system type.


Table 1: Chinchillones Diamond Drilling Program - Summary of Analytical Results

---

Hole ID

From

To                  Length                       Au

Ag         Cu       Mo      Pb

Zn

---

(m)

(m)                      (m) ((x))                  g/t

g/t                        %         ppm      ppm     ppm

---

CHDH20-01                              34.00                        
94.00                  60.00                       0.04                       
1.05       0.16%      67       62         21

---

CHDH20-02                              16.00                        
45.00                  29.00                       0.16                      
15.15       0.19%      46      242        604



Incl.                                44.00                        
45.00                   1.00                       0.27                         
66       0.93%      46     2030       4910


86.00                       112.70                  26.70                       
0.37                      64.23       0.45%      69     1055       2847



Incl.                               98.00                       
100.00                   2.00                       1.07                        
262       2.16%      34     2978      14050


44.00                       220.00                 176.00                       
0.12                      16.18       0.17%     109      506       1711



Incl.                                52.00                       
160.00                 108.00                       0.15                      
21.37       0.20%      82      599       2034


87.00                       100.00                  13.00                       
0.42                      84.28       0.64%      44     1659       4300



CHDH20-03
Intercepts hydrothermal pyrite halo


CHDH20-04                              16.00                        
44.00                  28.00                       0.64                      
73.35       0.02%      22     1068        130



Incl.                                32.00                        
40.00                   8.00                       0.61                     
154.25       0.02%      34     2061        149


54.00                       581.50                 527.50                       
0.09                       8.49       0.09%      37     1177       3243



Incl.                                96.00                       
126.00                  30.00                       0.23                      
10.79       0.14%      54      723       3081


260.00                       406.00                 
146.00                       0.12                      12.03       0.09%      
40     1969       5044


634.00                       738.00                 
104.00                       0.02                       8.77       0.29%     
202     1111       3365



CHDH20-05                             154.00                       
174.00                  20.00                       0.13                       
9.43       0.22%      48       93       1534


169.70                       191.00                  
21.30                       0.21                         18       0.33%      
37       95       1325



Incl.                               169.70                       
174.00                   4.30                       0.29                       
35.2       0.63%      20      236       4721


178.00                       191.00                  
13.00                       0.22                      17.58       0.32%      
40       68        540


360.00                       364.00                   
4.00                       0.48                       4.03       0.03%      
28       71        558


581.35                       582.00                   
0.65                       0.21                        9.1       2.60%     
318       11        347



CHDH20-06                              96.00                        
97.00                   1.00                       0.96                      
56.80       1.32%       6     1345       4780

---


168.00                              170.00                         
2.00                   0.18                      12.40                      
0.12%          6      939     3520

---


((x)) Intervals reported in the above table are not true thicknesses
Historical drilling data in the Chinchillones area is shown in Table 2
below and it highlights the most significant intersections of Polymetallic
Au-Ag-Cu-Mo-Pb-Zn grades values.
These results support and are indicative of the high potential of the
polymetallic epithermal Au-Ag-Cu-Pb-Zn trend in the Chinchillones target and
its continuity to the East and Northeast.


Table 2: Chinchillones historical drilling data

---

Hole ID                            From                  To        
Length                           Au                      Ag            
Cu            Mo       Pb        Zn

---

(m)                              (m)                (m) ((x))        
g/t                            g/t                     %             
ppm           ppm      ppm

---

CHS-11-01                                70.00                  74.00         
4.00                           0.13                    12.9           
0.18%             4        50       218

---


119.00                                 142.00                  23.00         
0.02                          10.12                   0.20%              
8            671      2505



151.00                                 168.00                  17.00         
0.02                          19.17                   0.07%              
7           1444      7283

---

CHS-11-03                                12.00                  15.00         
3.00                              0                    3.51           
0.04%             5      1291      3188

---


21.00                                  24.00                   3.00            
0                           4.06                   0.01%             
10            642      1458



38.00                                  45.00                   7.00         
0.11                          14.13                   0.02%              
6           5193     13143



98.00                                 101.00                   3.00         
0.18                          37.47                   0.06%              
3           6479      8590

---

CHS-11-04                                15.00                  21.00         
6.00                           0.02                   16.31           
0.17%             5       258       340

---


35.00                                  45.00                  10.00         
0.02                           5.62                   0.04%              
6            504      1967



57.00                                  72.00                  15.00         
0.07                          30.12                   0.11%              
7            886      4159



125.00                                 130.00                   5.00         
0.26                          52.55                   0.33%              
3            327       807



135.00                                 168.00                  33.00         
0.05                          13.33                   0.05%              
3            605      2021

---

CHS-11-05                                81.00                 104.00        
23.00                           0.07                    8.51           
0.01%             3       546      5604



Incl.                                 100.00                 102.00         
2.00                           0.35                   41.04           
0.01%             3      1135     43658


108.00                 115.00         7.00                           
0.07                   13.53           0.01%             4      1351      4478


135.00                 146.00        11.00                           
0.13                    34.5           0.02%             3      4422     15187



MSA08-A                                 98.00                 129.00        
31.00                           0.01                    0.41           
0.11%           146        14       112

---


136.00                                 149.00                  13.00            
0                           0.06                   0.09%            
158             10       131



167.00                                 180.00                  13.00         
0.03                           1.66                   0.09%            
110             32       208



222.00                                 239.00                  17.00         
0.08                           0.53                   0.19%            
101             39       396



264.00                                 276.00                  12.00         
0.01                           0.07                   0.04%            
184             10       118

---

MSA08-C                                 21.00                  28.00         
7.00                           0.01                    3.24           
0.76%             4       365       307

---


31.00                                  80.00                  49.00         
0.07                          13.82                   0.05%             
16           1884      6960



87.00                                  91.00                   4.00         
0.04                           5.48                   0.01%              
6            230      1210



104.00                                 108.00                   4.00         
0.16                          94.08                   0.24%              
6           4204      5225



127.00                                 133.00                   6.00         
0.18                          90.01                   0.27%              
5           1126      2017



141.00                                 215.00                  74.00         
0.11                          43.83                   0.13%              
8           2565     10286



240.00                                 279.00                  39.00         
0.02                           5.74                   0.02%              
6           1289      4116

---

C-96-01                                 14.00                  22.00         
8.00                            0.1                    5.75           0.00%
No data         1784        61

---

66.00                                  78.00                  12.00         
0.11                           9.52                   0.35%
No data               1292      2557



126.00                                 142.00                  16.00         
0.09                          11.36                   0.08%
No data               1465      7763

---

C-96-02                                 56.00                  74.00        
18.00                           0.07                    4.07           0.03%
No data          882      2547



Incl.                                  56.00                  60.00         
4.00                            0.2                    12.7           0.10%
No data         3113      7230


108.00                 120.00        12.00                           
0.09                    4.52           0.02%
No data          635      2503


C-96-03                                110.00                 120.00        
10.00                           0.21                    6.24           0.65%
No data          146       250


C-96-04                                 32.00                  94.00        
62.00                           0.05                    4.39           0.01%
No data          907      2354



144.00                                 170.00                  26.00         
0.21                          13.38                   0.10%
No data               1707      6656



Incl.                                 160.00                 164.00         
4.00                           0.75                    49.8           0.53%
No data         5808     15056

---


((x)) Intervals reported in the above table are not true thicknesses
Conceptual Geological Model at Chinchillones
The Map 1 below, displays the extension of the polymetallic veins system
(in red lines) open to the East and Northeast configuring a namely "Linked
Area" between Chinchillones and Chita porphyry target that highlights untested
porphyry systems and epithermal polymetallic veins associated.
This recent fieldwork also highlights the potential for a porphyry and
epithermal system at shallow depths and suggests the presence of a long-lived
mineralization system open to the East and linked with the Chita Porphyry,
located 2 km to the East.
As cooling of the intrusive complex progressed at Chinchillones, the
structural and chemical character of the mineralizing environment changed
largely in response to the inflow of meteoric water, represented by near
vertical presence of type D veins and phreatic breccia.
With continued cooling, upper and peripheral zones of late alteration
process and mineralization progressively collapsed inward and downward over
zones of early mineralization, penetrating deeper along continuous vein
structures (East-West structural system) as it is seen at the north and south
border of the Chita valley.
In the last stages, an acid hot-spring system was established in the
upper portions of the deposit (Phreatic Breccia at Chinchillones). Finally, a
relatively minor intrusion of late dacite dikes into this hot-spring system
caused brecciation and mineralization. This sequence can be observed in drill
hole CHDH20-02, where banded quartz veins with anomalous values of Au-Ag have
been identified.
Map 2 shows the relationship, along the East-West Chita Valley, of West
Chinchillones Project, Central link area project and the outcropping Chita
Porphyry to the East.
Quality Assurance/Quality Control
Diamond drill core was sampled as half core at two meters intervals and
check samples were submitted to the ALS Minerals Laboratory in Mendoza,
Argentina for preparation and analysis. ALS is certified to ISO-9001
international standards. All samples were analyzed for Au by fire assay/ AA
finish, 50 plus a 33-element ICP scan. Minsud has followed all industry
standard procedures for the work with a quality assurance/quality control
(QA/QC) program including the systematic utilization of certified reference
materials, blanks, field duplicates and check assays. Field duplicates,
standards and blanks were included with all sample shipments to the principal
laboratory.
Minsud's VP-Exploration, Dr. Mario Alfaro, conducted site visits and
detected no significant QA/QC issues during review of the data. Mr. Mario
Alfaro, Professional Geoscientist and a geological consultant, is a qualified
person as defined by Canadian National Instrument 43-101. Mr. Alfaro visited
the property and has read and approved the contents of this release.
About Minsud Resources Corp.
Minsud is a mineral exploration company focused on exploring its flagship
Chita Valley Cu-Mo- Au-Ag Project, in the Province of San Juan, Argentina. On
March 26, 2018, Minsud filed a National Instrument 43-101 ("NI 43-101")
Technical Report and updated Mineral Resource Estimate on the Chita South
Porphyry Deposit. The Mineral Resource Estimate considers copper as a primary
consideration along with molybdenum, gold and silver mineralization. The
latest estimate includes Indicated Resources of 33.02 million tonnes at a
grade of 0.43% Cu, 0.07 g/t Au. 2.28 g/t Ag and 0.018% Mo and Inferred
Resources of 8.59 million tonnes at a grade of 0.40% Cu, 0.07 g/t Au. 1.73 g/t
Ag and 0.016% Mo.
The Company also holds a 100% owned portfolio of selected early stage
prospects, including 6,000 ha in Santa Cruz Province, Argentina.
CAUTIONARY STATEMENT REGARDING FORWARD-LOOKING INFORMATION:
This news release includes certain information that may constitute
forward-looking information under applicable Canadian securities laws.
Forward-looking information includes, but is not limited to, statements about
strategic plans, spending commitments, future operations, results of
exploration, anticipated financial results, future work programs, capital
expenditures and objectives. Forward-looking information is necessarily based
upon a number of estimates and assumptions that, while considered reasonable,
are subject to known and unknown risks, uncertainties, and other factors which
may cause the actual results and future events to differ materially from those
expressed or implied by such forward-looking information including, but not
limited to: fluctuations in the currency markets (such as the Canadian dollar,
Argentina peso, and the U.S. dollar); changes in national and local
government, legislation, taxation, controls, regulations and political or
economic developments in Canada and Argentina or other countries in which the
Corporation may carry on business in the future; operating or technical
difficulties in connection with exploration and development activities; risks
and hazards associated with the business of mineral exploration and
development (including environmental hazards or industrial accidents); risks
relating to the credit worthiness or financial condition of suppliers and
other parties with whom the Company does business; presence of laws and
regulations that may impose restrictions on mining, including those currently
enacted in Argentina; employee relations; relationships with and claims by
local communities; availability and increasing costs associated with
operational inputs and labour; the speculative nature of mineral exploration
and development, including the risks of obtaining necessary licenses, permits
and approvals from government authorities; business opportunities that may be
presented to, or pursued by, the Company; challenges to, or difficulty in
maintaining, the Company's title to properties; risks relating to the
Company's ability to raise funds; and the factors identified under "Risk
Factors" in the Company's Filing Statement dated April 27, 2011. There can be
no assurance that such information will prove to be accurate, as actual
results and future events could differ materially from those anticipated in
such information. Accordingly, readers should not place undue reliance on
forward-looking information. All forward-looking-information contained in this
news release is given as of the date hereof and is based upon the opinions and
estimates of management and information available to management as at the date
hereof. The Company disclaims any intention or obligation to update or revise
any forward-looking information, whether as a result of new information,
future events or otherwise, except as required by law.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Minsud Resources Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/June2020/23/c4167.html

-0-                           06/23/2020
/For further information: Alberto F. Orcoyen, President and Chief
Executive Officer, info(at)minsud.com; Ramiro Massa, Controller and Corporate
Secretary, rmassa(at)minsud.com/
/Web Site: www.minsud.com/ /
(MSR.)

CO:  Minsud Resources Corp.
ST:  Ontario
IN:  MNG
SU:

-30-