Source	CANADA NEWSWIRE
Date	05/11/2021
Time	06:02:14 AM

Company	 Defense Metals Corp.
Title	Defense Metals Provides Pre-Pilot Hydrometallurgy Update, Achieves High
Rare Earth Extraction And Impurity Removal From Wicheeda Flotation
Concentrate





    CDNX Symbol: DEFN











Press Release




" BC-DefenseMetals-update   05-11 1322
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.375518:
^Defense Metals Provides Pre-Pilot Hydrometallurgy Update, Achieves High
Rare Earth Extraction And Impurity Removal From Wicheeda Flotation
Concentrate@

VANCOUVER, BC, May 11, 2021 /CNW/ - Defense Metals Corp. ("Defense
Metals" or the "Company") (TSXV: DEFN) (OTCQB: DFMTF) (FSE: 35D) is pleased to
provide an update regarding its ongoing pre-pilot hydrometallurgical test work
utilizing high-grade rare earth element (REE) mineral concentrate produced
during the Company's highly successful 26-tonne flotation pilot-plant that
yielded a mineral concentrate averaging 7.4% NdPr oxide
(neodymium-praseodymium)1.
The road accessible Wicheeda REE Property is located close to
infrastructure approximately 80 kilometres northeast of Prince George, British
Columbia (BC). The Wicheeda project has indicated mineral resources of
4,890,000 tonnes averaging 3.02% LREO (Light Rare Earth Elements) and inferred
mineral resources of 12,100,000 tonnes averaging 2.90% LREO2.
Highlights of ongoing infill hydrometallurgical test results, which
centred around optimizing caustic crack-acid leach conditions, and leach
liquor impurity removal conducted at SGS Canada Inc. ("SGS") Lakefield,
Ontario Site are as follows:
<<

--  High REE extraction (using neodymium as a proxy, Figure 1) for base case
bench and bulk (3 kg) caustic crack across the range of test conditions
in comparison to initial 2019/2020 bench test work (see Defense Metals
News Release dated February 16, 2021).
--  Comparable REE extraction via direct crack of mineral concentrate shows
promise with calculated neodymium extraction within a 5% range of the
base case.
--  The success of direct crack test results opens up the potential of
future optimization work to reduce circuit complexity though potential
elimination of gangue leaching and associated solid-liquid separation
steps.
--  Primary impurity removal tests on leach liquor at terminal pH yield very
efficient Th and Fe removal (>99% Th and >95% Fe) at negligible Nd
losses (Figure 2).
<>>
Ongoing hydrometallurgical optimisation test work being conducted at SGS
Lakefield is expected to be completed over the next 4-6 weeks resulting in
finalization of a base-case flowsheet to inform operation of a future
hydrometallurgical pilot plant. Final test work is expected to focus on
secondary impurity removal and the production of a purified mixed REE
precipitate and on the regeneration of hydrochloric acid.

_____________


(1) See Defense Metals News Release dated
September 23, 2020


(2) Technical Report on the Wicheeda
Property, British Columbia, effective
June 27, 2020 and prepared by APEX
Geoscience Ltd. (Steven J. Nicholls, B.A.
Sc., MAIG and Kristopher J. Raffle,
B.Sc., P.Geo.) is available under Defense
Metals Corp.'s profile on SEDAR
(www.sedar.com)
Craig Taylor, CEO of Defense Metals, stated: "Defense Metals continues to
be extremely pleased with its ongoing pre-pilot hydrometallurgical test work
campaign. These latest results establish that stable REE extractions are
achievable across a range of test conditions bracketing our emerging base case
flowsheet. Significantly, direct crack REE extractions were similarly high
opening up the door for potential circuit complexity and future capital cost
reductions. Primary impurity removal test show that at the bench scale we can
produce a high quality REE leach liquor suitable for conversion to mixed REE
oxide end product."
About the Wicheeda REE Property
The 1,708 hectare Wicheeda REE Property, located approximately 80 km
northeast of the city of Prince George, British Columbia, is readily
accessible by all-weather gravel roads and is nearby to infrastructure,
including power transmission lines, the CN railway and major highways.
Geologically, the property is situated in the Foreland Belt and within
the Rocky Mountain Trench, a major continental geologic feature. The Foreland
Belt contains part of a large alkaline igneous province, stretching from the
Canadian Cordillera to the southwestern United States, which includes several
carbonatite and alkaline intrusive complexes hosting the Aley (niobium), Rock
Canyon (REE), and Wicheeda (REE) deposits.
Qualified Person
The scientific and technical information contained in this news release
as it relates to the Wicheeda REE Property has been reviewed and approved by
Kristopher J. Raffle, P.Geo. (BC) Principal and Consultant of APEX Geoscience
Ltd. of Edmonton, AB, a director of Defense Metals and a "Qualified Person" as
defined in National Instrument 43-101 - Standards of Disclosure for Mineral
Projects. Mr. Raffle verified the data disclosed which includes a review of
the analytical and test data underlying the information and opinions contained
therein.
Methodology and QA/QC
Hydrometallurgical product assays for neodymium was determined via
lithium-borate fusion of a 0.5-gram sample analyzed via wavelength dispersion
X-ray fluorescence (WD-XRF). The remaining rare earth elements for the head
sample were determined via 0.5-gram sodium-peroxide fusion multi-element
ICP-MS.
The SGS analyses included a quality assurance / quality control (QA/QC)
program including the insertion of rare earth element standard and blank
samples. Defense Metals detected no significant QA/QC issues during review of
the data. Defense Metals is not aware of any drilling, sampling, recovery or
other factors that could materially affect the accuracy or reliability of the
data referred to herein. SGS is an ISO/IEC 17025 and ISO9001:2015 accredited
laboratory. SGS is independent of Defense Metals Corp.
About Defense Metals Corp.
Defense Metals Corp. is a mineral exploration company focused on the
acquisition of mineral deposits containing metals and elements commonly used
in the electric power market, military, national security and the production
of "GREEN" energy technologies, such as, high strength alloys and rare earth
magnets. Defense Metals has an option to acquire 100% of the 1,708 hectare
Wicheeda Rare Earth Element Property located near Prince George, British
Columbia, Canada. Defense Metals Corp. trades in Canada under the symbol
"DEFN" on the TSX Venture Exchange, in the United States, under "DFMTF" on the
OTCQB and in Germany on the Frankfurt Exchange under "35D".
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release.
Cautionary Statement Regarding "Forward-Looking" Information
This news release contains "forward-looking information or statements"
within the meaning of applicable securities laws, which may include, without
limitation, statements relating to the ongoing optimization test work and the
expected outcomes, operation of a future hydrometallurgical pilot plant, plans
for its Wicheeda Property, the advancement and development of the Wicheeda
Property, the technical, financial and business prospects of the Company, its
project and other matters. All statements in this news release, other than
statements of historical facts, that address events or developments that the
Company expects to occur, are forward-looking statements. Although the Company
believes the expectations expressed in such forward-looking statements are
based on reasonable assumptions, such statements are not guarantees of future
performance and actual results may differ materially from those in the
forward-looking statements. Such statements and information are based on
numerous assumptions regarding present and future business strategies and the
environment in which the Company will operate in the future, including the
price of rare earth elements, the ability to achieve its goals, that general
business and economic conditions will not change in a material adverse manner,
that financing will be available if and when needed and on reasonable terms.
Such forward-looking information reflects the Company's views with respect to
future events and is subject to risks, uncertainties and assumptions,
including those filed under the Company's profile on SEDAR at www.sedar.com.
While such estimates and assumptions are considered reasonable by the
management of the Company, they are inherently subject to significant
business, economic, competitive and regulatory uncertainties and risks.
Factors that could cause actual results to differ materially from those in
forward looking statements include, but are not limited to, continued
availability of capital and financing and general economic, market or business
conditions, adverse weather conditions, failure to maintain or obtain all
necessary government permits, approvals and authorizations, failure to
maintain community acceptance (including First Nations), decrease in the price
of rare earth elements, the impact of Covid-19 or other viruses and diseases
on the Company's ability to operate, increase in costs, litigation, and
failure of counterparties to perform their contractual obligations. The
Company does not undertake to update forward-looking statements or
forward-looking information, except as required by law.
View original content to download
multimedia:http://www.prnewswire.com/news-releases/defense-metals-provides-pre
-pilot-hydrometallurgy-update-achieves-high-rare-earth-extraction-and-impurity
-removal-from-wicheeda-flotation-concentrate-301288591.html
SOURCE Defense Metals Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/May2021/11/c6038.html

-0-                           05/11/2021
/For further information: Todd Hanas, Bluesky Corporate Communications
Ltd., Vice President, Investor Relations, Tel: (778) 994 8072, Email:
todd(at)blueskycorp.ca/
(DFMTF DEFN. 35D)

CO:  Defense Metals Corp.
ST:  British Columbia
IN:  MNG MIN OTC
SU:

-30-