Source	CANADA NEWSWIRE
Date	05/17/2021
Time	04:33:15 AM

Company	 Trillium Gold Mines Inc.
Title	Trillium Gold Extends the NT Zone with Visible Gold and Continued High
Grade Gold Intercepts





    CDNX Symbol: TGM











Press Release




" BC-Trillium-NT-Zone   05-17 2278
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.573686:
^Trillium Gold Extends the NT Zone with Visible Gold and Continued High
Grade Gold Intercepts@

<<

--  Assays for the next six holes at the NT Zone returned values up to 66.40
g/t Au over 1.0 metre
--  Other significant intercepts include 39.95 g/t Au over 0.6 metres, 5.84
g/t Au over 2.65 metres and 10.1 g/t Au over 0.7 metres
--  Confirmation and extension of the NT Zone an additional 150 metres to
the southwest
--  A series of fan holes within the NT structure nearing completion,
testing model to target higher grade shoots
>>
VANCOUVER, BC, May 17, 2021 /CNW/ - Trillium Gold Mines Inc. (TSXV: TGM)
(OTCQX: TGLDF) (FRA: 0702) ("Trillium" or the "Company") reports the results
from the next six drill holes in sequence from the 2021 drill program on the
Newman Todd Zone (NT Zone) at its flagship Newman Todd Property in Red Lake,
Ontario. The NT Zone is a 2.2 km long structural target situated 26 km from
Evolution Mining's Red Lake Operations.
These six drill holes (Figure 1) span the southern half of the NT Zone,
testing the gap in historical drilling under Abate Lake to further testing its
southwestern extents. These six holes (NT21-181 to 184 and RV21-26 & 27
totalling 3,436 metres) have now received complete and verified assays
bringing total reported drilling at Newman Todd in 2020 and 2021 to 10,505
metres in 24 drill holes. More drilling has been completed and will be
released as assays are received and verified.
"These recent drilling results have only begun to unlock the high grade
potential of gold mineralization at Newman Todd, particularly in the gap
underlying Abate Lake which was never previously drilled as well as deeper
along the footwall contact and extending to the southwest. Further drilling in
the southwest is revealing a structural corridor where the NT Zone has been
dislocated but still present. The significant intercepts encountered here all
indicate that the potential for infill drilling and expanding the
mineralization along strike and at depth continues to be promising and that
high grade gold permeates the entire NT structure. We have also seen the NT
Zone in recently exposed outcrops in this same area," stated Bill Paterson,
Trillium Gold's Vice President of Exploration.
Russell Starr, CEO of Trillium Gold commented, "We have now received the
bulk of the assays that were back-logged at the lab since early January and
are on the way to delivering a much more robust exploration model that will
positively impact the importance of the NT Zone as the next open-pittable
deposit in Red Lake with potential for more high grade mineralization at
depth. We are consistently encountering significant high grade gold results,
often accompanied by visible gold at surface, which is validating our
understanding of the structural and veining controls over the high grade
mineralization at the NT Zone."
Hole NT21-181 (Figure 3) was targeted to begin filling in the large
wedge-shaped gap in historical drilling under Abate Lake in the vicinity of
the Hinge Zone Fault. This hole was designed to test the NT Zone down to 650m
depth. The hole intersected the NT Zone from 264.5m depth, encountering
several mineralized breccia zones to 640.2m depth. VG was seen in a 5 mm
quartz vein in the 638.7-639m interval, a new intercept likely associated with
the lower mineralization zones intersected previously northeast and southwest
of this hole, thereby likely expanding the known resource at depth in this
area. The significant intercepts of 1.5m (at) 23.33 g/t Au from 433m, 0.6m (at)
39.95 g/t Au from 498.4m and 2.65m (at) 5.84 g/t Au from 636.85m indicate the
upside in filling in the drilling gap and expanding on the mineralization
downward, and that high grades are still present.
NT21-182 (Figure 4) was drilled in the opposite direction to the majority
of the drilling, following up to the northeast on the VG intersection in
NT20-175 near the collar of the hole. The drill hole collared in the same
limestone / carbonate breccia unit as in NT20-175 hole 60m southwest along
strike. While no similar silicified unit was logged in NT21-182, there were
still several mineralized intervals in this hole up to 0.43m (at) 4.65 g/t Au
from 175.9m.
NT21-183 (Figure 5) was drilled in similar fashion to NT21-182 except
approximately 60m to the southwest of NT20-175. Deep overburden was
encountered in this hole (70.9m) with the target breccia zone encountered from
86.36 to 95.17 metres depth. Weak gold mineralization was encountered here.
Further hanging wall units were intersected, including weak silica-sulphide
breccia zones to the upper NT Zone contact at 264.6m. NT Zone silica-carbonate
breccia was encountered to 288.6m followed by several patchy zones of
silica-sulphide breccia to 383.8m where the footwall contact of the NT Zone
was crossed. VG was noted at 344.5-346.6m in two 5mm quartz veins and
associated with fine acicular arsenopyrite and assayed 0.3m (at) 5.1 g/t from
346.28m. The lower assay for this interval can be explained by the typically
nuggetty nature in Red Lake mineralization.
NT21-184 (Figure 6) was a steeply-dipping hole designed to expand on
mineralization in the southwest NT Zone. Significant intercepts from this hole
include 1m (at) 66.4 g/t Au from 169m and 0.75m (at) 6.21 g/t Au from 406.15m
despite the absence of VG associated with the former. The hole collared in the
north band of the NT Zone in this area drilling 18.5m thereof. After an
interval of the usual felsic tuff footwall rocks, the hole again encountered
mainly NT Zone breccias, with minor intervening units of massive to sheared
felsic tuffs, from 106.15m to 645.3m. More felsic tuffs were encountered to
698m and the hole was discontinued for a later date in that the hanging wall
contact was never reached.
RV21-26 (Figure 7) was collared on the Rivard property and targeted the
projected southwest extension of the north band of the NT Zone. Significant
mineralization was noted sporadically over much of the hole length with a best
assay of 0.7m (at) 10.1 g/t Au from 463m. The hole collared in the NT Zone and
intersected weak sulphide mineralized silica-carbonate breccia and
stromatolite banded sections in the first 50m of the hole. This was followed
by moderately mineralized silica-sulphide-magnetic breccia bands and
silica-sulphide breccia bands. The hole ended in felsic tuff and based on the
NT Zone intersection at the collar, a second hole on section, RV21-27, was
planned.
RV21-27 (Figure 7) is in follow up to hole RV21-26, which it collared
behind and drilled below. The hole started in felsic tuff, and entered the
north band of the NT Zone at 160.48m and remained therein until 435.4m,
intersecting multiple sections of weak to moderately mineralized
silica-sulphide-magnetite breccia. The south band of the NT Zone was
intersected at 459.3m and the hole stayed in the Zone until 481.24m. From
there to 723.8m the hole intersected felsic tuffs with a best assay of 1m (at)
6.89 g/t Au from 556m. From 723.8m to the end of the hole at 728.0m, the hole
intersected quartz veining/silica breccia as well as cherty metasediments that
may be the hanging wall units of the NT Zone. The hole stopped in
mineralization and it is planned to be deepened in the future to test further
at depth.
These three southerly holes encountered non-traditional stratigraphy (but
the same rock types) showing that the NT Zone in this area is more complex
than previously understood. It has bifurcated and a prominent east-west
structural corridor is evident in magnetic surveys where the NT Zone has been
de-magnetized. Our drilling has confirmed the presence of the mineralized
breccias but more drilling is required to further model the structural
complexity of this area.
New significant assay composite results are compiled in Table 1 below.
Table 1: Newman Todd significant assay composite results.


Hole ID  From (m ) To (m)  Width (m)   Au (g/t)

---


NT21-181                  6    16.5        10.5        1.47

---


NT21-181              150.5  151.27        0.77        1.79

---


NT21-181                263  264.25        1.25        3.31

---


NT21-181              273.4   274.1         0.7        1.78

---


NT21-181                284     285           1        3.11

---


NT21-181                296     298           2        2.91

---


NT21-181              319.9   321.1         1.2        1.95

---


NT21-181                364  365.45        1.45        1.27

---


NT21-181                403     404           1        2.11

---


NT21-181                407     408           1        2.69

---


NT21-181              427.2     428         0.8        1.82

---


NT21-181                433   434.5         1.5       23.33

---


NT21-181                444     448           4        2.27

---


NT21-181                452     453           1        1.07

---


NT21-181              498.4     499         0.6       39.95

---


NT21-181                575     576           1        1.35

---


NT21-181              596.3   597.5         1.2        2.30

---


NT21-181                618     619           1        0.98

---


NT21-181              622.6   623.3         0.7        4.99

---

NT21-181    636.85   639.5        2.65        5.84

---


NT21-182                 62      64           2        1.97

---


NT21-182                 66      67           1        1.41

---


NT21-182                104     105           1        1.05

---


NT21-182             112.75  113.65         0.9        1.97

---


NT21-182              175.9  176.33        0.43        4.65

---


NT21-182                247     248           1        1.17

---


NT21-182                296     297           1        1.72

---


NT21-182                320     321           1        2.38

---


NT21-183                 75      76           1        1.48

---


NT21-183                 84      85           1        1.42

---


NT21-183                 94   94.75        0.75        1.46

---


NT21-183              130.5   131.3         0.8        1.62

---


NT21-183             151.25  152.25           1        2.83

---


NT21-183                311     312           1        1.27

---


NT21-183             314.85   315.7        0.85        1.60

---

NT21-183    346.28  346.58         0.3        5.10

---


NT21-184              21.65      23        1.35        2.42

---


NT21-184                123     124           1        1.00

---


NT21-184                157     159           2        2.21

---


NT21-184                169     170           1       66.40

---


NT21-184                180     181           1        1.64

---


NT21-184                239     240           1        1.04

---


NT21-184                378     379           1        1.59

---


NT21-184             396.75  397.65         0.9        1.16

---


NT21-184             406.15   406.9        0.75        6.21

---


NT21-184                448  448.65        0.65        2.13

---


NT21-184              537.9   538.9        1.00        1.09

---


RV21-26               26.25      27        0.75        3.97

---


RV21-26                34.1      36         1.9        3.04

---


RV21-26                  66    66.8         0.8        2.23

---


RV21-26                 373     374           1        1.10

---


RV21-26                 463   463.7         0.7       10.10

---


RV21-27                 307     308           1        1.36

---


RV21-27                 336     337           1        1.09

---


RV21-27                 386     387           1        1.00

---


RV21-27                 556     557           1        6.89

---
All widths are down-core
lengths. Not enough
information has been
collected to determine true
widths. Bolded intervals
contain visible gold.
Table 2: Table of drillhole location details for holes reported in the
current press release.
Hole ID Easting (m E)

Northing (m N)  Elevation (m)   Length (m)    Dip     Azimuth

---

NT21-181                420527             5656485             363           
737     -62         135

---

NT21-182                420361             5655854             365           
359     -70         315

---

NT21-183                420287             5655764             355           
404     -70         315

---

NT21-184                420132             5655970             364           
698     -70         135

---

RV21-26                 419909             5655887             389           
510     -45         135

---

RV21-27                 419876             5655929             389           
728     -54         135

---
Prior drilling on the NT Zone from 2013 and earlier had mostly focused on
testing the Zone by targeting the footwall with drilling toward the southeast,
now known to be sub-parallel to gold mineralized veining and structures,
potentially missing high-grade intersections or undercutting much of the
targeted zone. Newman Todd is a highly prospective target with 41% of the 165
historic drill holes having intervals of greater than 20 g/t gold over various
lengths. In addition, nearly all drilling has been conducted to depths of less
than 400 metres.
The Red Lake Camp is famously known for high grade gold mineralization at
depth, with Evolution Mining's Red Lake Gold Mine currently reaching depths of
several thousand feet. Trillium will continue to test various drill
orientations in order to develop a comprehensive understanding of the
mineralization and structural controls and test the depth potential of the
Newman Todd Zone. Figure 2 below shows the location of the Newman Todd 
Projectas well as its relative location to the nearby past producing mines 
within the
Red Lake Camp.
All drilling was supervised by Paul Barc, PGeo. The drilling was
conducted by Rodren Drilling Ltd., of West St. Paul, Manitoba. Drill core was
logged and sampled in a secure core facility on site. Core samples from the
program were cut in half, using a diamond cutting saw, and half cores were
sent for analysis to the SGS Laboratory in Red Lake, ON, and Burnaby, BC and
Activation Laboratories Ltd. in Dryden and Thunder Bay, ON, all accredited
mineral analysis laboratories. All samples were analysed for gold using
standard Fire Assay-AA techniques. Samples returning over 10.0 g/t gold were
analyzed utilizing standard Fire Assay-Gravimetric methods. Selected samples
with results greater than one ounce per ton gold were also analyzed with a
standard 1 kg metallic screen fire assay. Certified gold reference standards,
blanks and duplicates are routinely inserted into the sample stream, as part
of Trillium Gold's quality control/quality assurance program (QAQC) to monitor
accuracy and precision. No QAQC issues were noted with the results reported
herein. All drill intercepts reported are down-hole core lengths, which does
not necessarily represent true widths.
The technical information presented in this news release has been
reviewed and approved by William Paterson QP, PGeo, VP of Exploration of
Trillium Gold Mines., as defined by NI 43-101.
Visit our website at www.trilliumgold.com.
On behalf of the Board of Directors,
Trillium Gold Mines Inc.
"Russell Starr"
Russell StarrPresident, CEO and Director
About Trillium Gold Mines Inc. Trillium Gold Mines Inc. is a growth
focused company engaged in the business of acquisition, exploration and
develo

" BC-Trillium-NT-Zone   05-17 2278
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.573686:
^Trillium Gold Extends the NT Zone with Visible Gold and Continued High
Grade Gold Intercepts@

<<

--  Assays for the next six holes at the NT Zone returned values up to 66.40
g/t Au over 1.0 metre
--  Other significant intercepts include 39.95 g/t Au over 0.6 metres, 5.84
g/t Au over 2.65 metres and 10.1 g/t Au over 0.7 metres
--  Confirmation and extension of the NT Zone an additional 150 metres to
the southwest
--  A series of fan holes within the NT structure nearing completion,
testing model to target higher grade shoots
>>
VANCOUVER, BC, May 17, 2021 /CNW/ - Trillium Gold Mines Inc. (TSXV: TGM)
(OTCQX: TGLDF) (FRA: 0702) ("Trillium" or the "Company") reports the results
from the next six drill holes in sequence from the 2021 drill program on the
Newman Todd Zone (NT Zone) at its flagship Newman Todd Property in Red Lake,
Ontario. The NT Zone is a 2.2 km long structural target situated 26 km from
Evolution Mining's Red Lake Operations.
These six drill holes (Figure 1) span the southern half of the NT Zone,
testing the gap in historical drilling under Abate Lake to further testing its
southwestern extents. These six holes (NT21-181 to 184 and RV21-26 & 27
totalling 3,436 metres) have now received complete and verified assays
bringing total reported drilling at Newman Todd in 2020 and 2021 to 10,505
metres in 24 drill holes. More drilling has been completed and will be
released as assays are received and verified.
"These recent drilling results have only begun to unlock the high grade
potential of gold mineralization at Newman Todd, particularly in the gap
underlying Abate Lake which was never previously drilled as well as deeper
along the footwall contact and extending to the southwest. Further drilling in
the southwest is revealing a structural corridor where the NT Zone has been
dislocated but still present. The significant intercepts encountered here all
indicate that the potential for infill drilling and expanding the
mineralization along strike and at depth continues to be promising and that
high grade gold permeates the entire NT structure. We have also seen the NT
Zone in recently exposed outcrops in this same area," stated Bill Paterson,
Trillium Gold's Vice President of Exploration.
Russell Starr, CEO of Trillium Gold commented, "We have now received the
bulk of the assays that were back-logged at the lab since early January and
are on the way to delivering a much more robust exploration model that will
positively impact the importance of the NT Zone as the next open-pittable
deposit in Red Lake with potential for more high grade mineralization at
depth. We are consistently encountering significant high grade gold results,
often accompanied by visible gold at surface, which is validating our
understanding of the structural and veining controls over the high grade
mineralization at the NT Zone."
Hole NT21-181 (Figure 3) was targeted to begin filling in the large
wedge-shaped gap in historical drilling under Abate Lake in the vicinity of
the Hinge Zone Fault. This hole was designed to test the NT Zone down to 650m
depth. The hole intersected the NT Zone from 264.5m depth, encountering
several mineralized breccia zones to 640.2m depth. VG was seen in a 5 mm
quartz vein in the 638.7-639m interval, a new intercept likely associated with
the lower mineralization zones intersected previously northeast and southwest
of this hole, thereby likely expanding the known resource at depth in this
area. The significant intercepts of 1.5m (at) 23.33 g/t Au from 433m, 0.6m (at)
39.95 g/t Au from 498.4m and 2.65m (at) 5.84 g/t Au from 636.85m indicate the
upside in filling in the drilling gap and expanding on the mineralization
downward, and that high grades are still present.
NT21-182 (Figure 4) was drilled in the opposite direction to the majority
of the drilling, following up to the northeast on the VG intersection in
NT20-175 near the collar of the hole. The drill hole collared in the same
limestone / carbonate breccia unit as in NT20-175 hole 60m southwest along
strike. While no similar silicified unit was logged in NT21-182, there were
still several mineralized intervals in this hole up to 0.43m (at) 4.65 g/t Au
from 175.9m.
NT21-183 (Figure 5) was drilled in similar fashion to NT21-182 except
approximately 60m to the southwest of NT20-175. Deep overburden was
encountered in this hole (70.9m) with the target breccia zone encountered from
86.36 to 95.17 metres depth. Weak gold mineralization was encountered here.
Further hanging wall units were intersected, including weak silica-sulphide
breccia zones to the upper NT Zone contact at 264.6m. NT Zone silica-carbonate
breccia was encountered to 288.6m followed by several patchy zones of
silica-sulphide breccia to 383.8m where the footwall contact of the NT Zone
was crossed. VG was noted at 344.5-346.6m in two 5mm quartz veins and
associated with fine acicular arsenopyrite and assayed 0.3m (at) 5.1 g/t from
346.28m. The lower assay for this interval can be explained by the typically
nuggetty nature in Red Lake mineralization.
NT21-184 (Figure 6) was a steeply-dipping hole designed to expand on
mineralization in the southwest NT Zone. Significant intercepts from this hole
include 1m (at) 66.4 g/t Au from 169m and 0.75m (at) 6.21 g/t Au from 406.15m
despite the absence of VG associated with the former. The hole collared in the
north band of the NT Zone in this area drilling 18.5m thereof. After an
interval of the usual felsic tuff footwall rocks, the hole again encountered
mainly NT Zone breccias, with minor intervening units of massive to sheared
felsic tuffs, from 106.15m to 645.3m. More felsic tuffs were encountered to
698m and the hole was discontinued for a later date in that the hanging wall
contact was never reached.
RV21-26 (Figure 7) was collared on the Rivard property and targeted the
projected southwest extension of the north band of the NT Zone. Significant
mineralization was noted sporadically over much of the hole length with a best
assay of 0.7m (at) 10.1 g/t Au from 463m. The hole collared in the NT Zone and
intersected weak sulphide mineralized silica-carbonate breccia and
stromatolite banded sections in the first 50m of the hole. This was followed
by moderately mineralized silica-sulphide-magnetic breccia bands and
silica-sulphide breccia bands. The hole ended in felsic tuff and based on the
NT Zone intersection at the collar, a second hole on section, RV21-27, was
planned.
RV21-27 (Figure 7) is in follow up to hole RV21-26, which it collared
behind and drilled below. The hole started in felsic tuff, and entered the
north band of the NT Zone at 160.48m and remained therein until 435.4m,
intersecting multiple sections of weak to moderately mineralized
silica-sulphide-magnetite breccia. The south band of the NT Zone was
intersected at 459.3m and the hole stayed in the Zone until 481.24m. From
there to 723.8m the hole intersected felsic tuffs with a best assay of 1m (at)
6.89 g/t Au from 556m. From 723.8m to the end of the hole at 728.0m, the hole
intersected quartz veining/silica breccia as well as cherty metasediments that
may be the hanging wall units of the NT Zone. The hole stopped in
mineralization and it is planned to be deepened in the future to test further
at depth.
These three southerly holes encountered non-traditional stratigraphy (but
the same rock types) showing that the NT Zone in this area is more complex
than previously understood. It has bifurcated and a prominent east-west
structural corridor is evident in magnetic surveys where the NT Zone has been
de-magnetized. Our drilling has confirmed the presence of the mineralized
breccias but more drilling is required to further model the structural
complexity of this area.
New significant assay composite results are compiled in Table 1 below.
Table 1: Newman Todd significant assay composite results.


Hole ID  From (m ) To (m)  Width (m)   Au (g/t)

---


NT21-181                  6    16.5        10.5        1.47

---


NT21-181              150.5  151.27        0.77        1.79

---


NT21-181                263  264.25        1.25        3.31

---


NT21-181              273.4   274.1         0.7        1.78

---


NT21-181                284     285           1        3.11

---


NT21-181                296     298           2        2.91

---


NT21-181              319.9   321.1         1.2        1.95

---


NT21-181                364  365.45        1.45        1.27

---


NT21-181                403     404           1        2.11

---


NT21-181                407     408           1        2.69

---


NT21-181              427.2     428         0.8        1.82

---


NT21-181                433   434.5         1.5       23.33

---


NT21-181                444     448           4        2.27

---


NT21-181                452     453           1        1.07

---


NT21-181              498.4     499         0.6       39.95

---


NT21-181                575     576           1        1.35

---


NT21-181              596.3   597.5         1.2        2.30

---


NT21-181                618     619           1        0.98

---


NT21-181              622.6   623.3         0.7        4.99

---

NT21-181    636.85   639.5        2.65        5.84

---


NT21-182                 62      64           2        1.97

---


NT21-182                 66      67           1        1.41

---


NT21-182                104     105           1        1.05

---


NT21-182             112.75  113.65         0.9        1.97

---


NT21-182              175.9  176.33        0.43        4.65

---


NT21-182                247     248           1        1.17

---


NT21-182                296     297           1        1.72

---


NT21-182                320     321           1        2.38

---


NT21-183                 75      76           1        1.48

---


NT21-183                 84      85           1        1.42

---


NT21-183                 94   94.75        0.75        1.46

---


NT21-183              130.5   131.3         0.8        1.62

---


NT21-183             151.25  152.25           1        2.83

---


NT21-183                311     312           1        1.27

---


NT21-183             314.85   315.7        0.85        1.60

---

NT21-183    346.28  346.58         0.3        5.10

---


NT21-184              21.65      23        1.35        2.42

---


NT21-184                123     124           1        1.00

---


NT21-184                157     159           2        2.21

---


NT21-184                169     170           1       66.40

---


NT21-184                180     181           1        1.64

---


NT21-184                239     240           1        1.04

---


NT21-184                378     379           1        1.59

---


NT21-184             396.75  397.65         0.9        1.16

---


NT21-184             406.15   406.9        0.75        6.21

---


NT21-184                448  448.65        0.65        2.13

---


NT21-184              537.9   538.9        1.00        1.09

---


RV21-26               26.25      27        0.75        3.97

---


RV21-26                34.1      36         1.9        3.04

---


RV21-26                  66    66.8         0.8        2.23

---


RV21-26                 373     374           1        1.10

---


RV21-26                 463   463.7         0.7       10.10

---


RV21-27                 307     308           1        1.36

---


RV21-27                 336     337           1        1.09

---


RV21-27                 386     387           1        1.00

---


RV21-27                 556     557           1        6.89

---
All widths are down-core
lengths. Not enough
information has been
collected to determine true
widths. Bolded intervals
contain visible gold.
Table 2: Table of drillhole location details for holes reported in the
current press release.
Hole ID Easting (m E)

Northing (m N)  Elevation (m)   Length (m)    Dip     Azimuth

---

NT21-181                420527             5656485             363           
737     -62         135

---

NT21-182                420361             5655854             365           
359     -70         315

---

NT21-183                420287             5655764             355           
404     -70         315

---

NT21-184                420132             5655970             364           
698     -70         135

---

RV21-26                 419909             5655887             389           
510     -45         135

---

RV21-27                 419876             5655929             389           
728     -54         135

---
Prior drilling on the NT Zone from 2013 and earlier had mostly focused on
testing the Zone by targeting the footwall with drilling toward the southeast,
now known to be sub-parallel to gold mineralized veining and structures,
potentially missing high-grade intersections or undercutting much of the
targeted zone. Newman Todd is a highly prospective target with 41% of the 165
historic drill holes having intervals of greater than 20 g/t gold over various
lengths. In addition, nearly all drilling has been conducted to depths of less
than 400 metres.
The Red Lake Camp is famously known for high grade gold mineralization at
depth, with Evolution Mining's Red Lake Gold Mine currently reaching depths of
several thousand feet. Trillium will continue to test various drill
orientations in order to develop a comprehensive understanding of the
mineralization and structural controls and test the depth potential of the
Newman Todd Zone. Figure 2 below shows the location of the Newman Todd 
Projectas well as its relative location to the nearby past producing mines 
within the
Red Lake Camp.
All drilling was supervised by Paul Barc, PGeo. The drilling was
conducted by Rodren Drilling Ltd., of West St. Paul, Manitoba. Drill core was
logged and sampled in a secure core facility on site. Core samples from the
program were cut in half, using a diamond cutting saw, and half cores were
sent for analysis to the SGS Laboratory in Red Lake, ON, and Burnaby, BC and
Activation Laboratories Ltd. in Dryden and Thunder Bay, ON, all accredited
mineral analysis laboratories. All samples were analysed for gold using
standard Fire Assay-AA techniques. Samples returning over 10.0 g/t gold were
analyzed utilizing standard Fire Assay-Gravimetric methods. Selected samples
with results greater than one ounce per ton gold were also analyzed with a
standard 1 kg metallic screen fire assay. Certified gold reference standards,
blanks and duplicates are routinely inserted into the sample stream, as part
of Trillium Gold's quality control/quality assurance program (QAQC) to monitor
accuracy and precision. No QAQC issues were noted with the results reported
herein. All drill intercepts reported are down-hole core lengths, which does
not necessarily represent true widths.
The technical information presented in this news release has been
reviewed and approved by William Paterson QP, PGeo, VP of Exploration of
Trillium Gold Mines., as defined by NI 43-101.
Visit our website at www.trilliumgold.com.
On behalf of the Board of Directors,
Trillium Gold Mines Inc.
"Russell Starr"
Russell StarrPresident, CEO and Director
About Trillium Gold Mines Inc. Trillium Gold Mines Inc. is a growth
focused company engaged in the business of acquisition, exploration and
development of mineral properties located in the Red Lake Mining District of
Northern Ontario. The Company recently extended its holdings in the
Confederation Lake and Birch-Uchi greenstone belts, as well as in highly
prospective properties in Larder Lake, Ontario and the Matagami and
Chibougamou areas of Quebec.
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This news release contains forward-looking information, which involves
known and unknown risks, uncertainties and other factors that may cause actual
events to differ materially from current expectation. Readers are cautioned
not to place undue reliance on these forward-looking statements, which speak
only as of the date of this press release. The Company disclaims any intention
or obligation, except to the extent required by law, to update or revise any
forward-looking statements, whether as a result of new information, future
events or otherwise.

<br /><p> </p>
<p id(equal sign)"PURL">View original content to download 
multimedia:http://www.prnewswire.com/news-releases/trillium-gold-extends-the-nt-
zone-with-visible-gold-and-continued-high-grade-gold-intercepts-301292424.html</
p>

<p>SOURCE  Trillium Gold Mines Inc.</p>



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/May2021/17/c1535.html

-0-                           05/17/2021
/For further information: please contact Donna Yoshimatsu, VP Corporate
Development and Investor Relations at dyoshimatsu(at)trilliumgold.com, (416)
722-2456, or info(at)trilliumgold.com, 604-688-9588./
(TGLDF TGM. 0702)

CO:  Trillium Gold Mines Inc.
ST:  British Columbia
IN:  MIN MNG PRM OTC
SU:

-30-