Source	CANADA NEWSWIRE
Date	05/18/2021
Time	05:03:15 AM

Company	 Sailfish Royalty Corp.
Title	Sailfish Updates Mineral Resource Estimate for the Gavilanes Silver
Project; Highlighted by an Inferred Resource of 22.4 Million oz AgEq at
245.6 g/t AgEq





    CDNX Symbol: FISH











Press Release




" BC-SailfishRoyaltyUpdate   05-18 2251
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.329442:
^Sailfish Updates Mineral Resource Estimate for the Gavilanes Silver
Project; Highlighted by an Inferred Resource of 22.4 Million oz AgEq at
245.6 g/t AgEq@

TORTOLA, British Virgin Islands, May 18, 2021 /CNW/ - Sailfish Royalty
Corp. (TSXV: FISH) (OTCQX: SROYF) (the "Company" or "Sailfish") is pleased to
report the results of an updated mineral resource estimate prepared by Mine
Development Associates ("MDA"), a division of RESPEC, located in Reno, Nevada,
on the Company's wholly owned Gavilanes silver property ("Gavilanes") located
in Durango, Mexico.
A technical report for the updated mineral resource estimate jointly
prepared by MDA and Resource Geosciences Incorporated ("RGI") is expected to
be filed in accordance with National Instrument 43-101, Standards of
Disclosure for Mineral Projects ("NI 43-101") under the Company's SEDAR
profile at www.sedar.com within 45 days of this news release, and on the
Company's website at www.sailfishroyalty.com.
Highlights
<<

--  The updated mineral resource estimate of 22.4 million ounces ("oz") of
silver equivalent ("AgEg") at 245.6 AgEq (see Exhibit 1) is comprised of
the following metals:
o 18.9 million oz of silver ("Ag") at 207 g/t Ag
o 13,700 oz of gold ("Au") at 0.15 g/t Au
o 7.8 million pounds ("lbs") of copper ("Cu") at 0.12% Cu
o 37.9 million lbs of lead ("Pb") at 0.61% Pb
o 27.2 million lbs of zinc ("Zn") at 0.43% Zn
--  More than 84% of the AgEq mineral resource estimate is Ag only
--  The resource is all within 330 meters ("m") of surface and remains open
along strike and at depth
--  Only three veins (Guadalupe-Soledad, San Nicolas and Descubridora) are
included in the updated mineral resource estimate (see Exhibit 2)
--  Several nearby veins with similar surface geochemistry (El Muerto, La
Tuna, La Cruz) or geologic characteristics (Veta 1 and Providencia) have
been mapped but not yet drill tested (see Exhibit 2)
<>>
The updated mineral resource estimate is based on an improved geologic
model that considers distinct structural controls of mineralized zones that
were previously modeled as an unconstrained stockwork zone and distinct
mineralization models for all the metals (Ag, Au, Cu, Pb and Zn) reported in
the resource. This refinement to the geologic model by MDA has significantly
increased the grade profile of Gavilanes and better defined the orientation
and distribution of the mineralization. In addition to the improved grade
profile, the technical report is expected to highlight the exploration
potential at Gavilanes. High priority targets include testing the strike and
depth extents of the three veins included in the updated mineral resource
estimate and drill testing the several mapped yet untested veins nearby.
Cesar Gonzalez, Chief Executive Officer of Sailfish states that, "this
updated mineral resource estimate places Gavilanes among the highest-grade
silver exploration projects in Mexico and is a key milestone in the planned
spinout of the asset. We are excited to be one step closer to maximizing value
for shareholders, especially with silver trading near seven-year highs."
Updated Mineral Resource Estimate
The updated mineral resource estimate is summarized in Exhibit 1 and was
generated using reinterpreted data from 47 diamond drill holes (9,623.9 m)
that Santacruz Silver Mining Ltd. drilled in 2012 and 2013. The updated
resource was calculated by applying some consideration of the confidence in
the underlying database, sample integrity, analytical precision/reliability,
and geologic interpretations. The exploration drilling completed is of
sufficient quality to allow for higher classification. However, all material
in this estimate is classified as Inferred due to the complex geology,
significant gaps in the assay data created by lack of sampling, some spatial
imprecision in the block model coding, and a lack of metallurgical testing
data. It is expected that a majority of these Inferred resources would be
upgraded to Indicated resources with additional sampling of previously drilled
holes, continued exploration drilling, collection of metallurgy data, and
additional density data measurements. The resources are reported at a cutoff
grade of 100 g/t AgEq (see calculation below Exhibit 1) for underground
mining.
MDA used their judgment with respect to the technical and economic
factors likely to influence the "prospects for eventual economic extraction"
and believes that all cutoffs listed in Exhibit 1 could eventually be a basis
for economic extraction of the resources, though only the 100 g/t AgEq cutoff
is the current resource. Those technical factors include anticipated
metallurgical recoveries, current operating costs for anticipated mining and
processing, and metal prices consistent with recent market pricings. These
Mineral Resources are not Mineral Reserves and do not have demonstrated
economic viability.
Exhibit 1 - Estimated Underground Inferred Resource - Gavilanes
Cutoff

Tonnes          Average

Contained          g

oz Ag       g Au/t      oz Au       % Cu

lbs Cu          % Pb

lbs Pb            % Zn

lbs Zn
Grade g                           g                 oz AgEq(x)              Ag/t
AgEq/t(x)                        AgEq/t(x)

---


75            3,742,000            206.9                24,898,000      
172.4      20,747,000        0.13      15,500      0.11         9,046,000      
0.56          45,795,000        0.42          34,288,000

---



100      2,833,000            245.6                22,368,000      207.3      
18,878,000        0.15      13,700      0.12         7,772,000      
0.61          37,893,000        0.43          27,152,000

---


125           2,210,000            283.3                20,131,000      
241.3      17,146,000        0.17      12,100      0.14         6,753,000      
0.66          32,398,000        0.45          22,011,000

---


150           1,765,000            320.3                18,174,000      
275.1      15,607,000        0.19      10,500      0.15         5,745,000      
0.73          28,275,000        0.47          18,421,000

---


(x) The silver equivalent block grade was calculated
using the formula: g AgEq/t (equal sign) g Ag/t + (g Au/
t (x) (1/AgEqAu_Factor)) + (Cu ppm (x) (1/
AgEqCu_Factor)) + (Pb ppm (x) (1/AgEqPb_Factor))
+ (Zn ppm (x) (1/AgEqZn_Factor)). In which:
AgEqAu_Factor (equal sign) (Silver Price/Gold Price) (x)
(Silver Recovery/Gold Recovery) (equal sign) 0.01425,
AgEqCu_Factor (equal sign) (Silver Price / (Copper Price/
14.58333 oz./lbs.)) (x) (Silver Recovery/Copper
Recovery) (equal sign) 151.99997, AgEqPb_Factor (equal sign) (Silver
Price / (Lead Price/14.58333 oz./lbs.)) (x)
(Silver Recovery/Lead Recovery) (equal sign) 531.99988 and
AgEqZn_Factor (equal sign) (Silver Price / (Zinc Price/
14.58333 oz./lbs.)) (x) (Silver Recovery/Zinc
Recovery) (equal sign) 531.99988.
To determine the "reasonable prospects for eventual economic extraction"
MDA used a series of underground stope optimizations based on mining costs,
processing costs, and anticipated metallurgical recoveries. MDA chose to
report the current Inferred resources considering underground costs of
US$75.00 per-tonne for mining, G&A costs of US$6.30 per-tonne and processing
costs of US$40.00 per-tonne. The metals prices were assumed to be US$19.00
per-ounce for silver, US$1,600 per-ounce for gold, US$3.50 per-pound for
copper and US$1.00 per-pound for lead and zinc.
Because no metallurgical data was available at the time of the resource
update, recoveries were assumed to be 96% for silver, 80% for gold, and 50%
for copper, lead, and zinc. This reflects the fact that silver is the metal of
primary economic interest and any processing would likely be optimized to
recover silver.
Technical Report Recommendations
The estimated mineral resource presented in the technical report
comprises a precious and base-metal bearing, epithermal low to
intermediate-sulfidation deposit that is unoxidized, comprised of multiple
mineralized veins in a structural zone greater than 250 m wide
(northeast-southwest), with strike extent greater than 900 m
(northwest-southeast) and greater than 400 m dip extent. The deposit is open
in all directions. It is highly probable that the identified volume of
mineralized veins will be increased by drilling the dip and strike extensions
of the drill tested mineralized zones, and by drill testing untested
mineralized structures. High priority targets for drill testing have been
identified by the 2012-2013 drilling and historic reconnaissance mapping.
Opportunities exist to:
<<

1. Increase the identified resource by drilling the dip and strike extensions
of the mineralized zones identified at Descubridora and San Nicolas.
2. Identify new areas of mineralization by drill testing outcropping
mineralized structures thus far untested. The La Tuna, El Muerto and
Providencia structures have not been drill tested and a prior project
operator, Hochschild Mining PLC, conducted only a shallow three-hole test
of La Cruz, thus for practical purposes all four of these structures are
unevaluated and merit drill testing.
3. Discover concealed mineralization at depth, indicated by alteration zones
exposed at surface which may represent the highest levels of an epithermal
mineralized zone.
<>>
A two-stage work plan is recommended. The first stage encompasses: 3,000
m of step out drilling of the Inferred Resource estimated in the technical
report; 3,000 m of drill testing of the known veins in the immediate area of
the currently defined resource; systematic mapping and sampling through trench
exposures of the strike projections of known veins; property wide
reconnaissance geologic mapping and concurrent rock chip sampling; sampling
and assay of unsampled intervals of archived drill core; preliminary
metallurgical testing of samples obtained from drilling; geophysical surveys;
and environmental and permitting studies. A total of 6,000 m of diamond core
drilling is recommended for Stage 1.
The second stage, lasting 12 months, which is conditional upon positive
results from the first, comprises 15,000 m of diamond core definition drilling
of mineralized zones confirmed during the Stage 1 drill program.
Sampling and Analysis of Existing but Unsampled Drill Core
MDA identified significant gaps in the assay data created by lack of
sampling. Gaps in the sampled intervals force the model to treat unsampled
intervals as unmineralized, which is an assumption unlikely to be true in all
cases, thus the resource model may be improved, and the resource estimate
possibly increased, by obtaining assay data for the missing intervals. The
unsampled drill core is stored on site and is available for sampling. It is
recommended that all available drill core be sampled and assayed to create a
continuous assay database from collar to total depth of each drillhole.
Concurrently, the drill core should be used to obtain additional bulk density
data for the mineralized zones.
Qualified Person
Derick Unger, C.P.G., is an independent Qualified Person under NI 43-101
and is responsible for the mineral resource estimate. Matthew D. Gray, Ph.D.,
C.P.G, is an independent Qualified Person under NI 43-101 and is jointly
responsible with Derick Unger for the technical report at Gavilanes. Dr. Gray
is the President of RGI and Mr. Unger is a Project Geologist at MDA. Both Dr.
Gray and Mr. Unger are the Qualifed Persons, as defined in NI 43-101, that
have reviewed and approved the scientific and technical information contained
in this press release.
About Sailfish
Sailfish is a precious metals royalty and streaming company. Within
Sailfish's portfolio are three main assets on advanced stage projects in the
Americas: a gold stream equivalent to a 3% NSR on the San Albino gold project
(~3.5 sq. km) and a 2% NSR on the rest of the area (~134.5 sq. km) surrounding
San Albino in northern Nicaragua; an up to 2.75% NSR on the Tocantinzinho gold
project in the prolific Tapajos district of northern Brazil; and an up to 3%
NSR on the multi-million ounce Spring Valley gold project in Pershing County,
Nevada.
Sailfish is listed on the TSX Venture Exchange under the symbol "FISH"
and on the OTCQX under the symbol "SROYF". Please visit the Company's website
at www.sailfishroyalty.com for additional information.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
the term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary statement regarding forward-looking information
Certain disclosures in this release constitute "forward-looking
information" within the meaning of Canadian securities legislation.
Forward-looking statements are statements that are not historical facts and
are generally, but not always, identified by words such as the following:
expects, plans, anticipates, believes, intends, estimates, projects, assumes,
potential and similar expressions. Forward-looking statements also include
reference to events or conditions that will, would, may, could or should
occur, including, without limitation, that an updated technical report
including the mineral resource estimate is expected to be filed by MDA and RGI
in accordance with National Instrument 43-101, the technical report is
expected to highlight the exploration potential at Gavilanes, the planned
spinout of the Gavilanes property, that the identified volume of mineralized
veins are expected to be increased by drilling the dip and strike extensions
of the drill tested mineralized zones, and by drill testing untested
mineralized structures. In making the forward-looking statements in this news
release, the Company has applied certain factors and assumptions that the
Company believes are reasonable, including that that an updated technical
report including the mineral resource estimate will be filed by MDA and RGI in
accordance with National Instrument 43-101, the technical report will
highlight the exploration potential at Gavilanes, the spinout of the Gavilanes
property on the terms as anticipated by management will be successful, that
the identified volume of mineralized veins will be increased by drilling thedip 
and strike extensions of the drill tested mineralized zones, and by drill
testing untested mineralized structures. However, the forward-looking
statements in this news release are subject to numerous risks, uncertainties
and other factors that may cause future results to differ materially from
those expressed or implied in such forward-looking statements, including
without limitation: that that an updated technical report including the
mineral resource estimate will not be filed by MDA and RGI in accordance with
National Instrument 43-101, the spinout of the Gavilanes property will not be
on the terms as anticipated by management or will not be successful at all,
the technical report will not highlight the exploration potential at
Gavilanes, the planned spinout of the Gavilanes property that the identified
volume of mineralized veins will not be increased by drilling the dip and
strike extensions of the drill tested mineralized zones, and by drill testing
untested mineralized structures. There can be no assurance that such
statements will prove to be accurate, as actual results and future events
could differ materially from those anticipated in such statements.
Accordingly, readers should not place undue reliance on forward-looking
statements and forward-looking information. Readers are cautioned that
reliance on such information may not be appropriate for other purpose

" BC-SailfishRoyaltyUpdate   05-18 2251
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.329442:
^Sailfish Updates Mineral Resource Estimate for the Gavilanes Silver
Project; Highlighted by an Inferred Resource of 22.4 Million oz AgEq at
245.6 g/t AgEq@

TORTOLA, British Virgin Islands, May 18, 2021 /CNW/ - Sailfish Royalty
Corp. (TSXV: FISH) (OTCQX: SROYF) (the "Company" or "Sailfish") is pleased to
report the results of an updated mineral resource estimate prepared by Mine
Development Associates ("MDA"), a division of RESPEC, located in Reno, Nevada,
on the Company's wholly owned Gavilanes silver property ("Gavilanes") located
in Durango, Mexico.
A technical report for the updated mineral resource estimate jointly
prepared by MDA and Resource Geosciences Incorporated ("RGI") is expected to
be filed in accordance with National Instrument 43-101, Standards of
Disclosure for Mineral Projects ("NI 43-101") under the Company's SEDAR
profile at www.sedar.com within 45 days of this news release, and on the
Company's website at www.sailfishroyalty.com.
Highlights
<<

--  The updated mineral resource estimate of 22.4 million ounces ("oz") of
silver equivalent ("AgEg") at 245.6 AgEq (see Exhibit 1) is comprised of
the following metals:
o 18.9 million oz of silver ("Ag") at 207 g/t Ag
o 13,700 oz of gold ("Au") at 0.15 g/t Au
o 7.8 million pounds ("lbs") of copper ("Cu") at 0.12% Cu
o 37.9 million lbs of lead ("Pb") at 0.61% Pb
o 27.2 million lbs of zinc ("Zn") at 0.43% Zn
--  More than 84% of the AgEq mineral resource estimate is Ag only
--  The resource is all within 330 meters ("m") of surface and remains open
along strike and at depth
--  Only three veins (Guadalupe-Soledad, San Nicolas and Descubridora) are
included in the updated mineral resource estimate (see Exhibit 2)
--  Several nearby veins with similar surface geochemistry (El Muerto, La
Tuna, La Cruz) or geologic characteristics (Veta 1 and Providencia) have
been mapped but not yet drill tested (see Exhibit 2)
<>>
The updated mineral resource estimate is based on an improved geologic
model that considers distinct structural controls of mineralized zones that
were previously modeled as an unconstrained stockwork zone and distinct
mineralization models for all the metals (Ag, Au, Cu, Pb and Zn) reported in
the resource. This refinement to the geologic model by MDA has significantly
increased the grade profile of Gavilanes and better defined the orientation
and distribution of the mineralization. In addition to the improved grade
profile, the technical report is expected to highlight the exploration
potential at Gavilanes. High priority targets include testing the strike and
depth extents of the three veins included in the updated mineral resource
estimate and drill testing the several mapped yet untested veins nearby.
Cesar Gonzalez, Chief Executive Officer of Sailfish states that, "this
updated mineral resource estimate places Gavilanes among the highest-grade
silver exploration projects in Mexico and is a key milestone in the planned
spinout of the asset. We are excited to be one step closer to maximizing value
for shareholders, especially with silver trading near seven-year highs."
Updated Mineral Resource Estimate
The updated mineral resource estimate is summarized in Exhibit 1 and was
generated using reinterpreted data from 47 diamond drill holes (9,623.9 m)
that Santacruz Silver Mining Ltd. drilled in 2012 and 2013. The updated
resource was calculated by applying some consideration of the confidence in
the underlying database, sample integrity, analytical precision/reliability,
and geologic interpretations. The exploration drilling completed is of
sufficient quality to allow for higher classification. However, all material
in this estimate is classified as Inferred due to the complex geology,
significant gaps in the assay data created by lack of sampling, some spatial
imprecision in the block model coding, and a lack of metallurgical testing
data. It is expected that a majority of these Inferred resources would be
upgraded to Indicated resources with additional sampling of previously drilled
holes, continued exploration drilling, collection of metallurgy data, and
additional density data measurements. The resources are reported at a cutoff
grade of 100 g/t AgEq (see calculation below Exhibit 1) for underground
mining.
MDA used their judgment with respect to the technical and economic
factors likely to influence the "prospects for eventual economic extraction"
and believes that all cutoffs listed in Exhibit 1 could eventually be a basis
for economic extraction of the resources, though only the 100 g/t AgEq cutoff
is the current resource. Those technical factors include anticipated
metallurgical recoveries, current operating costs for anticipated mining and
processing, and metal prices consistent with recent market pricings. These
Mineral Resources are not Mineral Reserves and do not have demonstrated
economic viability.
Exhibit 1 - Estimated Underground Inferred Resource - Gavilanes
Cutoff

Tonnes          Average

Contained          g

oz Ag       g Au/t      oz Au       % Cu

lbs Cu          % Pb

lbs Pb            % Zn

lbs Zn
Grade g                           g                 oz AgEq(x)              Ag/t
AgEq/t(x)                        AgEq/t(x)

---


75            3,742,000            206.9                24,898,000      
172.4      20,747,000        0.13      15,500      0.11         9,046,000      
0.56          45,795,000        0.42          34,288,000

---



100      2,833,000            245.6                22,368,000      207.3      
18,878,000        0.15      13,700      0.12         7,772,000      
0.61          37,893,000        0.43          27,152,000

---


125           2,210,000            283.3                20,131,000      
241.3      17,146,000        0.17      12,100      0.14         6,753,000      
0.66          32,398,000        0.45          22,011,000

---


150           1,765,000            320.3                18,174,000      
275.1      15,607,000        0.19      10,500      0.15         5,745,000      
0.73          28,275,000        0.47          18,421,000

---


(x) The silver equivalent block grade was calculated
using the formula: g AgEq/t (equal sign) g Ag/t + (g Au/
t (x) (1/AgEqAu_Factor)) + (Cu ppm (x) (1/
AgEqCu_Factor)) + (Pb ppm (x) (1/AgEqPb_Factor))
+ (Zn ppm (x) (1/AgEqZn_Factor)). In which:
AgEqAu_Factor (equal sign) (Silver Price/Gold Price) (x)
(Silver Recovery/Gold Recovery) (equal sign) 0.01425,
AgEqCu_Factor (equal sign) (Silver Price / (Copper Price/
14.58333 oz./lbs.)) (x) (Silver Recovery/Copper
Recovery) (equal sign) 151.99997, AgEqPb_Factor (equal sign) (Silver
Price / (Lead Price/14.58333 oz./lbs.)) (x)
(Silver Recovery/Lead Recovery) (equal sign) 531.99988 and
AgEqZn_Factor (equal sign) (Silver Price / (Zinc Price/
14.58333 oz./lbs.)) (x) (Silver Recovery/Zinc
Recovery) (equal sign) 531.99988.
To determine the "reasonable prospects for eventual economic extraction"
MDA used a series of underground stope optimizations based on mining costs,
processing costs, and anticipated metallurgical recoveries. MDA chose to
report the current Inferred resources considering underground costs of
US$75.00 per-tonne for mining, G&A costs of US$6.30 per-tonne and processing
costs of US$40.00 per-tonne. The metals prices were assumed to be US$19.00
per-ounce for silver, US$1,600 per-ounce for gold, US$3.50 per-pound for
copper and US$1.00 per-pound for lead and zinc.
Because no metallurgical data was available at the time of the resource
update, recoveries were assumed to be 96% for silver, 80% for gold, and 50%
for copper, lead, and zinc. This reflects the fact that silver is the metal of
primary economic interest and any processing would likely be optimized to
recover silver.
Technical Report Recommendations
The estimated mineral resource presented in the technical report
comprises a precious and base-metal bearing, epithermal low to
intermediate-sulfidation deposit that is unoxidized, comprised of multiple
mineralized veins in a structural zone greater than 250 m wide
(northeast-southwest), with strike extent greater than 900 m
(northwest-southeast) and greater than 400 m dip extent. The deposit is open
in all directions. It is highly probable that the identified volume of
mineralized veins will be increased by drilling the dip and strike extensions
of the drill tested mineralized zones, and by drill testing untested
mineralized structures. High priority targets for drill testing have been
identified by the 2012-2013 drilling and historic reconnaissance mapping.
Opportunities exist to:
<<

1. Increase the identified resource by drilling the dip and strike extensions
of the mineralized zones identified at Descubridora and San Nicolas.
2. Identify new areas of mineralization by drill testing outcropping
mineralized structures thus far untested. The La Tuna, El Muerto and
Providencia structures have not been drill tested and a prior project
operator, Hochschild Mining PLC, conducted only a shallow three-hole test
of La Cruz, thus for practical purposes all four of these structures are
unevaluated and merit drill testing.
3. Discover concealed mineralization at depth, indicated by alteration zones
exposed at surface which may represent the highest levels of an epithermal
mineralized zone.
<>>
A two-stage work plan is recommended. The first stage encompasses: 3,000
m of step out drilling of the Inferred Resource estimated in the technical
report; 3,000 m of drill testing of the known veins in the immediate area of
the currently defined resource; systematic mapping and sampling through trench
exposures of the strike projections of known veins; property wide
reconnaissance geologic mapping and concurrent rock chip sampling; sampling
and assay of unsampled intervals of archived drill core; preliminary
metallurgical testing of samples obtained from drilling; geophysical surveys;
and environmental and permitting studies. A total of 6,000 m of diamond core
drilling is recommended for Stage 1.
The second stage, lasting 12 months, which is conditional upon positive
results from the first, comprises 15,000 m of diamond core definition drilling
of mineralized zones confirmed during the Stage 1 drill program.
Sampling and Analysis of Existing but Unsampled Drill Core
MDA identified significant gaps in the assay data created by lack of
sampling. Gaps in the sampled intervals force the model to treat unsampled
intervals as unmineralized, which is an assumption unlikely to be true in all
cases, thus the resource model may be improved, and the resource estimate
possibly increased, by obtaining assay data for the missing intervals. The
unsampled drill core is stored on site and is available for sampling. It is
recommended that all available drill core be sampled and assayed to create a
continuous assay database from collar to total depth of each drillhole.
Concurrently, the drill core should be used to obtain additional bulk density
data for the mineralized zones.
Qualified Person
Derick Unger, C.P.G., is an independent Qualified Person under NI 43-101
and is responsible for the mineral resource estimate. Matthew D. Gray, Ph.D.,
C.P.G, is an independent Qualified Person under NI 43-101 and is jointly
responsible with Derick Unger for the technical report at Gavilanes. Dr. Gray
is the President of RGI and Mr. Unger is a Project Geologist at MDA. Both Dr.
Gray and Mr. Unger are the Qualifed Persons, as defined in NI 43-101, that
have reviewed and approved the scientific and technical information contained
in this press release.
About Sailfish
Sailfish is a precious metals royalty and streaming company. Within
Sailfish's portfolio are three main assets on advanced stage projects in the
Americas: a gold stream equivalent to a 3% NSR on the San Albino gold project
(~3.5 sq. km) and a 2% NSR on the rest of the area (~134.5 sq. km) surrounding
San Albino in northern Nicaragua; an up to 2.75% NSR on the Tocantinzinho gold
project in the prolific Tapajos district of northern Brazil; and an up to 3%
NSR on the multi-million ounce Spring Valley gold project in Pershing County,
Nevada.
Sailfish is listed on the TSX Venture Exchange under the symbol "FISH"
and on the OTCQX under the symbol "SROYF". Please visit the Company's website
at www.sailfishroyalty.com for additional information.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
the term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary statement regarding forward-looking information
Certain disclosures in this release constitute "forward-looking
information" within the meaning of Canadian securities legislation.
Forward-looking statements are statements that are not historical facts and
are generally, but not always, identified by words such as the following:
expects, plans, anticipates, believes, intends, estimates, projects, assumes,
potential and similar expressions. Forward-looking statements also include
reference to events or conditions that will, would, may, could or should
occur, including, without limitation, that an updated technical report
including the mineral resource estimate is expected to be filed by MDA and RGI
in accordance with National Instrument 43-101, the technical report is
expected to highlight the exploration potential at Gavilanes, the planned
spinout of the Gavilanes property, that the identified volume of mineralized
veins are expected to be increased by drilling the dip and strike extensions
of the drill tested mineralized zones, and by drill testing untested
mineralized structures. In making the forward-looking statements in this news
release, the Company has applied certain factors and assumptions that the
Company believes are reasonable, including that that an updated technical
report including the mineral resource estimate will be filed by MDA and RGI in
accordance with National Instrument 43-101, the technical report will
highlight the exploration potential at Gavilanes, the spinout of the Gavilanes
property on the terms as anticipated by management will be successful, that
the identified volume of mineralized veins will be increased by drilling thedip 
and strike extensions of the drill tested mineralized zones, and by drill
testing untested mineralized structures. However, the forward-looking
statements in this news release are subject to numerous risks, uncertainties
and other factors that may cause future results to differ materially from
those expressed or implied in such forward-looking statements, including
without limitation: that that an updated technical report including the
mineral resource estimate will not be filed by MDA and RGI in accordance with
National Instrument 43-101, the spinout of the Gavilanes property will not be
on the terms as anticipated by management or will not be successful at all,
the technical report will not highlight the exploration potential at
Gavilanes, the planned spinout of the Gavilanes property that the identified
volume of mineralized veins will not be increased by drilling the dip and
strike extensions of the drill tested mineralized zones, and by drill testing
untested mineralized structures. There can be no assurance that such
statements will prove to be accurate, as actual results and future events
could differ materially from those anticipated in such statements.
Accordingly, readers should not place undue reliance on forward-looking
statements and forward-looking information. Readers are cautioned that
reliance on such information may not be appropriate for other purposes. The
Company expressly disclaims any intention or obligation to update or revise
any forward-looking statements whether as a result of new information, future
events or otherwise except as otherwise required by applicable securities
legislation.
SOURCE Sailfish Royalty Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/May2021/18/c7685.html

-0-                           05/18/2021
/For further information: Cesar Gonzalez, CEO, tel. 203-862-7009 or Akiba
Leisman, Executive Chairman of the Board, tel. 203-862-7059./
/Web Site: http://www.sailfishroyalty.com/ /
(SROYF FISH.)

CO:  Sailfish Royalty Corp.
ST:  British Virgin Islands
IN:  MIN MNG OTC
SU:

-30-