Source	CANADA NEWSWIRE
Date	05/18/2021
Time	04:03:15 AM

Company	 Northern Vertex Mining Corp.
Title	Northern Vertex Intersects 28.96 Meters Grading 2.28 g/t Gold and 28.84
g/t Silver in Resource Expansion Drilling at the Moss Mine, Arizona





    CDNX Symbol: NEE











Press Release




" BC-Northern-Vertex-AZ   05-18 1802
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.313199:
^Northern Vertex Intersects 28.96 Meters Grading 2.28 g/t Gold and 28.84
g/t Silver in Resource Expansion Drilling at the Moss Mine, Arizona@

VANCOUVER, BC, May 18, 2021 /CNW/ - Northern Vertex Mining Corp. (TSXV:
NEE) (OTC Nasdaq Intl.: NHVCF) (the "Company" or "Northern Vertex") a
U.S.-focused gold producer with district-scale exploration projects in the
Walker Lane Trend, is pleased to report recent results from its multi-phase
infill and resource expansion drilling program at the Moss Mine in NW Arizona.
Results presented in this release are focused on the Ruth and Moss veins
immediately south and down dip of the Moss Mine Center pit.
Key Points:
<<

--  Significant intersections included 9.15 meters grading 4.90 g/t Au and
57.18 g/t Ag for the Moss vein in drillhole AR20-359R and 4.6 meters
grading 4.01 g/t Au and 27.97 g/t Ag for the Ruth Vein in drillhole
AR20-364R.
--  The north-dipping Ruth Vein is subparallel and related to the Moss Vein
--  The distance between the Ruth and Moss veins is approximately 175 meters
on surface, diminishing with depth as the two veins dip towards each
other, intersecting at a depth of approximately 100 meters below the
south wall of the Center pit.
--  Drilling indicates consistent intersections of elevated gold and silver
mineralization along more than 500 meters of the Ruth Vein,
approximately 100 meters south of the crest of the Moss Center pit.
<>>
Northern Vertex President, Michael G. Allen commented, "The Ruth Vein is
one of the many intra-mine opportunities we have identified to optimize and
expand existing Moss Mine operations. Our vision is to scale up the Moss Mine
into a much larger operation by capturing these optimization opportunities,
expanding resources and making new regional discoveries like we aim to do
through our recently announced work at West Oatman."
Vein Geology South of the Center Pit: Ruth Vein Drilling Area
The Ruth Vein is a fault-hosted epithermal quartz-calcite vein and vein
stockwork that is very similar to and was likely formed at the same time as
the Moss Vein. The Ruth vein strikes slightly north of east and dips to the
north towards the south-dipping Moss Vein. The intersection of the two veins
is approximately 100 meters below the south wall of the Center pit. The Ruth
Vein is subparallel to the Moss Vein and has been delineated over a strike
length of approximately 510 meters. The Ruth Vein ranges from less than a
meter to almost 15 meters thick. When hanging wall stockworks are included,
especially in the upper parts of the fault-hosted vein system, overall
thickness increases to almost 30 meters in places. The Moss Vein dips to the
south at approximately 70 degrees in this area.
Resource Expansion Drilling
Assay results for 18 reverse circulation (RC) drillholes drilled from
four different locations are included in this news release (see Table 1).
Numerous thick zones of epithermal vein-hosted gold and silver mineralization
have been intersected adjacent to the Moss Center Pit (Figure 1 Ruth Vein
Drilling Area Location Map; Figure 2 Drillhole Location Map).
Significant intersections include drillhole AR20-359R which returned
28.96 meters grading 2.28 g/t gold, and 28.84 g/t silver (2.66 g/t gold
equivalent), including 9.15 meters grading 4.90 g/t gold and 57.18 g/t silver
(5.67 g/t gold equivalent) for the Moss Vein below the Center pit, and
drillhole AR20-364R, which returned 16.76 meters grading 1.75 g/t gold, and
14.08 g/t silver, (1.94 g/t gold equivalent), including 4.6 meters grading
4.01 g/t gold and 27.97 g/t silver (4.37 g/t gold equivalent), in the Ruth
Vein to the south of and below the Center pit (Figure 3 Cross Section: Well 16
Site, Ruth Vein Drilling Area).
The Moss Mine resource expansion drilling continues to demonstrate strong
and consistent gold and silver mineralization along the Ruth vein
approximately 100 meters south of the crest of the Moss mine Center pit, and
in the Moss Vein approximately 100 meters below the Center pit.
Table 1: Results of Northern Vertex's 2020 Resource Expansion RC Drilling
in the Ruth Vein Drilling Area
Drillhole

Location

Az/Dip              From                      To    Length      Au        
Ag       AuEq

(Degrees)            (m)                       (m)     (m)     (g/t)     
(g/t)      (g/t)

---

AR20-352R
Well 17
205/-45       16.76                     27.43     10.67      0.29       
0.71        0.30

---

Including                                                                    
21.34        24.38                      3.05      0.48      0.30       0.48

---


And                                                                          
83.82        88.39                      4.57      0.27      0.53       0.28

---


And                                                                         
118.87       140.21                     21.34      0.27      3.14       0.31

---

Including                                                                   
129.54       132.59                      3.05      0.53      7.15       0.63

---

AR20-355R
25/-83                           141.73       260.60                    
118.87      0.30      4.67       0.36

---

Including                                                                   
167.64       179.83                     12.19      0.41      4.53       0.47

---


And                                                                         
192.02       205.74                     13.72      0.55     19.17       0.80

---

AR20-359R
Well 16
0/-85      118.87                    147.83     28.96      2.28      
28.84        2.66

---

Including                                                         129.54       
138.68                      9.14      4.90     57.18       5.67

---


And                                                                         
173.74       186.05                     12.31      0.32      5.81       0.40

---


And                                                                         
202.69       211.84                      9.14      0.85     18.63       1.10

---

AR20-363R
180/-45                            99.06       103.63                      
4.57      0.53      5.33       0.60

---

AR20-364R
180/-65                           109.73       126.49                     
16.76      1.75     14.08       1.94

---

Including                                                         109.73       
114.30                      4.57      4.00     27.97       4.37

---


And                                                                         
179.83       182.88                      3.05      0.66      2.25       0.69

---

AR20-366R
180/-81                           140.21       167.64                     
27.43      0.32      4.91       0.39

---

Including                                                                   
140.21       149.35                      9.14      0.53      8.07       0.63

---


And                                                                         
175.26       178.31                      3.05      0.39     13.25       0.57

---


And                                                                         
195.07       199.64                      4.57      0.35      1.57       0.37

---

AR20-369R
205/-65                           114.30       141.73                     
27.43      0.42      5.06       0.48

---

Including                                                         123.44       
128.02                      4.57      1.27     11.63       1.43

---

AR20-356R
Mid-Tier
180/-88
No Significant Intersections

---

AR20-357R
180/-70
No Significant Intersections

---

AR20-358R
180/-45
No Significant Intersections

---

AR20-360R
270/-75                            50.29        67.06                     
16.76      0.30      2.67       0.33

---

AR20-361R
310/-85                            74.68        77.72                      
3.05      0.38      3.35       0.42

---

AR20-362R
200/-80
No Significant Intersections

---

AR20-367R
ROM Pad 2
0/-75       56.39                     85.34     28.96      0.30       
4.96        0.37

---

Including                                                                    
68.58        71.63                      3.05      0.81     10.25       0.94

---

AR20-368R
0/-65                            32.00        45.72                     
13.72      0.44     10.72       0.59

---

Including                                                          42.67        
45.72                      3.05      1.13     29.40       1.52

---


And                                                                          
70.10        80.77                     10.67      0.28      1.27       0.30

---


And                                                                         
120.40       126.49                      6.10      0.29      1.70       0.31

---

And                                                               256.03       
275.84                     19.81      0.45      0.88       0.46

---

Including                                                         268.22       
272.80                      4.57      1.12      0.70       1.13

---

AR20-370R
45/-75                            60.96        85.34                     
24.38      0.29      4.46       0.35

---

Including                                                                    
60.96        68.58                      7.62      0.57      8.06       0.68

---

AR20-371R
45/-60                            27.43       303.28                    
275.84      0.27      3.75       0.32

---

Including                                                                    
28.96        41.15                     12.19      0.45      1.55       0.47

---

Including                                                                    
85.34        92.96                      7.62      0.66      1.30       0.67

---

Including                                                                   
140.21       144.78                      4.57      0.43      0.77       0.44

---

Including                                                                   
198.12       295.66                     97.54      0.41      8.61       0.52

---

Including                                                                   
216.41       225.55                      9.14      0.74     19.88       1.01

---

Including                                                                   
234.70       243.84                      9.14      1.01     26.88       1.37

---

Including                                                                   
286.51       294.13                      7.62      0.49      3.32       0.54

---

AR20-372R
340/-60                            25.91        30.48                      
4.57      0.36     15.57       0.57

---


And                                                                          
64.01        70.10                      6.10      1.10     21.57       1.38

---


And                                                                          
96.01       109.73                     13.72      0.33      1.19       0.34

---


And                                                                         
123.44       126.49                      3.05      0.26      0.95       0.27

---


And                                                                         
143.26       147.83                      4.57      0.61      4.50       0.67

---


And                                                                         
176.78       187.45                     10.67      0.28      2.37       0.32

---


And                                                                         
234.70       242.32                      7.62      0.24      1.18       0.25

---


And                                                                         
251.46       260.60                      9.14      0.35      1.20       0.37

---
Note: True thickness ranges between
approximately 62% of the reported
interval thickness for subvertical
drilling and 99% for drilling
inclined at -45 degrees to the
Ruth vein. Assay data are
uncapped. AuEq (equal sign) Au + Ag/75. RC
drilling was conducted by Boart
Longyear. RC samples, collected
every 1.52 m, were transported in
sealed bags to Skyline Assayers
and Laboratories (Skyline) in
Tucson, AZ. Field control QAQC
samples, including standards,
blanks, and field duplicates, wereinserted into the sample stream at
a rate of three field control
samples approximately every 20
regular samples. Gold was
determined by fire-assay fusion
of a 30 g sub-samples with atomic
absorption spectroscopy (method
FA-01). Overlimit samples of gold
were assayed by gravimetric means
(FA-02). Skyline Laboratories is
accredited in accordance with ISO/
IEC 17025:2017 and ISO 9001:2015.
Qualified Person
Dr. Warwick Board, P.Geo., Vice President Exploration of Northern Vertex,
is the Qualified Person as defined by NI 43-101 responsible for the Moss
Regional Exploration Project and has reviewed and approved the scientific and
technical information in this news release related thereto.
About Northern Vertex Mining Corp.
Northern Vertex offers investors a rare combination of cash flow,
production, top-tier management, and exceptional exploration potential within
two projects on the Walker Lane Gold Trend of western Nevada and Arizona.
Management is executing a clear strategy that expands production and resources
at the Moss Mine in Arizona while aggressively exploring the Hercules Project
in Nevada.
ON BEHALF OF THE BOARD OF NORTHERN VERTEX MINING CORP
"Michael G. Allen"President
TSXV: NEE | Nasdaq Intl: NHVCF | Frankfurt: 54N | ISIN: CA6660061012 |
WKN: A1JUA0
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary Statement Regarding Forward-Looking Information
All statements, trend analysis and other information contained in this
press release about anticipated future events or results constitute
forward-looking statements. Forward-looking statements are often, but not
always, identified by the use of words such as "seek", "anticipate",
"believe", "plan", "estimate", "expect" and "intend" and statements that an
event or result "may", "will", "should", "could" or "might" occur or be
achieved and other similar expressions. All statements, other than statements
of historical fact, included herein, are forward-looking statements. Although
Northern Vertex believes that the expectations reflected in such
forward-looking statements and/or information are reasonable, undue reliance
should not be placed on forward-looking statements since Northern Vertex can
give no assurance that such expectations will prove to be correct. These
statements involve known and unknown risks, uncertainties and other factors
that may cause actual results or events to differ materially from those
anticipated in such forward-looking statements, including the risks,
uncertainties and other factors identified in Northern Vertex's periodic
filings with Canadian securities regulators. Forward-looking statements are
subject to business and economic risks and uncertainties and other factors
that could cause actual results of operations to differ materially from thos

" BC-Northern-Vertex-AZ   05-18 1802
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.313199:
^Northern Vertex Intersects 28.96 Meters Grading 2.28 g/t Gold and 28.84
g/t Silver in Resource Expansion Drilling at the Moss Mine, Arizona@

VANCOUVER, BC, May 18, 2021 /CNW/ - Northern Vertex Mining Corp. (TSXV:
NEE) (OTC Nasdaq Intl.: NHVCF) (the "Company" or "Northern Vertex") a
U.S.-focused gold producer with district-scale exploration projects in the
Walker Lane Trend, is pleased to report recent results from its multi-phase
infill and resource expansion drilling program at the Moss Mine in NW Arizona.
Results presented in this release are focused on the Ruth and Moss veins
immediately south and down dip of the Moss Mine Center pit.
Key Points:
<<

--  Significant intersections included 9.15 meters grading 4.90 g/t Au and
57.18 g/t Ag for the Moss vein in drillhole AR20-359R and 4.6 meters
grading 4.01 g/t Au and 27.97 g/t Ag for the Ruth Vein in drillhole
AR20-364R.
--  The north-dipping Ruth Vein is subparallel and related to the Moss Vein
--  The distance between the Ruth and Moss veins is approximately 175 meters
on surface, diminishing with depth as the two veins dip towards each
other, intersecting at a depth of approximately 100 meters below the
south wall of the Center pit.
--  Drilling indicates consistent intersections of elevated gold and silver
mineralization along more than 500 meters of the Ruth Vein,
approximately 100 meters south of the crest of the Moss Center pit.
<>>
Northern Vertex President, Michael G. Allen commented, "The Ruth Vein is
one of the many intra-mine opportunities we have identified to optimize and
expand existing Moss Mine operations. Our vision is to scale up the Moss Mine
into a much larger operation by capturing these optimization opportunities,
expanding resources and making new regional discoveries like we aim to do
through our recently announced work at West Oatman."
Vein Geology South of the Center Pit: Ruth Vein Drilling Area
The Ruth Vein is a fault-hosted epithermal quartz-calcite vein and vein
stockwork that is very similar to and was likely formed at the same time as
the Moss Vein. The Ruth vein strikes slightly north of east and dips to the
north towards the south-dipping Moss Vein. The intersection of the two veins
is approximately 100 meters below the south wall of the Center pit. The Ruth
Vein is subparallel to the Moss Vein and has been delineated over a strike
length of approximately 510 meters. The Ruth Vein ranges from less than a
meter to almost 15 meters thick. When hanging wall stockworks are included,
especially in the upper parts of the fault-hosted vein system, overall
thickness increases to almost 30 meters in places. The Moss Vein dips to the
south at approximately 70 degrees in this area.
Resource Expansion Drilling
Assay results for 18 reverse circulation (RC) drillholes drilled from
four different locations are included in this news release (see Table 1).
Numerous thick zones of epithermal vein-hosted gold and silver mineralization
have been intersected adjacent to the Moss Center Pit (Figure 1 Ruth Vein
Drilling Area Location Map; Figure 2 Drillhole Location Map).
Significant intersections include drillhole AR20-359R which returned
28.96 meters grading 2.28 g/t gold, and 28.84 g/t silver (2.66 g/t gold
equivalent), including 9.15 meters grading 4.90 g/t gold and 57.18 g/t silver
(5.67 g/t gold equivalent) for the Moss Vein below the Center pit, and
drillhole AR20-364R, which returned 16.76 meters grading 1.75 g/t gold, and
14.08 g/t silver, (1.94 g/t gold equivalent), including 4.6 meters grading
4.01 g/t gold and 27.97 g/t silver (4.37 g/t gold equivalent), in the Ruth
Vein to the south of and below the Center pit (Figure 3 Cross Section: Well 16
Site, Ruth Vein Drilling Area).
The Moss Mine resource expansion drilling continues to demonstrate strong
and consistent gold and silver mineralization along the Ruth vein
approximately 100 meters south of the crest of the Moss mine Center pit, and
in the Moss Vein approximately 100 meters below the Center pit.
Table 1: Results of Northern Vertex's 2020 Resource Expansion RC Drilling
in the Ruth Vein Drilling Area
Drillhole

Location

Az/Dip              From                      To    Length      Au        
Ag       AuEq

(Degrees)            (m)                       (m)     (m)     (g/t)     
(g/t)      (g/t)

---

AR20-352R
Well 17
205/-45       16.76                     27.43     10.67      0.29       
0.71        0.30

---

Including                                                                    
21.34        24.38                      3.05      0.48      0.30       0.48

---


And                                                                          
83.82        88.39                      4.57      0.27      0.53       0.28

---


And                                                                         
118.87       140.21                     21.34      0.27      3.14       0.31

---

Including                                                                   
129.54       132.59                      3.05      0.53      7.15       0.63

---

AR20-355R
25/-83                           141.73       260.60                    
118.87      0.30      4.67       0.36

---

Including                                                                   
167.64       179.83                     12.19      0.41      4.53       0.47

---


And                                                                         
192.02       205.74                     13.72      0.55     19.17       0.80

---

AR20-359R
Well 16
0/-85      118.87                    147.83     28.96      2.28      
28.84        2.66

---

Including                                                         129.54       
138.68                      9.14      4.90     57.18       5.67

---


And                                                                         
173.74       186.05                     12.31      0.32      5.81       0.40

---


And                                                                         
202.69       211.84                      9.14      0.85     18.63       1.10

---

AR20-363R
180/-45                            99.06       103.63                      
4.57      0.53      5.33       0.60

---

AR20-364R
180/-65                           109.73       126.49                     
16.76      1.75     14.08       1.94

---

Including                                                         109.73       
114.30                      4.57      4.00     27.97       4.37

---


And                                                                         
179.83       182.88                      3.05      0.66      2.25       0.69

---

AR20-366R
180/-81                           140.21       167.64                     
27.43      0.32      4.91       0.39

---

Including                                                                   
140.21       149.35                      9.14      0.53      8.07       0.63

---


And                                                                         
175.26       178.31                      3.05      0.39     13.25       0.57

---


And                                                                         
195.07       199.64                      4.57      0.35      1.57       0.37

---

AR20-369R
205/-65                           114.30       141.73                     
27.43      0.42      5.06       0.48

---

Including                                                         123.44       
128.02                      4.57      1.27     11.63       1.43

---

AR20-356R
Mid-Tier
180/-88
No Significant Intersections

---

AR20-357R
180/-70
No Significant Intersections

---

AR20-358R
180/-45
No Significant Intersections

---

AR20-360R
270/-75                            50.29        67.06                     
16.76      0.30      2.67       0.33

---

AR20-361R
310/-85                            74.68        77.72                      
3.05      0.38      3.35       0.42

---

AR20-362R
200/-80
No Significant Intersections

---

AR20-367R
ROM Pad 2
0/-75       56.39                     85.34     28.96      0.30       
4.96        0.37

---

Including                                                                    
68.58        71.63                      3.05      0.81     10.25       0.94

---

AR20-368R
0/-65                            32.00        45.72                     
13.72      0.44     10.72       0.59

---

Including                                                          42.67        
45.72                      3.05      1.13     29.40       1.52

---


And                                                                          
70.10        80.77                     10.67      0.28      1.27       0.30

---


And                                                                         
120.40       126.49                      6.10      0.29      1.70       0.31

---

And                                                               256.03       
275.84                     19.81      0.45      0.88       0.46

---

Including                                                         268.22       
272.80                      4.57      1.12      0.70       1.13

---

AR20-370R
45/-75                            60.96        85.34                     
24.38      0.29      4.46       0.35

---

Including                                                                    
60.96        68.58                      7.62      0.57      8.06       0.68

---

AR20-371R
45/-60                            27.43       303.28                    
275.84      0.27      3.75       0.32

---

Including                                                                    
28.96        41.15                     12.19      0.45      1.55       0.47

---

Including                                                                    
85.34        92.96                      7.62      0.66      1.30       0.67

---

Including                                                                   
140.21       144.78                      4.57      0.43      0.77       0.44

---

Including                                                                   
198.12       295.66                     97.54      0.41      8.61       0.52

---

Including                                                                   
216.41       225.55                      9.14      0.74     19.88       1.01

---

Including                                                                   
234.70       243.84                      9.14      1.01     26.88       1.37

---

Including                                                                   
286.51       294.13                      7.62      0.49      3.32       0.54

---

AR20-372R
340/-60                            25.91        30.48                      
4.57      0.36     15.57       0.57

---


And                                                                          
64.01        70.10                      6.10      1.10     21.57       1.38

---


And                                                                          
96.01       109.73                     13.72      0.33      1.19       0.34

---


And                                                                         
123.44       126.49                      3.05      0.26      0.95       0.27

---


And                                                                         
143.26       147.83                      4.57      0.61      4.50       0.67

---


And                                                                         
176.78       187.45                     10.67      0.28      2.37       0.32

---


And                                                                         
234.70       242.32                      7.62      0.24      1.18       0.25

---


And                                                                         
251.46       260.60                      9.14      0.35      1.20       0.37

---
Note: True thickness ranges between
approximately 62% of the reported
interval thickness for subvertical
drilling and 99% for drilling
inclined at -45 degrees to the
Ruth vein. Assay data are
uncapped. AuEq (equal sign) Au + Ag/75. RC
drilling was conducted by Boart
Longyear. RC samples, collected
every 1.52 m, were transported in
sealed bags to Skyline Assayers
and Laboratories (Skyline) in
Tucson, AZ. Field control QAQC
samples, including standards,
blanks, and field duplicates, wereinserted into the sample stream at
a rate of three field control
samples approximately every 20
regular samples. Gold was
determined by fire-assay fusion
of a 30 g sub-samples with atomic
absorption spectroscopy (method
FA-01). Overlimit samples of gold
were assayed by gravimetric means
(FA-02). Skyline Laboratories is
accredited in accordance with ISO/
IEC 17025:2017 and ISO 9001:2015.
Qualified Person
Dr. Warwick Board, P.Geo., Vice President Exploration of Northern Vertex,
is the Qualified Person as defined by NI 43-101 responsible for the Moss
Regional Exploration Project and has reviewed and approved the scientific and
technical information in this news release related thereto.
About Northern Vertex Mining Corp.
Northern Vertex offers investors a rare combination of cash flow,
production, top-tier management, and exceptional exploration potential within
two projects on the Walker Lane Gold Trend of western Nevada and Arizona.
Management is executing a clear strategy that expands production and resources
at the Moss Mine in Arizona while aggressively exploring the Hercules Project
in Nevada.
ON BEHALF OF THE BOARD OF NORTHERN VERTEX MINING CORP
"Michael G. Allen"President
TSXV: NEE | Nasdaq Intl: NHVCF | Frankfurt: 54N | ISIN: CA6660061012 |
WKN: A1JUA0
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary Statement Regarding Forward-Looking Information
All statements, trend analysis and other information contained in this
press release about anticipated future events or results constitute
forward-looking statements. Forward-looking statements are often, but not
always, identified by the use of words such as "seek", "anticipate",
"believe", "plan", "estimate", "expect" and "intend" and statements that an
event or result "may", "will", "should", "could" or "might" occur or be
achieved and other similar expressions. All statements, other than statements
of historical fact, included herein, are forward-looking statements. Although
Northern Vertex believes that the expectations reflected in such
forward-looking statements and/or information are reasonable, undue reliance
should not be placed on forward-looking statements since Northern Vertex can
give no assurance that such expectations will prove to be correct. These
statements involve known and unknown risks, uncertainties and other factors
that may cause actual results or events to differ materially from those
anticipated in such forward-looking statements, including the risks,
uncertainties and other factors identified in Northern Vertex's periodic
filings with Canadian securities regulators. Forward-looking statements are
subject to business and economic risks and uncertainties and other factors
that could cause actual results of operations to differ materially from those
contained in the forward-looking statements. Important factors that could
cause actual results to differ materially from Northern Vertex's expectations
include risks associated with the business of Northern Vertex; risks related
to reliance on technical information provided by Northern Vertex; risks
related to exploration and potential development of Northern Vertex's
projects; business and economic conditions in the mining industry generally;
fluctuations in commodity prices and currency exchange rates; uncertainties
relating to interpretation of drill results and the geology, continuity and
grade of mineral deposits; the need for cooperation of government agencies in
the exploration and development of properties and the issuance of required
permits; the need to obtain additional financing to develop properties and
uncertainty as to the availability and terms of future financing; the
possibility of delay in exploration or development programs and uncertainty of
meeting anticipated program milestones; uncertainty as to timely availability
of permits and other governmental approvals; and other risk factors as
detailed from time to time and additional risks identified in Northern
Vertex's filings with Canadian securities regulators on SEDAR (available at
www.sedar.com). Forward-looking statements are based on estimates and opinions
of management at the date the statements are made. Northern Vertex does not
undertake any obligation to update forward-looking statements except as
required by applicable securities laws. Investors should not place undue
reliance on forward-looking statements.
View original content to download
multimedia:http://www.prnewswire.com/news-releases/northern-vertex-intersects-
28-96-meters-grading-2-28-gt-gold-and-28-84-gt-silver-in-resource-expansion-dr
illing-at-the-moss-mine-arizona-301293209.html
SOURCE Northern Vertex Mining Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/May2021/18/c7560.html

-0-                           05/18/2021
/For further information: CORPORATE INQUIRIES: Michael G. Allen,
President, Company Website: www.northernvertex.com, +1 (855) 633-8798 Toll
Free, +1 (604) 601-3656 Office, Email: mike(at)northernvertex.com/
/Web Site: www.northernvertex.com /
(NHVCF NEE.)

CO:  Northern Vertex Mining Corp.
ST:  British Columbia
IN:  MNG OTC PRM MIN
SU:

-30-