Source	Marketwire
Date	11/06/2013
Time	06:00:42 AM

Company	 PAN GLOBAL RESOURCES INC.
Title	Pan Global Increases Extent, Thickness and Grade of Borate Mineralisation 
in the Valjevo Licence, Serbia





    CDNX Symbol: PGZ











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Pan Global Resources Inc.

TSX VENTURE SYMBOL: PGZ

November 6, 2013

Pan Global Increases Extent, Thickness and Grade of Borate Mineralisation in 
the Valjevo Licence, Serbia


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Nov. 6, 2013) - Pan Global 
Resources Inc. ("Pan Global" or the "Company") (TSX VENTURE:PGZ) is pleased to 
announce that it has received assay results from the 10th and 11th holes 
recently completed in the Valjevo basin which have significantly increased the 
extent, thickness and overall grade of borate mineralization while providing a 
vector to shallower, and thicker mineralization for follow up drilling.

Hole VBN-011 has intersected the shallowest and thickest mineralization to date 
with 20.9m of preserved borate from 258.4m with a best 3m assaying 14.13%B2O3 
from 264.4m. This width included 1 metre intervals of 14.7, 15.13 and 
13.2%B2O3. These grades continue to compare well to drill results from Rio 
Tinto's Jadar deposit 56km away, which has an average grade of 12.9% B2O3 and 
1.8% Li2O and is now undergoing feasibility studies.

Including these recent results, 7 of the 11 holes drilled by the company in the 
basin to date have directly intersected borate mineralization over an area now 
estimated at between 9.3km2 and 14.7 km2, and three other holes have 
intersected pseudomorphs of pre-existing borate mineralization which further 
extend the zone of potential mineralization. See Figure 1 on link below.

http://clients.blendermedia.com/panglobal/nr_2013_11_05_figures.pdf

Julian Bavin, President and CEO of Pan Global stated, 'We are very encouraged 
by the results of this latest drilling which continue to show grades which 
compare well to drill results from Rio Tinto's Jadar deposit, but which suggest 
potential mineralization of considerably greater extent. We have little doubt 
that further drilling will continue to provide evidence that Valjevo hosts a 
major body of borate mineralization. In addition we still have 7 high priority 
licenses which warrant drilling, any of which could contain similar or better 
bodies of borate and associated mineralization."

These latest results have been incorporated into a weighted grade distribution 
(grade x thickness of preserved borate) that indicate a thickening and 
shallowing of mineralization to the northwest. It also suggests a vector to the 
core of the mineralized system to the west and north- west of hole 11 that will 
be the focus of future drilling. For full details of assays and calculations 
please see Figure 2 on same link above.

In other work, further follow up geological assessment has resulted in further 
prioritization of the remaining licenses with the result that a total of 7 have 
been assessed as high priority. See Figure 3 on same link above.

The technical information provided in this news release was reviewed and 
approved by Robert. W. Baxter (FAusIMM), a director of the Company and a 
qualified person for the purposes of National Instrument 43-101. Pan Global 
core samples are delivered to the ALS laboratory in Romania, where all samples 
are bar-coded, weighed, air-dried, crushed and pulverized. The prepared 
pulverized samples are sent to the ALS laboratory in Vancouver, British 
Columbia for analyses by ICP-AES for 34 elements.

www.panglobalresources.com.

NEITHER TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT TERM 
IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS RESPONSIBILITY 
FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

Shares Issued and Outstanding: 38,230,187

- 30 -

CONTACT INFO:

Pan Global Resources Inc.
Mr. Julian Bavin
President and CEO
jbavin@panglobalresources.com

or

Pan Global Resources Inc.
Dan McIntyre
Investor Relations
dmcintyre@panglobalresources.com
www.panglobalresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=452941966