Source	Marketwire
Date	11/12/2013
Time	04:00:39 AM

Company	 UNIGOLD INC.
Title	Unigold Reports Initial 2.0 Million Ounce Gold Inferred Mineral Resource 
at Candelones Project in the Dominican Republic





    CDNX Symbol: UGD











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Unigold Inc.

TSX VENTURE SYMBOL: UGD

November 12, 2013

Unigold Reports Initial 2.0 Million Ounce Gold Inferred Mineral Resource at 
Candelones Project in the Dominican Republic


TORONTO, ONTARIO--(Marketwired - Nov. 12, 2013) - Unigold Inc. ("Unigold" or 
the "Company") (TSX VENTURE:UGD) is pleased to report the initial mineral 
resource estimate for its 100% owned Candelones Main, Extension and Connector 
Zones ("Candelones Project") within the Company's wholly owned, 22,600 hectare 
Neita Concession in the Dominican Republic.

Summary:

/T/

Open pit (inferred)   33.8 M tonnes averaging 1.5 g/t Au    1.6 M ounces Au
Underground
(inferred)            5.7 M tonnes averaging 2.4 g/t Au    0.4 M ounces Au
---------------------------------------------------------------------------
TOTAL                 39.5 M tonnes averaging 1.6 g/t Au    2.0 M ounces Au

/T/

The mineral resource was estimated by Mr. W. Lewis, P.Geo. and Mr. A. San 
Martin, MAusIMM(CP) of Micon International Limited. 
(www.micon-international.com, "Micon"), a Toronto based consulting company, 
independent of Unigold. Mr. Lewis and Mr. San Martin both meet the requirements 
of a "qualified person" as established by the Canadian Institute of Mining, 
Metallurgy and Petroleum (CIM) Definition Standards for Mineral Resources and 
Mineral Reserves (2010) ("the CIM Standards").

Andrew Cheatle, President and CEO of Unigold notes: "We are delighted with the 
results of our maiden mineral resource estimate at Candelones which we 
delivered within 18 months of discovering significant gold mineralization, with 
exceptional continuity, at the Candelones Extension. This multi-million ounce 
mineral resource represents only a small portion of our land position and 
confirms that the Central Cordillera of the Dominican Republic offers 
outstanding potential for additional significant discovery: a potential that we 
intend to capture as we begin to evaluate multiple targets along the Candelones 
trend and elsewhere within our 22,600 hectare concession."

Summary of Estimation Methodology

Micon completed a site visit to the Candelones Project in May, 2013, reviewing 
the Company's drilling, logging, sampling, chain of custody, quality assurance, 
database and data management procedures. During the site visit, Micon 
independently collected samples for analysis independent of Unigold. Micon 
notes that their site visit and subsequent review did not identify any 
significant errors or omissions that would materially affect the mineral 
resource estimate and further note that the results of their independent 
sampling are consistent with the sample results provided by Unigold. Micon did 
advise that the silver, copper and zinc grades may offer additional value that 
the mineral resource estimate does not capture. The Company has chosen to await 
the results of additional metallurgical testing that is specifically designed 
to evaluate copper and zinc recovery, before estimating the potential impact on 
the mineral resource estimate.

Micon received the final drilling database for the Candelones Project 
consisting of 315 drill holes and over 48,000 individual sample intervals. 
Micon verified a representative subset of the final database, through direct 
comparison to original logs, sample logs and certified assay certificates. 
Micon also reviewed the quality assurance and quality control procedures 
established by Unigold and determined that the data was free of gross errors 
and omissions and was collected according to industry accepted best practices 
as established by the Canadian Institute of Mining Metallurgy and Petroleum's 
Exploration Best Practices Guidelines.

Micon advises that the drill hole spacing at the Candelones Main and Connector 
Zones is approximately 50 metres while at the Candelones Extension deposit, the 
drilling was completed on sections that were spaced on 100 metre intervals. 
Micon is confident that the drill hole spacing is adequate to support an 
inferred mineral resource classification.

Micon received, reviewed and where warranted, edited the company's geological 
interpretation of the Candelones Main, Connector and Extension Zones prior to 
utilizing said interpretation in estimating the mineral resource.

Micon independently completed the statistical and geostatistical analyses of 
the data, established the block model parameters and interpolated grades into 
the model blocks based on their geostatistical analyses. Micon verified the 
grade interpolation utilizing industry standard methods and procedures. Micon 
then utilized industry standard open pit optimization software to evaluate the 
portion of the block model recoverable by open pit mining and reported this as 
the inferred open pit mineral resource.

Micon then evaluated the model blocks external to the optimized pit shells and 
concluded a portion of that material would be recoverable utilizing underground 
mining methods. This was reported as an inferred underground mineral resource.

Micon's mineral resource estimate is further sub-divided into oxide and 
sulphide components, recognizing the more robust metallurgical recovery of the 
oxide component. Micon notes that the oxide mineral resource is restricted to 
the near surface mineralization the Candelones Main and Connector deposits with 
no oxide mineral resource identified at the Candelones Extension.

Micon then classified and reported the mineral resource according to Canadian 
Institute of Mining, Metallurgy and Petroleum's Definition Standards for 
Mineral Resources and Mineral Reserves.

A Technical Report supporting the mineral resource estimate disclosed herein is 
currently underway.

The Effective Date of the Inferred Mineral Resource Estimate disclosed herein 
is November 4, 2013.

Table 1 summarizes Micon's mineral resource estimate and highlights the key 
assumptions used to complete the estimate.

/T/

Table 1 - Inferred Mineral Resource Estimate for the Candelones Project as
at November 4, 2013

---------------------------------------------------------------------------
Source      Mineralization Deposit       Tonnes       Au     Au ozs   Strip
Type                       (x1,000)    (g/t)  (x 1,000)   Ratio
---------------------------------------------------------------------------
Open Pit    Oxide          Extension          -        -          -       -
Main           2,448     0.92         72     1.3
Connector      1,108     1.12         40     1.3
---------------------------------------------------------------
Subtotal                      3,556     0.98        112     1.3
---------------------------------------------------------------
Sulphide       Extension     24,223     1.59      1,241     7.6
Main           5,003     1.16        186     1.3
Connector        980     1.08         34     1.3
---------------------------------------------------------------
Subtotal                     30,206     1.50      1,461     6.4
---------------------------------------------------------------------------
Subtotal                                 33,762     1.45      1,573     5.8
---------------------------------------------------------------------------
Underground Sulphide       Extension      4,977     2.42        387
Main             704     2.21         50
Connector         50     2.49          4
---------------------------------------------------------------------------
Subtotal                                  5,731     2.39        441
---------------------------------------------------------------------------
ALL                                      39,493     1.59      2,014
---------------------------------------------------------------------------

/T/

Notes:

/T/

1.  The mineral resource estimate presented above has been prepared under
the supervision of Mr. Alan J. San Martin, MAusIMM(CP) and Mr. William
J. Lewis (P.Geo.) of Micon International Limited., both of whom are
"qualified persons" as per the CIM Standards and independent of Unigold
Inc. The Effective date of the mineral resource estimate is November 4,
2013.
2.  The mineral resource estimate presented above is classified as an
Inferred Mineral Resource. The CIM Standards define a Mineral Resource
as "a concentration of material in or on the Earth's crust in such form
and quantity and of such grade or quality that it has reasonable
prospects for economic extraction." The CIM Standards further define an
Inferred Mineral Resource as "that part of a Mineral Resource for which
quantity and grade or quality can be estimated on the basis of
geological evidence and limited sampling and reasonable assumed but not
verified, geological and grade continuity." The CIM Standards state;
"Due to the uncertainty that may be attached to Inferred Mineral
Resources, it cannot be assumed that all or part of an Inferred Mineral
Resource will be upgraded to an Indicated or Measured Mineral Resource
as a result of continued exploration."
3.  Micon has not identified any legal, political, environmental or other
risks that could materially affect the potential development of the
mineral resource estimate presented.
4.  The mineral resource estimate presented above includes both open pit
mineral resources; reported within an optimized pit shell and
underground mineral resources; reported below the optimized pit shell.
Both open pit and underground mineral resources are reported above an
estimated economic cut-off grade developed using the following key
economic assumptions.

/T/

Key Economic Assumptions:

/T/

Gold Price                             US $1,500 per ounce
Mining Costs            Open Pit       US $2.00 per tonne
Underground    US $30.00 per tonne
Process Costs           Oxide          US $10.00 per tonne
Sulphide       US $18.00 per tonne
G&A Costs                              US $2.50 per tonne
Recovery                Oxide          95%
Sulphide       84%
Pit Slope Limits                       45 degrees
Estimated Cutoff Grades
Open Pit              Oxide          0.32 g/t Au
Sulphide       0.56 g/t Au
Underground           Oxide          Not applicable
Sulphide       1.25 g/t Au

/T/

Premier Mining Destination - Dominican Republic

The Dominican Republic is host to world-class gold and base metal mines and 
deposits. The government supports development and exploration in the mining 
sector. In addition, the country has well established Mining Laws and 
Environmental Laws. Unigold's wholly owned flagship property, Neita is 
compliant with all mineral and environmental requirements and work is conducted 
to internationally accepted environmental and social standards. The Neita 
concession exploration license was renewed in 2012 and is in good standing.

Unigold has sufficient funding to meet the goals and objectives established for 
the current exploration program.

QA/QC

Diamond drilling at the Candelones Project included both HQ and NQ diameter 
core for sampling. Holes were typically started with larger diameter HQ core 
and the hole diameter is reduced to NQ at depth. Samples are logged, split by 
wet diamond saw, and half sent for assaying with the other half stored on site. 
Sample lengths typically average 1 m, but vary by geological boundaries. 
Continuous chip samples from trenches are typically 3 m to 5 m in length. QA/QC 
included inserting certified standards and blanks into the sample stream at 
industry standard intervals. Samples are prepped by ACME Analytical Labs in the 
Dominican Republic, with assaying performed through ACME's laboratory in 
Santiago, Chile. Analytical procedures include a 36-element ICP-ES analysis 
(1E) and a 50 g FA AA finish for gold (G6-50).

W. Lewis P.Geo. and A. San Martin, MAusIMM(CP), both employed by Micon 
International Limited., were the "qualified persons" supervising the mineral 
resource estimate. Both are independent of Unigold and both have reviewed the 
contents of this press release.

Wes Hanson P.Geo., Chief Operating Officer of Unigold, has reviewed and 
approved the contents of this press release.

About Unigold Inc. - Discovering Gold in the Caribbean

Unigold is a Canadian based mineral exploration company traded on the TSX 
Venture Exchange under the symbol UGD, focused primarily on exploring and 
developing its gold assets in the Dominican Republic.

Forward-looking Statements

Certain statements contained in this document, including statements regarding 
events and financial trends that may affect our future operating results, 
financial position and cash flows, may constitute forward-looking statements 
within the meaning of the federal securities laws. These statements are based 
on our assumptions and estimates and are subject to risk and uncertainties. You 
can identify these forward-looking statements by the use of words like 
"strategy", "expects", "plans", "believes", "will", "estimates", "intends", 
"projects", "goals", "targets", and other words of similar meaning. You can 
also identify them by the fact that they do not relate strictly to historical 
or current facts. We wish to caution you that such statements contained are 
just predictions or opinions and that actual events or results may differ 
materially. The forward-looking statements contained in this document are made 
as of the date hereof and we assume no obligation to update the forward-looking 
statements, or to update the reasons why actual results could differ materially 
from those projected in the forward-looking statements. Where applicable, we 
claim the protection of the safe harbour for forward-looking statements 
provided by the (United States) Private Securities Litigation Reform Act of 
1995.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

To view the map accompanying this press release please click on the following 
link: http://media3.marketwire.com/docs/UGD1112.pdf

- 30 -

CONTACT INFO:

Unigold Inc.
Mr. Andrew M. Cheatle, P.Geo
President & CEO
acheatle@unigoldinc.com

or

Unigold Inc.
Ms. Amanda Dillon
Investor Relations
416.866.8157
Fax: 416.866.8674
adillon@unigoldinc.com
www.unigoldinc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=454226980