Source	Marketwire
Date	11/28/2013
Time	11:22:29 AM

Company	 KESTREL GOLD INC.
Title	Kestrel Gold Inc. Announces Summer-Fall Drilling Results at King Solomon's 
Dome Property, Yukon and Termination of Rackla Metals Inc. Option





    CDNX Symbol: KGC











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Kestrel Gold Inc.

TSX VENTURE SYMBOL: KGC

November 28, 2013

Kestrel Gold Inc. Announces Summer-Fall Drilling Results at King Solomon's Dome 
Property, Yukon and Termination of Rackla Metals Inc. Option


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Nov. 28, 2013) -

NOT FOR DISTRIBUTION TO U.S. NEWSWIRE SERVICES OR FOR DISSEMINATION IN THE 
UNITED STATES

Mr. Kevin Nephin, the President of Kestrel Gold Inc. ("Kestrel" or the 
"Corporation") (TSX VENTURE:KGC) announces the results of the summer-fall 
diamond drilling program carried out on the King Solomon's Dome ("KSD") 
property in conjunction with Rackla Metals Inc. ("Rackla"). The road accessible 
property, jointly explored by the Corporation and Rackla, is located in the 
heart of the Klondike goldfields, roughly 30 km southeast of Dawson City in the 
Yukon Territory.

Three diamond drill holes were completed (1,191m), spaced approximately 250 to 
300 metres apart, to test known quartz veins, surface rock and soil geochemical 
anomalies and resistivity and induced polarization (IP) geophysical anomalies. 
The holes were drilled on a westerly to south westerly azimuth and inclined 
between 50 and 55 degrees at the collars. A map of the drill locations will be 
shown on Kestrel's website at www.kestrelgold.com.

All three holes intersected low grade gold mineralization with some high grade 
gold (up to 4.89 g/t Au) in hole DDH13-02, particulars of which are set forth 
below.

/T/

----------------------------------------------------------------------------
INTERVAL (m)
INTERVAL
HOLE                       From             To     LENGTH (m)         Au g/t
----------------------------------------------------------------------------
----------------------------------------------------------------------------
DDH13-01                  217.0          218.0            1.0           0.35
----------------------------------------------------------------------------
DDH13-01                  223.0          224.0            1.0           0.27
----------------------------------------------------------------------------
----------------------------------------------------------------------------
DDH13-02                   34.0           43.0            9.0           0.27
----------------------------------------------------------------------------
including                                               2.0           0.66
----------------------------------------------------------------------------
DDH13-02                  53.90          57.91           4.01           0.27
----------------------------------------------------------------------------
including                                              0.13           4.89
----------------------------------------------------------------------------
DDH13-02                   63.0          65.53           2.53           0.50
----------------------------------------------------------------------------
including                                              0.53           1.80
----------------------------------------------------------------------------
DDH13-02                  116.0          118.0            2.0           0.43
----------------------------------------------------------------------------
DDH13-02                  121.0         126.09           5.09           0.35
----------------------------------------------------------------------------
including                                              0.29           1.08
----------------------------------------------------------------------------
DDH13-02                  244.0         246.00            2.0           0.37
----------------------------------------------------------------------------
----------------------------------------------------------------------------
DDH13-03                  189.0          195.5            6.5           0.65
----------------------------------------------------------------------------
including                                               1.5           2.48
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

The several intervals of gold mineralization in DDH13-02 between 34 metres and 
127 metres down hole, are believed to be related to the easterly dipping Sheba 
Vein system and it's hanging wall mineralization as was sampled in 2011 by 
Kestrel at surface (see Kestrel Gold Inc. news release: December 16, 2011). The 
gold mineralization, although generally low grade, shows continuity with 
surface trench sampling and remains open to depth.

The two zones of gold mineralization encountered in DDH13-01 and DDH13-03 are 
believed correlate with the geophysical chargeability anomaly at depths of 217 
- 224 metres and 189 - 195.5 metres respectively and increased sulphide content.

At least two phases of silicification are recognized, with the later quartz 
veining generally having increased gold content. Where gold mineralization 
occurs, quartz veins and silicified wall rock in some cases, exhibit very 
localized brecciation with sulphides, mainly pyrite, occurring as matrix 
in-fills, fracture filling as well as being disseminated. Occasional blebs of 
galena and sphalerite are present. The sulphide zones often have corresponding 
elevated arsenic and/or elevated lead and zinc values with sporadic silver 
values up to 45.6 g/t Ag, consistent with surface pathfinder geochemical 
signatures. Sericitic and limonitic alteration is proximal to the anomalous and 
mineralized quartz veins in places. Haloes of wall rock with increased 
magnetite occur several metres from the gold mineralization in DDH13-03.

The Klondike chloritic schist host lithology is fairly homogeneous across the 
three holes but the level of structural complexity varies - suggesting that the 
frequency, distribution, orientation and nature of cross cutting structures 
needs to be incorporated into the geological model to help delineate possible 
zones of higher grade gold and silver mineralization.

No visible gold was encountered as has been historically reported at surface 
and no samples returned greater than 5 g/t Au in the three holes. Kestrel is 
planning to conduct further analyses to investigate if a "nugget effect" is 
present in some of the drill core. The limited scope of the 2013 fall drilling 
campaign has partially explained the large geophysical anomaly but large areas 
of the soil and rock surface geochemical anomaly remain untested. Kestrel is of 
the opinion that this initial and modest diamond drill program does not 
preclude the possibility that high grade zones of gold and silver 
mineralization are present elsewhere on the KSD Property.

Untested zones include:

/T/

--  Other geophysical anomalies - in particular on the western side of the
KSD Property nearer to the "Dome" peak - that have different resistivity
signatures to the drilled anomaly.
--  The high grade gold area sampled in the vicinity of the Mitchell vein
some 750 metres NNW of DDH13-02 with a corresponding geochemical soil
anomaly (Kestrel news releases: December 16 and 14, 2011).
--  The property wide extent of the large gold geochemical soil anomaly with
samples of up to 4 g/t Au some 1.5km along strike south from DDH13-03.

/T/

Planned further drilling and trenching in 2014 is anticipated to coincide with 
a first phase diamond drilling program on the Corporation's Gold Run property 
20 km along strike of the KSD Property, where Kestrel's 2011 soil sampling 
program has confirmed the presence of previously defined anomalous gold in soil 
in the area of the "Doron Zone" trenches (see Kestrel news release: November 
18, 2011). All anticipated 2014 exploration work on the KSD Property and Gold 
Run property is contingent upon Kestrel obtaining further financing.

Kestrel has been advised by Rackla that sampling was conducted under the 
supervision of the on-site project geologist of Rackla. Samples were tracked by 
the project geologist from the project site to the sample preparation facility 
and were transported by Rackla personnel or commercial trucking companies.

Samples are generally 0.5 to 1.5 m in length. Rock pulp standards, blank gravel 
aggregate, and lab duplicates were inserted into the sample stream each at a 
rate of one per 30 samples, for a total of 9-per-cent check samples. All data 
received from the laboratory was verified for quality control using both the 
laboratory and the inline check samples.

All samples were sent to Acme Analytical Laboratories Ltd.'s preparation 
facility in Whitehorse, Yukon Territory, for crushing and pulping. Pulp splits 
were forwarded from Whitehorse by Acme to its laboratory in Vancouver, B.C., 
for analysis. Gold in rock samples was determined by a 30-gram fire assay 
fusion followed by ICP-ES analysis (method 3B01). An additional 32 elements 
were analyzed by a 0.5-gram sample split leached in hot aqua regia followed by 
ICP-ES analysis (method 1D).

The reader is referred to Kestrel's website at www.kestrelgold.com for 
background information on the KSD property.

In addition to the foregoing, Rackla has terminated the previous announced 
Option Agreement, dated August 30, 2013 and has relinquished all interest 
whatsoever back to Kestrel in the KSD Property.

Technical aspects of this news release have been reviewed and approved by W. A. 
Taylor, P. Geo, hereby designated as a qualified person under National 
Instrument 43-101.

About Kestrel Gold Inc.

Kestrel Gold Inc. is a gold exploration corporation headquartered in Canada. 
Kestrel Gold (TSX VENTURE:KGC) is listed on the TSX Venture Exchange Inc. 
Kestrel, in conjunction with Rackla is the first to diamond drill at the KSD 
property which is the high point of a prominent topographical feature from 
which some of the richest producing placer gold creeks of the great Klondike 
gold rush (to the present day), find their headwaters. Kestrel's principal 
properties include King Solomon's Dome, Gold Run Creek and Dominion Mountain, 
located in the Dawson Mining District, Yukon Territory, Canada.

Cautionary Statements

This news release contains "forward-looking information" within the meaning of 
applicable securities laws relating to certain explorations activities, 
including the contemplated future exploration and potential mineralization of 
the King Solomon Dome group of properties. Readers are cautioned to not place 
undue reliance on forward-looking statements. Forward-looking statements are 
based on certain key assumptions made by the Corporation, including assumptions 
based on the Corporation's current exploration results, and assumptions related 
to obtaining sufficient financing and other resources to carry out any future 
exploration. Actual results and developments may differ materially from those 
contemplated by these statements depending on, among other things, the inherent 
risks involved in the exploration and development of mineral properties, the 
uncertainties involved in interpreting exploration results and other geological 
data and the ability of the Corporation to obtain the funds and resources 
required to carry out further exploration. The forward-looking statements in 
this press release are made as of the date of this release and the Corporation 
undertakes no obligation to update publicly or revise any forward looking 
statements whether as a result of new information or otherwise, except as 
required by applicable securities laws. The Corporation undertakes no 
obligation to comment on analyses, expectations or statements made by third 
parties in respect of the Corporation or its financial or operating results or 
(as applicable) their securities.

The TSX Venture Exchange has not reviewed and does not accept responsibility 
for the adequacy or accuracy of this news release.

Not for distribution to U.S. Newswire Services or for dissemination in the 
United States. Any failure to comply with this restriction may constitute a 
violation of U.S. Securities laws.

- 30 -

CONTACT INFO:

Kestrel Gold Inc.
Kevin Nephin
President & CEO
(604) 824-6056
kvnephin@gmail.com
www.kestrelgold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=457619193