Source	CANADA NEWSWIRE
Date	11/25/2014
Time	05:47:51 AM

Company	 Tinka Resources Limited
Title	Tinka Discovers Tin - Copper Mineralization Beneath High-Grade Zinc at
Ayawilca, Peru





    CDNX Symbol: TK











Press Release	




" BC-Tinka-New-Tin/Copper   11-25 3078
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Tinka Discovers Tin - Copper Mineralization Beneath High-Grade Zinc at
Ayawilca, Peru@

VANCOUVER, Nov. 25, 2014 /CNW/ - Tinka Resources Limited ("Tinka" or the
"Company") (TSXV: TK) (OTCPK: TKRFF) announces the discovery of tin - copper
mineralization in drill holes at the Company's 100%-owned Ayawilca project,
central Peru. The tin mineralization was discovered in the Central Ayawilca
area following the re-assaying of nine 2012-2013 drill holes, and one recent
2014 drill hole. The tin - copper mineralization lies beneath the zinc
sulphide mineralization, which is the focus of the current drill program. Tin
(copper) mineralization at Central Ayawilca extends over an area at least 500
metres across, open in all directions, and is cassiterite, the most common ore
mineral of tin.
Dr. Graham Carman, Tinka's President and CEO, stated: "The tin and copper
mineralization discovered at Ayawilca is an exciting new development for the
project. Tin is currently valued at US$19,775 per tonne (official price on the
LME November 20, 2014) which is close to nine times the current value of zinc,
and three times copper. The potential value of a major tin - copper discovery
could therefore be substantial. We interpret that the zinc mineralization,
which occurs with abundant iron minerals, lies on the periphery of a tin -
copper porphyry system which is only now being discovered. Zinc exploration
remains the Company's focus. However, it is important for the Company to
properly assess the tin - copper potential of Ayawilca in upcoming drill
programs, so that the potential value can be unlocked."
Significant tin - copper drill results:
<<

--  A13-11: 16.2 metres at 1.03% tin and 0.67% copper from 328.0 metres
depth (hole stopped in mineralization at 344.2 metres) including 2.0
metres at 4.8% tin and 2.1% copper from 330 metres;
--  A13-12A: 30.8 metres at 0.54% tin and 0.17% copper from 326 metres
depth, including 2.0 metres at 2.5% tin and 0.2% copper from 326 metres
depth (hole stopped in mineralization at 356.8 metres);
--  A13-01: 76.0 metres at 0.21 % tin and 0.36% copper from 276 metres
depth, including 8 metres at 0.94% tin and 0.43% copper.
>>
Tin and copper mineralogy:
<<

--  Based on a mineralogical study of eight drill samples from Ayawilca, tin
occurs predominantly as cassiterite, the most common ore mineral of tin,
with only minor stannite (tin sulphide);
--  Almost half of the cassiterite in these samples is coarse-grained (> 0.3
mm), providing the opportunity for possible gravity separation of the
coarser tin fractions in any future mining operation;
--  Copper occurs as chalcopyrite, the most common sulphide mineral of
copper;
--  Tin - copper mineralization occurs in flat lying massive sulphide bodies
and stockwork vein systems underlying the zinc sulphide mineralization;
>>
Next steps:
<<

--  A new drill hole, A14-27, has recently been completed to 500.70 metres
depth, targeting tin-copper mineralization beneath drill holes A13-01
and A13-12A. Assays are pending;
--  Metallurgical tests will be carried out on the tin, including
gravimetric and flotation separation tests;
--  Exploration drilling for zinc at Ayawilca is continuing: nine holes have
been completed with four holes reported (see news release November 12
2014 , including 148 metres at 4.3% zinc in A14-22) with five holes
awaiting assays, and a further seven holes to be completed prior to the
Christmas - New Year break.
>>
Discovery of tin mineralization at AyawilcaDrill samples considered to
have 'anomalous' tin values in the ICP multi-element data were re-assayed for
ore-grade tin by a standard fusion technique. The re-assays generally returned
significantly higher tin values (i.e., anywhere between 1 and 50 times higher
than the original ICP assays). Approximately 700 samples from 18 drill holes
were re-assayed for tin by fusion. Significant tin was found in ten drill
holes (nine 2012-2013 holes and one recent 2014 hole) and these intersections
are highlighted in Table 1. The tin and copper intersections were calculated
using a 0.2% tin or 0.2% copper cut off. Drill hole collar information for all
Ayawilca holes is presented in Table 2.
Geological controls to the mineralizationA simplified geological map of
Ayawilca is shown in Figure 1. The mineralization at Ayawilca is "blind"
beneath 150 metres of flat-lying sandstone. Beneath the sandstone is a
sedimentary breccia/siltstone/limestone sequence up to 250 metres thick (Oyon
Formation) which is host to the zinc sulphide mineralization, and is the focus
of the current drill program. Zinc sulphides (with both high-iron and low-iron
sphalerites) generally occur with massive to semi-massive pyrite and/or
magnetite with minor pyrrhotite, replacing the siltstones along fracture zones
and in the matrix of the sedimentary breccias. The sedimentary rocks are
typically replaced by chlorite, clay, and siderite.
Tin - copper mineralization occurs at the base of the zinc mineralization
in two general styles; (1) disseminated in massive to semi-massive
iron-sulphide (pyrrhotite) lenses at the contact between the overlying
sedimentary sequence and underlying metamorphics (phyllite), and (2) as quartz
sulphide stockwork veinlets hosted by phyllite. The tin is predominantly
cassiterite, with stannite and rare berndtite (both tin sulphides) also noted
in mineralogical studies. Common sulphides occurring with tin are pyrrhotite
(magnetic) with lesser chalcopyrite, pyrite, arsenopyrite, and galena.
Alteration recognized within the phyllite is dominated by quartz and sericite,
with minor to trace biotite, chlorite and tourmaline.
Intrusive rocks have not yet been observed at Ayawilca. We believe that
the style of the alteration and mineralization is consistent with the source
being derived from an intrusive porphyry system at depth.
A longitudinal west-east section of Ayawilca is shown in Figure 2 showing
the styles of mineralization and conceptual targets.
QEMSCAN mineralogy studiesEight samples were chosen from two metre
composite drill samples (crushed to -2 millimetres) from different holes and
geological units for QEMSCAN analyses (Quantitative Evaluation of Materials by
Scanning Electron Microscopy) at SGS Laboratories in Santiago, Chile. Table 3
summarises the sample information. The samples sent for QEMSCAN analyses were
each between 5 and 10 kilograms, and are considered representative of the 2
metre composite intervals. In seven of eight samples, a minimum of 75% of the
tin is in the form of cassiterite. In five of these samples (62% of samples)
cassiterite represents a minimum of 94% of the tin present. Table 4 shows the
tin minerals present in each sample, and the liberation of the tin minerals.
Table 5 shows the size fraction of the tin in the combined 8 samples.
Approximately half of the cassiterite is coarser than 0.30 millimetres, and
approximately 75% of the cassiterite is coarser than 0.053 millimetres.
Colquipucro drill programTinka has now completed a 10-hole, 1,500 metre
drill program at the Colquipucro silver oxide project, located 2 kilometres
north of Ayawilca. Results of the full program will be released by the end of
January 2014.
The qualified person, Dr Graham Carman, Tinka's President and CEO, and a
Fellow of the Australasian Institute of Mining and Metallurgy, has reviewed
and verified the technical contents of this release.
About Tinka Resources Limited
Tinka is a junior resource acquisition and exploration company with
projects in Peru. Tinka's focus is on its 100%-owned Ayawilca and Colquipucro
projects in the highly mineralized zinc-lead-silver belt of central Peru, 200
kilometres north of Lima. The Ayawilca project, located 40 kilometres from
Peru's largest historic zinc mine, Cerro de Pasco, has the potential to be a
major zinc sulphide discovery. The nearby Colquipucro silver oxide project is
a near-surface, sandstone hosted silver oxide deposit with a current inferred
resource containing 32 million ounces silver with potential for expansion.
On behalf of the Board,
"Graham Carman"Dr. Graham Carman, President & CEO
Forward Looking Statements. Certain information in this news release
contains forward-looking statements and forward-looking information within the
meaning of applicable securities laws (collectively "forward-looking
statements"). All statements, other than statements of historical fact are
forward-looking statements. Forward-looking statements are based on the
beliefs and expectations of Tinka as well as assumptions made by and
information currently available to Tinka's management. Such statements reflect
the current risks, uncertainties and assumptions related to certain factors
including, without limitations, capital and other costs varying significantly
from estimates, production rates varying from estimates, changes in world
metal markets, changes in equity markets, uncertainties relating to the
availability and costs of financing needed in the future, equipment failure,
unexpected geological conditions, imprecision in resource estimates or metal
recoveries, success of future development initiatives, competition, operating
performance, environmental and safety risks, delays in obtaining or failure to
obtain necessary permits and approvals from local authorities, community
relations, and other development and operating risks. Should any one or more
of these risks or uncertainties materialize, or should any underlying
assumptions prove incorrect, actual results may vary materially from those
described herein. Although Tinka believes that assumptions inherent in the
forward-looking statements are reasonable, forward-looking statements are not
guarantees of future performance and accordingly undue reliance should not be
put on such statements due to the inherent uncertainty therein. Except as may
be required by applicable securities laws, Tinka disclaims any intent or
obligation to update any forward-looking statement.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release.
Notes on core sampling:All holes are diamond cores with recoveries
generally at or close to 100%. The drill core (typically HQ size) is marked
up, logged, and photographed on site. The cores are then cut in half at the
Company's core storage facility with half-cores stored as a future reference.
The other half-core is bagged on average over 2 metre composite intervals and
sent to SGS laboratory in Lima for assay in batches. Standards and blanks are
inserted into each batch prior to departure from the Company's core storage
facilities. At the laboratory, samples are dried, crushed to 100% passing 2mm,
then 500 grams pulverized for multi-element analysis by ICP using multi-acid
digestion. Samples assaying over 1% zinc, lead, or copper are reassayed using
precise ore-grade AAS techniques. Samples which assayed approximately 200 ppm
tin or greater in the ICP analysis were re-assayed for tin by fusion with
sodium peroxide and AAS finish (SGS laboratory method SGS-MN-ME-112).

Table 1. Summary of significant tin - copper drill intercepts from Ayawilca


Drill hole                    Depth                    To(m)                   
Interval        Sn        Cu        Zn          Pb         Ag Geology
From                                               (m)          (%)      
(%)       (%)        (%)     (g/t)
(m)
---                           ---

A14-21                                        298.00                    
300.00           2.00     1.94                0.15                        
Breccia with magnetite

and                                           308.90                    
324.00          15.10     0.35      0.08       0.18       0.06         19    
Massive Po

and                                           348.00                    
370.60          22.60     0.39      0.11       1.00       0.10         23    
Massive Po

including                    370.00                    370.60           
0.60     4.10      0.14                             11    Massive Po with 
phyllite

A12-09                                        238.00                    
250.00          12.00     0.40      0.06       3.27                    5    
Massive Po

and                                           318.00                    
328.00          10.00     0.90      0.11                              1    
Massive Po

including                            324.00                    326.00           
2.00     3.23      0.09                              1    Massive Po

A12-10                                        324.00                    
343.40          19.40     0.27      0.11                              5    
Massive Po

A13-01                                        276.00                    
352.00          76.00     0.21      0.36                              8    
Massive Po and phyllite

including                            308.00                    332.00          
24.00     0.51      0.61                             12    Massive Po with 
phyllite

including                            308.00                    316.00           
8.00     0.94      0.43                              9    Massive Po with 
phyllite

A13-04                                        342.00                    
368.00          26.00     0.22      0.69                             31    
Massive Po with phyllite

including                            348.00                    360.00          
12.00     0.18      0.99                             46    Phyllite

A13-08                                        322.00                    
337.40          15.40     0.39      0.13                              4    
Massive Po

A13-10                                        272.00                    
282.00          10.00     0.51      0.07                              3    
Breccia / semi-massive Po

and                                           298.00                    
319.50          21.50     0.20      0.13                              3    
Massive Po

A13-11(x)                                       328.00                    
344.20          16.20     1.03      0.67                             22    
Massive Po with phyllite
including                            330.00                    332.00           
2.00     4.81      2.07                             77    Massive Po with 
phyllite

A13-12A(x)                                      326.00                    
356.80          30.80     0.54      0.17                              6    
Massive Po with phyllite

including                            326.00                    328.00           
2.00     2.50      0.20                              9    Massive Po

A13-17                                        384.00                    
396.00          12.00     0.37      0.08       2.27                   25    
Massive Po
------                                        ------                    
------          -----     ----      ----       ----                  ---    
----------
Sn (equal sign) tin. Cu (equal sign) copper. Zn (equal sign) zinc. Pb (equal 
sign) lead. Ag (equal sign) silver. Po (equal sign) Pyrrhotite
All results are in weight percent except silver is grams per tonne. (x)
Drill hole ended in tin/copper mineralization
Notes on assay results:Intersections have been calculated on the basis of
a 0.2% copper or 0.2% tin cut-off over 6 metre intervals.
The tin - copper mineralization is interpreted from drill core
mea
     
8.76          10.62          16.11          13.70          11.35           
3.90           6.74
-----           ----          -----          -----          -----          
-----           ----           ----

Sn Minerals 
Locked                                                                   
18.88          12.58          35.94          17.15          16.40          
28.74          11.79          79.51
------------------                                                              
     -----          -----          -----          -----          -----          
-----          -----          -----

Total                            100.00         100.00         100.00         
100.00         100.00         100.00         100.00         100.00
(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)                            (equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)         (equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)         (equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)         (equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)         
(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)         (equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)         (equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)         (equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)
Free >(equal sign) 95%; Lib <95% & >(equal sign) 80%; Mid <80% & >(equal sign) 
50%; Sub-Mid <50% & >(equal sign)20%;
Locked <20%.
For the QEMSCAN analyses, 1 kilogram of each primary sample (crushed to
-2mm) was further reduced to 0.21 millimetres. A briquette of each sample was
introduced into an electron microscope at SGS Chile for QEMSCAN analysis. The
technique maps the surface of each mineral particle on an automated grid so
that composition and texture of each particle can be measured. Table 4 shows
only the tin minerals - the full QEMSCAN analyses provides information on all
sulphides as well as silicate and oxide minerals present.

Table 5. Average tin analysis by size fraction for the combined 8 samples


Product                                                                   
Weight % Tin grade %   Distribution %
-------                                                                    
-------   ----------     -------------

Sample + (number sign)50 
(0.30mm)                                                        48.54          
1.12              48.65

Sample + (number sign)100 
(0.15mm)                                                       11.63          
0.94              11.27

Sample + (number sign)200 
(0.074mm)                                                       9.62          
1.09              10.16

Sample + (number sign)270 
(0.053mm)                                                       4.26          
1.25               4.78

Sample + (number sign)325 
(0.044mm)                                                       1.86          
1.17               1.97

Sample + (number sign)450 
(0.030mm)                                                       2.59          
1.49               3.27

Sample PAN (<0.030mm)                                                         
21.5          1.14               19.9
--------------------                                                          
----          ----               ----
The tin analysis by size fraction was done by sieving 1 kilogram of each
sample (-2mm) to the various mesh sizes with each size fraction assayed for
tin.
Figure 1. Geology of Ayawilca-Colquipucro highlighting tin-copper and
zinc target areas at Ayawilca
Figure 2. Longitudinal section through Ayawilca showing zinc sulphide
bodies and tin - copper targets
SOURCE Tinka Resources Limited



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/November2014/25/c8056.html

PDF available at:
http://stream1.newswire.ca/media/2014/11/25/20141125_C8056_PDF_EN_8479.pdf

PDF available at:
http://stream1.newswire.ca/media/2014/11/25/20141125_C8056_PDF_EN_8480.pdf

-0-                           11/25/2014
/For further information: Investor Information: www.tinkaresources.com,
1305 - 1090 West Georgia St., Vancouver, BC, V6E 3V7, James Powell +
1-647-478-8976, Seema Sindwani +1 647-478-3017, info(at)tinkaresources.com/
/Web Site: http://www.tinkaresources.com /
(TLD TKRFF TK.)

CO:  Tinka Resources Limited
ST:  British Columbia
IN:  MNG


" BC-Tinka-New-Tin/Copper   11-25 3078
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Tinka Discovers Tin - Copper Mineralization Beneath High-Grade Zinc at
Ayawilca, Peru@

VANCOUVER, Nov. 25, 2014 /CNW/ - Tinka Resources Limited ("Tinka" or the
"Company") (TSXV: TK) (OTCPK: TKRFF) announces the discovery of tin - copper
mineralization in drill holes at the Company's 100%-owned Ayawilca project,
central Peru. The tin mineralization was discovered in the Central Ayawilca
area following the re-assaying of nine 2012-2013 drill holes, and one recent
2014 drill hole. The tin - copper mineralization lies beneath the zinc
sulphide mineralization, which is the focus of the current drill program. Tin
(copper) mineralization at Central Ayawilca extends over an area at least 500
metres across, open in all directions, and is cassiterite, the most common ore
mineral of tin.
Dr. Graham Carman, Tinka's President and CEO, stated: "The tin and copper
mineralization discovered at Ayawilca is an exciting new development for the
project. Tin is currently valued at US$19,775 per tonne (official price on the
LME November 20, 2014) which is close to nine times the current value of zinc,
and three times copper. The potential value of a major tin - copper discovery
could therefore be substantial. We interpret that the zinc mineralization,
which occurs with abundant iron minerals, lies on the periphery of a tin -
copper porphyry system which is only now being discovered. Zinc exploration
remains the Company's focus. However, it is important for the Company to
properly assess the tin - copper potential of Ayawilca in upcoming drill
programs, so that the potential value can be unlocked."
Significant tin - copper drill results:
<<

--  A13-11: 16.2 metres at 1.03% tin and 0.67% copper from 328.0 metres
depth (hole stopped in mineralization at 344.2 metres) including 2.0
metres at 4.8% tin and 2.1% copper from 330 metres;
--  A13-12A: 30.8 metres at 0.54% tin and 0.17% copper from 326 metres
depth, including 2.0 metres at 2.5% tin and 0.2% copper from 326 metres
depth (hole stopped in mineralization at 356.8 metres);
--  A13-01: 76.0 metres at 0.21 % tin and 0.36% copper from 276 metres
depth, including 8 metres at 0.94% tin and 0.43% copper.
>>
Tin and copper mineralogy:
<<

--  Based on a mineralogical study of eight drill samples from Ayawilca, tin
occurs predominantly as cassiterite, the most common ore mineral of tin,
with only minor stannite (tin sulphide);
--  Almost half of the cassiterite in these samples is coarse-grained (> 0.3
mm), providing the opportunity for possible gravity separation of the
coarser tin fractions in any future mining operation;
--  Copper occurs as chalcopyrite, the most common sulphide mineral of
copper;
--  Tin - copper mineralization occurs in flat lying massive sulphide bodies
and stockwork vein systems underlying the zinc sulphide mineralization;
>>
Next steps:
<<

--  A new drill hole, A14-27, has recently been completed to 500.70 metres
depth, targeting tin-copper mineralization beneath drill holes A13-01
and A13-12A. Assays are pending;
--  Metallurgical tests will be carried out on the tin, including
gravimetric and flotation separation tests;
--  Exploration drilling for zinc at Ayawilca is continuing: nine holes have
been completed with four holes reported (see news release November 12
2014 , including 148 metres at 4.3% zinc in A14-22) with five holes
awaiting assays, and a further seven holes to be completed prior to the
Christmas - New Year break.
>>
Discovery of tin mineralization at AyawilcaDrill samples considered to
have 'anomalous' tin values in the ICP multi-element data were re-assayed for
ore-grade tin by a standard fusion technique. The re-assays generally returned
significantly higher tin values (i.e., anywhere between 1 and 50 times higher
than the original ICP assays). Approximately 700 samples from 18 drill holes
were re-assayed for tin by fusion. Significant tin was found in ten drill
holes (nine 2012-2013 holes and one recent 2014 hole) and these intersections
are highlighted in Table 1. The tin and copper intersections were calculated
using a 0.2% tin or 0.2% copper cut off. Drill hole collar information for all
Ayawilca holes is presented in Table 2.
Geological controls to the mineralizationA simplified geological map of
Ayawilca is shown in Figure 1. The mineralization at Ayawilca is "blind"
beneath 150 metres of flat-lying sandstone. Beneath the sandstone is a
sedimentary breccia/siltstone/limestone sequence up to 250 metres thick (Oyon
Formation) which is host to the zinc sulphide mineralization, and is the focus
of the current drill program. Zinc sulphides (with both high-iron and low-iron
sphalerites) generally occur with massive to semi-massive pyrite and/or
magnetite with minor pyrrhotite, replacing the siltstones along fracture zones
and in the matrix of the sedimentary breccias. The sedimentary rocks are
typically replaced by chlorite, clay, and siderite.
Tin - copper mineralization occurs at the base of the zinc mineralization
in two general styles; (1) disseminated in massive to semi-massive
iron-sulphide (pyrrhotite) lenses at the contact between the overlying
sedimentary sequence and underlying metamorphics (phyllite), and (2) as quartz
sulphide stockwork veinlets hosted by phyllite. The tin is predominantly
cassiterite, with stannite and rare berndtite (both tin sulphides) also noted
in mineralogical studies. Common sulphides occurring with tin are pyrrhotite
(magnetic) with lesser chalcopyrite, pyrite, arsenopyrite, and galena.
Alteration recognized within the phyllite is dominated by quartz and sericite,
with minor to trace biotite, chlorite and tourmaline.
Intrusive rocks have not yet been observed at Ayawilca. We believe that
the style of the alteration and mineralization is consistent with the source
being derived from an intrusive porphyry system at depth.
A longitudinal west-east section of Ayawilca is shown in Figure 2 showing
the styles of mineralization and conceptual targets.
QEMSCAN mineralogy studiesEight samples were chosen from two metre
composite drill samples (crushed to -2 millimetres) from different holes and
geological units for QEMSCAN analyses (Quantitative Evaluation of Materials by
Scanning Electron Microscopy) at SGS Laboratories in Santiago, Chile. Table 3
summarises the sample information. The samples sent for QEMSCAN analyses were
each between 5 and 10 kilograms, and are considered representative of the 2
metre composite intervals. In seven of eight samples, a minimum of 75% of the
tin is in the form of cassiterite. In five of these samples (62% of samples)
cassiterite represents a minimum of 94% of the tin present. Table 4 shows the
tin minerals present in each sample, and the liberation of the tin minerals.
Table 5 shows the size fraction of the tin in the combined 8 samples.
Approximately half of the cassiterite is coarser than 0.30 millimetres, and
approximately 75% of the cassiterite is coarser than 0.053 millimetres.
Colquipucro drill programTinka has now completed a 10-hole, 1,500 metre
drill program at the Colquipucro silver oxide project, located 2 kilometres
north of Ayawilca. Results of the full program will be released by the end of
January 2014.
The qualified person, Dr Graham Carman, Tinka's President and CEO, and a
Fellow of the Australasian Institute of Mining and Metallurgy, has reviewed
and verified the technical contents of this release.
About Tinka Resources Limited
Tinka is a junior resource acquisition and exploration company with
projects in Peru. Tinka's focus is on its 100%-owned Ayawilca and Colquipucro
projects in the highly mineralized zinc-lead-silver belt of central Peru, 200
kilometres north of Lima. The Ayawilca project, located 40 kilometres from
Peru's largest historic zinc mine, Cerro de Pasco, has the potential to be a
major zinc sulphide discovery. The nearby Colquipucro silver oxide project is
a near-surface, sandstone hosted silver oxide deposit with a current inferred
resource containing 32 million ounces silver with potential for expansion.
On behalf of the Board,
"Graham Carman"Dr. Graham Carman, President & CEO
Forward Looking Statements. Certain information in this news release
contains forward-looking statements and forward-looking information within the
meaning of applicable securities laws (collectively "forward-looking
statements"). All statements, other than statements of historical fact are
forward-looking statements. Forward-looking statements are based on the
beliefs and expectations of Tinka as well as assumptions made by and
information currently available to Tinka's management. Such statements reflect
the current risks, uncertainties and assumptions related to certain factors
including, without limitations, capital and other costs varying significantly
from estimates, production rates varying from estimates, changes in world
metal markets, changes in equity markets, uncertainties relating to the
availability and costs of financing needed in the future, equipment failure,
unexpected geological conditions, imprecision in resource estimates or metal
recoveries, success of future development initiatives, competition, operating
performance, environmental and safety risks, delays in obtaining or failure to
obtain necessary permits and approvals from local authorities, community
relations, and other development and operating risks. Should any one or more
of these risks or uncertainties materialize, or should any underlying
assumptions prove incorrect, actual results may vary materially from those
described herein. Although Tinka believes that assumptions inherent in the
forward-looking statements are reasonable, forward-looking statements are not
guarantees of future performance and accordingly undue reliance should not be
put on such statements due to the inherent uncertainty therein. Except as may
be required by applicable securities laws, Tinka disclaims any intent or
obligation to update any forward-looking statement.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release.
Notes on core sampling:All holes are diamond cores with recoveries
generally at or close to 100%. The drill core (typically HQ size) is marked
up, logged, and photographed on site. The cores are then cut in half at the
Company's core storage facility with half-cores stored as a future reference.
The other half-core is bagged on average over 2 metre composite intervals and
sent to SGS laboratory in Lima for assay in batches. Standards and blanks are
inserted into each batch prior to departure from the Company's core storage
facilities. At the laboratory, samples are dried, crushed to 100% passing 2mm,
then 500 grams pulverized for multi-element analysis by ICP using multi-acid
digestion. Samples assaying over 1% zinc, lead, or copper are reassayed using
precise ore-grade AAS techniques. Samples which assayed approximately 200 ppm
tin or greater in the ICP analysis were re-assayed for tin by fusion with
sodium peroxide and AAS finish (SGS laboratory method SGS-MN-ME-112).

Table 1. Summary of significant tin - copper drill intercepts from Ayawilca


Drill hole                    Depth                    To(m)                   
Interval        Sn        Cu        Zn          Pb         Ag Geology
From                                               (m)          (%)      
(%)       (%)        (%)     (g/t)
(m)
---                           ---

A14-21                                        298.00                    
300.00           2.00     1.94                0.15                        
Breccia with magnetite

and                                           308.90                    
324.00          15.10     0.35      0.08       0.18       0.06         19    
Massive Po

and                                           348.00                    
370.60          22.60     0.39      0.11       1.00       0.10         23    
Massive Po

including                    370.00                    370.60           
0.60     4.10      0.14                             11    Massive Po with 
phyllite

A12-09                                        238.00                    
250.00          12.00     0.40      0.06       3.27                    5    
Massive Po

and                                           318.00                    
328.00          10.00     0.90      0.11                              1    
Massive Po

including                            324.00                    326.00           
2.00     3.23      0.09                              1    Massive Po

A12-10                                        324.00                    
343.40          19.40     0.27      0.11                              5    
Massive Po

A13-01                                        276.00                    
352.00          76.00     0.21      0.36                              8    
Massive Po and phyllite

including                            308.00                    332.00          
24.00     0.51      0.61                             12    Massive Po with 
phyllite

including                            308.00                    316.00           
8.00     0.94      0.43                              9    Massive Po with 
phyllite

A13-04                                        342.00                    
368.00          26.00     0.22      0.69                             31    
Massive Po with phyllite

including                            348.00                    360.00          
12.00     0.18      0.99                             46    Phyllite

A13-08                                        322.00                    
337.40          15.40     0.39      0.13                              4    
Massive Po

A13-10                                        272.00                    
282.00          10.00     0.51      0.07                              3    
Breccia / semi-massive Po

and                                           298.00                    
319.50          21.50     0.20      0.13                              3    
Massive Po

A13-11(x)                                       328.00                    
344.20          16.20     1.03      0.67                             22    
Massive Po with phyllite
including                            330.00                    332.00           
2.00     4.81      2.07                             77    Massive Po with 
phyllite

A13-12A(x)                                      326.00                    
356.80          30.80     0.54      0.17                              6    
Massive Po with phyllite

including                            326.00                    328.00           
2.00     2.50      0.20                              9    Massive Po

A13-17                                        384.00                    
396.00          12.00     0.37      0.08       2.27                   25    
Massive Po
------                                        ------                    
------          -----     ----      ----       ----                  ---    
----------
Sn (equal sign) tin. Cu (equal sign) copper. Zn (equal sign) zinc. Pb (equal 
sign) lead. Ag (equal sign) silver. Po (equal sign) Pyrrhotite
All results are in weight percent except silver is grams per tonne. (x)
Drill hole ended in tin/copper mineralization
Notes on assay results:Intersections have been calculated on the basis of
a 0.2% copper or 0.2% tin cut-off over 6 metre intervals.
The tin - copper mineralization is interpreted from drill core
measurements to be either gently-dipping in massive pyrrhotite sulphide lenses
or disseminated within stockwork veinlets in phyllite. The true widths of the
intercepts are believed to be at least 75% of the down-hole widths.

Table 2. Drill hole collar coordinates and hole details


Drill hole                    Easting                  Northing         
Elevation      Depth       Azimuth    Dip    Comment
----------                    -------                  --------         
---------      -----       -------    ---    -------

DRILL HOLES IN CURRENT PROGRAM:

A14-19                                        332951            
8845940           4263       407.90         360     
-75                             Zn results 11/12/2014

A14-20                                        332896            
8845986           4270       362.70         360     
-70                             Zn results 11/12/2014

A14-21                                        334112            
8846100           4000       515.00         350     -60    New tin results here

A14-22                                        333000            
8845928           4261       355.10          10     
-70                             Zn results 11/12/2014

A14-23                                        333078            
8845921           4242       323.10         360     -75    Pending

A14-24                                        334100            
8846385           4055       455.90         360     -70    Pending

A14-25                                        332903            
8846062           4263       350.40         360     -70    Pending

A14-26                                        333002            
8845930           4256        321.4         180     -85    Pending

A14-27                                        333612            
8845713           4202        500.7         360     -82    Pending

A14-28                                        334326            
8846392           4075                     340     -70    Drilling

A14-29                                        334106            
8846526           4118                     360     -70    Drilling

A14-30                                        332950            
8845942           4263                     180     -83    Drilling

PAST AYAWILCA DRILL HOLES:

A12-09                                        333389            
8846042           4191       360.80         360     -90    New tin results here

A12-10                                        333391            
8846197           4181       366.55         180     -70    New tin results here

A13-01                                        333590            
8846039           4145       359.95         180     -70    New tin results here

A13-04                                        333591            
8846038           4145       380.10         180     -60    New tin results here

A13-08                                        332954            
8846075           4252       350.60          90     -70    New tin results here

A13-10                                        333500            
8845870           4168       326.10         360   -69.9    New tin results here

A13-11                                        333500            
8845870           4168       344.20         180   -69.8    New tin results here

A13-12A                                       333691            
8846004           4133       356.80         180   -69.9    New tin results here

A13-17                                        333898            
8846294           4112       422.30         360   -75.6    New tin results here

DD52                                          332950            
8846081           4254       196.60         310     -50    Released 2011

DD66                                          332909            
8846064           4252       230.60         165     -50    Released 2011

DD67                                          332817            
8846037           4272       230.80         165     -50    Released 2011

DD68                                          332873            
8846192           4260       176.40         165     -50    Released 2011

DD69                                          332775            
8846170           4277       198.20         165     -50    Released 2011

A12-01                                        333188            
8846050           4210       327.10         360     -60    Released 2012

A12-02                                        333188            
8846049           4210       303.00         360     -90    Released 2012

A12-03                                        333194            
8846208           4227       349.45         180     -70    Released 2012

A12-05                                        332967            
8846188           4241       327.70         360     -60    Released 2012

A12-06                                        333591            
8846155           4153       359.45         360     -60    Released 2012

A12-07                                        333591            
8846154           4153       367.10         360     -90    Released 2012

A13-09                                        333188            
8846050           4210       347.80         180     -60    Released 2013

A13-13                                        333797            
8845950           4120       386.80         180   -65.5    Released 2013

A13-14                                        333500            
8846134           4167       398.70         360   -60.9    Released 2013

A12-04A                                       332967            
8846187           4241       285.60         360     -90                         
Zn re-released 11/12/2014

A12-08                                        333389            
8846042           4191       344.20         180     -70                         
Zn re-released 11/12/2014

A13-02                                        333389            
8846040           4191       370.90         180     -60                         
Zn re-released 11/12/2014

A13-03                                        333590            
8846041           4145       338.25         180     -90                         
Zn re-released 11/12/2014

A13-05                                        332954            
8846075           4252       361.50         360     -90                         
Zn re-released 11/12/2014

A13-06                                        332953            
8846074           4251       400.10         180     -70                         
Zn re-released 11/12/2014

A13-07                                        332952            
8846074           4251       314.10         270     -60                         
Zn re-released 11/12/2014

A13-15                                        333300            
8846065           4200       355.40         180   -64.9                         
Zn re-released 11/12/2014

A13-16                                        333898            
8846295           4112       454.70         360   -59.6                         
Zn re-released 11/12/2014

A14-18                                        333900            
8846429           4122       448.30         360     -60                         
Zn re-released 11/12/2014

DD52B                                         332953            
8846076           4252       318.80         360     -70                         
Zn re-released 11/12/2014

DD53                                          332967            
8846186           4241       315.10         165     -60                         
Zn re-released 11/12/2014

DD70                                          332826            
8846305           4264       243.30         165     -50                         
Zn re-released 11/12/2014

DD71                                          332733            
8846277           4291       231.10         165     -50                         
Zn re-released 11/12/2014
----                                          ------            
-------           ----       ------         ---     ---                         
-------------------------
Notes on drill hole data:Eastings and Northings are based on the
PSAD56/18S UTM datum. The coordinates for the current drill holes are
collected via a hand-held GPS and are considered accurate to within a few
metres. Drill hole locations from past programs were surveyed with a
theodolite or determined by tape and compass from a known survey point.
Elevations are taken from a digital topographic model of the project based on
a number of known points and are considered accurate to within a few metres.
Azimuth and dip measurements were taken using compass and inclinometer at
surface. All holes from A13-10 onwards were down-hole surveyed; small
variances in both azimuth and dip do occur down hole.


Table 3. Tin-copper-zinc assays of drill samples used in QEMSCAN analyses


Drill hole                    Sample no.                        Depth from     
Depth to     Sn %    Cu %      Zn %  Geology
----------                    ----------                        ----------     
--------      ---      ---        ---   -------

A12-09                                                  12803              
240          242    0.70      0.09        6.36    Sedimentary breccia

A12-09                                                  12851              
324          326    4.31      0.09        0.01    Massive Po

A13-01                                                  13174              
310          312    0.33      0.21        0.01    Massive Po

A13-04                                                  13662              
356          358    1.29      0.88        0.36    Phyllite

A13-05                                                  13715              
142          144    0.63      0.31        6.22    Sedimentary breccia

A13-11                                                  14712              
340          342    0.47      0.37        0.01    Phyllite

A13-12A                                                 14873              
346          348    0.72      0.08        0.01    Phyllite

A14-18                                                  15884              
396          398    0.23      0.17        2.58    Semi-massive Po
------                                                  -----              
---          ---    ----      ----        ----    ---------------

Table 4. Summary of tin mineral occurrence and liberation in eight QEMSCAN 
samples


Name                                                   Sample         
Sample         Sample         Sample         Sample         Sample         
Sample         Sample
12803          12851          13174          13662          13715          
14712          14873          15884
-----          -----          -----          -----          -----          
-----          -----          -----

Tin                                 
Stannite                                                        2.46           
1.56           4.59          55.69          19.91           4.86           
0.83           0.05
Occurrence
%


Cassiterite                                                                     
     81.64          95.73          94.59          44.05          78.51          
94.57          99.08          96.49
-----          -----          -----          -----          -----          
-----          -----          -----

Berndtite                                                                       
     15.90           2.70           0.82           0.26           
1.58           0.57           0.10           3.46
---------                                                                       
     -----           ----           ----           ----           
----           ----           ----           ----

Total                            100.00         100.00         100.00         
100.00         100.00         100.00         100.00         100.00
(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)                            (equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)         (equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)         (equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)         (equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)         
(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)         (equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)         (equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)         (equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)

Liberation                          Free Sn 
Minerals                                               48.57          
60.25          47.37          33.88          63.58          41.61          
75.34          12.10
%

Liberated Sn Minerals> 
80%                                                          3.04          
10.97           4.26          14.55           3.05           7.93           
2.07           0.00
----          -----           ----          -----           ----           
----           ----           ----

Sn Minerals Mid > 
50%                                                               
2.07           7.44           1.80          18.31           3.27          
10.37           6.90           1.65
----           ----           ----          -----           ----          
-----           ----           ----

Sn Minerals Sub-Mid > 
20%                                                          27.43      
     
8.76          10.62          16.11          13.70          11.35           
3.90           6.74
-----           ----          -----          -----          -----          
-----           ----           ----

Sn Minerals 
Locked                                                                   
18.88          12.58          35.94          17.15          16.40          
28.74          11.79          79.51
------------------                                                              
     -----          -----          -----          -----          -----          
-----          -----          -----

Total                            100.00         100.00         100.00         
100.00         100.00         100.00         100.00         100.00
(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)                            (equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)         (equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)         (equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)         (equal 
sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)         
(equal sign)(equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)         (equal sign)(equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)         (equal sign)(equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)         (equal sign)(equal sign)(equal 
sign)(equal sign)(equal sign)(equal sign)
Free >(equal sign) 95%; Lib <95% & >(equal sign) 80%; Mid <80% & >(equal sign) 
50%; Sub-Mid <50% & >(equal sign)20%;
Locked <20%.
For the QEMSCAN analyses, 1 kilogram of each primary sample (crushed to
-2mm) was further reduced to 0.21 millimetres. A briquette of each sample was
introduced into an electron microscope at SGS Chile for QEMSCAN analysis. The
technique maps the surface of each mineral particle on an automated grid so
that composition and texture of each particle can be measured. Table 4 shows
only the tin minerals - the full QEMSCAN analyses provides information on all
sulphides as well as silicate and oxide minerals present.

Table 5. Average tin analysis by size fraction for the combined 8 samples


Product                                                                   
Weight % Tin grade %   Distribution %
-------                                                                    
-------   ----------     -------------

Sample + (number sign)50 
(0.30mm)                                                        48.54          
1.12              48.65

Sample + (number sign)100 
(0.15mm)                                                       11.63          
0.94              11.27

Sample + (number sign)200 
(0.074mm)                                                       9.62          
1.09              10.16

Sample + (number sign)270 
(0.053mm)                                                       4.26          
1.25               4.78

Sample + (number sign)325 
(0.044mm)                                                       1.86          
1.17               1.97

Sample + (number sign)450 
(0.030mm)                                                       2.59          
1.49               3.27

Sample PAN (<0.030mm)                                                         
21.5          1.14               19.9
--------------------                                                          
----          ----               ----
The tin analysis by size fraction was done by sieving 1 kilogram of each
sample (-2mm) to the various mesh sizes with each size fraction assayed for
tin.
Figure 1. Geology of Ayawilca-Colquipucro highlighting tin-copper and
zinc target areas at Ayawilca
Figure 2. Longitudinal section through Ayawilca showing zinc sulphide
bodies and tin - copper targets
SOURCE Tinka Resources Limited



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/November2014/25/c8056.html

PDF available at:
http://stream1.newswire.ca/media/2014/11/25/20141125_C8056_PDF_EN_8479.pdf

PDF available at:
http://stream1.newswire.ca/media/2014/11/25/20141125_C8056_PDF_EN_8480.pdf

-0-                           11/25/2014
/For further information: Investor Information: www.tinkaresources.com,
1305 - 1090 West Georgia St., Vancouver, BC, V6E 3V7, James Powell +
1-647-478-8976, Seema Sindwani +1 647-478-3017, info(at)tinkaresources.com/
/Web Site: http://www.tinkaresources.com /
(TLD TKRFF TK.)

CO:  Tinka Resources Limited
ST:  British Columbia
IN:  MNG