Source	MARKET NEWS
Date	11/25/2014
Time	07:01:30 AM

Company	 Lamêlée Iron Ore Ltd.
Title	Completed 
A Preliminary Economic Assessment Whic





    CDNX Symbol: LIR











Press Release	





LAMELEE IRON ORE LTD ("LIR-V")
- Completed A Preliminary Economic Assessment Which Offers
- Very Promising Results

NOT FOR RELEASE OR DISTRIBUTION IN THE UNITED STATES OR FOR
DISSEMINATION TO US NEWSWIRE SERVICES.

The Board of directors of Lamelee Iron Ore Ltd. ("Lamelee" or
the "Company") is pleased to announce that it has received the results
of a Preliminary Economic Assessment ("PEA") prepared by CIMA+ in
respect to the Company's Lac Lamelee South Property Project (the
"Lamelee Project") located in the Province of Quebec, 50 km South of
Fermont.

A summary of the PEA results from the NI 43-101 Technical
Report is presented below. The NI 43-101 Technical Report on the PEA
will be filed on SEDAR and on the Company's website within the next 45
days.

LAMELEE PEA HIGHLIGHTS:

//st

Net Present Value ("NPV") of $529.9 M (pre-tax) at an 8% discount rate;

Internal Rate of Return ("IRR") of 15.4% (pre-tax);

Pre-tax payback estimated at 5.8 years (years from production start-up);

Mine life of 20 years at 5 million tonnes per year ("Mtpy") of iron
concentrate;

Initial project Capex of $816.7 M;

Total average operating cost of $54.81/tonne of concentrate;

Conservative long-term price assumptions US$ 79.50/tonne, FOB Sept-Iles

Accuracy of the estimate -15% + 30%.

//et

Hubert Vallee, President and CEO of Lamelee stated: "We are
very pleased with the PEA of the Lamelee Project. It shows a pre-tax
IRR of 15.4% on a capital expenditure of $ 816 million and a payback
period of 5.8 years, based on conservative long-term price assumptions.
This is one of the lowest capital expenditure requirement for this kind
of project in the Labrador Trough area. All of the numbers in the
assessment are realistic and achievable, based on recent construction
projects and successful operations recently delivered. The good
potential for mining development and production level will lead Lamelee
to the next step, namely the Bankable Feasibility Study.

Pierre Lortie, Chairman of the Board added that "the favorable
results reported in the PEA of the Lamelee Project reflect the valuable
experience and know-how of our team which will make the difference in
the success of this promising project. Our confidence in the success of
the project stems also, in part, on the superior quality of the iron
concentrate to be produced by Lamelee which opens many markets. It
needs to be emphasized that the concentrate is needed by Asian steel
mills to blend with concentrate from other producing regions, notably
Australia and Brazil, to ensure efficiency of production."

PEA PROJECT SUMMARY

The Lamelee property is located 560 km north of Baie-Comeau and
80 km (by road) south of the town of Fermont, all connected by the
provincial road 389 (the "Lamelee Property"). The Lamelee Property is
approximately 270 km in straight line north of Port-Cartier. The
Lamelee Property is accessible by road 389 and the ArcelorMittal
railroad passes by the Lamelee Property. The city of Wabush, located at
35 km of Fermont, has an airport with daily flights to Sept-Iles and
Montreal. The Lamelee Project is entirely located in Quebec.

In May 2014, Lamelee mandated CIMA+ to prepare the PEA. The
services of Met-Chem Canada Inc. ("Met-Chem") were retained to produce
an update of the mineral resource estimate, the mine design and the
mine plan. Soutex Inc. ("Soutex") provided their expertise for the
metallurgical testing and the elaboration of the process. AMEC Inc.
developed the tailings disposal strategy and the pond design. The
environmental considerations and permitting were carried out by WSP
Canada Inc. ("WSP"). Michel L. Bilodeau carried out the economic
analysis of the PEA.

UPDATED MINERAL RESOURCE ESTIMATE

The Property is located in the western margin of the Labrador
Trough that contains world-class iron deposits hosted in the Sokoman
Formation. The iron mineralization on the Property is hosted in the
Wabush Formation (metamorphosed equivalent of the Sokoman Formation).

Met-Chem carried out an updated Mineral Resource estimate based
on the results of the exploration work carried out during 2011 and
2012, which consisted of 2 trenches and 57 holes for a total of 18,221
m. Additional characterization work completed in 2014 included 3,133
Satmagan tests, 266 Davis Tube tests, as well as Heavy Liquid
Separation tests on composite samples.

The Mineral Resources were limited to the tonnage of blocks
constrained within the Iron Oxide envelopes which include MIF
(Magnetite Iron Formation), HIF (Hematite Iron Formation) and MHIF
(Mixed Magnetite Hematite Iron Formation). They don't encompass the
tonnage of QpyrxM (Silicates Iron Formation) envelope.

A 3D block model was created using the MineSight(r) software
package to discretize the project domain into blocks of 30 m by 30 m by
15 m (X, Y and Z directions). The Mineral Resource was interpolated on
the total iron content (T Fe%) using the Inverse Distance Squared
("IDW2") method. A constant density factor of 3.35, representing an
average for all iron oxides, was used to convert volumes into tonnes.

The Mineral Resource estimate was performed by Schadrac
Ibrango, P.Geo, PhD., a Qualified Person (QP). Under CIM definitions,
Mineral Resources should have a reasonable prospect of economic
extraction. Met-Chem chose to exclude the portion of the mineralization
that lies below Lac Lamelee from the Mineral Resource estimate since
the complete dewatering of Lac Lamelee, the construction of dykes to
cut-off portions of the lake or underground mining of this mineralized
material would most likely not be an economic option for the Project.
In order to determine the mineralized zones that can be potentially
mined without affecting the lake, Met-Chem created a pit shell with an
overall pit slope of 52 degrees and limited the crest of the pit to a
minimum distance of 50 m from the lake.

The resource classification follows the guidelines adopted by
the CIM through the NI 43-101 standards and guidelines. All the Mineral
Resources were classified as Inferred.

SUMMARY OF THE MINERAL RESOURCES

(Cut-Off of 15% T Fe)

//st
Category                 Tonnage                  T Fe
(Mt)                   (%)
Inferred                   354.1                 29.49

//et

Mineral resources cannot be considered Mineral Reserves until
they have demonstrated economic viability. Environmental, permitting,
legal, title, taxation, socio-political, marketing, or other relevant
issues may materially affect the estimate of mineral resources. The
quantity and grade of reported Inferred Mineral Resources in this
estimate are uncertain in nature and there has been insufficient
exploration to define these Inferred Mineral Resources as Indicated or
Measured Mineral Resources and it is uncertain if further exploration
will result in upgrading them to the Indicated or Measured Mineral
Resource categories.

MINING

In order to determine the amount of recoverable iron contained
within each block of mineralized material, Soutex provided Met-Chem
with a formula to calculate the weight recovery as a function of the
total iron which is based on the results of the metallurgical testwork.


A pit optimization analysis was then carried out using the
MS-Economic Planner module of MineSight(r) which ran the
Lerchs-Grossmann algorithm to determine the economic limits of the
deposit. The analysis showed that the open pit design for the PEA
should be based on a 20-year mine life.

The In-Pit Mineral Resources for the Lamelee Project which
account for mining dilution and losses total 272 Mt of Inferred Mineral
Resources at a Total Fe grade of 29.7% (Weight Recovery of 36.3%). In
order to access these resources, 636 Mt of overburden and waste rock
must be mined which results in a stripping ratio of 2.3 to 1.

The mining method selected for the Lamelee Project is a
conventional open pit, drill and blast, truck and shovel operation
which is carried out with an owner operated fleet. Following the
development of a 20- year mine plan, Met-Chem estimated the mine
equipment fleet to include 22 haul trucks (227 tonne), 3 electric drive
hydraulic shovels (26.5 m3 bucket), 3 production drills as well as a
fleet of support and service equipment.

METALLURGICAL AND PROCESS

The following process was designed based on the results of the
testing program.

Ground run of mine feed is discharged from the mill as a slurry
to the scalping screens and then to the classification screens.

The first stage of gravity separation is performed by rougher
spirals from where the concentrate is sent to the cleaning hydrosizers
that will efficiently remove medium and fine silica. The cleaning
hydrosizers produce a high grade concentrate at their underflows. The
hydrosizers overflow, consisting in fine iron minerals and fine silica,
is processed by the scavenger spirals.

The two (2) concentrates produced (fine and coarse) are mixed
together to produce a constant final concentrate fed to the pan
filters.

The tails of both the rougher and the scavenger spirals are
final and sent to the tailings cyclones to be processed in the tailings
dewatering circuit.

During the summer, the fine and the coarse tailings are
disposed of separately in the same settling basin. The coarse tailings
are then used for dam building.

During the winter, the fine is mixed to the coarse tailings and
disposed of together.

PRELIMINARY IRON CONCENTRATE SPECIFICATIONS

//st
Element or Mineral     Formula Typical Value  (%)
Iron                        Fe               64.3
Silica                    SiO2                4.5
Aluminium Oxide          Al2O3               0.38
Calcium Oxide              CaO               0.65
Magnesium Oxide            MgO               1.16
Sodium Oxide              Na2O               0.02
Potassium Oxide            K2O               0.01
Titanium Oxide            TiO2               0.51
Phosphorus                   P              (0.01
Manganese                   Mn               0.61
Chromium                    Cr              (0.01
Vanadium                     V              (0.01
Loss of Ignition (LOI)       -              -1.14
Sizing: -150um               -               30.0
//et

PORT FACILITIES AND PRODUCT HAULING

Lamelee plans to use the services of a local carrier to haul
the product from the mine to the Port owned by the town of
Port-Cartier.

Local infrastructures, such as car dumper, ore handling yard
and ship loading facilities will be built by Lamelee.

Transshipping will be used at the beginning to load Cape size
ships.

PRODUCT SALES PRICE

Lamelee used different analysts and bankers forecasts combined
with an independent market analysis to estimate the long-term market
price of iron concentrate. The results of this analysis are listed
below and were used in the Economic Assessment of the Project:

//st

Concentrate selling price: CAD$ 88.33/tonne, FOB Sept-Iles

//et

OPERATING COST SUMMARY

The following operating costs were estimated by CIMA+, with
input from other experienced parties. Total average operating costs
over the life of mine are estimated at CAD$ 54.81/tonneof concentrate
based on the following:
//st
OPERATING COST                   $/tonne of concentrate

Mine                                              21.92
Concentrator                                       8.24
General & administration                           7.04
Logistic                                          17.61
TOTAL                                             54.81

//et

Qualified Persons

The complete NI 43-101 Technical Report ("Report") being
prepared by CIMA+ will include an updated mineral resource estimate and
in-pit mineral resource estimate which were prepared respectively by
Schadrac Ibrango, PGeo., PhD. and Jeffrey Cassoff, Eng. of Met-Chem.
Both Mr. Ibrango and Mr. Cassoff are independent Qualified Persons as
defined by NI 43-101. The Report is being prepared under the direction
of Jean-Sebastien Tremblay, Eng. of CIMA+ and will be reviewed and
certified by individuals responsible for their respective portions of
the Report. Mr. Tremblay and all other individuals providing
certifications are Independent Qualified Persons as defined by NI
43-101. Among them are, Mr. Mathieu Girard, Eng, of Soutex, David
Bedard, Eng. of AMEC, Michel L. Bilodeau, Eng. independent consultant
and Jean-Sebastien Houle, Eng. of WSP.

About Lamelee Iron Ore Ltd

The Company is a new iron ore mineral exploration company
focused on the development of an iron mine project located in the
southern segment of the Labrador Trough near the border with
Newfoundland and Labrador, approximately 50 km south of the city of
Fermont (Quebec). The project consists of 29 mineral claims covering
1,524 hectares or 15 km2. The common shares are listed on the TSX-V
under the symbol "LIR". In December 2013, the Company acquired 100% of
Fancamp Exploration's Lac Lamelee South Iron Project located in the
Fermont Mining District of northeastern Quebec, subject to a 1.5% Net
Smelter Return royalty in favour of the Sheridan Platinum Group Ltd.,
of which 0.5% is subject to a buy-back option by the Company for $1.5
million. The Company also granted an additional 1.5% Net Smelter Return
royalty in favor of Fancamp Exploration on the Lac Lamelee South Iron
Project, of which 0.5% is subject to a buy-back option by the Company
for $1.5 million.

Information set forth in this news release may contain
forward-looking statements that are based on assumptions as of the date
of this news release. These statements reflect management's current
estimates, beliefs, intentions and expectations. They are no guarantees
of future performance. Lamelee cautions that all forward looking
statements are inherently uncertain and that actual performance may be
affected by a number of material factors, many of which are beyond
Lamelee's control. Except as required under applicable securities
legislation, Lamelee undertakes no obligation to publicly update or
revise forward-looking information.

Neither TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TEL: +1 514 793-7153       Hubert Vallee, President and CEO























Lamelee Iron Ore Ltd
TSX Venture closing price for LIR-V
Date: 2014/11/24
Closing Price: 0.05
TEL: +1 514 910-6906       Marc Duchesne, CFO
MDuchesne@LameleeIron.com  Lamelee Iron Ore Ltd
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1432800022TS11432800965-07003320141125