Source	MARKET NEWS
Date	11/28/2014
Time	12:25:52 PM

Company	 Lamêlée Iron Ore Ltd.
Title	Completed 
A Preliminary Economic Assessment Whic





    CDNX Symbol: LIR











Press Release	




[200/News Release]LIRVLAMELEE IRON ORE LTDNOV 28 2014  12:23 PMCompleted 
A Preliminary Economic Assessment Which Offers VeryPromising Results 
--->@NEWS RELEASE
LAMELEE IRON ORE LTD ("LIR-V")
- Completed A Preliminary Economic Assessment Which Offers
- Very Promising Results

Not for release or distribution in the United States or for
dissemination to US Newswire Services.

The Board of directors of Lamelee Iron Ore Ltd. ("Lamelee" or the
"Company") wishes to re-issue the press release disseminated on
November 25, 2014 in order to add the following information: (i) the
Net Present Value ("NPV") after tax, (ii) the Internal Rate of Return
("IRR") after tax and (iii) the standard caution specified in National
Instrument 43-101 ("NI 43-101").

The Company announced on November 25, 2014 that it has received
the results of a Preliminary Economic Assessment ("PEA") prepared by
CIMA+ in respect to the Company's Lac Lamelee South Property Project
(the "Lamelee Project") located in the Province of Quebec, 50 km South
of Fermont.

A summary of the PEA results from the NI 43-101 Technical Report
is presented below. The NI 43-101 Technical Report on the PEA will be
filed on SEDAR and on the Company's website within the next 45 days.

LAMELEE PEA HIGHLIGHTS:

NPV of $529.9 M (pre-tax) or of $243.8 M (after tax) at an 8%
discount rate;

IRR of 15.4% (pre-tax) or of 12.1% (after tax);

Pre-tax payback estimated at 5.8 years (years from production
start-up);

Mine life of 20 years at 5 million tonnes per year ("Mtpy") of
iron concentrate;

Initial project Capex of $816.7 M;

Total average operating cost of $54.81/tonne of concentrate;

Conservative long-term price assumptions US$ 79.50/tonne, FOB
Sept-Iles;

Accuracy of the estimate -15% + 30%.

The PEA is preliminary in nature. It includes Inferred Mineral
Resources that are considered too speculative geologically to have the
economic considerations applied to them that would enable them to be
categorized as Mineral Reserves. Moreover, there is no certainty that
the PEA will be realized.

Hubert Vallee, President and CEO of Lamelee stated: "We are very
pleased with the PEA of the Lamelee Project. It shows a pre-tax IRR of
15.4% or an after tax IRR of 12.1% on a capital expenditure of $ 816
million and a payback period of 5.8 years, based on conservative
long-term price assumptions. This is one of the lowest capital
expenditure requirement for this kind of project in the Labrador Trough
area. All of the numbers in the assessment are realistic and
achievable, based on recent construction projects and successful
operations recently delivered. The good potential for mining
development and production level will lead Lamelee to the next step,
namely the Bankable Feasibility Study.

Pierre Lortie, Chairman of the Board added that "the favorable
results reported in the PEA of the Lamelee Project reflect the valuable
experience and know-how of our team which will make the difference in
the success of this promising project. Our confidence in the success of
the project stems also, in part, on the superior quality of the iron
concentrate to be produced by Lamelee which opens many markets. It
needs to be emphasized that the concentrate is needed by Asian steel
mills to blend with concentrate from other producing regions, notably
Australia and Brazil, to ensure efficiency of production."

PEA PROJECT SUMMARY

The Lamelee property is located 560 km north of Baie-Comeau and 80
km (by road) south of the town of Fermont, all connected by the
provincial road 389 (the "Lamelee Property"). The Lamelee Property is
approximately 270 km in straight line north of Port-Cartier. The
Lamelee Property is accessible by road 389 and the ArcelorMittal
railroad passes by the Lamelee Property. The city of Wabush, located at
35 km of Fermont, has an airport with daily flights to Sept-Iles and
Montreal. The Lamelee Project is entirely located in Quebec.

In May 2014, Lamelee mandated CIMA+ to prepare the PEA. The
services of Met-Chem Canada Inc. ("Met-Chem") were retained to produce
an update of the mineral resource estimate, the mine design and the
mine plan. Soutex Inc. ("Soutex") provided their expertise for the
metallurgical testing and the elaboration of the process. AMEC Inc.
developed the tailings disposal strategy and the pond design. The
environmental considerations and permitting were carried out by WSP
Canada Inc. ("WSP"). Michel L. Bilodeau carried out the economic
analysis of the PEA.

UPDATED MINERAL RESOURCE ESTIMATE

The Property is located in the western margin of the Labrador
Trough that contains world-class iron deposits hosted in the Sokoman
Formation. The iron mineralization on the Property is hosted in the
Wabush Formation (metamorphosed equivalent of the Sokoman Formation).

Met-Chem carried out an updated Mineral Resource estimate based on
the results of the exploration work carried out during 2011 and 2012,
which consisted of 2 trenches and 57 holes for a total of 18,221 m.
Additional characterization work completed in 2014 included 3,133
Satmagan tests, 266 Davis Tube tests, as well as Heavy Liquid
Separation tests on composite samples.

The Mineral Resources were limited to the tonnage of blocks
constrained within the Iron Oxide envelopes which include MIF
(Magnetite Iron Formation), HIF (Hematite Iron Formation) and MHIF
(Mixed Magnetite Hematite Iron Formation). They don't encompass the
tonnage of QpyrxM (Silicates Iron Formation) envelope.

A 3D block model was created using the MineSight(r) software
package to discretize the project domain into blocks of 30 m by 30 m by
15 m (X, Y and Z directions). The Mineral Resource was interpolated on
the total iron content (T Fe%) using the Inverse Distance Squared
("IDW2") method. A constant density factor of 3.35, representing an
average for all iron oxides, was used to convert volumes into tonnes.

The Mineral Resource estimate was performed by Schadrac Ibrango,
P.Geo, PhD., a Qualified Person (QP). Under CIM definitions, Mineral
Resources should have a reasonable prospect of economic extraction.
Met-Chem chose to exclude the portion of the mineralization that lies
below Lac Lamelee from the Mineral Resource estimate since the complete
dewatering of Lac Lamelee, the construction of dykes to cut-off
portions of the lake or underground mining of this mineralized material
would most likely not be an economic option for the Project. In order
to determine the mineralized zones that can be potentially mined
without affecting the lake, Met-Chem created a pit shell with an
overall pit slope of 52 degrees and limited the crest of the pit to a
minimum distance of 50 m from the lake.

The resource classification follows the guidelines adopted by the
CIM through the NI 43-101 standards and guidelines. All the Mineral
Resources were classified as Inferred.

//st
SUMMARY OF THE MINERAL RESOURCES
(Cut-Off of 15% T Fe)
Category                      Tonnage           T Fe
(Mt)            (%)
Inferred                        354.1          29.49
//et

Mineral resources cannot be considered Mineral Reserves until
they have demonstrated economic viability. Environmental, permitting,
legal, title, taxation, socio-political, marketing, or other relevant
issues may materially affect the estimate of mineral resources. The
quantity and grade of reported Inferred Mineral Resources in this
estimate are uncertain in nature and there has been insufficient
exploration to define these Inferred Mineral Resources as Indicated or
Measured Mineral Resources and it is uncertain if further exploration
will result in upgrading them to the Indicated or Measured Mineral
Resource categories.

MINING

In order to determine the amount of recoverable iron contained
within each block of mineralized material, Soutex provided Met-Chem
with a formula to calculate the weight recovery as a function of the
total iron which is based on the results of the metallurgical testwork.


A pit optimization analysis was then carried out using the
MS-Economic Planner module of MineSight(r) which ran the
Lerchs-Grossmann algorithm to determine the economic limits of the
deposit. The analysis showed that the open pit design for the PEA
should be based on a 20-year mine life.

The In-Pit Mineral Resources for the Lamelee Project which account
for mining dilution and losses total 272 Mt of Inferred Mineral
Resources at a Total Fe grade of 29.7% (Weight Recovery of 36.3%). In
order to access these resources, 636 Mt of overburden and waste rock
must be mined which results in a stripping ratio of 2.3 to 1.

The mining method selected for the Lamelee Project is a
conventional open pit, drill and blast, truck and shovel operation
which is carried out with an owner operated fleet. Following the
development of a 20- year mine plan, Met-Chem estimated the mine
equipment fleet to include 22 haul trucks (227 tonne), 3 electric drive
hydraulic shovels (26.5 m3 bucket), 3 production drills as well as a
fleet of support and service equipment.

METALLURGICAL AND PROCESS

The following process was designed based on the results of the
testing program.

Ground run of mine feed is discharged from the mill as a slurry to
the scalping screens and then to the classification screens.

The first stage of gravity separation is performed by rougher
spirals from where the concentrate is sent to the cleaning hydrosizers
that will efficiently remove medium and fine silica. The cleaning
hydrosizers produce a high grade concentrate at their underflows. The
hydrosizers overflow, consisting in fine iron minerals and fine silica,
is processed by the scavenger spirals.

The two (2) concentrates produced (fine and coarse) are mixed
together to produce a constant final concentrate fed to the pan
filters.

The tails of both the rougher and the scavenger spirals are final
and sent to the tailings cyclones to be processed in the tailings
dewatering circuit.

During the summer, the fine and the coarse tailings are disposed
of separately in the same settling basin. The coarse tailings are then
used for dam building.

During the winter, the fine is mixed to the coarse tailings and
disposed of together.

PRELIMINARY IRON CONCENTRATE SPECIFICATIONS

//st
Element or Mineral     Formula Typical Value                         (%)
Iron                        Fe                                      64.3
Silica                    SiO2                                       4.5
Aluminium Oxide          Al2O3                                      0.38
Calcium Oxide              CaO                                      0.65
Magnesium Oxide            MgO                                      1.16
Sodium Oxide              Na2O                                      0.02
Potassium Oxide            K2O                                      0.01
Titanium Oxide            TiO2                                      0.51
Phosphorus                   P                                     (0.01
Manganese                   Mn                                      0.61
Chromium                    Cr                                     (0.01
Vanadium                     V                                     (0.01
Loss of Ignition (LOI)       -                                     -1.14
Sizing: -150um               -                                      30.0
//et

PORT FACILITIES AND PRODUCT HAULING

Lamelee plans to use the services of a local carrier to haul the
product from the mine to the Port owned by the town of Port-Cartier.

Local infrastructures, such as car dumper, ore handling yard and
ship loading facilities will be built by Lamelee.

Transshipping will be used at the beginning to load Cape size
ships.

PRODUCT SALES PRICE

Lamelee used different analysts and bankers forecasts combined
with an independent market analysis to estimate the long-term market
price of iron concentrate. The results of this analysis are listed
below and were used in the Economic Assessment of the Project:

Concentrate selling price: CAD$ 88.33/tonne, FOB Sept-Iles

OPERATING COST SUMMARY

The following operating costs were estimated by CIMA+, with input
from other experienced parties. Total average operating costs over the
life of mine are estimated at CAD$ 54.81/tonneof concentrate based on
the following:

//st
OPERATING COST                       $/tonne of concentrate

Mine                                                  21.92
Concentrator                                           8.24
General & administration                               7.04
Logistic                                              17.61

TOTAL                                                 54.81
//et

Qualified Persons

The complete NI 43-101 Technical Report ("Report") being prepared
by CIMA+ will include an updated mineral resource estimate and in-pit
mineral resource estimate which were prepared respectively by Schadrac
Ibrango, PGeo., PhD. and Jeffrey Cassoff, Eng. of Met-Chem. Both Mr.
Ibrango and Mr. Cassoff are independent Qualified Persons as defined by
NI 43-101. The Report is being prepared under the direction of
Jean-Sebastien Tremblay, Eng. of CIMA+ and will be reviewed and
certified by individuals responsible for their respective portions of
the Report. Mr. Tremblay and all other individuals providing
certifications are Independent Qualified Persons as defined by NI
43-101. Among them are, Mr. Mathieu Girard, Eng, of Soutex, David
Bedard, Eng. of AMEC, Michel L. Bilodeau, Eng. independent consultant
and Jean-Sebastien Houle, Eng. of WSP.

About Lamelee Iron Ore Ltd

The Company is a new iron ore mineral exploration company focused
on the development of an iron mine project located in the southern
segment of the Labrador Trough near the border with Newfoundland and
Labrador, approximately 50 km south of the city of Fermont (Quebec).
The project consists of 29 mineral claims covering 1,524 hectares or 15
km2. The common shares are listed on the TSX-V under the symbol "LIR".
In December 2013, the Company acquired 100% of Fancamp Exploration's
Lac Lamelee South Iron Project located in the Fermont Mining District
of northeastern Quebec, subject to a 1.5% Net Smelter Return royalty in
favour of the Sheridan Platinum Group Ltd., of which 0.5% is subject to
a buy-back option by the Company for $1.5 million. The Company also
granted an additional 1.5% Net Smelter Return royalty in favor of
Fancamp Exploration on the Lac Lamelee South Iron Project, of which
0.5% is subject to a buy-back option by the Company for $1.5 million.

Information set forth in this news release may contain
forward-looking statements that are based on assumptions as of the dateof this 
news release. These statements reflect management's current
estimates, beliefs, intentions and expectations. They are no guarantees
of future performance. Lamelee cautions that all forward looking
statements are inherently uncertain and that actual performance may be
affected by a number of material factors, many of which are beyond
Lamelee's control. Except as required under applicable securities
legislation, Lamelee undertakes no obligation to publicly update or
revise forward-looking information.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TSX Venture closing price for LIR-V
Date: 2014/11/26
Closing Price: 0.05

TEL:  +1 514 910-6906  Marc Duchesne, Chief Financial Officer
EMAIL:  MDuchesne@LameleeIron.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1433100023TS11433100807-12234220141128