Source	MARKET NEWS
Date	11/13/2014
Time	07:32:09 AM

Company	 Terrax Minerals Inc.
Title	Tenders 
Drill Contract For Yellowknife City Gold





    CDNX Symbol: TXR











Press Release	




[200/News Release]TXRVTERRAX MINERALS INCNOV 13 2014  07:29 AMTenders 
Drill Contract For Yellowknife City Gold Project --->@NEWS RELEASE
TERRAX MINERALS INC ("TXR-V")
- Tenders Drill Contract For Yellowknife City Gold Project

Assays 18.54 M @ 2.15 G/t Au In Historic Core; Assays Up To 126
G/t Au In Grab Samples From New Shear In Core Gold Area

TerraX Minerals Inc. has tendered a 5,000 meter drill contract,
expandable to 20,000 meters, on the Yellowknife City Gold Project
(YCGP"). The contract will be awarded by December 8th, with drilling
scheduled to start after the holiday season in January 2015. Drilling
will be concentrated on the "Core Gold Area" identified by drilling,
surface sampling and mapping conducted during 2014. The Gold Core Area
encompasses the advanced Crestaurum and Barney Shear zones, as well as
several adjacent and intersecting veins and shears identified between
the two, including a new shear structure that returned assays up to 126
g/t Au in grab samples reported below.

To prepare for the 2015 drill program, TerraX has continued to
evaluate and re-assay historical drill core from holes drilled within
the Core Gold Area and carried out selected surface sampling and
mapping prior to winter freeze-up. The Core Gold Area covers at least a
3km x 5km NNE trending area bounded by the Barney Lake Shear Corridor
in the east and the Ryan Lake Pluton to the west; it remains open along
strike (see TerraX presentation at www.terraxminerals.com). The drill
holes and surface results reported here were sampled to better
understand the relationships between the multiple known gold
structures, and to help characterize the geological controls on the
mineralized zones within these structures.

DRILL CORE RESULTS

The eight drill holes reported in this news release were drilled
between 1994 and 1996. The core from these holes is part of the 30,000
m of core recovered in 2013 from the Giant Mine core yard and relocated
to TerraX's core facility in Yellowknife. Logging has been carried out
on drill holes that cored through multiple areas of geological interest
to TerraX.

Four drill holes reported below are from the Barney Lake Shear
Corridor. These holes were logged and sampled to expand our knowledge
of what is already considered a promising zone of gold mineralization
within the Core Gold Area (2014 drill results include hole 95-16W1 with
22.42m @ 6.35 g/t Au inclusive of 5.16m @ 18.40 g/t Au reported August
25th, 2014). Results of sampling of the historical core include:

--  Hole NB96-21 returned 18.54 m @ 2.15 g/t Au and 6.2 g/t Ag, including
3.94 m @ 5.04 g/t Au and 13.2 g/t Ag. This intersection was missing
81
cm of the highest grade core from selective samples taken for
display
purposes in 1996. Hole NB96-21 was drilled on section and west of
hole
NB96-04 (1.90 g/t over 27.00 m, including 8.97 g/t Au over 2.70 m -
see
news release of November 14, 2013) NB96-21 and NB96-04 were the two
most
northerly holes drilled on the Barney Lake Shear Structure prior to

TerraX drilling during the winter of 2014.

--  Hole NB96-13 was drilled 30 m to the south and 60 m west of NB96-21 and
intercepted 2.67 m @ 7.83 g/t Au and 8.1 g/t Ag in a zone
interpreted to
be in the hanging wall of the zone intersected in NB96-21.
Extensive
alteration and mineralization were encountered, with stronger gold
mineralization consistent with a close approach to the interpreted
strongest portion of the known Barney Mineralized Zone.

--  Hole NB96-09 drilled 50 m down dip of the gold zone in NB96-13 was
interpreted to be in the hanging wall of the zone intersected in
NB96-21
and returned 6.38 m @ 2.74 g/t Au and 5.2 g/t Ag.

--  Hole NB96-15 was drilled west of the previously known Barney Zone and up
dip of NB96-24 (which returned 4.0 m @ 7.73 g/t Au - see news
release
December 3, 2013). Results include a gold zone of 5.01 m @ 3.14 g/t
Au.

//st
Drill Hole Intervals from Barney Lake Shear Zone

---------------------------------------------------------------------------
-
Drill Hole  UTM East    UTM North      Azimuth       Dip  FROM (m)    TO (m)
---------------------------------------------------------------------------
-
NB96-09     636725      6946413             88       -64    337.02    353.43
---------------------------------------------------------------------------
-
incl                                                        347.05    353.43
---------------------------------------------------------------------------
-
NB96-13     636723      6946413             88       -50    294.37    301.93
---------------------------------------------------------------------------
-
incl                                                        297.74    300.41
---------------------------------------------------------------------------
-
NB96-15     636707      6943256                             362.37    367.38
---------------------------------------------------------------------------
-
NB96-21     636789      6943441             88       -50    243.41    261.95
---------------------------------------------------------------------------
-
incl                                                        243.41    247.35
---------------------------------------------------------------------------
-
NB96-04(i)  637174      6943469            268       -45       399       426
---------------------------------------------------------------------------
-
NB96-24(i)  637051      6943278            268       -66       603       607
---------------------------------------------------------------------------
-

------------------------------------------------------------------------
Drill Hole  UTM East    UTM North      Width (m)      Au g/t      Ag g/t
------------------------------------------------------------------------
NB96-09     636725      6946413            16.41        1.43         4.0
------------------------------------------------------------------------
incl                                        6.38        2.74         5.2
------------------------------------------------------------------------
NB96-13     636723      6946413             7.56        2.90         5.4
------------------------------------------------------------------------
incl                                        2.67        7.83         8.1
------------------------------------------------------------------------
NB96-15     636707      6943256             5.01        3.14
------------------------------------------------------------------------
NB96-21     636789      6943441            18.54        2.15         6.1
------------------------------------------------------------------------
incl                                        3.94        5.04        13.2
------------------------------------------------------------------------
NB96-04(i)  637174      6943469            27.00        1.90         6.9
------------------------------------------------------------------------
NB96-24(i)  637051      6943278             4.00        7.73         6.8
------------------------------------------------------------------------
(i) Previously reported - see text above
//et

A map showing the location of these drill holes is available under
"2014 Field Exploration" on our web site at www.terraxminerals.com

Four holes were re-logged from areas that are between the
Crestaurum Zone, 20 Shear and 19 Shear, which collectively lie to the
west and south of the Barney Zone (see table below), and form part of
the mineralizing structures within the Core Gold Area. These holes were
drilled in 1994 and are not directly associated with the two best known
zones of gold mineralization (Crestaurum, Barney), but were logged and
sampled by TerraX to gain a better understanding of the relationship of
these zones to each other, and to ascertain the controls on their gold
mineralization. Results include 1.45 m @ 6.05 g/t Au in hole NB94-03;
11.36 m @ 0.92 g/t Au in hole NB94-05; 1.50 m @ 5.36 g/t Au in hole
NB94-13; and 1.90 m @ 5.05 g/t Au from in hole NB94-15 (see table
below).

//st

Assay Intervals from Areas between the
Crestaurum Shear and Shears 20 & 19
---------------------------------------------------------------------------
-
Drill Hole  UTM East    UTM North            Azimuth         Dip    FROM (m)
---------------------------------------------------------------------------
-
NB94-03     636283      6942335                   88         -60      176.32
---------------------------------------------------------------------------
-
and                                                                   209.85
---------------------------------------------------------------------------
-
and                                                                   313.75
---------------------------------------------------------------------------
-
NB94-05     6366421     6942684                  268         -45       56.94
---------------------------------------------------------------------------
-
incl                                                                   56.94
---------------------------------------------------------------------------
-
NB94-13     636342      6942158                   88         -60       50.51
---------------------------------------------------------------------------
-
NB94-15     636624      6942277                   88         -60       35.33
---------------------------------------------------------------------------
-
and                                                                    47.95
---------------------------------------------------------------------------
-
and                                                                    67.64
---------------------------------------------------------------------------
-
and                                                                   139.51
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
Drill Hole  UTM East    UTM North             TO (m)   Width (m)      Au g/t
---------------------------------------------------------------------------
-
NB94-03     636283      6942335               177.09        0.77        2.59
---------------------------------------------------------------------------
-
and                                           210.88        1.03        1.90
---------------------------------------------------------------------------
-
and                                            315.2        1.45        6.05
---------------------------------------------------------------------------
-
NB94-05     6366421     6942684                 68.3       11.36        0.92
---------------------------------------------------------------------------
-
incl                                           58.98        2.04        3.83
---------------------------------------------------------------------------
-
NB94-13     636342      6942158                52.01        1.50        5.36
---------------------------------------------------------------------------
-
NB94-15     636624      6942277                36.27        0.94        1.76
---------------------------------------------------------------------------
-
and                                            49.85        1.90        5.05
---------------------------------------------------------------------------
-
and                                             69.8        2.16        3.56
---------------------------------------------------------------------------
-
and                                           140.21        0.70        2.19
---------------------------------------------------------------------------
-

//et

The drill core was subjected to a full geological and geotechnical
analysis which included refitting of the core, revealing 100% recovery
except for selected mineralized core intervals (10-20 cm) that had been
removed for display or other test work by past workers. Core showed
excellent geotechnical rock quality values. Core distances were
converted from the original imperial measurements (feet) to metric
(meters) and new core sampling intervals were designated from the
metric measurements.

TerraX collected 241 samples for assay from the Barney Lake Shear
Corridor area and 239 samples from other areas within the Core Gold
Area. Results ranged from below detection to a high of 22.7 g/t Au.
Core samples were cut with a diamond saw blade. Sampling over several
intervals was done by quarter core sampling of half sawn core that
remained from previous sampling in 1994, 1995 and 1996. In these areas
a quarter core sample remains in the core boxes for further examination
if required. True thickness of the zones of mineralization is unknown
at present. Based on core foliation angles it is estimated to be
between 65-95% of drill intersection width.

A map of the new shear surface samples and the drill holes
reported above from Barney, Crestaurum, 20 Shear and 19 Shear is
available under "2014 Field Exploration" on our web site.

SURFACE SAMPLING RESULTS

Surface sampling and mapping was carried out in early fall on the
YCGP. The assay results reported here were from structural mapping of
known mineralized features within the Core Gold Area, and sampling of
strike extensions to these structures. Results included:



--  A grab sample with 126 g/t Au in veining within a new shear in the Core
Gold Area that is 300 m north of a sample grading 44.3 g/t Au (news

release of Sept 8th, 2014) taken during prospecting this summer.
Both
samples are interpreted to be on the same northerly trending shear
structure, which is sub-parallel to and 150 m west of the main
Barney
Shear, with today's sample approximately 500 m south of drilling
completed this summer at the Barney Shear

--  A grab sample with 6.42 g/t Au from a NNW structure within the Core Gold
Area that is sub-parallel to and 50 m east of Shear 17. This sample
is
85 m from a channel sample on Shear 17 that ran 6 m @ 2.03 g/t Au,
0.09%
Cu and 0.05% Mo (news release Aug 19th, 2014).

--  Grab samples of 2.82 and 13.95 g/t Au from the NNE trending Finger Lake
Shear on the U-Breccia property which is in the southwest portion
of the
YCGP, and approximately 2 km south of the current southern boundary
of
the Gold Core Area, potentially expanding our area of interest.



A map showing the location of the fall surface samples is available
under "2014 Field Exploration" on our web site.

It should be noted that, due to their selective nature, assay
results from grab samples may not be indicative of the overall grade
and extent of mineralization on the subject area. The surface program
consisted of 62 samples with grades ranging from below detection limit
to 126 g/t Au. Certified standards and blanks were inserted into thestream of 
samples for chemical analysis. Samples were prepared at ALS
Chemex's laboratory in Yellowknife and shipped to their Vancouver
facility for gold analysis by fire assay and other elements by ICP
analysis. ALS is a certified and accredited laboratory service.

The technical information contained in this news release has been
approved by Joseph Campbell, the President of TerraX, who is a
Qualified Person as defined in "National Instrument 43-101, Standards
of Disclosure for Mineral Projects."

About the Yellowknife City Gold Project

The Yellowknife City Gold Project encompasses 93.5 sq km of
contiguous land immediately north of the City of Yellowknife in the
Northwest Territories and includes TerraX's wholly-owned Northbelt
property acquired in February 2013.

The project lies on the prolific Yellowknife greenstone belt and
covers 15 km of strike length on the northern extension of the shear
system that hosts the high-grade Con and Giant gold mines. The project
area contains multiple shears that are the recognized hosts for gold
deposits in the Yellowknife gold district, with innumerable gold
showings and historic high grade drill results. Since January 2013,
TerraX has consolidated the project area by acquiring and optioning
numerous properties, including: Northbelt, Goodwin, Ryan Lake, Walsh
Lake, and U-Breccia, as well as staking additional contiguous lands.
Being all-season road accessible and within 15 km of the City of
Yellowknife, the YCPG is close to vital infrastructure, including
transportation, service providers, hydro-electric power and skilled
trades people.

On behalf of the Board of Directors

Joseph Campbell, President

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release contains forward-looking information, which
involves known and unknown risks, uncertainties and other factors that
may cause actual events to differ materially from current expectation.
Important factors - including the availability of funds, the results of
financing efforts, the completion of due diligence and the results of
exploration activities - that could cause actual results to differ
materially from the Company's expectations are disclosed in the
Company's documents filed from time to time on SEDAR (see
www.sedar.com). Readers are cautioned not to place undue reliance on
these forward-looking statements, which speak only as of the date of
this press release. The company disclaims any intention or obligation,
except to the extent required by law, to update or revise any
forward-looking statements, whether as a result of new information,
future events or otherwise.

TSX Venture closing price for TXR-V
Date: 2014/11/12
Closing Price: 0.33

TEL:  514-341-0408  Paradox Public Relations
Toll Free: 1-866-460-0408
E-mail: info@paradox-pr.ca
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1431600012TS11431601416-07294920141113