Source	Filing Services Canada
Date	11/12/2014
Time	05:30:09 AM

Company	 GOLDEN PREDATOR MINING CORP.
Title	Golden Predator Announces Positive Preliminary Economic Assessment (PEA) 
Results for the Brewery Creek Project, Yukon





    CDNX Symbol: GPY











Press Release	




SOURCE: Filing Services Canada
Date: 11/12/2014
Time: 08:30:00

Company: GOLDEN PREDATOR MINING CORP
Title:Golden Predator Announces Positive Preliminary Economic Assessment (PEA) 
Results for the Brewery Creek Project, Yukon (GPY - TSXV) 
TSXV SYMBOL: GPY


NEWS TRANSMITTED BY FILING SERVICES CANADA
FOR: Golden Predator Mining Corp
TSXV SYMBOL: GPY
Wednesday, November 12, 2014 - 8:30 AM

Original Source Location: 
http://www.fscwire.com/newsrelease/golden-predator-announces-positive-preliminar
y-economic-assessment-pea-results-brewery

Golden Predator Announces Positive Preliminary Economic Assessment (PEA) 
Results for the Brewery Creek Project, Yukon


Hayden, Idaho (FSCwire) - Golden Predator Mining Corp. (TSX.V: GPY) (the 
Company or Golden Predator) is pleased to announce the results of a Preliminary 
Economic Assessment (PEA) for the companys year-round road accessible Brewery 
Creek Gold Project. The NPV of the project ranges from $18.1 million at $1,150 
gold to $114.5 million at $1,500 gold with IRRs ranging from 12% to 45% with 
corresponding gold prices; these scenarios are pre-tax and assume a 5% discount 
rate. Total Life of Mine Capital is estimated to be $89.4 million which 
includes initial capital, sustaining capital, indirect costs and owner costs.



We are happy to have our belief regarding the potential economics of re-opening 
the Brewery Creek mine confirmed by this study. Having a project with truly 
modest CAPEX and a break-even point around $1,100 gold provides us with a 
quality asset with only a minimal revival in the price of gold, said Janet 
Lee-Sheriff, Chief Executive Officer, The compelling low start-up cost along 
with the untapped exploration potential of the project should make this an 
attractive opportunity for a prospective joint venture candidate.



The PEA evaluated the economics of resuming mining at Brewery Creek through a 
combination of open pit mining and reprocessing former heap leach material for 
gold recovery to dor[[107]]. The study was prepared by Tetra Tech EBA Inc. in 
cooperation with Tetra Tech Inc. of Tucson, AZ; SGS-ESEngineering Solutions 
Inc. of Tucson, AZ; Resource Modeling Inc. of Stites, ID; Gustavson and 
Associates of Lakewood, CO and Access Consulting Group of Whitehorse, YT.



PEA Summary Mine Plan and Operating Assumptions

To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-announces-positive-preliminar
y-economic-assessment-pea-results-brewery


1Based on a cut-off grade of 0.50 g/t gold

2Based on a cut-off grade of 0.30 g/t gold



PEA Summary Capital and Operating Costs

To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-announces-positive-preliminar
y-economic-assessment-pea-results-brewery

1Mining cost of leach feed from pits is higher than waste mining due to longer 
haul distance to deliver feed to crushers than to deliver waste rock to 
repositories. 

2Includes $0.59 per tonne for equipment leasing



PEA Summary Economics at $1250/oz. Gold

To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-announces-positive-preliminar
y-economic-assessment-pea-results-brewery



To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-announces-positive-preliminar
y-economic-assessment-pea-results-brewery



The base case summarized above assumes the owner will lease all mining 
equipment, instead of owner purchasing all mining equipment, to result in a 
lower initial capital cost. The base case assumes mining and crushing for 230 
days per year at an average rate of 7,500 tonnes per day. All heap leach feed 
material would be crushed to 80% passing 9.5 mm. Some material on the old heap 
leach pad would be re-processed by crushing and re-leaching on an as needed 
basis to meet demand when open pit mining is not at full capacity. The existing 
leach pad would have the last three original designed cells built. Recent 
geotechnical studies indicate the pad can safely accommodate an increase in 
stacking height from 30 meters to 40 meters providing more capacity on the pad. 
Solutions would be circulated and gold recovered year round through a carbon 
Adsorption Desorption Recovery (ADR) plant to produce dor[[107]] on site.



The existing road to Brewery Creek will continue to provide access. Power 
generation for the PEA was modeled as diesel powered providing a total of 5.0 
megawatts with normal power draws of 3.93 MW. Waste rock generated from some of 
the new open pits has been designed to be used to backfill existing and new 
pits as scheduling allows.



Sensitivities

To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-announces-positive-preliminar
y-economic-assessment-pea-results-brewery



Opportunities to Enhance Value



Trade off studies were evaluated against the base case and these included the 
owner purchasing all mining equipment. The owner purchase scenario, while 
increasing initial capital costs, project NPV remained relatively consistent, 
with less $1 million decrease in NPV. This scenario will be evaluated further 
in the future engineering studies. The current model includes commencing 
drilling and blasting activities at the surface of the deposits but in the 
previous operation it was found that level of oxidation was such that the 
surface material and some initial mining benches did not require drilling and 
blasting which would provide a positive effect on the economics. Additional 
economic enhancements could be found by reducing the base case throughput rate 
of 7,500 tonnes per day which would result in lower capital costs and extend 
mine life. The opportunity to mine and crush more than 230 days per year would 
also provide enhanced economics to the project. The property has high potential 
for resource expansion and discovery of new deposits. The known resources at 
the Classic and Lone Star deposits were not considered in this PEA and both 
deposits remain open to expansion. The Lone Star deposit has encountered higher 
grade skarn mineralization which has not been found before on the property and 
could develop in to a higher grade resource.



Mineral Resources



The mineral resources used in this PEA include Indicated and Inferred mineral 
resources estimated by three independent Qualified Persons (QP), Don Hulse, 
P.E., of Gustavson, Michael J. Lechner, P. Geo. of RMI, and James Barr, P. 
Geo., of Tetra Tech EBA. The resources are found in fifteen different deposits 
currently identified on the Brewery Creek property and the run of mine material 
(not crushed) on the old heap leach pad. The in-situ estimates used sample data 
from 2,608 drill holes and over 198,829 meters of drilling and the remaining 
resources in the existing heap were estimated using 18 sonic drills with a 
total of 266 meters of drilling.



The PEA utilized Indicated and Inferred resources from eight of the fifteen 
deposits and the old heap leach pad to develop the plans included in this PEA. 
The PEA mines a total of 10.2 million tonnes of oxide material at 1.35 g/t gold 
from the eight open pits and reprocesses 3.1 million tonnes from the old heap 
at 0.77 g/t gold. The total oxide resources for the Brewery Creek are estimated 
at 14.1 million tonnes at 1.27 g/t gold classified as Indicated and 9.3 million 
tonnes at 0.93 g/t gold classified as Inferred. For further details on the 
mineral resources the reader is referred to the complete PEA document.



Capital and Operating Costs 

To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-announces-positive-preliminar
y-economic-assessment-pea-results-brewery



To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-announces-positive-preliminar
y-economic-assessment-pea-results-brewery

1Includes $0.59 per tonnes for equipment leasing



Mining



The Brewery Creek project was evaluated for mining in the PEA as open pit truck 
and shovel operation. Mining was considered on the oxide portions of eight 
deposits aligned in a more or less east-west trend along 8 kilometers in what 
is known locally as the reserve trend. The deposits are West Big Rock, East Big 
Rock, Lower Fosters, Kokanee, Golden, Lucky, Bohemian and Schooner. The mine 
schedule shows calls for mining and processing over 10.0 million tonnes of heap 
leach feed and 43.5 million tonnes of waste for a strip ratio of 4.2:1. The 
current life of mine is nine years. The mine plan also includes reprocessing 
4.1 million tonnes of material from the old heap leach pad. An additional 3.3 
million tonnes of old heap material will be moved but not processed. Recent 
studies have shown that since the original material was not crushed an 
additional 45% of the remaining contained gold can be recovered after crushing. 
The old pad material will be mined and processed when the mining in the open 
pits is not at full capacity.



To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-announces-positive-preliminar
y-economic-assessment-pea-results-brewery

1Based on a cut-off grade of 0.50 g/t gold

2Based on a cut-off grade of 0.30 g/t gold



The mine plan was developed by importing the resource block models for the 
deposits into a pit optimization software package called GeoviaTM. Criteria 
were applied to the mining and processing of the mineralized and waste blocks 
that would be mined to create pit shells. The criteria included pit slopes 
generally ranging from 45o to 55o with small portions of individual pits 
allowing for slightly steeper or shallower pit slopes based on geotechnical 
assessment by Tetra Tech EBA. Gold recoveries for the pits ranged from 70.0% to 
82.9% based on metallurgical testing including column leach tests.

The mining equipment was matched to achieve the planned daily mining rate of 
7,500 tonnes on seasonal basis. The mining season is an anticipated 230 days of 
active mining and based on what the former Viceroy operation at Brewery Creek 
was able to achieve during its mine life. The PEA considered leasing of mining 
equipment to keep the initial capital costs low but does result in increasing 
the operating costs.



Operating costs average US$19.95/tonnes processed over the life of mine, 
including equipment leasing, which equates to US$778 per troy ounce sold. The 
estimation of operating costs is based on consumables, labor, maintenance and 
other requirements. Since the deposits considered in the PEA lie along an 8 
kilometer trend and a crushing and heap leach pad which are located near the 
western end of the deposit trend different haulage costs of ore were estimated 
for each deposit. The cost of waste transport is generally less than the 
transport of the heap leach feed because the waste material is generally 
schedule to be deposited in engineered facilities near the respective open pits.



To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-announces-positive-preliminar
y-economic-assessment-pea-results-brewery

1Includes $0.59 per tonnes for equipment leasing



Processing



The process plant flow sheet was developed by SGS and is designed to crush and 
stack heap leach feed approximately 230 days per year and to recover gold from 
the heap leach solutions 365 days per year. The flow sheet used a daily feed 
rate of 7,500 tonnes per day or an annual feed rate of 1.7 million tonnes.



Material will be delivered to the crushing area and reduced to a nominal 80% 
passing 9.5 mm after tertiary crushing with modular crushing units. Feed 
material from the Fosters deposit and re-processed material from the old heap 
are planned to be agglomerated. The crushed material will be stacked on the 
leach pad by truck. Gold recovery for the leach solutions is done by through an 
ADR plant.



Estimates for gold recovery and consumption rates of regent is based on recent 
metallurgical testing conducted by McClelland Laboratories for five of the 
deposits and the old heap leach material. Recoveries and consumption rates for 
three of the deposits which were previously mined by Viceroy are based on 
historical data.



To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-announces-positive-preliminar
y-economic-assessment-pea-results-brewery



Operating costs for the processing at Brewery Creek are estimated to be 
slightly variable depending on the material being processed and the table below 
shows the overall average processing plant operating costs. The costs include 
crushing, reagents, fuel, power, assay laboratory, labor and maintenance.



To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-announces-positive-preliminar
y-economic-assessment-pea-results-brewery



First Nations, Community Engagement and Environment



Community and First Nation engagement has been a strong component of the 
Brewery Creek Project dating to the initial mine operator, Viceroy Resources. 
In 2011 Golden Predator updated and modernized the Socio Economic Agreement 
with the Trondek Hwechin (TH), which addresses environmental responsibilities, 
permitting, education and employment as well as preferential contracting 
opportunities and wealth sharing. The Brewery Creek Project lies with the 
traditional territory of both the Trondek Hwechin and the First Nation of Na 
Cho Nyak Dun (NND). Regardless of the pre-existing relationship and agreement 
with TH and the proximity to Dawson City, Yukon the Company has and will 
continue to consult with both First Nations on all permitting and regulatory 
matters.



The previous operator and the company have conducted extensive environmental 
studies and monitoring programs that document the property since the early 
1990s. Studies include water quality, fisheries, wildlife, heritage and 
vegetation. The company continues to conduct regular environmental sampling and 
monitoring on the property.



Disclosure



The PEA is only summarized in this press release as an initial high-level 
review of the project the complete detailed report will filed on SEDAR within 
20 days of this press release. The PEA is preliminary in nature and it includes 
inferred mineral resources that are considered too speculative to be used in an 
economic analysis except as allowed for by Canadian Securities Administrators 
National Instrument 43-101 in PEA studies. There is no guarantee that the 
inferred mineral resources can be converted to Indicated or Measured mineral 
resources, and as such, there is no guarantee the project economics described 
in this report will be achieved.



Qualified Persons



The independent qualified persons responsible for preparing the Brewery Creek 
Preliminary Economic Assessment are James Barr, P. Geo., of Tetra Tech EBA Inc. 
Mark Horan, P. Eng., of Tetra Tech EBA Inc., Marvin Silva, Ph.D., P. Eng., of 
Tetra Tech EBA Inc., Joseph Keane, P. E., of SGS-ESEngineering Solutions Inc., 
Mike Lechner, P. Geo., of Resource Modeling Inc., Donald E. Hulse, P.E., of 
Gustavson and Associates and Claiborne Newton, III, Ph.D., SME(RM), of 
Gustavson and Associates.



Michael Maslowski, CPG, a consultant to the company is the Companys designated 
QP for this news release within the meaning of NI 43-101 and has reviewed and 
validated that the information contained in the release is consistent with that 
provided by the QPs responsible for the PEA.



Golden Predator Mining Corp.



Golden Predators corporate mandate is to advance the Brewery Creek project 
towards production through a joint venture arrangement. The Brewery Creek mine 
operated from 1996 to 2002, before closing due to low gold prices. Mining 
licenses and permits are in place for continued exploration along with a Socio 
Economic Accord with the Tr'ondek Hwech'in. The Company holds additional 
projects with current resources and/or new discovery potential, including the 
high-grade 3 Aces and Grew Creek gold projects and the Marg and Clear Lake 
polymetallic massive sulfide deposits.



For additional information:

Janet Lee-Sheriff, Chief Executive Officer

(208) 635 5415

info@goldenpredator.com (mailto:info@goldenpredator.com)

www.goldenpredator.com (http://www.goldenpredator.com)



Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in policies of the TSX Venture Exchange) accepts responsibility for 
the adequacy or accuracy of this release. 



No stock exchange, securities commission or other regulatory authority has 
approved or disapproved the information contained herein. This press release 
contains projections and forward-looking information that involve various risks 
and uncertainties regarding future events. Such forward-looking information can 
include without limitation statements based on current expectations involving a 
number of risks and uncertainties and are not guarantees of future performance. 
There are numerous risks and uncertainties that could cause actual results and 
the Companys plans and objectives to differ materially from those expressed in 
the forward-looking information. Actual results and future events could differ 
materially from those anticipated in such information. These and all subsequent 
written and oral forward-looking information are based on estimates and 
opinions of management on the dates they are made and are expressly qualified 
in their entirety by this notice. Except as required by law, the Company 
assumes no obligation to update forward-looking information should 
circumstances or management's estimates or opinions change.





To view this press release as a PDF file, click onto the following link:
http://www.fscwire.com/sites/default/files/news_release_pdf/goldenpredator111220
14.pdf
Source: Golden Predator Mining Corp (TSX Venture:GPY) 
http://www.goldenpredator.com



Maximum News Dissemination by FSCwire. http://www.fscwire.com



Copyright(C)2014 Filing Services Canada Inc.