Source	Marketwire
Date	11/12/2014
Time	08:39:54 AM

Company	 UCORE RARE METALS INC.
Title	Ucore Uses Molecular Recognition Technology to Generate 99%+ Pure Heavy 
Rare Earth Concentrate





    CDNX Symbol: UCU











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Ucore Rare Metals Inc.

TSX VENTURE SYMBOL: UCU
OTCQX SYMBOL: UURAF
FRANKFURT SYMBOL: U9U

November 12, 2014

Ucore Uses Molecular Recognition Technology to Generate 99%+ Pure Heavy Rare 
Earth Concentrate


HALIFAX, NOVA SCOTIA--(Marketwired - Nov. 12, 2014) - Ucore Rare Metals Inc 
(TSX VENTURE:UCU) (OTCQX:UURAF) (FRANKFURT:U9U) ("Ucore" or "the Company") is 
pleased to announce the results of the Company's recent testing of Molecular 
Recognition Technology ("MRT"). Ucore has successfully utilized MRT to produce 
a near quantitative separation of a heavy rare earth concentrate ("HREE 
Concentrate") consisting of 99+% of rare earth elements from a pregnant leach 
solution ("PLS"). The PLS was created by the extraction of metal values from 
beneficiated material sourced from the company's Bokan Dotson-Ridge property in 
Southeast Alaska ("Bokan").

The production of a high purity HREE Concentrate is the key and critical first 
step in the production, by separation, of individual high purity heavy rare 
earth salts. The resultant salts can be utilized to readily generate output 
products tailored to customer specifications. Those products include oxides, 
carbonates, nitrates and other salts of each of the individual rare earth 
elements ("REE's"). A highly purified HREE Concentrate can be considered an end 
product to be sold to independent rare earth separation facilities, or can be 
used as input material for an in-house individual rare earth salt separation 
facility.

The tests on the PLS using MRT were conducted by IBC Advanced Technologies, 
Inc. headquartered near Salt Lake City, Utah ("IBC"). The MRT process yielded a 
greater than 99% pure HREE Concentrate, separated as a group, using proprietary 
MRT SuperLig(R) resins in fixed bed format. Greater than 99% of the contained 
HREE's were recovered from the Bokan PLS.

The greater than 99% pure HREE Concentrate is a carbonate salt rare earth 
concentrate ("REC") comprised of heavy rare earths ranging from samarium (Sm) 
through lutetium (Lu). The REC is easily convertible to oxide or other salt 
forms depending upon commercial requirements and contains the following rare 
earth content:

/T/

----------------------------------------------------------------------------
Carbonate               Sm    Eu    Gd    Tb              Dy              Ho
----------------------------------------------------------------------------
Content, %           24.54  4.00 21.82  6.01           25.65            3.14
----------------------------------------------------------------------------

----------------------------------------------------------------------------

----------------------------------------------------------------------------
Carbonate               Er    Tm    Yb    Lu         Non-REC             REC
----------------------------------------------------------------------------
Content, %            5.96  1.71  6.09  1.08    less than 1 greater than 99
----------------------------------------------------------------------------

/T/

"This achievement speaks not just to the quality of Bokan feedstock but also to 
the Company's industry leading advancements in hydrometallurgy." said Jim 
McKenzie, President and CEO of Ucore. "MRT is a disruptive technology in every 
positive sense. It's a revolutionary alternative to the more costly, slower and 
environmentally invasive Solvent Extraction (SX) based methods of REE 
concentration and separation. What's more, we're excited to now be testing MRT 
as a platform for obtaining individual high purity rare earth oxides. This 
objective that has proven highly elusive in the REE processing community, 
outside of the more expensive and environmentally burdensome SX methodologies 
currently in use in China and beyond. Ucore will keep our shareholders posted 
on these further tests as they become available."

"We're exceptionally pleased with the results of this testing on the Bokan 
PLS," said Ken Collison, COO of Ucore. "The ability to generate an HREE 
enriched concentrate efficiently is crucial to the success of any rare earth 
project outside of China. We're excited to be introducing MRT to the REE 
sector, especially given its substantial record of success in other industries 
and its potential for rapid, clean and cost effective throughput."

"The MRT process is remarkable in that it uses green chemistry procedures 
throughout," said Ed Bentzen, Project Manager of Lyntek Inc. of Lakeview, 
Colorado. "No solvents or pernicious chemicals are used. The highly selective 
separations achieved with the MRT process make REE separations and recovery at 
high purities possible. Conservation of the rare earth metals has great 
importance, especially since large amounts, as much as 30% of these metals, 
remain unrecovered using conventional separation processes such as Solvent 
Extraction."

"This is an exceptionally clean and high grade heavy REE mixed concentrate," 
said Jack Lifton, a consultant to Ucore. "By clean, I mean free of radioactive 
elements and free of commonly produced elements that interfere with traditional 
Solvent Extraction separation such as Al, Fe, and Fluoride. MRT is a proven 
industrial technology that is now being applied to rare earth ore metallurgy. I 
look forward to the next logical step, the separation and purification of the 
individual rare earths from the mixed concentrate via MRT."

MRT Background

MRT is a branch of Supramolecular chemistry, originally pioneered by Charles 
Pederson at E.I. DuPont Laboratories in the 1960's. That original research into 
the remarkable capabilities of MRT for selective binding of metal ions 
culminated in the awarding of the Nobel Prize for Chemistry to three 
researchers in the development of the technology in 1987 (Lehn, Pedersen and 
Cram).

The MRT platform now being utilized by Ucore is derived from the pioneering 
research of the founders of IBC (Dr's. Reed M. Izatt, Jerald S. Bradshaw and 
James J. Christensen) and associates who have developed and applied this 
technology to the separations of metal ions. MRT is currently utilized 
extensively in metals processing, and is now being ushered into the rare earth 
separation field by Ucore as a means of both selectively extracting the rare 
earths as a group from a mixed polymetallic solution and of selectively 
isolating and refining individual high purity rare earth elements.

PLS & Mixed Concentrate Preparation

The Bokan PLS was initially produced using a beneficiation circuit set out in 
the Company's PEA (see Ucore press release dated Jan 15, 2013). That 
beneficiation circuit, which included X-Ray Fluorescence ore sorting, magnetic 
separation, and a nitric acid leach to generate the REE pregnant solution, has 
been upgraded during the ensuing period, as described herein.

As preparation for the MRT testing process, non-REEs, including Al, Fe, Th, Ti, 
and Zr, are first removed from the Bokan PLS by way of precipitation at 
controlled pH levels. Removal by way of pH controlled precipitation results in 
cost saving economies and reduction in the number of MRT SuperLig(R) resin 
columns used in the process. Greater than 99% of the REEs remain in solution 
along with non-target elements including Cu, Ni, Zn, Co and Mn. This output 
solution is then fed into the first SuperLig(R) column designed to selectively 
remove these non-target elements. The rare earth metals, as a group, are then 
selectively removed from the resulting raffinate through binding onto an 
additional SuperLig(R) column. These bound elements are then eluted into 
solution as essentially a pure mixed rare earth concentrate.

The resulting solution contains greater than 99% of the REE originally 
contained in the Bokan PLS. Mass balance calculations show the percentage of 
each individual rare earth metal in the Bokan PLS and in the combined rare 
earth eluate to be equal within analytical error indicating minimal or no loss 
of the rare earth metals during the separation procedure. Recovery percentages 
of the combined rare earth metals are very high, i.e., near 100%.

This rare earth enriched raffinate solution is fed through a further 
SuperLig(R) extraction column which is designed to separate the HREE's, as a 
group. The HREE's are then eluted from the column with a small amount of eluant 
and easily precipitated from the resulting concentrated solution to form the 
carbonate salt. Recovery rates for the HREE's from the Bokan PLS to the salt 
are in excess of 99%. The remaining raffinate containing the light rare earths, 
as well as yttrium, is preserved for further processing. Ucore is working to 
develop a high purity yttrium salt as an additional output product of the MRT 
process.

About Ucore Rare Metals Inc.

Ucore Rare Metals Inc. is a development-phase mining company focused on 
establishing rare metal resources with near term production potential. With 
multiple projects across North America, Ucore's primary focus is the 100% owned 
Bokan - Dotson Ridge REE property in Alaska. The Bokan - Dotson Ridge REE 
project is located 60 km southwest of Ketchikan, Alaska and 140 km northwest of 
Prince Rupert, British Columbia and has direct ocean access to the western 
seaboard and the Pacific Rim, a significant advantage in developing near term 
production facilities and limiting the capital costs associated with mine 
construction.

Ed Bentzen, Project Manager of Lyntek Inc. of Lakeview, Colorado, has approved 
the scientific and technical content of this news release and is the Qualified 
Person responsible for its accuracy.

This press release includes certain statements that may be deemed 
"forward-looking statements". All statements in this release, other than 
statements of historical facts, that address future exploration drilling, 
exploration activities, development timelines, and events or developments that 
the Company expects, are forward looking statements. Although the Company 
believes the expectations expressed in such forward-looking statements are 
based on reasonable assumptions, such statements are not guarantees of future 
performance and actual results or developments may differ materially from those 
in forward-looking statements. Factors that could cause actual results to 
differ materially from those in forward-looking statements include exploitation 
and exploration successes, continued availability of financing, and general 
economic, market or business conditions.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined by the TSX Venture Exchange) accepts responsibility for the 
adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Ucore Rare Metals Inc.
Mr. Jim McKenzie
President and Chief Executive Officer
(902) 482-5214
www.ucore.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=506974224