Source	MARKET NEWS
Date	11/12/2014
Time	09:58:31 AM

Company	 Silver Range Resources Ltd.
Title	Completes Updated Resource And Barite Marketing





    CDNX Symbol: SNG











Press Release	





Completes Updated Resource And Barite Marketing Study --->@NEWS RELEASE
SILVER RANGE RESOURCES LTD ("SNG-V;SLRRF-0")
- Completes Updated Resource And Barite Marketing Study
- For Its Mel Property, Yukon

Silver Range Resources Ltd. ("Silver Range") is pleased to announce
that it has received an updated independent resource estimate for the
Mel Main Zone on its wholly owned Mel Property, located in southeastern
Yukon. Silver Range also announces results of an independent barite
marketing study relating to the property. Highlights include:

//st

-- The Mel Main Zone hosts an inferred resource of 5.38 million tonnes
grading 6.45% zinc, 1.85% lead and 44.79% barite (BaSO(sub)4(/sub)), at a
cut-off grade of 5.0% zinc-equivalent.

-- The barite marketing study concludes that sales of 50,000 tonnes of
barite per year at $US 100/tonne would be reasonable into the Western
Canadian market.

//et

The Mel Property lies 80 km east of Watson Lake and 40 km north of
the Alaska Highway. At the Mel Main Zone, Cambrian to Ordovician-age
marine sediments with minor coeval volcanics host stratabound
zinc-lead-barite mineralization comprising coarse-grained sphalerite
and galena disseminated throughout a mixture of mudstone,
silica-carbonate and coarsely crystalline barite. Minor amounts of
fine-grained, sparsely disseminated pyrite occur locally. Wallrocks are
predominately limestone.

Preliminary metallurgical testing on drill core from the Mel Main
Zone by Lakefield Research in 1978, indicates that after grinding to
100 mesh, the mineralization responded well to flotation and yielded
concentrates ranging from 60.9 to 64.7% zinc, 78.0 to 79.6% lead and
90.3 to 94.4% barite with recoveries of 90.3 to 96.2% for zinc, 97.7 to
98.0% for lead and 88 to 90.9% for barite. A later, larger-scale test
was done for barite concentrate market evaluation. Concentrate grading
95.1% barite with a recovery of 92.6% was produced from feed grading
53.5% barite. A second round of preliminary metallurgical testing on
drill core from the Mel Main Zone was performed by Westcoast Mineral
Testing in 1990, which yielded similar results to the Lakefield
Research tests.

"Silver Range is very encouraged by the resource estimate -
especially considering that the Mel Main Zone remains open to extension
and is only one of four known zones on the property," states Doug
Eaton, CEO and President. "Project economics will certainly be enhanced
with barite as a potential co-product."

Resource Estimate

The Mel Main Zone mineral resource estimation was completed by
Gary Giroux, P.Eng., M.A.Sc. (Giroux Consultants Ltd.) who is a
qualified person and independent of Silver Range, based on the criteria
defined by National Instrument 43-101. A summary of inferred mineral
resources is tabulated below:

//st
-----------------------------------------------------------------------
-----
Inferred Resource within mineralized solids using a zinc-equivalent cut-off
---------------------------------------------------------------------------
-
Tonnes
greater than
Cut-Off          Cut-off             Grade greater than Cut-off
---------------------------------------------------------------------------
-
ZnEQ%(i)          Tonnes       Zn (%)       Pb (%)     ZnEQ (%)     BaSO4(%)
---------------------------------------------------------------------------
-
3.5            5,620,000         6.31         1.82         8.43       44.21
---------------------------------------------------------------------------
-
4.0            5,570,000         6.34         1.83         8.48       44.29
---------------------------------------------------------------------------
-
4.5            5,500,000         6.38         1.84         8.53       44.43
---------------------------------------------------------------------------
-
5.0            5,380,000         6.45         1.85         8.61       44.79
---------------------------------------------------------------------------
-
5.5            5,180,000         6.56         1.87         8.74       45.10
---------------------------------------------------------------------------
-
6.0            4,960,000         6.66         1.90         8.87       44.95
---------------------------------------------------------------------------
-
6.5            4,630,000         6.79         1.95         9.06       44.77
---------------------------------------------------------------------------
-
7.0            4,220,000         6.95         2.00         9.28       44.65
---------------------------------------------------------------------------
-
(i) Zinc-equivalence (ZnEQ%) was calculated using metal prices of US$0.89/lb
zinc and US$0.96/lb lead and assuming 90.3% zinc recovery and 97.7% lead
recovery.
//et

Data generated during various historical drill programs conducted
at the Mel Main Zone were independently reviewed by Giroux Consultants
Ltd. as part of the resource study. The resource estimate for the Mel
Main Zone was initiated by constructing a wire-frame 3D solid model in
"GEMS". Three-dimensional solids were manually digitized from the
available drill data and were used to constrain the interpolation of
mineralization. The model was constructed based upon lithological
boundaries and structural controls. Two solids were created, each
representing a separate mineralogical domain. Samples were capped for
all variables within each domain. Block grades were estimated by
Ordinary Kriging of composites within each domain. Block densities were
established from 47 samples.

Further details of the estimation procedure will be available in a
NI 43-101 report authored by Giroux Consultants Ltd. and H. Leo King.
P. Geo., which will be posted under the Silver Range profile at
www.sedar.com no later than 45 days from the date of this news release.


Barite Marketing Study

A Barite Marketing Study regarding potential production of barite
from the Mel Property was recently completed by World Industrial
Minerals Inc ("WIM"), of Arvada, Colorado. This study concluded that
barite from the Mel Property could likely be sold into the drilling
products market in Western Canada and Alaska. Based on current demand,
WIM estimated that sales of 50,000 tonnes per year at $US 100/tonne
would be reasonable into the Western Canadian market. The study also
recommended that further work be conducted to verify that impurity
levels meet specifications.

Future Exploration

Silver Range will soon be filing exploration permitting
applications in regard to the Mel Property, which will include plans
for detailed drilling at the Mel Main Zone to define an indicated
resource, and exploration drilling at Mel Main and other zones on the
property to further evaluate and expand resource potential. The
application will also include various environmental, heritage and
geotechnical studies needed to advance development of the project.

About Silver Range Resources Ltd.

Silver Range is a junior mineral exploration company listed on the
TSX Venture Exchange. The Company is exploring for zinc, lead and
silver at its wholly-owned projects in Yukon Territory. Silver Range is
well funded, with no debt and approximately $2.8 million in unallocated
working capital.

Technical information in this news release has been approved by
Matthew R. Dumala, P. Eng., a geological engineer with Archer, Cathro &
Associates (1981) Limited and qualified person for the purposes of NI
43-101.

ON BEHALF OF THE BOARD

W. Douglas Eaton, President and Chief Executive Officer

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

ENQUIRIES:
Silver Range Resources Ltd. - Corporate Information
W. Douglas Eaton
President and C.E.O.
(604) 688-2568
info@nordacres.com

Silver Range Resources Ltd. - Investor Inquiries
Richard Drechsler
V.P. Communications
(604) 687-2522 or NA Toll-Free: (888) 688-2522
rdrechsler@silverrangeresources.com
www.silverrangeresources.com

NA Toll-Free: (888) 688-2522     Silver Range Resources Ltd.
______________________________
_______________________________________________
TSX Venture closing price for SNG-V
Date: 2014/11/11
Closing Price: 0.09
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1431500032TS11431502031-09561620141112