Source	CANADA NEWSWIRE
Date	11/12/2014
Time	01:09:58 PM

Company	 Tinka Resources Limited
Title	Tinka Intersects Thick High-grade Zinc Mineralization in Four Drill
Holes at Ayawilca





    CDNX Symbol: TK











Press Release	




" BC-Tinka-Drill-Holes   11-12 2593
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Tinka Intersects Thick High-grade Zinc Mineralization in Four Drill
Holes at Ayawilca@

VANCOUVER, Nov. 12, 2014 /CNW/ - Tinka Resources Limited ("Tinka" or the
"Company") (TSXV: TK) (OTCPK: TKRFF) is pleased to announce results of the
first four holes of its current drill program at the Ayawilca zinc project,
central Peru. All four holes have intersected high-grade zinc sulphide
mineralization over substantial thicknesses. Tinka continues to prove the
large scale zinc potential of Ayawilca.
Key drill results:
West Ayawilca area:
<<

--  A14-22: 148.5 metres at 4.3% zinc from 170.0 metres depth, including
32.8 metres at 7.4% zinc from 211.2 metres depth, and 31.0 metres at
6.3% zinc from 283.5 metres depth;
--  A14-20: 2.2 metres at 21.0% zinc from 164 metres depth; and 34.15 metres
at 5.3% zinc from 179.85 metres depth, including 12.0 metres at 10.5%
zinc from 179.85 metres depth; and 42 metres at 4.3% zinc from 268
metres depth;
--  A14-19: 144.9 metres at 3.9% zinc from 184.0 metres depth, including
18.0 metres at 7.1% zinc from 250 metres depth;
>>
East Ayawilca area:
<<

--  A14-21: 19.6 metres at 5.7% zinc from 164.0 metres depth, including 6.0
metres at 10.2% zinc from 166.0 metres depth.
>>
Three of the holes at West Ayawilca (A14-19, A14-20, A14-22) were
collared within 150 metres of a previous Tinka drill hole, A13-05, which
intersected 213 metres at 5.3 % zinc from 130 metres depth (see Figures 1 and
2). The fourth hole (A14-21) targeted a previously untested geophysical
magnetic anomaly at East Ayawilca and also intersected significant zinc
mineralization. A 1% zinc cut-off grade over 6 metre intervals was used by the
Company. Credits of lead (0.1-0.4%) and silver (10 to 20 g/t Ag) typically
accompany the zinc mineralization. The mineralized rock is interpreted from
drill core measurements to be generally gently-dipping. The true widths of the
intercepts are believed to be at least 75% of the down-hole widths.
Dr. Graham Carman, Tinka's President and CEO, stated: "These results from
the first four holes in the current drill campaign are very significant, with
all holes intersecting strong zinc sulphide mineralization over substantial
vertical thicknesses. At West Ayawilca we are starting to see definition of
the zinc mineralization around A13-05 with good probability of continuity of
mineralization between holes covering a surface area of approximately 200
metres (north-south) by 130 metres (east-west). Mineralization remains open,
and drilling is continuing."
"At East Ayawilca, one kilometre to the east, the first hole drilled to
test a geophysical anomaly (A14-21) intersected significant zinc
mineralization over a 20 metre interval. We await assays for an additional
hole, A14-24, which has just been completed. Further holes are planned at East
Ayawilca in the current campaign as we believe this area has large scale zinc
potential. It is very exciting that Tinka is intersecting zinc mineralization
in two separate areas at Ayawilca, with a number of other targets including
Central Ayawilca yet to be adequately followed up (e.g., drill hole A12-08
intersected 36.5 metres at 6.5% zinc in 2012)." "Tinka is now approximately
midway through the current drill program at Ayawilca, with two drill rigs
operating. Seven holes have now been completed with assays awaited for three
additional holes. Drilling will continue until mid-December, when operations
will close down for Christmas and New Year. This will allow the Company time
to compile and interpret results, and plan the 2015 drill programs."
Geology of the zinc mineralization
Zinc mineralization at Ayawilca occurs in the form of massive to
semi-massive sulphide replacements of sedimentary rocks, with lesser
vein-style mineralization. The sulphides consist of sphalerite, pyrite, and
pyrrhotite (with minor galena, chalcopyrite, and arsenopyrite) generally
accompanied by chlorite, carbonate, and sometimes magnetite. The host rocks
are a sedimentary sequence consisting of sedimentary breccia, siltstone, shale
and limestone up to 250 metres thick ("Oyon Formation") overlain by sandstone
around 150 metres thick ("Goyllar Group") forming a barren cap to the
mineralization, although the sandstone can host sporadic sulphide veins.
Beneath the Oyon Formation, which dips gently to the east, lies a metamorphic
rock known as phyllite ("Excelsior Group") which is barren of zinc. Drill
holes are generally stopped a few metres into phyllite, with the average hole
depth being 395 metres so far. Drill holes are angled steeply between 60
degrees and 85 degrees to the horizontal. See Tables 1 and 2 for a summary of
the drill results and drill collar information.
Gravity geophysical survey
To further assist with the drill targeting, a geophysical gravity survey
is now underway at Ayawilca. The gravity survey should assist our geological
team in identifying massive sulphide target zones that are not associated with
magnetic anomalies, which has been our principal targeting tool in the program
to date. An area of approximately 2 km2 will be covered with a 100 metre by
100 metre gravity point spacing. A surrounding area of approximately 9 km2
will be covered with 200 metre x 200 metre point spacing. The gravity survey
is expected to be completed by the end of November 2014.
Colquipucro drill program
Drilling is continuing with one drill rig at the adjacent Colquipucro
silver oxide project, located 2 kilometres to the north of Ayawilca (see
Figure 3). Tinka is carrying out a 10-hole, 1,500 metre drill program
consisting of infill and resource extension drilling. We expect the drill
program at Colquipucro to be completed by the end of November, with results of
the full program to be released by the end of January 2015.
The qualified person, Dr. Graham Carman, Tinka's President and CEO, and a
Fellow of the Australasian Institute of Mining and Metallurgy, has reviewed
and verified the technical contents of this release.
About Tinka Resources Limited
Tinka is a junior resource acquisition and exploration company with
projects in Peru. Tinka's focus is on its 100%-owned Ayawilca and Colquipucro
projects in the highly mineralized zinc-lead-silver belt of central Peru, 200
kilometres north of Lima. The Ayawilca project, located 40 kilometres from
Peru's largest historic zinc mine, Cerro de Pasco, has the potential to be a
major zinc sulphide discovery. The nearby Colquipucro silver oxide project is
a near-surface, sandstone hosted silver oxide deposit with a current inferred
resource containing 32 million ounces silver with potential for expansion.
On behalf of the Board,



"Graham Carman"

Dr. Graham Carman,
President & CEO
Forward Looking Statements. Certain information in this news release
contains forward-looking statements and forward-looking information within the
meaning of applicable securities laws (collectively "forward-looking
statements"). All statements, other than statements of historical fact are
forward-looking statements. Forward-looking statements are based on the
beliefs and expectations of Tinka as well as assumptions made by and
information currently available to Tinka's management. Such statements reflect
the current risks, uncertainties and assumptions related to certain factors
including, without limitations, capital and other costs varying significantly
from estimates, production rates varying from estimates, changes in world
metal markets, changes in equity markets, uncertainties relating to the
availability and costs of financing needed in the future, equipment failure,
unexpected geological conditions, imprecision in resource estimates or metal
recoveries, success of future development initiatives, competition, operating
performance, environmental and safety risks, delays in obtaining or failure to
obtain necessary permits and approvals from local authorities, community
relations, and other development and operating risks. Should any one or more
of these risks or uncertainties materialize, or should any underlying
assumptions prove incorrect, actual results may vary materially from those
described herein. Although Tinka believes that assumptions inherent in the
forward-looking statements are reasonable, forward-looking statements are not
guarantees of future performance and accordingly undue reliance should not be
put on such statements due to the inherent uncertainty therein. Except as may
be required by applicable securities laws, Tinka disclaims any intent or
obligation to update any forward-looking statement.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release.
Notes on core sampling:All holes are diamond cores with recoveries
generally at or close to 100%. The drill core (typically HQ size) is marked
up, logged, and photographed on site. The cores are then cut in half at the
Company's core storage facility with half-cores stored as a future reference.
The other half-core is bagged on average over 2 metre composite intervals and
sent to SGS laboratory in Lima for assay in batches. Standards and blanks are
inserted into each batch prior to departure from the Company's core storage
facilities. At the laboratory, samples are dried, crushed to 100% passing 2mm,
then 500 grams pulverized for multi-element analysis by ICP using multi-acid
digestion. Samples assaying over 1% zinc, lead, or copper are reassayed using
precise ore-grade AAS techniques.
Notes on assay results (see Table1):Zinc intersections have been
calculated on the basis of a 1% zinc cut-off over 6 metre intervals.
Table 1. Summary of drill results (new results highlighted) and
significant past drill results from Ayawilca

Drill hole                From (m)        To (m)        Interval  (m)        Zn 
(%)     Pb (%)  Ag (g/t)   Cu (%)
----------                -------         -----         ------------         
-----       -----    --------   -----

A14-22                             170.00        318.50               
148.50         4.33      0.36          15    0.03

including                          211.20        244.00                
32.80         7.44      0.02          10    0.02

including                          228.00        233.75                 
5.75        16.76      0.02          24    0.07

and                                283.50        314.50                
31.00         6.31      0.39          13    0.02

including                          293.90        295.90                 
2.00        28.94      5.84         139    0.09

A14-21                             164.00        183.60                
19.60         5.67      0.02           8    0.05

including                          166.00        172.00                 
6.00        10.15      0.04          14    0.06

and                                298.00        370.60                
72.60         0.44      0.05          15    0.08

including                          298.00        300.00                 
2.00         0.15      0.00           0    0.00

A14-20                             164.00        166.20                 
2.20        20.96      0.11          80    0.37

and                                179.85        214.00                
34.15         5.27      0.25          22    0.04

including                          179.85        191.80                
11.95        10.52      0.40          23    0.02

including                          179.85        184.00                 
4.15        24.80      1.00          58    0.04

and                                242.00        250.00                 
8.00         2.23      1.28         181    0.09

and                                268.00        310.00                
42.00         4.26      0.08          25    0.04

including                          299.80        301.00                 
1.20        18.64      0.14          52    0.01

A14-19                             184.00        328.90               
144.90         3.88      0.03           7    0.02

including                          250.00        268.00                
18.00         7.11      0.01          11    0.03


SIGNIFICANT PAST RESULTS:
-------------------------

A12-04A                            260.00        280.00                
20.00         7.12      0.02           9    0.04

including                          266.00        278.00                
12.00        10.51      0.03          14    0.05

A12-08                             162.00        232.00                
70.00         4.77      0.16           5    0.03

including                          170.00        174.00                 
4.00        11.66      0.03           9    0.05

and                                195.50        232.00                
36.50         6.51      0.02           5    0.06

including                          195.50        214.50                
19.00         9.02      0.02           6    0.08

and                                266.00        322.80                
56.80         3.60      0.02           5    0.02

A12-09                             216.00        245.50                
29.50         3.21      0.12           6    0.06

A13-01                             228.00        235.20                 
7.20         8.54      0.09           6    0.07

A13-02                             236.00        328.00                
92.00         2.90      0.10           5    0.02

A13-03                             165.30        174.00                 
8.70         4.31      0.57          11    0.07

A13-04                             190.00        198.00                 
8.00         8.37      0.02           6    0.04

and                                266.00        332.00                
66.00         2.28      0.11           4    0.02

A13-05                             130.30        343.20               
212.90         5.34      0.17          15    0.03

including                          130.30        179.50                
49.20        10.07      0.55          32    0.16

including                          150.00        166.00                
16.00        18.14      0.05          39    0.25

and                                316.00        326.00                
10.00        12.93      0.02          42    0.04

A13-06                             170.00        196.00                
26.00         2.20      0.05           5    0.01

and                                210.00        322.00               
112.00         3.71      0.04           6    0.01
including                          262.00        322.00                
60.00         4.67      0.07           7    0.01

including                          264.65        278.00                
13.35         8.42      0.20          14    0.02

and                                312.00        322.00                
10.00         7.85      0.07           7    0.01

A13-07                              75.80         76.90                 
1.10        30.00      0.06          54    0.10

A13-12A                               250           268                
18.00         3.84      0.03           5    0.05

and                                280.00        292.00                
12.00         4.22      0.24          16    0.05

A13-15                             329.20        344.00                
14.80         4.80      0.01           5    0.09

A13-16                             370.00        394.00                
24.00         2.80      0.01           2    0.01

A13-17  

" BC-Tinka-Drill-Holes   11-12 2593
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Tinka Intersects Thick High-grade Zinc Mineralization in Four Drill
Holes at Ayawilca@

VANCOUVER, Nov. 12, 2014 /CNW/ - Tinka Resources Limited ("Tinka" or the
"Company") (TSXV: TK) (OTCPK: TKRFF) is pleased to announce results of the
first four holes of its current drill program at the Ayawilca zinc project,
central Peru. All four holes have intersected high-grade zinc sulphide
mineralization over substantial thicknesses. Tinka continues to prove the
large scale zinc potential of Ayawilca.
Key drill results:
West Ayawilca area:
<<

--  A14-22: 148.5 metres at 4.3% zinc from 170.0 metres depth, including
32.8 metres at 7.4% zinc from 211.2 metres depth, and 31.0 metres at
6.3% zinc from 283.5 metres depth;
--  A14-20: 2.2 metres at 21.0% zinc from 164 metres depth; and 34.15 metres
at 5.3% zinc from 179.85 metres depth, including 12.0 metres at 10.5%
zinc from 179.85 metres depth; and 42 metres at 4.3% zinc from 268
metres depth;
--  A14-19: 144.9 metres at 3.9% zinc from 184.0 metres depth, including
18.0 metres at 7.1% zinc from 250 metres depth;
>>
East Ayawilca area:
<<

--  A14-21: 19.6 metres at 5.7% zinc from 164.0 metres depth, including 6.0
metres at 10.2% zinc from 166.0 metres depth.
>>
Three of the holes at West Ayawilca (A14-19, A14-20, A14-22) were
collared within 150 metres of a previous Tinka drill hole, A13-05, which
intersected 213 metres at 5.3 % zinc from 130 metres depth (see Figures 1 and
2). The fourth hole (A14-21) targeted a previously untested geophysical
magnetic anomaly at East Ayawilca and also intersected significant zinc
mineralization. A 1% zinc cut-off grade over 6 metre intervals was used by the
Company. Credits of lead (0.1-0.4%) and silver (10 to 20 g/t Ag) typically
accompany the zinc mineralization. The mineralized rock is interpreted from
drill core measurements to be generally gently-dipping. The true widths of the
intercepts are believed to be at least 75% of the down-hole widths.
Dr. Graham Carman, Tinka's President and CEO, stated: "These results from
the first four holes in the current drill campaign are very significant, with
all holes intersecting strong zinc sulphide mineralization over substantial
vertical thicknesses. At West Ayawilca we are starting to see definition of
the zinc mineralization around A13-05 with good probability of continuity of
mineralization between holes covering a surface area of approximately 200
metres (north-south) by 130 metres (east-west). Mineralization remains open,
and drilling is continuing."
"At East Ayawilca, one kilometre to the east, the first hole drilled to
test a geophysical anomaly (A14-21) intersected significant zinc
mineralization over a 20 metre interval. We await assays for an additional
hole, A14-24, which has just been completed. Further holes are planned at East
Ayawilca in the current campaign as we believe this area has large scale zinc
potential. It is very exciting that Tinka is intersecting zinc mineralization
in two separate areas at Ayawilca, with a number of other targets including
Central Ayawilca yet to be adequately followed up (e.g., drill hole A12-08
intersected 36.5 metres at 6.5% zinc in 2012)." "Tinka is now approximately
midway through the current drill program at Ayawilca, with two drill rigs
operating. Seven holes have now been completed with assays awaited for three
additional holes. Drilling will continue until mid-December, when operations
will close down for Christmas and New Year. This will allow the Company time
to compile and interpret results, and plan the 2015 drill programs."
Geology of the zinc mineralization
Zinc mineralization at Ayawilca occurs in the form of massive to
semi-massive sulphide replacements of sedimentary rocks, with lesser
vein-style mineralization. The sulphides consist of sphalerite, pyrite, and
pyrrhotite (with minor galena, chalcopyrite, and arsenopyrite) generally
accompanied by chlorite, carbonate, and sometimes magnetite. The host rocks
are a sedimentary sequence consisting of sedimentary breccia, siltstone, shale
and limestone up to 250 metres thick ("Oyon Formation") overlain by sandstone
around 150 metres thick ("Goyllar Group") forming a barren cap to the
mineralization, although the sandstone can host sporadic sulphide veins.
Beneath the Oyon Formation, which dips gently to the east, lies a metamorphic
rock known as phyllite ("Excelsior Group") which is barren of zinc. Drill
holes are generally stopped a few metres into phyllite, with the average hole
depth being 395 metres so far. Drill holes are angled steeply between 60
degrees and 85 degrees to the horizontal. See Tables 1 and 2 for a summary of
the drill results and drill collar information.
Gravity geophysical survey
To further assist with the drill targeting, a geophysical gravity survey
is now underway at Ayawilca. The gravity survey should assist our geological
team in identifying massive sulphide target zones that are not associated with
magnetic anomalies, which has been our principal targeting tool in the program
to date. An area of approximately 2 km2 will be covered with a 100 metre by
100 metre gravity point spacing. A surrounding area of approximately 9 km2
will be covered with 200 metre x 200 metre point spacing. The gravity survey
is expected to be completed by the end of November 2014.
Colquipucro drill program
Drilling is continuing with one drill rig at the adjacent Colquipucro
silver oxide project, located 2 kilometres to the north of Ayawilca (see
Figure 3). Tinka is carrying out a 10-hole, 1,500 metre drill program
consisting of infill and resource extension drilling. We expect the drill
program at Colquipucro to be completed by the end of November, with results of
the full program to be released by the end of January 2015.
The qualified person, Dr. Graham Carman, Tinka's President and CEO, and a
Fellow of the Australasian Institute of Mining and Metallurgy, has reviewed
and verified the technical contents of this release.
About Tinka Resources Limited
Tinka is a junior resource acquisition and exploration company with
projects in Peru. Tinka's focus is on its 100%-owned Ayawilca and Colquipucro
projects in the highly mineralized zinc-lead-silver belt of central Peru, 200
kilometres north of Lima. The Ayawilca project, located 40 kilometres from
Peru's largest historic zinc mine, Cerro de Pasco, has the potential to be a
major zinc sulphide discovery. The nearby Colquipucro silver oxide project is
a near-surface, sandstone hosted silver oxide deposit with a current inferred
resource containing 32 million ounces silver with potential for expansion.
On behalf of the Board,



"Graham Carman"

Dr. Graham Carman,
President & CEO
Forward Looking Statements. Certain information in this news release
contains forward-looking statements and forward-looking information within the
meaning of applicable securities laws (collectively "forward-looking
statements"). All statements, other than statements of historical fact are
forward-looking statements. Forward-looking statements are based on the
beliefs and expectations of Tinka as well as assumptions made by and
information currently available to Tinka's management. Such statements reflect
the current risks, uncertainties and assumptions related to certain factors
including, without limitations, capital and other costs varying significantly
from estimates, production rates varying from estimates, changes in world
metal markets, changes in equity markets, uncertainties relating to the
availability and costs of financing needed in the future, equipment failure,
unexpected geological conditions, imprecision in resource estimates or metal
recoveries, success of future development initiatives, competition, operating
performance, environmental and safety risks, delays in obtaining or failure to
obtain necessary permits and approvals from local authorities, community
relations, and other development and operating risks. Should any one or more
of these risks or uncertainties materialize, or should any underlying
assumptions prove incorrect, actual results may vary materially from those
described herein. Although Tinka believes that assumptions inherent in the
forward-looking statements are reasonable, forward-looking statements are not
guarantees of future performance and accordingly undue reliance should not be
put on such statements due to the inherent uncertainty therein. Except as may
be required by applicable securities laws, Tinka disclaims any intent or
obligation to update any forward-looking statement.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release.
Notes on core sampling:All holes are diamond cores with recoveries
generally at or close to 100%. The drill core (typically HQ size) is marked
up, logged, and photographed on site. The cores are then cut in half at the
Company's core storage facility with half-cores stored as a future reference.
The other half-core is bagged on average over 2 metre composite intervals and
sent to SGS laboratory in Lima for assay in batches. Standards and blanks are
inserted into each batch prior to departure from the Company's core storage
facilities. At the laboratory, samples are dried, crushed to 100% passing 2mm,
then 500 grams pulverized for multi-element analysis by ICP using multi-acid
digestion. Samples assaying over 1% zinc, lead, or copper are reassayed using
precise ore-grade AAS techniques.
Notes on assay results (see Table1):Zinc intersections have been
calculated on the basis of a 1% zinc cut-off over 6 metre intervals.
Table 1. Summary of drill results (new results highlighted) and
significant past drill results from Ayawilca

Drill hole                From (m)        To (m)        Interval  (m)        Zn 
(%)     Pb (%)  Ag (g/t)   Cu (%)
----------                -------         -----         ------------         
-----       -----    --------   -----

A14-22                             170.00        318.50               
148.50         4.33      0.36          15    0.03

including                          211.20        244.00                
32.80         7.44      0.02          10    0.02

including                          228.00        233.75                 
5.75        16.76      0.02          24    0.07

and                                283.50        314.50                
31.00         6.31      0.39          13    0.02

including                          293.90        295.90                 
2.00        28.94      5.84         139    0.09

A14-21                             164.00        183.60                
19.60         5.67      0.02           8    0.05

including                          166.00        172.00                 
6.00        10.15      0.04          14    0.06

and                                298.00        370.60                
72.60         0.44      0.05          15    0.08

including                          298.00        300.00                 
2.00         0.15      0.00           0    0.00

A14-20                             164.00        166.20                 
2.20        20.96      0.11          80    0.37

and                                179.85        214.00                
34.15         5.27      0.25          22    0.04

including                          179.85        191.80                
11.95        10.52      0.40          23    0.02

including                          179.85        184.00                 
4.15        24.80      1.00          58    0.04

and                                242.00        250.00                 
8.00         2.23      1.28         181    0.09

and                                268.00        310.00                
42.00         4.26      0.08          25    0.04

including                          299.80        301.00                 
1.20        18.64      0.14          52    0.01

A14-19                             184.00        328.90               
144.90         3.88      0.03           7    0.02

including                          250.00        268.00                
18.00         7.11      0.01          11    0.03


SIGNIFICANT PAST RESULTS:
-------------------------

A12-04A                            260.00        280.00                
20.00         7.12      0.02           9    0.04

including                          266.00        278.00                
12.00        10.51      0.03          14    0.05

A12-08                             162.00        232.00                
70.00         4.77      0.16           5    0.03

including                          170.00        174.00                 
4.00        11.66      0.03           9    0.05

and                                195.50        232.00                
36.50         6.51      0.02           5    0.06

including                          195.50        214.50                
19.00         9.02      0.02           6    0.08

and                                266.00        322.80                
56.80         3.60      0.02           5    0.02

A12-09                             216.00        245.50                
29.50         3.21      0.12           6    0.06

A13-01                             228.00        235.20                 
7.20         8.54      0.09           6    0.07

A13-02                             236.00        328.00                
92.00         2.90      0.10           5    0.02

A13-03                             165.30        174.00                 
8.70         4.31      0.57          11    0.07

A13-04                             190.00        198.00                 
8.00         8.37      0.02           6    0.04

and                                266.00        332.00                
66.00         2.28      0.11           4    0.02

A13-05                             130.30        343.20               
212.90         5.34      0.17          15    0.03

including                          130.30        179.50                
49.20        10.07      0.55          32    0.16

including                          150.00        166.00                
16.00        18.14      0.05          39    0.25

and                                316.00        326.00                
10.00        12.93      0.02          42    0.04

A13-06                             170.00        196.00                
26.00         2.20      0.05           5    0.01

and                                210.00        322.00               
112.00         3.71      0.04           6    0.01
including                          262.00        322.00                
60.00         4.67      0.07           7    0.01

including                          264.65        278.00                
13.35         8.42      0.20          14    0.02

and                                312.00        322.00                
10.00         7.85      0.07           7    0.01

A13-07                              75.80         76.90                 
1.10        30.00      0.06          54    0.10

A13-12A                               250           268                
18.00         3.84      0.03           5    0.05

and                                280.00        292.00                
12.00         4.22      0.24          16    0.05

A13-15                             329.20        344.00                
14.80         4.80      0.01           5    0.09

A13-16                             370.00        394.00                
24.00         2.80      0.01           2    0.01

A13-17                             372.10        394.00                
21.90         3.10      0.19          17    0.05

A14-18                             331.20        360.00                
28.80         5.62      0.17          10    0.02

including                          342.50        350.00                 
7.50         8.75      0.30          20    0.04

and                                375.10        412.00                
36.90         5.62      0.41           9    0.04

DD53                               226.00        280.00                
54.00         3.50      0.12           8    0.03

and                                292.00        315.10                
23.10         2.54      0.03           2    0.01

DD52B                              272.00        288.00                
16.00         6.80      0.13           9    0.00

DD70                               100.00        104.00                 
4.00        10.45      0.04          59    0.13

and                                156.00        170.00                
14.00         4.18      0.07          12    0.02

DD71                               196.00        200.00                 
4.00        30.90      0.32          63    0.13
----                               ------        ------                 
----        -----      ----         ---    ----

Table 2. Drill hole collar coordinates and hole details (new drill holes
shown in bold)

Drill hole                 Easting        Northing         Elevation      
Depth       Azimuth   Dip    Comment           Date
----------                 -------        --------         ---------      
-----       -------   ---    -------           ----

A14-19                             332951          8845940           4263       
407.90        360     -75    New results      2014

A14-20                             332896          8845986           4270       
362.70        360     -70    New results      2014

A14-21                             334112          8846100           4000       
515.00        350     -60    New results      2014

A14-22                             333000          8845928           4261       
355.10         10     -70    New results      2014

A14-23                             333078          8845921           4242       
323.10        360     -75    Pending          2014

A14-24                             334100          8846385           4055       
455.90        360     -70    Pending          2014

A14-25                             332903          8846062           4263       
350.40        360     -70    Pending          2014


PAST AYAWILCA DRILL HOLES:
--------------------------

A12-01                             333188          8846050           4210       
327.10        360     -60    Released         2012

A12-02                             333188          8846049           4210       
303.00        360     -90    Released         2012

A12-03                             333194          8846208           4227       
349.45        180     -70    Released         2012

A12-04A                            332967          8846187           4241       
285.60        360     -90    Released         2012

A12-05                             332967          8846188           4241       
327.70        360     -60    Released         2012

A12-06                             333591          8846155           4153       
359.45        360     -60    Released         2012

A12-07                             333591          8846154           4153       
367.10        360     -90    Released         2012

A12-08                             333389          8846042           4191       
344.20        180     -70    Released         2012

A12-09                             333389          8846042           4191       
360.80        360     -90    Released         2012

A12-10                             333391          8846197           4181       
366.55        180     -70    Released         2012

A13-01                             333590          8846039           4145       
359.95        180     -70    Released         2013

A13-02                             333389          8846040           4191       
370.90        180     -60    Released         2013

A13-03                             333590          8846041           4145       
338.25        180     -90    Released         2013

A13-04                             333591          8846038           4145       
380.10        180     -60    Released         2013

A13-05                             332954          8846075           4252       
361.50        360     -90    Released         2013

A13-06                             332953          8846074           4251       
400.10        180     -70    Released         2013

A13-07                             332952          8846074           4251       
314.10        270     -60    Released         2013

A13-08                             332954          8846075           4252       
350.60         90     -70    Released         2013

A13-09                             333188          8846050           4210       
347.80        180     -60    Released         2013

A13-10                             333500          8845870           4168       
326.10        360   -69.9    Released         2013

A13-11                             333500          8845870           4168       
344.20        180   -69.8    Released         2013

A13-12                             333691          8846004           4133       
122.00        180     -60    Released         2013

A13-12A                            333691          8846004           4133       
356.80        180   -69.9    Released         2013

A13-13                             333797          8845950           4120       
386.80        180   -65.5    Released         2013

A13-14                             333500          8846134           4167       
398.70        360   -60.9    Released         2013

A13-15                             333300          8846065           4200       
355.40        180   -64.9    Released         2013

A13-16                             333898          8846295           4112       
454.70        360   -59.6    Released         2013

A13-17                             333898          8846294           4112       
422.30        360   -75.6    Released         2013

A14-18                             333900          8846429           4122       
448.30        360     -60    Released         2014

DD52                               332950          8846081           4254       
196.60        310     -50    Released         2011

DD52B                              332953          8846076           4252       
318.80        360     -70    Released         2011

DD53                               332967          8846186           4241       
315.10        165     -60    Released         2011

DD66                               332909          8846064           4252       
230.60        165     -50    Released         2011

DD67                               332817          8846037           4272       
230.80        165     -50    Released         2011

DD68                               332873          8846192           4260       
176.40        165     -50    Released         2011

DD69                               332775          8846170           4277       
198.20        165     -50    Released         2011

DD70                               332826          8846305           4264       
243.30        165     -50    Released         2011

DD71                               332733          8846277           4291       
231.10        165     -50    Released         2011
----                               ------          -------           ----       
------        ---     ---    --------         ----
Note: the mineralized rock is interpreted from drill core measurements to
be generally gently-dipping. The true widths of the intercepts are believed to
be at least 75% of the down-hole widths.
Note on drill hole data:
Eastings and Northings are based on the PSAD56/18S UTM datum. The
coordinates for the current drill holes are collected via a hand-held GPS and
are considered accurate to within a few metres. Drill hole locations from the
previous programs were surveyed with a theodolite or determined by tape and
compass from a known survey point. Elevations are taken from a digital
topographic model of the project based on a number of known points and are
considered accurate to within a few metres. Azimuth and dip measurements were
taken using compass and inclinometer at surface. All holes from A13-10 onwards
were down-hole surveyed; small variances in both azimuth and dip do occur down
hole.
IMAGES:
Figure 1. Drill map of Ayawilca over ground magnetics image (white-red
areas are magnetic bodies)
Figure 2. West Ayawilca drill map (plan view) with current drill holes
and intersections
Figure 3. Geology and location map of Ayawilca-Colquipucro projects,
central Peru
SOURCE Tinka Resources Limited



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/November2014/12/c6757.html

PDF available at:
http://stream1.newswire.ca/media/2014/11/12/20141112_C6757_PDF_EN_7846.pdf

PDF available at:
http://stream1.newswire.ca/media/2014/11/12/20141112_C6757_PDF_EN_7847.pdf

PDF available at:
http://stream1.newswire.ca/media/2014/11/12/20141112_C6757_PDF_EN_7848.pdf

-0-                           11/12/2014
/For further information: Investor Information: www.tinkaresources.com,
1305 - 1090 West Georgia St., Vancouver, BC, V6E 3V7, James Powell +
1-647-478-8976, Seema Sindwani +1 647-478-3017, info(at)tinkaresources.com/
/Web Site: http://www.tinkaresources.com /
(TKRFF TK.)

CO:  Tinka Resources Limited
ST:  British Columbia
IN:  MNG
SU:

-30-