Source	MARKET NEWS
Date	11/12/2014
Time	01:57:07 PM

Company	 Tinka Resources Limited
Title	Intersects 
Thick High grade Zinc Mineralization





    CDNX Symbol: TK











Press Release	




[200/News Release]TKVTINKA RESOURCES LTDNOV 12 2014  13:54 PMIntersects 
Thick High grade Zinc Mineralization in Four Drill Holesat Ayawilca --->@NEWS 
RELEASE
TINKA RESOURCES LTD ("TK-V;TKRFF-0")
- Intersects Thick High-grade Zinc Mineralization in Four Drill
- Holes at Ayawilca

Tinka Resources Limited ("Tinka" or the "Company") is pleased to
announce results of the first four holes of its current drill program
at the Ayawilca zinc project, central Peru.  All four holes have
intersected high-grade zinc sulphide mineralization over substantial
thicknesses. Tinka continues to prove the large scale zinc potential of
Ayawilca.

Key drill results:

West Ayawilca area:

//st

A14-22: 148.5 metres at 4.3% zinc from 170.0 metres depth, including
32.8 metres at 7.4% zinc from 211.2 metres depth, and 31.0 metres at 6.3%
zinc from 283.5 metres depth;
A14-20: 2.2 metres at 21.0% zinc from 164 metres depth; and 34.15 metres
at 5.3% zinc from 179.85 metres depth, including 12.0 metres at 10.5% zinc
from 179.85 metres depth; and 42 metres at 4.3% zinc from 268 metres depth;
A14-19: 144.9 metres at 3.9% zinc from 184.0 metres depth, including
18.0 metres at 7.1% zinc from 250 metres depth;
//et

East Ayawilca area:

//st

A14-21: 19.6 metres at 5.7% zinc from 164.0 metres depth, including 6.0
metres at 10.2% zinc from 166.0 metres depth.
//et

Three of the holes at West Ayawilca (A14-19, A14-20, A14-22) were
collared within 150 metres of a previous Tinka drill hole, A13-05,
which intersected 213 metres at 5.3 % zinc from 130 metres depth (see
Figures 1 and 2). The fourth hole (A14-21) targeted a previously
untested geophysical magnetic anomaly at East Ayawilca and also
intersected significant zinc mineralization.  A 1% zinc cut-off grade
over 6 metre intervals was used by the Company. Credits of lead
(0.1-0.4%) and silver (10 to 20 g/t Ag) typically accompany the zinc
mineralization.  The mineralized rock is interpreted from drill core
measurements to be generally gently-dipping. The true widths of the
intercepts are believed to be at least 75% of the down-hole widths.

Dr. Graham Carman, Tinka's President and CEO, stated: "These
results from the first four holes in the current drill campaign are
very significant, with all holes intersecting strong zinc sulphide
mineralization over substantial vertical thicknesses.  At West Ayawilca
we are starting to see definition of the zinc mineralization around
A13-05 with good probability of continuity of mineralization between
holes covering a surface area of approximately 200 metres (north-south)
by 130 metres (east-west).  Mineralization remains open, and drilling
is continuing."

"At East Ayawilca, one kilometre to the east, the first hole
drilled to test a geophysical anomaly (A14-21) intersected significant
zinc mineralization over a 20 metre interval.  We await assays for an
additional hole, A14-24, which has just been completed. Further holes
are planned at East Ayawilca in the current campaign as we believe this
area has large scale zinc potential. It is very exciting that Tinka is
intersecting zinc mineralization in two separate areas at Ayawilca,
with a number of other targets including Central Ayawilca yet to be
adequately followed up (e.g., drill hole A12-08 intersected 36.5 metres
at 6.5% zinc in 2012)."
"Tinka is now approximately midway through the current drill
program at Ayawilca, with two drill rigs operating.  Seven holes have
now been completed with assays awaited for three additional holes.
Drilling will continue until mid-December, when operations will close
down for Christmas and New Year.  This will allow the Company time to
compile and interpret results, and plan the 2015 drill programs."

Geology of the zinc mineralization

Zinc mineralization at Ayawilca occurs in the form of massive to
semi-massive sulphide replacements of sedimentary rocks, with lesser
vein-style mineralization. The sulphides consist of sphalerite, pyrite,
and pyrrhotite (with minor galena, chalcopyrite, and arsenopyrite)
generally accompanied by chlorite, carbonate, and sometimes magnetite.
The host rocks are a sedimentary sequence consisting of sedimentary
breccia, siltstone, shale and limestone up to 250 metres thick ("Oyon
Formation") overlain by sandstone around 150 metres thick ("Goyllar
Group") forming a barren cap to the mineralization, although the
sandstone can host sporadic sulphide veins.  Beneath the Oyon
Formation, which dips gently to the east, lies a metamorphic rock known
as phyllite ("Excelsior Group") which is barren of zinc.  Drill holes
are generally stopped a few metres into phyllite, with the average hole
depth being 395 metres so far.  Drill holes are angled steeply between
60 degrees and 85 degrees to the horizontal. See Tables 1 and 2 for a
summary of the drill results and drill collar information.

Gravity geophysical survey

To further assist with the drill targeting, a geophysical gravity
survey is now underway at Ayawilca.  The gravity survey should assist
our geological team in identifying massive sulphide target zones that
are not associated with magnetic anomalies, which has been our
principal targeting tool in the program to date.  An area of
approximately 2 km2 will be covered with a 100 metre by 100 metre
gravity point spacing.  A surrounding area of approximately 9 km2 will
be covered with 200 metre x 200 metre point spacing.  The gravity
survey is expected to be completed by the end of November 2014.

Colquipucro drill program

Drilling is continuing with one drill rig at the adjacent
Colquipucro silver oxide project, located 2 kilometres to the north of
Ayawilca (see Figure 3).  Tinka is carrying out a 10-hole, 1,500 metre
drill program consisting of infill and resource extension drilling.  We
expect the drill program at Colquipucro to be completed by the end of
November, with results of the full program to be released by the end of
January 2015.

The qualified person, Dr. Graham Carman, Tinka's President and
CEO, and a Fellow of the Australasian Institute of Mining and
Metallurgy, has reviewed and verified the technical contents of this
release.

About Tinka Resources Limited
Tinka is a junior resource acquisition and exploration company
with projects in Peru.  Tinka's focus is on its 100%-owned Ayawilca and
Colquipucro projects in the highly mineralized zinc-lead-silver belt of
central Peru, 200 kilometres north of Lima. The Ayawilca project,
located 40 kilometres from Peru's largest historic zinc mine, Cerro de
Pasco, has the potential to be a major zinc sulphide discovery.  The
nearby Colquipucro silver oxide project is a near-surface, sandstone
hosted silver oxide deposit with a current inferred resource containing
32 million ounces silver with potential for expansion.

//st
On behalf of the Board,           "Graham Carman"        Dr. Graham Carman,
President & CEO



//et

Forward Looking Statements. Certain information in this news
release contains forward-looking statements and forward-looking
information within the meaning of applicable securities laws
(collectively "forward-looking statements").  All statements, other
than statements of historical fact are forward-looking statements.
Forward-looking statements are based on the beliefs and expectations of
Tinka as well as assumptions made by and information currently
available to Tinka's management.  Such statements reflect the current
risks, uncertainties and assumptions related to certain factors
including, without limitations, capital and other costs varying
significantly from estimates, production rates varying from estimates,
changes in world metal markets, changes in equity markets,
uncertainties relating to the availability and costs of financing
needed in the future, equipment failure, unexpected geological
conditions, imprecision in resource estimates or metal recoveries,
success of future development initiatives, competition, operating
performance, environmental and safety risks, delays in obtaining or
failure to obtain necessary permits and approvals from local
authorities, community relations, and other development and operating
risks. Should any one or more of these risks or uncertainties
materialize, or should any underlying assumptions prove incorrect,
actual results may vary materially from those described herein.
Although Tinka believes that assumptions inherent in the
forward-looking statements are reasonable, forward-looking statements
are not guarantees of future performance and accordingly undue reliance
should not be put on such statements due to the inherent uncertainty
therein. Except as may be required by applicable securities laws, Tinka
disclaims any intent or obligation to update any forward-looking
statement.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release.

Notes on core sampling:
All holes are diamond cores with recoveries generally at or close
to 100%.  The drill core (typically HQ size) is marked up, logged, and
photographed on site.  The cores are then cut in half at the Company's
core storage facility with half-cores stored as a future reference.
The other half-core is bagged on average over 2 metre composite
intervals and sent to SGS laboratory in Lima for assay in batches.
Standards and blanks are inserted into each batch prior to departure
from the Company's core storage facilities.  At the laboratory, samples
are dried, crushed to 100% passing 2mm, then 500 grams pulverized for
multi-element analysis by ICP using multi-acid digestion. Samples
assaying over 1% zinc, lead, or copper are reassayed using precise
ore-grade AAS techniques.

Notes on assay results (see Table1):
Zinc intersections have been calculated on the basis of a 1% zinc
cut-off over 6 metre intervals.

Table 1.  Summary of drill results (new results highlighted) and
significant past drill results from Ayawilca

//st










Drill hole From (m) To (m) Interval  (m) Zn (%) Pb (%) Ag (g/t) Cu (%)
A14-22       170.00 318.50        148.50   4.33   0.36       15   0.03
including    211.20 244.00         32.80   7.44   0.02       10   0.02
including    228.00 233.75          5.75  16.76   0.02       24   0.07
&            283.50 314.50         31.00   6.31   0.39       13   0.02
including    293.90 295.90          2.00  28.94   5.84      139   0.09
A14-21       164.00 183.60         19.60   5.67   0.02        8   0.05
including    166.00 172.00          6.00  10.15   0.04       14   0.06
&            298.00 370.60         72.60   0.44   0.05       15   0.08
including    298.00 300.00          2.00   0.15   0.00        0   0.00
A14-20       164.00 166.20          2.20  20.96   0.11       80   0.37
&            179.85 214.00         34.15   5.27   0.25       22   0.04
including    179.85 191.80         11.95  10.52   0.40       23   0.02
including    179.85 184.00          4.15  24.80   1.00       58   0.04
&            242.00 250.00          8.00   2.23   1.28      181   0.09
&            268.00 310.00         42.00   4.26   0.08       25   0.04
including    299.80 301.00          1.20  18.64   0.14       52   0.01
A14-19       184.00 328.90        144.90   3.88   0.03        7   0.02
including    250.00 268.00         18.00   7.11   0.01       11   0.03



SIGNIFICANT PAST RESULTS:

A12-04A      260.00 280.00         20.00   7.12   0.02        9   0.04
including    266.00 278.00         12.00  10.51   0.03       14   0.05
A12-08       162.00 232.00         70.00   4.77   0.16        5   0.03
including    170.00 174.00          4.00  11.66   0.03        9   0.05
&            195.50 232.00         36.50   6.51   0.02        5   0.06
including    195.50 214.50         19.00   9.02   0.02        6   0.08
&            266.00 322.80         56.80   3.60   0.02        5   0.02
A12-09       216.00 245.50         29.50   3.21   0.12        6   0.06
A13-01       228.00 235.20          7.20   8.54   0.09        6   0.07
A13-02       236.00 328.00         92.00   2.90   0.10        5   0.02
A13-03       165.30 174.00          8.70   4.31   0.57       11   0.07
A13-04       190.00 198.00          8.00   8.37   0.02        6   0.04
&            266.00 332.00         66.00   2.28   0.11        4   0.02
A13-05       130.30 343.20        212.90   5.34   0.17       15   0.03
including    130.30 179.50         49.20  10.07   0.55       32   0.16
including    150.00 166.00         16.00  18.14   0.05       39   0.25
&            316.00 326.00         10.00  12.93   0.02       42   0.04
A13-06       170.00 196.00         26.00   2.20   0.05        5   0.01
&            210.00 322.00        112.00   3.71   0.04        6   0.01
including    262.00 322.00         60.00   4.67   0.07        7   0.01
including    264.65 278.00         13.35   8.42   0.20       14   0.02
&            312.00 322.00         10.00   7.85   0.07        7   0.01
A13-07        75.80  76.90          1.10  30.00   0.06       54   0.10
A13-12A         250    268         18.00   3.84   0.03        5   0.05
&            280.00 292.00         12.00   4.22   0.24       16   0.05
A13-15       329.20 344.00         14.80   4.80   0.01        5   0.09
A13-16       370.00 394.00         24.00   2.80   0.01        2   0.01
A13-17       372.10 394.00         21.90   3.10   0.19       17   0.05
A14-18       331.20 360.00         28.80   5.62   0.17       10   0.02
including    342.50 350.00          7.50   8.75   0.30       20   0.04
&            375.10 412.00         36.90   5.62   0.41        9   0.04
DD53         226.00 280.00         54.00   3.50   0.12        8   0.03
&            292.00 315.10         23.10   2.54   0.03        2   0.01
DD52B        272.00 288.00         16.00   6.80   0.13        9   0.00
DD70         100.00 104.00          4.00  10.45   0.04       59   0.13
&            156.00 170.00         14.00   4.18   0.07       12   0.02
DD71         196.00 200.00          4.00  30.90   0.32       63   0.13

//et

Table 2.  Drill hole collar coordinates and hole details (new
drill holes shown in bold)

//st
Drill hole Easting Northing Elevation  Depth Azimuth   Dip     Comment Date
A14-19      332951  8845940      4263 407.90     360   -75 New results 2014
A14-20      332896  8845986      4270 362.70     360   -70 New results 2014
A14-21      334112  8846100      4000 515.00     350   -60 New results 2014
A14-22      333000  8845928      4261 355.10      10   -70 New results 2014
A14-23      333078  8845921      4242 323.10     360   -75     Pending 2014
A14-24      334100  8846385      4055 455.90     360   -70     Pending 2014
A14-25      332903  8846062      4263 350.40     360   -70     Pending 2014

PAST AYAWILCA DRILL HOLES:

A12-01      333188  8846050      4210 327.10     360   -60    Released 2012
A12-02      333188  8846049      4210 303.00     360   -90    Released 
2012A12-03      333194  8846208      4227 349.45     180   -70    Released 2012
A12-04A     332967  8846187      4241 285.60     360   -90    Released 2012
A12-05      332967  8846188      4241 327.70     360   -60    Released 2012
A12-06      333591  8846155      4153 359.45     360   -60    Released 2012
A12-07      333591  8846154      4153 367.10     360   -90    Released 2012
A12-08      333389  8846042      4191 344.20     180   -70    Released 2012
A12-09      333389  8846042      4191 360.80     360   -90    Released 2012
A12-10      333391  8846197      4181 366.55     180   -70    Released 2012
A13-01      333590  8846039      4145 359.95     180   -70    Released 2013
A13-02      333389  8846040      4191 370.90     180   -60    Released 2013
A13-03      333590  8846041      4145 338.25     180   -90    Released 2013
A13-04      333591  8846038      4145 380.10     180   -60    Released 2013
A13-05      332954  8846075      4252 361.50     360   -90    Released 2013
A13-06      332953  8846074      4251 400.10     180   -70    Released 2013
A13-07      332952  8846074      4251 314.10     270   -60    Released 2013
A13-08      332954  8846075      4252 350.60      90   -70    Released 2013
A13-09      333188  8846050      4210 347.80     180   -60    Released 2013
A13-10      333500  8845870      4168 326.10     360 -69.9    Released 2013
A13-11      333500  8845870      4168 344.20     180 -69.8    Released 2013
A13-12      333691  8846004      4133 122.00     180   -60    Released 2013
A13-12A     333691  8846004      4133 356.80     180 -69.9    Released 2013
A13-13      333797  8845950      4120 386.80     180 -65.5    Released 2013
A13-14      333500  8846134      4167 398.70     360 -60.9    Released 2013
A13-15      333300  8846065      4200 355.40     180 -64.9    Released 2013
A13-16      333898  8846295      4112 454.70     360 -59.6    Released 2013
A13-17      333898  8846294      4112 422.30     360 -75.6    Released 2013
A14-18      333900  8846429      4122 448.30     360   -60    Released 2014
DD52        332950  8846081      4254 196.60     310   -50    Released 2011
DD52B       332953  8846076      4252 318.80     360   -70    Released 2011
DD53        332967  8846186      4241 315.10     165   -60    Released 2011
DD66        332909  8846064      4252 230.60     165   -50    Released 2011
DD67        332817  8846037      4272 230.80     165   -50    Released 2011
DD68        332873  8846192      4260 176.40     165   -50    Released 2011
DD69        332775  8846170      4277 198.20     165   -50    Released 2011
DD70        332826  8846305      4264 243.30     165   -50    Released 2011
DD71        332733  8846277      4291 231.10     165   -50    Released 2011

//et

Note: the mineralized rock is interpreted from drill core
measurements to be generally gently-dipping.  The true widths of the
intercepts are believed to be at least 75% of the down-hole widths.

Note on drill hole data:

Eastings and Northings are based on the PSAD56/18S UTM datum.  The
coordinates for the current drill holes are collected via a hand-held
GPS and are considered accurate to within a few metres. Drill hole
locations from the previous programs were surveyed with a theodolite or
determined by tape and compass from a known survey point. Elevations
are taken from a digital topographic model of the project based on a
number of known points and are considered accurate to within a few
metres.  Azimuth and dip measurements were taken using compass and
inclinometer at surface. All holes from A13-10 onwards were down-hole
surveyed; small variances in both azimuth and dip do occur down hole.

IMAGES:

Figure 1.  Drill map of Ayawilca over ground magnetics image
(white-red areas are magnetic bodies)

Figure 2.   West Ayawilca drill map (plan view) with current drill
holes and intersections

Figure 3. Geology and location map of Ayawilca-Colquipucro
projects, central Peru

PDF available at:
http://stream1.newswire.ca/media/2014/11/12/20141112_C6757_PDF_EN_7846.pdf


PDF available at:
http://stream1.newswire.ca/media/2014/11/12/20141112_C6757_PDF_EN_7847.pdf


PDF available at:
http://stream1.newswire.ca/media/2014/11/12/20141112_C6757_PDF_EN_7848.pdf

TSX Venture closing price for TK-V
Date: 2014/11/11
Closing Price: 0.23

TEL:  + 1-647-478-8976  Investor Information: James Powell
INTERNET:  www.tinkaresources.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1431500050TS11431502794-13541420141112