Source	Marketwire
Date	11/13/2014
Time	05:25:14 AM

Company	 RIVERSIDE RESOURCES INC.
Title	Riverside Resources and Partner Antofagasta Drill 23.4 g/t Gold, 0.62% 
Copper and 435 g/t Silver Over 1.5 Metres at the Swift Katie Project in British 
Columbia, Canada





    CDNX Symbol: RRI











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Riverside Resources Inc.

TSX VENTURE SYMBOL: RRI
PINKSHEETS SYMBOL: RVSDF
FRANKFURT SYMBOL: R99

November 13, 2014

Riverside Resources and Partner Antofagasta Drill 23.4 g/t Gold, 0.62% Copper 
and 435 g/t Silver Over 1.5 Metres at the Swift Katie Project in British 
Columbia, Canada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Nov. 13, 2014) - Riverside 
Resources Inc. ("Riverside" or the "Company") (TSX 
VENTURE:RRI)(FRANKFURT:R99)(PINKSHEETS:RVSDF) is pleased to announce the 
results of a recently completed reconnaissance drilling campaign at the Swift 
Katie Project (the "Project") located in southeastern BC. Five diamond drill 
holes, totaling 1423m, were completed at the Swift porphyry target with some 
encouraging results. These holes tested soil and resistivity anomalies over a 1 
km2 area. Spacing between drill hole collars ranges from 350m to 900m(Click 
here to view: http://rivres.com/images/PR_2014DH-locations.jpg).

The 2014 drill program encountered numerous zones of precious metal 
mineralization. Highlighted assays include 23.4 g/t gold, 0.62% copper and 435 
g/t silver over 1.5 m as well as 5.69 g/t gold, 0.13% copper and 26.6 g/t 
silver over 2 m (both intervals from SK14-002). The Company believes these 
high-grade gold-silver vein intercepts warrant further exploration and 
follow-up, as the primary exploration objective to-date has only focused on the 
large-scale copper-gold porphyry potential of the Swift target. The two zones 
associated with the high-grade precious metals include 20-40cm wide 
pyrite-pyrrhotite-chalcopyrite veins at the contact between andesite and 
diorite. The interval from 179.5 to 181m has associated polymetallic 
mineralization including 0.6% lead. This polymetallic mineralization may be an 
indication of a transition from a peripheral porphyry environment to a proximal 
porphyry environment.

Highlighted drill results are summarized in the table below:

/T/

----------------------------------------------------------------------------
From       To  Interval    Gold   Copper  Silver  Gold Eq.
Drill Hole    (metres) (metres)  (metres)   (g/t)      (%)   (g/t)  (g/t)(i)
----------------------------------------------------------------------------
SK14-002         177.5    179.5         2    5.69     0.13    26.6      6.44
----------------------------------------------------------------------------
SK14-002         179.5      181       1.5    23.4     0.62     435     31.15
----------------------------------------------------------------------------
SK14-002           183      185         2   0.344     0.04    4.84      0.54
----------------------------------------------------------------------------
SK14-002           209      211         2    1.14     0.01    0.71      1.19
----------------------------------------------------------------------------
SK14-002           288      290         2   0.595     0.02    1.69      0.67
----------------------------------------------------------------------------
SK14-002           300      302         2    1.12     0.13    5.04      1.58
----------------------------------------------------------------------------

----------------------------------------------------------------------------
SK14-004           112      114         2   0.626     0.03     0.5      0.71
----------------------------------------------------------------------------
SK14-004           132      140         8   0.451     0.03   0.758      0.56
----------------------------------------------------------------------------

----------------------------------------------------------------------------
SK14-005           211      217         6   0.457     0.04   0.730      0.58
----------------------------------------------------------------------------
SK14-005           223      225         2   0.513     0.03    0.39      0.60
----------------------------------------------------------------------------
SK14-005           247      249         2   0.562     0.02    0.51      0.62
----------------------------------------------------------------------------
Reported intervals are core lengths, true widths undetermined.
(i)Gold Equivalent calculation, Au Eq =(Au g/t + ((Cu grade x Cu price)+(Ag
grade x Ag price))/(Au price), was used with $1,144 gold, $15.42 silver and
$3.03 copper.

/T/

SK14-001 and SK14-003 did not intersect significant copper or gold values, 
however hydrothermal alteration in the form of chlorite, epidote, calcite, 
pyrite and magnetite were intercepted in both holes. In addition, indicators of 
porphyry-style mineralization have been intersected, including zones of 
potassic alteration (biotite-magnetite) in SK14-002, SK14-004 and SK14-005. The 
results support Riverside's belief that there is a hydrothermal system 
associated with porphyry Cu-Au mineralization at Swift. These results are being 
evaluated along with property-scale targets to determine the next phase of work.

Riverside's President and CEO, John-Mark Staude, stated: "The drill results are 
positive in finding gold mineralization and alkalic porphyry Cu-Au style 
alteration. With further work, we hope to further expand the known extent of 
mineralization and with over a half dozen targets to potentially test, 
Riverside looks forward to further work in the year ahead."

Qualified Person and QA/QC:

The scientific and technical data contained in this news release pertaining to 
the Swift Katie Project was reviewed by Danette Schwab, P.Geo - Project 
Manager, a non-independent qualified person to Riverside Resources, who is 
responsible for ensuring that the geologic information provided in this news 
release is accurate and who acts as a "qualified person" under National 
Instrument 43-101 Standards of Disclosure for Mineral Projects. Rock samples 
were prepared for assay at AGAT Labs in Burnaby, BC and analyzed for multiple 
elements at AGAT Labs in Mississauga, Ontario. Accuracy of results is tested 
through the systematic inclusion of standards, blanks and duplicates.

About Riverside Resources Inc.:

Riverside is a well-funded prospect generation team of focused, proactive 
precious and base metal discoverers with the breadth of knowledge to dig much 
deeper. The Company currently has approximately $3,500,000 in the treasury and 
approximately 37,000,000 shares outstanding. The Company's model of growth 
through partnerships and exploration uses the prospect generation business 
approach to own resources, while partners share in de-risking projects en route 
to discovery. Riverside has additional properties available for option with 
more information available on the Company's website at www.rivres.com.

ON BEHALF OF RIVERSIDE RESOURCES INC.

Dr. John-Mark Staude, President & CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Riverside Resources Inc.
John-Mark Staude
President & CEO
Phone: (778) 327-6671
Fax: (778) 327-6675
info@rivres.com
www.rivres.com

or

Riverside Resources Inc.
Joness Lang
VP, Corporate Development
Phone: (800) RIV-RES1
Fax: (778) 327-6675
jlang@rivres.com
www.rivres.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=507175554