Source	Marketwire
Date	11/13/2014
Time	05:01:13 AM

Company	 TERRAX MINERALS INC.
Title	TerraX Tenders Drill Contract for Yellowknife City Gold Project; Assays 
18.54 m @ 2.15 g/t Au in Historic Core; Assays Up to 126 g/t Au in Grab Samples 
from New Shear in Core Gold Area





    CDNX Symbol: TXR











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: TerraX Minerals Inc.

TSX VENTURE SYMBOL: TXR
FRANKFURT SYMBOL: TX0
PINKSHEETS SYMBOL: TRXXF

November 13, 2014

TerraX Tenders Drill Contract for Yellowknife City Gold Project; Assays 18.54 m 
@ 2.15 g/t Au in Historic Core; Assays Up to 126 g/t Au in Grab Samples from 
New Shear in Core Gold Area


YELLOWKNIFE, NORTHWEST TERRITORIES--(Marketwired - Nov. 13, 2014) - TerraX 
Minerals Inc. (TSX VENTURE:TXR)(FRANKFURT:TX0)(OTC PINK:TRXXF) has tendered a 
5,000 meter drill contract, expandable to 20,000 meters, on the Yellowknife 
City Gold Project (YCGP"). The contract will be awarded by December 8th, with 
drilling scheduled to start after the holiday season in January 2015. Drilling 
will be concentrated on the "Core Gold Area" identified by drilling, surface 
sampling and mapping conducted during 2014. The Gold Core Area encompasses the 
advanced Crestaurum and Barney Shear zones, as well as several adjacent and 
intersecting veins and shears identified between the two, including a new shear 
structure that returned assays up to 126 g/t Au in grab samples reported below.

To prepare for the 2015 drill program, TerraX has continued to evaluate and 
re-assay historical drill core from holes drilled within the Core Gold Area and 
carried out selected surface sampling and mapping prior to winter freeze-up. 
The Core Gold Area covers at least a 3km x 5km NNE trending area bounded by the 
Barney Lake Shear Corridor in the east and the Ryan Lake Pluton to the west; it 
remains open along strike (see TerraX presentation at www.terraxminerals.com). 
The drill holes and surface results reported here were sampled to better 
understand the relationships between the multiple known gold structures, and to 
help characterize the geological controls on the mineralized zones within these 
structures.

DRILL CORE RESULTS

The eight drill holes reported in this news release were drilled between 1994 
and 1996. The core from these holes is part of the 30,000 m of core recovered 
in 2013 from the Giant Mine core yard and relocated to TerraX's core facility 
in Yellowknife. Logging has been carried out on drill holes that cored through 
multiple areas of geological interest to TerraX.

Four drill holes reported below are from the Barney Lake Shear Corridor. These 
holes were logged and sampled to expand our knowledge of what is already 
considered a promising zone of gold mineralization within the Core Gold Area 
(2014 drill results include hole 95-16W1 with 22.42m @ 6.35 g/t Au inclusive of 
5.16m @ 18.40 g/t Au reported August 25th, 2014). Results of sampling of the 
historical core include:

/T/

--  Hole NB96-21 returned 18.54 m @ 2.15 g/t Au and 6.2 g/t Ag, including
3.94 m @ 5.04 g/t Au and 13.2 g/t Ag. This intersection was missing 81
cm of the highest grade core from selective samples taken for display
purposes in 1996. Hole NB96-21 was drilled on section and west of hole
NB96-04 (1.90 g/t over 27.00 m, including 8.97 g/t Au over 2.70 m - see
news release of November 14, 2013) NB96-21 and NB96-04 were the two most
northerly holes drilled on the Barney Lake Shear Structure prior to
TerraX drilling during the winter of 2014.

--  Hole NB96-13 was drilled 30 m to the south and 60 m west of NB96-21 and
intercepted 2.67 m @ 7.83 g/t Au and 8.1 g/t Ag in a zone interpreted to
be in the hanging wall of the zone intersected in NB96-21. Extensive
alteration and mineralization were encountered, with stronger gold
mineralization consistent with a close approach to the interpreted
strongest portion of the known Barney Mineralized Zone.

--  Hole NB96-09 drilled 50 m down dip of the gold zone in NB96-13 was
interpreted to be in the hanging wall of the zone intersected in NB96-21
and returned 6.38 m @ 2.74 g/t Au and 5.2 g/t Ag.

--  Hole NB96-15 was drilled west of the previously known Barney Zone and up
dip of NB96-24 (which returned 4.0 m @ 7.73 g/t Au - see news release
December 3, 2013). Results include a gold zone of 5.01 m @ 3.14 g/t Au.

/T/

Drill Hole Intervals from Barney Lake Shear Zone

/T/

----------------------------------------------------------------------------
Drill Hole  UTM East    UTM North      Azimuth       Dip  FROM (m)    TO (m)
----------------------------------------------------------------------------
NB96-09     636725      6946413             88       -64    337.02    353.43
----------------------------------------------------------------------------
incl                                                        347.05    353.43
----------------------------------------------------------------------------
NB96-13     636723      6946413             88       -50    294.37    301.93
----------------------------------------------------------------------------
incl                                                        297.74    300.41
----------------------------------------------------------------------------
NB96-15     636707      6943256                             362.37    367.38
----------------------------------------------------------------------------
NB96-21     636789      6943441             88       -50    243.41    261.95
----------------------------------------------------------------------------
incl                                                        243.41    247.35
----------------------------------------------------------------------------
NB96-04(i)  637174      6943469            268       -45       399       426
----------------------------------------------------------------------------
NB96-24(i)  637051      6943278            268       -66       603       607
----------------------------------------------------------------------------

------------------------------------------------------------------------
Drill Hole  UTM East    UTM North      Width (m)      Au g/t      Ag g/t
------------------------------------------------------------------------
NB96-09     636725      6946413            16.41        1.43         4.0
------------------------------------------------------------------------
incl                                        6.38        2.74         5.2
------------------------------------------------------------------------
NB96-13     636723      6946413             7.56        2.90         5.4
------------------------------------------------------------------------
incl                                        2.67        7.83         8.1
------------------------------------------------------------------------
NB96-15     636707      6943256             5.01        3.14
------------------------------------------------------------------------
NB96-21     636789      6943441            18.54        2.15         6.1
------------------------------------------------------------------------
incl                                        3.94        5.04        13.2
------------------------------------------------------------------------
NB96-04(i)  637174      6943469            27.00        1.90         6.9
------------------------------------------------------------------------
NB96-24(i)  637051      6943278             4.00        7.73         6.8
------------------------------------------------------------------------
(i) Previously reported - see text above

/T/

A map showing the location of these drill holes is available under "2014 Field 
Exploration" on our web site at www.terraxminerals.com

Four holes were re-logged from areas that are between the Crestaurum Zone, 20 
Shear and 19 Shear, which collectively lie to the west and south of the Barney 
Zone (see table below), and form part of the mineralizing structures within the 
Core Gold Area. These holes were drilled in 1994 and are not directly 
associated with the two best known zones of gold mineralization (Crestaurum, 
Barney), but were logged and sampled by TerraX to gain a better understanding 
of the relationship of these zones to each other, and to ascertain the controls 
on their gold mineralization. Results include 1.45 m @ 6.05 g/t Au in hole 
NB94-03; 11.36 m @ 0.92 g/t Au in hole NB94-05; 1.50 m @ 5.36 g/t Au in hole 
NB94-13; and 1.90 m @ 5.05 g/t Au from in hole NB94-15 (see table below).

/T/

Assay Intervals from Areas between the
Crestaurum Shear and Shears 20 & 19
----------------------------------------------------------------------------
Drill Hole  UTM East    UTM North            Azimuth         Dip    FROM (m)
----------------------------------------------------------------------------
NB94-03     636283      6942335                   88         -60      176.32
----------------------------------------------------------------------------
and                                                                   209.85
----------------------------------------------------------------------------
and                                                                   313.75
----------------------------------------------------------------------------
NB94-05     6366421     6942684                  268         -45       56.94
----------------------------------------------------------------------------
incl                                                                   56.94
----------------------------------------------------------------------------
NB94-13     636342      6942158                   88         -60       50.51
----------------------------------------------------------------------------
NB94-15     636624      6942277                   88         -60       35.33
----------------------------------------------------------------------------
and                                                                    47.95
----------------------------------------------------------------------------
and                                                                    67.64
----------------------------------------------------------------------------
and                                                                   139.51
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Drill Hole  UTM East    UTM North             TO (m)   Width (m)      Au g/t
----------------------------------------------------------------------------
NB94-03     636283      6942335               177.09        0.77        2.59
----------------------------------------------------------------------------
and                                           210.88        1.03        1.90
----------------------------------------------------------------------------
and                                            315.2        1.45        6.05
----------------------------------------------------------------------------
NB94-05     6366421     6942684                 68.3       11.36        0.92
----------------------------------------------------------------------------
incl                                           58.98        2.04        3.83
----------------------------------------------------------------------------
NB94-13     636342      6942158                52.01        1.50        5.36
----------------------------------------------------------------------------
NB94-15     636624      6942277                36.27        0.94        1.76
----------------------------------------------------------------------------
and                                            49.85        1.90        5.05
----------------------------------------------------------------------------
and                                             69.8        2.16        3.56
----------------------------------------------------------------------------
and                                           140.21        0.70        2.19
----------------------------------------------------------------------------

/T/

The drill core was subjected to a full geological and geotechnical analysis 
which included refitting of the core, revealing 100% recovery except for 
selected mineralized core intervals (10-20 cm) that had been removed for 
display or other test work by past workers. Core showed excellent geotechnical 
rock quality values. Core distances were converted from the original imperial 
measurements (feet) to metric (meters) and new core sampling intervals were 
designated from the metric measurements.

TerraX collected 241 samples for assay from the Barney Lake Shear Corridor area 
and 239 samples from other areas within the Core Gold Area. Results ranged from 
below detection to a high of 22.7 g/t Au. Core samples were cut with a diamond 
saw blade. Sampling over several intervals was done by quarter core sampling of 
half sawn core that remained from previous sampling in 1994, 1995 and 1996. In 
these areas a quarter core sample remains in the core boxes for further 
examination if required. True thickness of the zones of mineralization is 
unknown at present. Based on core foliation angles it is estimated to be 
between 65-95% of drill intersection width.

A map of the new shear surface samples and the drill holes reported above from 
Barney, Crestaurum, 20 Shear and 19 Shear is available under "2014 Field 
Exploration" on our web site.

SURFACE SAMPLING RESULTS

Surface sampling and mapping was carried out in early fall on the YCGP. The 
assay results reported here were from structural mapping of known mineralized 
features within the Core Gold Area, and sampling of strike extensions to these 
structures. Results included:

/T/

--  A grab sample with 126 g/t Au in veining within a new shear in the Core
Gold Area that is 300 m north of a sample grading 44.3 g/t Au (news
release of Sept 8th, 2014) taken during prospecting this summer. Both
samples are interpreted to be on the same northerly trending shear
structure, which is sub-parallel to and 150 m west of the main Barney
Shear, with today's sample approximately 500 m south of drilling
completed this summer at the Barney Shear

--  A grab sample with 6.42 g/t Au from a NNW structure within the Core Gold
Area that is sub-parallel to and 50 m east of Shear 17. This sample is
85 m from a channel sample on Shear 17 that ran 6 m @ 2.03 g/t Au, 0.09%
Cu and 0.05% Mo (news release Aug 19th, 2014).

--  Grab samples of 2.82 and 13.95 g/t Au from the NNE trending Finger Lake
Shear on the U-Breccia property which is in the southwest portion of the
YCGP, and approximately 2 km south of the current southern boundary of
the Gold Core Area, potentially expanding our area of interest.

/T/

A map showing the location of the fall surface samples is available under "2014 
Field Exploration" on our web site.
It should be noted that, due to their selective nature, assay results from grab 
samples may not be indicative of the overall grade and extent of mineralization 
on the subject area. The surface program consisted of 62 samples with grades 
ranging from below detection limit to 126 g/t Au. Certified standards and 
blanks were inserted into the stream of samples for chemical analysis. Samples 
were prepared at ALS Chemex's laboratory in Yellowknife and shipped to their 
Vancouver facility for gold analysis by fire assay and other elements by ICP 
analysis. ALS is a certified and accredited laboratory service.

The technical information contained in this news release has been approved by 
Joseph Campbell, the President of TerraX, who is a Qualified Person as defined 
in "National Instrument 43-101, Standards of Disclosure for Mineral Projects."

About the Yellowknife City Gold Project

The Yellowknife City Gold Project encompasses 93.5 sq km of contiguous land 
immediately north of the City of Yellowknife in the Northwest Territories and 
includes TerraX's wholly-owned Northbelt property acquired in February 2013.

The project lies on the prolific Yellowknife greenstone belt and covers 15 km 
of strike length on the northern extension of the shear system that hosts the 
high-grade Con and Giant gold mines. The project area contains multiple shears 
that are the recognized hosts for gold deposits in the Yellowknife gold 
district, with innumerable gold showings and historic high grade drill results. 
Since January 2013, TerraX has consolidated the project area by acquiring and 
optioning numerous properties, including: Northbelt, Goodwin, Ryan Lake, Walsh 
Lake, and U-Breccia, as well as staking additional contiguous lands. Being 
all-season road accessible and within 15 km of the City of Yellowknife, the 
YCPG is close to vital infrastructure, including transportation, service 
providers, hydro-electric power and skilled trades people.

On behalf of the Board of Directors

Joseph Campbell, President

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This news release contains forward-looking information, which involves known 
and unknown risks, uncertainties and other factors that may cause actual events 
to differ materially from current expectation. Important factors - including 
the availability of funds, the results of financing efforts, the completion of 
due diligence and the results of exploration activities - that could cause 
actual results to differ materially from the Company's expectations are 
disclosed in the Company's documents filed from time to time on SEDAR (see 
www.sedar.com). Readers are cautioned not to place undue reliance on these 
forward-looking statements, which speak only as of the date of this press 
release. The company disclaims any intention or obligation, except to the 
extent required by law, to update or revise any forward-looking statements, 
whether as a result of new information, future events or otherwise.

- 30 -

CONTACT INFO:

Paradox Public Relations
514-341-0408
Toll Free: 1-866-460-0408
info@paradox-pr.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=507185693