Source	MARKET NEWS
Date	11/20/2014
Time	12:53:25 PM

Company	 Westminster Resources Ltd.
Title	Sierra Exploration Project Update





    CDNX Symbol: WMR











Press Release	





Sierra Exploration Project Update --->@NEWS RELEASE
WESTMINSTER RESOURCES LTD ("WMR-V")
- Sierra Exploration Project Update

During the summer, 2014, WMR ("the Company") conducted a follow-up
program of exploration at the 100% owned Sierra Breccia target
discovered in 2013 (See WMR Press Release 13-05 of October 18, 2013 for
details, including analytical methods).  The breccia zone has been
traced for a length of approximately 200 meters in a series of four
equally  spaced historic (1950's?) mined-out pits and trenches.  The
steeply-dipping breccia zone has a vertical extent of 70 meters over
the known strike length, and is hosted in a rhyolite sequence of
Tertiary volcanic rocks. The Sierra target lies 700 meters above the
Company's porphyry intrusion El Cobre exploration target.

The Sierra hydrothermal breccia contains high grades of copper,
silver and gold where seventeen grab samples averaged 4.8% Cu, 101 g/t
Ag and 4.4 g/t Au (see Press Release WMR 13-05, October 18, 2013) as
well as high sulphidation system geochemical signatures anomalous in
the elements iron, barium, bismuth and mercury.

Sierra Trench One is located at the lowest elevation of the four
hand mined workings where due to the contour of the land the exposed
high grade breccia material was peeled from the upslope footwall cliff
face contact at all four trenches.  The exposed footwall zone shows
hematitic fractures and minor quartz stockwork development in
argillic-hematitic altered rhyolite crystal-ash tuff adjacent to the
mined out one to two meters wide breccia zone.  The poorly exposed
downslope hanging wall shows argillic and sericitic alteration of the
crystal-ash tuff adjacent to the breccia zone. In Trench One the only
exposure of remaining in situ breccia material assayed 147.9 g/t
silver, 2.38 g/t gold and 1.4% copper and 15.5% iron across 0.4 meters.
The only observed continuous exposure of footwall mineralization
adjacent to the breccia was chip sampled in Trench One for an into the
footwall ( width) upslope distance of 7.9 meters from the high grade
breccia contact.  This continuous zone sampling averaged 61.8 g/t
silver, 0.895 g/t gold and 0.17% copper over the 7.9 meters.  Also in
Trench One the only in situ exposure of the hanging wall available to
chip sample was a 1.2 meter width of sericitic-argillic altered
rhyolite assaying 29.5 g/t silver, 0.09 g/t gold and 0.8% copper. At
the other 3 higher elevation trenches, cliff face footwall chip
sampling of altered hematitic fractured rhyolite returned copper, gold
and silver contents comparable to those sampled in intervals at Trench
One over its 7.9 meter width.  However at Trenches 2, 3 and 4 ,width
extent sampling of footwall mineralization is limited due to the near
vertical cliff face footwall contour.

The highest grade grab sample of Sierra hydrothermal breccia was
collected from the Trench Two area.  Its contents of 6.0% copper, 87.2
g/t silver and 2.74 g/t gold compares well with results from the
seventeen breccia grab samples as reported in 2013.

The results from the recent outcrop sampling along the mapped
exposure of the Sierra breccia target confirm the high grades found in
previously collected  breccia grab samples.  In addition, the new 2014
sampling of in situ hanging wall and footwall altered volcanics
adjacent to the mapped breccia zone demonstrated that Sierra system
mineralization contains copper, silver and gold and  extends for at
least 9.5 meters in width at Trench One.

A campaign of exploration along strike and to depth is warranted
as the Sierra target hydrothermal breccias with diatreme
characteristics and high-sulphidation system affinities make the
potential at the Sierra system attractive.

This news release has been reviewed and approved by Glen
Macdonald, P.Geo (a qualified person for the purpose of National
Instrument 43-101, Standards of Disclosure for Mineral Projects).

ON BEHALF OF THE BOARD OF DIRECTORS
WESTMINSTER RESOURCES LTD.

"Glen Macdonald"

Director



About Westminster:

Managed by an experienced exploration team, Westminster is focused
on exploring and developing prospects on a land package of
approximately 53,613 hectares of contiguous mineral concessions in
Sonora, Mexico.  These concessions constitute a mineral district scale
property serviced by roads, power and water.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release may contain forward-looking information which is
not comprised of historical facts. Forward-looking information involves
risks, uncertainties and other factors that could cause actual events,
results, performance, prospects and opportunities to differ materially
from those expressed or implied by such forward-looking information.
Forward looking information in this news release may include, but is
not limited to, the Company's objectives, goals or future plans.
Factors that could cause actual results to differ materially from such
forward-looking information include, but are not limited to, those
risks set out in the Company's public documents filed on SEDAR.
Although the Company believes that the assumptions and factors used in
preparing the forward-looking information in this news release  are
reasonable, undue reliance should not be placed on such information,
which only applies as of the date of this news release, and no
assurance can be given that such events will occur in the disclosed
time frames or at all. The Company disclaims any intention or
obligation to update or revise any forward-looking information, whether
as a result of new information, future events or otherwise, other than
as required by law.

TSX Venture closing price for WMR-V
Date: 2014/11/19
Closing Price: 0.07

TEL:  604-608-0400 Bill Conlin
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1432300042TS11432302254-12521320141120