Source	MARKET NEWS
Date	11/20/2014
Time	08:20:51 AM

Company	 Endurance Gold Corporation
Title	Endurance 
Provides Update from the Pardo Joint V





    CDNX Symbol: EDG











Press Release	





ENDURANCE GOLD CORPORATION ("EDG-V")
GINGURO EXPLORATION INC. ("GEG-V")
- Endurance Provides Update from the Pardo Joint Venture, Ontario

Endurance Gold Corporation announces further results from the
Pardo Joint Venture Property ("Pardo JV Property"). The Pardo JV
Property is comprised of 16 claims located approximately 65 kilometres
("km") northeast of Sudbury, Ontario. Ginguro Exploration Inc.
("Ginguro") is the operator of the Pardo JV Property and holds a 64.5%
ownership interest and Endurance owns a 35.5% ownership interest. Both
parties are funding the 2014 program on a pro rata basis, based on
ownership.

@ The operator has reported that the 2014 Pardo JV field program
is now concluded. Highlights in this release include 53.6 grams per
tonne (g/t) gold over 0.7 metres in a Line 34 channel sample and 1.5
g/t gold over 0.2 metres in a drill hole with visible gold.
@ Channel sample results from Line 34, sampled within the
Matinenda paleoplacer confirm anomalous gold and the potential for
high-grade gold bearing layers. A series of five (5) trenches oriented
north to south were excavated to expose the Matinenda. A total of 17
channels were systematically taken to evaluate the mineralized
conglomerates. Channel highlights include: channel 77 with 53.6 g/t
over 0.7 metres, channel 70 with 1.2 g/t over 4 metres, channel 66 with
1.1 g/t over 6 metres. Detailed maps of the trenches indicating channel
locations can also be found on the Company's website at
www.endurancegold.com.

@ The operator reports the high-grade assay of 53.6 g/t over 0.7
metres suggests that the Matinenda paleoplacer is prospective for
hosting high grade strata. A table of the results is listed below.

//st

----------------------------------------------
|Table 1: Summary of Line 34 channel sampling|
|--------------------------------------------|
|Channel       |Length(m)     |Gold(g/t)     |
|--------------------------------------------|
|PD-14-66      |6             |1.1           |
|--------------------------------------------|
|PD-14-67      |0.9           |0.0           |
|--------------------------------------------|
|PD-14-68      |0.8           |0.5           |
|--------------------------------------------|
|PD-14-69      |2.5           |1.1           |
|--------------------------------------------|
|PD-14-70      |4             |1.2           |
|--------------------------------------------|
|PD-14-71      |1.5           |0.2           |
|--------------------------------------------|
|PD-14-72      |1             |0.2           |
|--------------------------------------------|
|PD-14-73      |3             |0.2           |
|--------------------------------------------|
|PD-14-74      |1             |0.7           |
|--------------------------------------------|
|PD-14-75      |1.5           |0.1           |
|--------------------------------------------|
|PD-14-76      |1.5           |0.2           |
|--------------------------------------------|
|PD-14-77      |0.7           |53.6          |
|--------------------------------------------|
|PD-14-78      |1.5           |0.6           |
|--------------------------------------------|
|PD-14-79      |3             |0.4           |
|--------------------------------------------|
|PD-14-80      |0.8           |0.3           |
|--------------------------------------------|
|PD-14-81      |0.9           |0.2           |
|--------------------------------------------|
|PD-14-82      |5             |0.1           |
----------------------------------------------

//et

Due to the near flat lying nature of the sedimentary strata, it is
not always possible to cut samples across the gold-bearing strata.
Samples are usually collected either parallel or perpendicular to the
interpreted paleochannel direction. Therefore, the channel lengths
reported in this release represent the gold distribution over the
surface area sampled and do not represent true thicknesses of the
mineralized unit.

@ Two diamond drill holes from the 2014 program tested the
eastern extension of the Godzilla Zone. Drill holes PD-14-20 and 21
located about 200 metres east of Godzilla tested the gold bearing
Mississagi conglomerates discovered at the Godzilla Zone and
intersected a 1.2 to 3 metre flat lying conglomerate package at depth
from 4 to 36 metres. Visible gold was detected in PD-14-21 at a depth
of 34.93 metres. The other core half was sent for assay and returned a
value of 1.5 g/t gold over 0.2 metres @ .

//st

----------------------------------------------------
|Table 2: Highlights of drill hole assays          |
|--------------------------------------------------|
|Drill Hole|From(m) |To(m)   |Interval(m)|Gold(g/t)|
|--------------------------------------------------|
|PD-14-20  |4.3     |4.6     |0.3        |3.2      |
|--------------------------------------------------|
|PD-14-20  |9.9     |11.7    |1.8        |0.5      |
|--------------------------------------------------|
|PD-14-20  |32.5    |35.5    |3          |0.9      |
|--------------------------------------------------|
|PD-14-21  |20.5    |20.8    |0.3        |2.3      |
|--------------------------------------------------|
|PD-14-21  |34.8    |36.0    |1.2        |1.0      |
|--------------------------------------------------|
|Note:                                             |
|Intervals                                         |
|reported                                          |
|approximate                                       |
|true                                              |
|widths                                            |
|of                                                |
|mineralization.                                   |
|                                                 |
----------------------------------------------------

//et

In the preparation of this news release, Endurance has relied on
data collected and compiled by the operator of exploration programs,
and summarized to the Company for this release. Robert T. Boyd, P.Geo.
is a qualified person as defined in National Instrument 43-101 and
supervised the compilation of the technical information provided by the
operator and forming the basis for this release. There has been
insufficient exploration to define a mineral resource on the Pardo JV
Property to date, and it is uncertain if further exploration will
result in the target being delineated as a mineral resource. The
operator reports that Pardo JV samples are transported in security
sealed bags for preparation at AGAT Prep Lab located in Sudbury,
Ontario. Prepped samples are shipped for analysis to the AGAT Assay
Laboratory in Mississauga, Ontario. AGAT Laboratories Ltd. is an ISO
17025 registered laboratory. The new samples reported in this release
were crushed in their entirety, with a 1 kg split then pulverized. Two
50 g aliquots of the pulp were cut out and fire assayed. Results were
reported as a weighted average of gold in the fractions. In instances
where the averages exceed 10 g/t, the sample is re-run with a
gravimetric finish and the gravimetric result is reported. The operator
inserts a certified reference standard or an analytical blank in every
batch of 20 samples. The operator reports that validation parameters
are established in the database to ensure quality control.

About Endurance

Endurance Gold Corporation is a company focused on the
acquisition, exploration and development of highly prospective North
American mineral properties with the potential to develop world-class
deposits. The Company's exploration focus, for projects operated by
Endurance, is intrusive-related mineral systems with potential for
discovery of major new precious or rare metals deposits, and its
business plan offers shareholders exposure to several majority-owned
exploration projects with significant discovery potential such as the
Elephant Gold Property in Alaska, the Rattlesnake Hills Gold Property
in Wyoming, and the Bandito Rare Earth-Niobium Property in the Yukon.
Please visit www.endurancegold.com.

ENDURANCE GOLD CORPORATION

Robert T. Boyd

Per:

President & CEO

FOR FURTHER INFORMATION, PLEASE CONTACT

Endurance Gold Corporation

(604) 682-2707, info@endurancegold.com

www.endurancegold.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release. This news release may contain forward looking statements
based on assumptions and judgments of management regarding future
events or results that may prove to be inaccurate as a result of
factors beyond its control, and actual results may differ materially
from the expected results.



__________________________________________________
_______________________________________________
TSX Venture closing price for EDG-V
Date: 2014/11/10
Closing Price: 0.05
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1432300027TS11432301390-08200920141120