Source	CANADA NEWSWIRE
Date	11/06/2015
Time	12:03:01 PM

Company	 Golden Band Resources Inc.
Title	Golden Band Files NI43-101 Technical Report





    CDNX Symbol: GBN











Press Release	




" BC-GoldenBand-TechReport   11-06 1310
News release via Canada NewsWire, Calgary 403-269-7605 -ME-

Attention Business Editors:
^Golden Band Files NI43-101 Technical Report@


TSX.V: GBN
SASKATOON, Nov. 6, 2015 /CNW/ - Golden Band Resources Inc. (Golden Band
or Company) (TSXV: GBN) announces that further to the news releases dated May
1, 2015 and July 7, 2015, it has filed a technical report dated November 3,
2015 entitled "NI 43-101 Technical Report and Mineral Resource Estimate
Update, Bingo Gold Deposit, Roy Lloyd Mine Project Area" (the "Technical
Report") prepared by Frank Hrdy, P. Geo., Eugene Puiritch, P. Eng, and Mike
Yakimchuk, P. Eng, all independent Qualified Persons under National Instrument
43-101 ("NI43-101").
The updated Indicated Resource estimate for the Bingo Gold deposit (Roy
Lloyd Mine) is 268,184 tonnes grading 9.60 g/t gold and the Inferred Resource
is 194,634 tonnes grading 11.47 g/t gold (see Table 1). This update to the
mineral resource estimate for the Bingo deposit (Roy Lloyd mine site) takes
into account mined areas and 100 new exploration drill holes since the May 26,
2009 resource update.
Resource EstimateTable 1: Resource Estimate for the Bingo Gold Deposit
(Roy Lloyd Mine). A 5 g/t gold cutoff grade was used for this estimation.
5g/t Au Cut tonnes (t)         Grade g/t Au       Au Ounces
----------- ---------          ------------       ---------

Indicated              268,184               9.60           82,817
---------              -------               ----           ------

Inferred               194,634              11.47           71.773
--------               -------              -----           ------
Note: Mineral resources that are not mineral reserves do not have
demonstrated economic viability.
Please note that this mineral resource update (dated October 26, 2015)
supersedes the technical report entitled "Technical Report and Mineral
Resource Update - Bingo Gold Deposit, Roy Lloyd Mine, Dickens West Project"
dated May 2, 2013. The amended report dated October 26, 2015 also includes the
results from the most recent underground drill program (Press Release dated
April 24, 2014).
QA/QC
Mr. Hrdy carried out validation prior to resource modeling including
visual inspection of the data files, statistical analysis and 3D computer
visualizations of data. During the course of this investigation many errors in
the post 2008 channel sample database were found so this database was not
used. Some drillhole id's occurred more than once in drillholes added since
late 2009 and this was corrected. The Author also read through all of the
Company's press releases located on their website to verify the number of
drillholes, meters drilled, etc. matched what was in the database and to
review the QA/QC discussions in these releases. Drill logs from 2006 to late
2009 (WD-113 to WD-188B) were also reviewed as the earlier drilling was
verified by the 2006 Technical Report and Resource Estimate by GeoSim Services
Inc. Drill logs for holes drilled in 2012 were not available as this was the
time period when a deviation from the QA/QC occurred; however, the database
supplied by the Company did include these drillholes. To ensure appropriate
quality assurance exists for samples collected from this time period the
Author only used assays derived from drillcore and selected the critical
samples (that fall in this time period) used for the estimation for check
analysis at an external lab. Table 2 lists the sample rejects that were sent
to TSL Laboratories in Saskatoon as a check quality assurance measure. In
addition, no channel samples taken from underground were used.
Table 2- Check Samples sent to TSL Laboratories in Saskatoon.
Original                                                               Check 
Assay (g/t      Check Assay Repeat
Sample                                                                 
gold)                 (g/t gold)
Number   Drillhole Collar Assay (g/t gold)     Check Sample Number
--------- ---------------- ----------------     -------------------     
----------------      ------------------

637028    RLUG-02                         19.23                  
637028                  27.5                  23.73
------    -------                         -----                  
------                  ----                  -----

533444    WD-204                           0.23                  
533444                  0.27
------    ------                           ----                  
------                  ----

637258    RLUB-04                          20.8                  
637258                 11.76                  11.87
------    -------                          ----                  
------                 -----                  -----

636895    RLUG-01                         10.63                  
636895                 11.66                   10.7
------    -------                         -----                  
------                 -----                   ----

680734    RLUG-10                          3.47                  680734  <.03
------    -------                          ----                  ------  ----

681054    RLUG-12          <0.03                                681054  <.03
------    -------          -----                                ------  ----

681057    RLUG-15          <0.03                                
681057                  0.03
------    -------          -----                                
------                  ----
Estimation Method
As of 2014 the total exploration drill holes completed on the property
since 1991 is 290 drill holes (47,260.8 m). There are a total of 211
drillholes that intersect the grade shell that represents the main resource
and 773 composite samples (each 1.0 m in length) that are hosted within the
grade shell and were used for the resource estimation.
The entire resource estimation disclosed in Table 4 of the technical
report was constrained by two three-dimensional grade shells that have a
minimum horizontal width of 2 meters and were used independently to better
constrain the higher grade ore chutes. Block size is 2 x 2 x 2 meters (with
sub-blocks to 1 x 1 x 1 meter) and grade estimation was carried out by the
inverse distance cubed method (ID3) using 1.0 meter down-hole composite
samples. A cap (upper cut) of 31 g/t gold and a lower cut grade of 5 g/t gold
were used for all resource classes. Blocks were estimated using a search
ellipse at an orientation of 340 degrees, -65 degrees plunge, and -10 degree
dip and with a search ellipse major/semi-major ratio 3, major-minor ratio 3.
Maximum search distance of 50 meters for Indicated and 100 meters for Inferred
class categories. Tonnages were calculated using an average specific gravity
of 2.75 g/cm3, based on 773 composite samples (each 1.0 meters in length). In
order to be included in the estimate, a block was required to have a minimum
of 2 and a maximum of 15 composite samples within the given search radius.
Surpac version 6.4.1 was the software used to create the geological model and
to estimate the resource.
Please refer to the Technical report, which is available under the
Company's profile at www.sedar.com for further details including Estimation
Method and QA/QC and Data Verification overview.
Frank Hrdy, P., Geo, a Geologist of CanMine Consultants and an
independent consultant to the Company, is the Qualified Person as defined in
NI 43-101 for this disclosure and has reviewed and approved the scientific and
technical information contained in this release.
The technical reports for the Company's other Material Properties (the
Jolu Area and Greywacke properties) are in progress and the Company is working
with its consultants and Qualified Persons (as that term is defined under NI
43-101) to file the revised technical reports as soon as possible.
About Golden Band
Golden Band Resources Inc. is a gold producer operating in the La Ronge
gold belt in northern Saskatchewan and is listed on the TSX Venture Exchange
in Canada under the symbol GBN. Commercial production was declared on April 1,
2011. The Company has recently suspended mining operations (see news release
of June 30, 2014) but has been actively exploring the La Ronge Gold Belt since
1994 and has assembled a land package of 870 km2, including 13 known gold
deposits and five former producing mines, being Jolu, Decade, Star Lake, EP
and Komis.
On behalf of the Board of Directors of Golden Band Resources Inc.,
"Paul Saxton"Paul Saxton, CEO
Caution Regarding Forward-Looking Information and StatementsThis news
release includes certain forward-looking statements or information. All
statements other than statements of historical fact included in this release,
including, without limitation, statements regarding the updated technical
reports, operational plans, estimates and costs of production, and other
future plans, objectives or expectations of Golden Band Resources Inc.
(Company) are forward-looking statements that involve various risks and
uncertainties. There can be no assurance that such statements will prove to be
accurate and actual results and future events could differ materially from
those anticipated in such statements. Important factors that could cause
actual results to differ materially from the Company's plans or expectations
include risks relating to the actual results of operations, current
exploration activities, fluctuating gold prices, possibility of equipment
breakdowns and delays, cost overruns, general economic, market or business
conditions, regulatory changes, timeliness of government or regulatory
approvals and other risks detailed herein and from time to time in the filings
made by the Company. The Company makes all reasonable efforts to update its
corporate information on a timely basis.
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Golden Band Resources Inc.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/November2015/06/c4305.html

-0-                           11/06/2015
/For further information: Investor Relations: 604-682-6852, Email:
info(at)goldenbandresources.com, www.goldenbandresources.com/
(GBN. GBRIF)

CO:  Golden Band Resources Inc.
ST:  Saskatchewan
IN:  MNG OTC
SU:

-30-