Source	MARKET NEWS
Date	11/05/2015
Time	04:29:54 AM

Company	 Kiska Metals Corporation
Title	Drilling 
Extends Porphyry Mineralization at Kisk





    CDNX Symbol: KSK











Press Release	





KISKA METALS CORP ("KSK-V")
TECK RESOURCES LTD ("TCK.A-T")
- Drilling Extends Porphyry Mineralization at Kiska's Kliyul
- Project

Kiska Metals Corporation ("Kiska" or the "Company") is pleased to
report that drilling by its partner, Teck Resources Limited ("Teck"),
at its Kliyul porphyry copper-gold project in north-central B.C., has
returned significant widths of porphyry mineralization, and has
extended mineralization along trend, to depth, and in new geophysical
domains that greatly expand the potential of the Kliyul Zone.

Teck completed four diamond drillholes for a total of 1,908
metres. "We are very encouraged by these first four drillholes by Teck
at the Kliyul Zone," stated Dr. Mike Roberts, V.P. Exploration for
Kiska, "because they show copper and gold mineralization over long
intervals with higher-grade sub-zones, and most significantly, that the
Kliyul Zone is a robust porphyry system that remains open in multiple
directions."

Highlights

- 245.0 metres of 0.18% Cu and 0.53 g/t Au (from 123.0 metres),
including 20.4 metres of 0.39 % Cu and 2.55 g/t Au from hole KLI-15-034

- 162.4 metres of 0.20% Cu and 0.26 g/t Au (from 32.5 metres),
including 66.5 metres of 0.30% Cu and 0.40 g/t Au from hole KLI-15-033
- Significant grade intercepts in a covered and previously
untested area of the Kliyul Zone

The goal of the drilling program was three-fold: 1) holes KLI
15-032 and KLI-15-034 were drilled to target the down-dip extension of
mineralized magnetite breccias intersected in shallow, historical
holes, 2) hole KLI-15-033 was drilled as a 200 metre step-out
south-east of the only previous deep drilling, and 3) KLI-15-035 was
drilled to target a coincident magnetic low and an Induced Polarization
chargeability high anomaly that occurs north of a major east-west fault
(the "Valley Fault"), which is in an overburden covered area that is
essentially untested by previously drilling
(http://www.kiskametals.com/i/pdf/Kliyul_Web_Maps_04Nov2015.pdf).




True widths of mineralization are unknown at this time due to a
lack of geometrical constraints; Interval includes several 1 to 5 metre
wide barren dykes;  Core recovery throughout this interval was on
average 52% due to the friable nature of the rocks near surface. At
this time it is unclear what effect this recovery has on the reported
copper and gold grades, and this will be investigated in future work;
Interval truncated at 465.7 metres by two approximately 5 metre wide,
late barren dykes, yet gold-copper mineralization persists to bottom of
hole at 489 metres.

All holes intersected long intervals of copper-gold mineralization
associated with disseminated and vein hosted chalcopyrite, and these
are mainly hosted by andesitic volcanic rocks with magnetite +/-
biotite alteration. Later stages of alteration, including sodic-calcic
and phyllic alteration, overprint and occur outboard of these zones.
Higher grade sub-zones, particularly in hole KLI-15-034, are hosted by
magnetite breccias, where chalcopyrite and local bornite occur as
cement and within quartz veins. In contrast, a higher grade interval
was intercepted in hole KLI-15-035 starting at 399.5 metres and is
associated with bornite-chalcopyrite mineralization as disseminations
and within quartz veins proximal to a syn-mineral feldspar porphyry
dyke. Mineralization in this zone is open both up- and down-dip. The
style and location of this mineralization has three important
implications: 1) the overburden-covered area north of the Valley Fault
is very prospective and is largely untested; 2) not all copper-gold
mineralization at Kliyul is associated with magnetite breccias and
magnetic high anomalies, indicating the potential footprint of the
Kliyul Zone is greatly expanded; 3) the proximity to syn-mineral
intrusive rocks may drive higher grade copper-gold mineralization, and
yet the centre of this intrusive body has yet to be discovered.

Teck can earn a 51% interest in the Property from Kiska by
incurring a cumulative aggregate of $5.5 million in exploration
expenditures on the Property on or before January 31, 2018 (the "First
Option"). Teck may elect to acquire an additional 14% interest in the
Property, for a total interest of 65%, by incurring an additional $6.5
million in exploration expenditures (for a total of $12.0 million) on
the Property on or before the third anniversary of the exercise of
Teck's First Option.

The technical content of this document was reviewed and approved
by Michael Roberts, Ph.D., P.Geo., Vice President of Exploration for
Kiska Metals Corporation, a Qualified Person as defined by National
Instrument 43-101. The drilling program, core logging, core sampling
and QA/QC were conducted and supervised by Teck personnel. Core samples
were on average approximately 2 metres long and were split by a diamond
saw. Half-core samples were assayed by Bureau Veritas in Vancouver,
B.C. for gold by Fire Assay of a 30 gram charge with AAS finish;
samples with gold greater than 10 ppm were analyzed by Fire Assay and
gravimetric method. Cu and other elements were determined by 4-acid
digestion with ICP-ES finish. QA/QC included the insertion and
monitoring of standards and blanks into the sample stream, and the
analysis of duplicate samples at random intervals. On average at least
one QA/QC sample or duplicate was analyzed for every four regular
samples.

About Kiska Metals Corporation

Kiska Metals Corporation is a prospect generator company with a
high quality portfolio of gold and copper projects throughout North
America. Two of Kiska's projects are held under option agreements with
major mining companies. Kiska has several other gold and copper
projects available for option-joint venture as well as an extensive
royalty portfolio.

On behalf of Kiska Metals Corporation

"Grant Ewing"
Grant Ewing, President & CEO

Contact:

575-510 Burrard St. Vancouver, BC, Canada V6C 3A8
Tel: 604.669.6660 Fax: 604.669.0898
http://www.kiskametals.com
Contact: Brian Miller or Grant Ewing

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

CAUTIONARY STATEMENT: No stock exchange, securities commission or
other regulatory authority has approved or disapproved the information
contained herein. This News Release includes certain "forward-looking
statements". Other than statements of historical fact, all statements
included in this release, including, without limitation, statements
regarding future plans and objectives of Kiska Metals Corporation, are
forward-looking statements that involve various risks and
uncertainties. There can be no assurance that such statements will
prove to be accurate, and actual results and future events could differ
materially from those anticipated in such statements. Important factors
that could cause actual results to differ materially from Kiska's
expectations are the risks detailed herein and from time to time in the
filings made by Kiska Metals Corporation with securities regulators.
Those filings can be found on the Internet at http://www.sedar.com.

SOURCE: Kiska Metals Corporation
______________________________________
_______________________________________________
TSX Venture closing price for KSK-V
Date: 2015/11/04
Closing Price: 0.02
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1530800003TS11530800438-04282720151105