Source	MARKET NEWS
Date	11/05/2015
Time	08:36:43 AM

Company	 Visible Gold Mines Inc.
Title	Summer 
Exploration and Corporate Update





    CDNX Symbol: VGD











Press Release	





VISIBLE GOLD MINES INC ("VGD-V;VGMIF-0")
- Summer Exploration and Corporate Update

Visible Gold Mines Inc. is pleased to provide an update of its
summer exploration activities as well as a corporate update.

Summer Exploration Update

Induced Polarization Ground Survey

Visible Gold Mines completed a 50-kilometre phase-domain induced
polarization ground survey along the new 167 Provincial Road. The
purpose of this survey was to map the lithologies, geological units and
structural features underlying Visible Gold Mines' 100%-owned 167
Property, to investigate potentially favourable zones of alteration and
to map with better accuracy the distribution of disseminated and
stringer sulfides in the bedrock. The phase-domain induced polarization
ground survey was conducted by Remy Belanger Geophysics. This
geophysical survey was carried out along the new 167 Provincial Road
and was chained and picketed every 50 metres. The phase-domain induced
polarization survey used a dipole-dipole electrode configuration. The
dipole dimension is 50 metres and successive separations at multiples
of n=1,2,3,4,5 and 6 times the dipole dimensions were used, in order to
investigate at depth. This configuration should provide a depth
penetration of about 125 to 180 metres, depending on target size.

Mr. Joel Dube, P. Eng. from Dynamic Discovery Geoscience of
Ottawa, an engineering firm specialized in geophysics, has processed
and analysed the data obtained from the phase-domain induced
polarization ground survey. Inversion models of the resistivity and
chargeability distribution within the ground have been generated to
better understand the geometry and possible nature of anomaly sources.
These models will be integrated in Visible Gold Mines' available data
in the area and will ultimately provide guidance for the current
exploration program, which includes exploratory drilling. The table
below represents the strength of induced polarization anomalies
identified.

//st
Induced Polarization Anomalies Strength       Strong    Medium    Weak
South Block                                        4         7       5
Central Block                                      0         2      11
North Block                                        3         2       5

//et

Till Sampling

Inlandsis Consultants, a firm specialized in boulder tracing since
1996 and which has been involved in many technical successes with a
wide range of exploration companies, completed a first appraisal of
glacial landforms and ice-flow sequences for Visible Gold Mines' 167
Property. Two successful exploration campaigns based on full use of the
glacial indicator tracing technique have been completed and a third
exploration campaign is expected to be initiated shortly, in order to
locate the bedrock source of the gold-rich boulders discovered on the
167 Property. Each campaign used both rock fragments and free gold
grains in till as tracers to be followed-up to their source. The table
below is a summary of Phase 1 and Phase 2 results to date;

//st

Till samples Till with visual        Till concentrate
gold grains with gold value )0.5g/t
Phase 1 (T1-T33)            33                7                       3
Phase 2 (T34-T92)           59               32                       5

//et

*Till concentrate no.18 (T18) located 80 meters off the road has
returned over 1.0 g/t of gold.

**Till concentrate no. 67 (T67) located 630 meters off the road
has returned over 3.8 g/t of gold.

Drilling Program

A 25-hole diamond drilling program totalling approximately 5,000
metres is in preparation and is expected to begin in November 2015. Six
holes, for a total of 1,200 metres, should be completed before year end
and the remainder of the drilling program is expected to be completed
early in 2016. The main objective of this drilling campaign will be to
test the numerous induced polarization anomalies identified during the
summer 2015 exploration program and certain of the electromagnetic
conductors identified during the 2014 airborne survey.

"We are very pleased with our 2015 summer exploration program,"
stated Martin Dallaire, President and Chief Executive Officer of
Visible Gold Mines.  "Visible Gold Mines obtained a considerable amount
of gold in its till samples located hundreds of metres off the 167
Provincial Road and has found mineralized boulders containing gold
north of the former Eastmain Mine, and the induced polarization survey
along the 167 Provincial Road has generated many "ready to drill"
targets. A drilling program is currently in preparation and is expected
to begin in November 2015. Despite market conditions, this is an
exciting year for Visible Gold Mines." added Mr. Dallaire.

Visible Gold Mines Increases its Land Position on the 167 Property


Visible Gold Mines acquired a 60% interest in 80 mining claims
along the new 167 Provincial Road. The 60% interest in the 80 mining
claims was acquired by performing a $50,000 exploration program on
these claims. The claim block covers a distance of approximately 15
kilometres of the 167 Provincial Road and has an area of approximately
40 km2. The south boundary of these mining claims is located 15
kilometres north of the former Eastman Mine and the north boundary is
located 30 kilometres south of the Stornoway Diamond's Renard project.
Mineralized boulders containing gold were found along these claims
during the 2015 summer prospection program and a five-kilometre induced
polarization survey has generated many medium-to-strong induced
polarization anomalies. In order to acquire an additional interest of
30% in these mining claims, which will bring Visible Gold Mines' total
interest to 90%, Visible Gold Mines must execute a 1,000-metre diamond
drilling program to essentially test the induced polarization anomalies
identified during its 2015 summer prospection program.

Corporate Update

Visible Gold Mines Options Hazeur Gold Project to TomaGold
Corporation

Visible Gold Mines has entered into an option and exploration
agreement with TomaGold Corporation (LOT-TSXV) pursuant to which
TomaGold has an option to acquire a 70% interest in the Hazeur
Property. In order to acquire the 70% interest, TomaGold must: (i) pay
$5,000 to Visible Gold Mines on the signature date of the option and
exploration agreement; (ii) issue 1.55 million common shares to Visible
Gold Mines over a three-year period; and (iii) incur $225,000 in
exploration work on the Hazeur Property over a three-year period. The
Hazeur Property is comprised of 61 mining claims covering an area of
approximately 2,863 hectares on the southern border of the Monster Lake
property. TomaGold will be the project operator with support from
Visible Gold Mines' staff during the earn-in period.

Visible Gold Mines Terminates Joutel Option

Due to difficult market conditions, Visible Gold Mines decided to
terminate the Option Agreement entered into with Agnico-Eagle Mines
Limited in March 2011. Pursuant to this agreement, Visible Gold Mines
had the option to acquire a 50% undivided interest in the Joutel
Property. The Joutel Property is comprised of one mining lease and 477
mining claims located 150 km north of Rouyn-Noranda, northwestern
Quebec.

Qualified Persons
Mr. Martin Dallaire, P.Eng., President and Chief Executive Officer
of Visible Gold Mines, is the qualified person on the 167 Project
exploration information presented in this press release under National
Instrument 43-101 Standards of Disclosure for Mineral Projects, is also
responsible for the technical contents of this press release and has
approved the disclosure of the technical and exploration information
contained herein. The data verification was conducted by Jeannot
Theberge, P.Geo. under the supervision of Martin Dallaire, P.Eng.

QualityControl

Visible Gold Mines has implemented and adheres to a strict Quality
Assurance/Quality Control. Tills Analyses are performed by Activation
Laboratories Ltd., Ancaster, Ontario.

About the 167 Project

In 2011, the Quebec Government launched its ambitious Plan Nord
project to develop Quebec's northern region, which included the
construction of a 243 kilometre-long all-season road linking
Stornoway's Renard Diamond project to the provincial highway network.
At that time, Visible Gold Mines' management decided to acquire the
available mining rights along each side of the new road in order to
have access to new outcrops and strippings generated by the road
construction. Visible Gold Mines acquired claims by acquisition and
staking, and so the 167 Property was born. Out of the 140 kilometres of
new road available for mining exploration (the first 102 kilometres are
in a provincial park), Visible Gold Mines owns more than 110
kilometres. The road was completed in October 2014 at a construction
cost of approximately $350 million. The 167 Property is 100% owned by
Visible Gold Mines and with recent acquisitions covers up to 61,178
hectares, or 611 km2.

About Visible Gold Mines

Visible Gold Mines Inc. is a dynamic corporation aggressively
searching for the next important gold deposit in the province of
Quebec, an area consistently ranked as one of the world's best
jurisdictions for mining and exploration.

Forward-Looking Statements

This news release contains statements that may constitute
"forward-looking information" within the meaning of applicable Canadian
securities legislation. Forward-looking information may include, among
others, statements regarding the future plans, costs, objectives or
performance of Visible Gold Mines, or the assumptions underlying any of
the foregoing. In this news release, words such as "may", "would",
"could", "will", "likely", "believe", "expect", "anticipate", "intend",
"plan", "estimate" and similar words and the negative form thereof are
used to identify forward-looking statements. Forward-looking statements
should not be read as guarantees of future performance or results, and
will not necessarily be accurate indications of whether, or the times
at or by which, such future performance will be achieved. No assurance
can be given that any events anticipated by the forward-looking
information will transpire or occur, including the development of the
167 Project, or if any of them do so, what benefits Visible Gold Mines
will derive. Forward-looking information are based on information
available at the time and/or management's good-faith belief with
respect to future events and are subject to known or unknown risks,
uncertainties, assumptions and other unpredictable factors, many of
which are beyond Visible Gold Mines' control. These risks,
uncertainties and assumptions include, but are not limited to, those
described under "Financial Risk Management Objectives and Policies, and
Financial Risks" in Visible Gold Mines' Annual Report for the fiscal
year ended on July 31, 2014, a copy of which is available on SEDAR at
www.sedar.com, and could cause actual events or results to differ
materially from those projected in any forward-looking statements.
Visible Gold Mines does not intend, nor does Visible Gold Mines
undertake any obligation, to update or revise any forward-looking
information contained in this news release to reflect subsequent
information, events or circumstances or otherwise, except if required
by applicable laws.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of the
release.

For further information:  Martin Dallaire, President and Chief
Executive Officer, Telephone: 819-762-0107, Fax: 819-762-0097, E-mail:
mdallaire@visiblegoldmines.com Website: www.visiblegoldmines.com
______________________________________
_______________________________________________
TSX Venture closing price for VGD-V
Date: 2015/11/04
Closing Price: 0.04
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1530800032TS11530801596-08350720151105