Source	Marketwire
Date	11/12/2015
Time	07:37:11 AM

Company	 DIOS EXPLORATION INC.
Title	DIOS: Drilling 105 m North of Heberto Gold Discovery Hits Gold-Bearing 
Heberto Style Zones





    CDNX Symbol: DOS











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: DIOS Exploration Inc.

TSX VENTURE SYMBOL: DOS

November 12, 2015

DIOS: Drilling 105 m North of Heberto Gold Discovery Hits Gold-Bearing Heberto 
Style Zones


MONTREAL, QUEBEC--(Marketwired - Nov. 12, 2015) - DIOS EXPLORATION (TSX 
VENTURE:DOS) reports significant positive 3D interpretation results and assay 
checks from HEBERTO GOLD drilling discovery. Several distinct gold zones were 
intersected in strike over hundreds of metres and at depth. Data compilation in 
plan view and vertical sections shows several 10-20 true width zones with high 
potential for future gold discoveries in strike over hundreds of meters or at 
depth.

Several drill holes hit 10 to 20 m gold zones with at least 3 altered zones or 
splays defined in same section this fall, the main one discovered in surface 
and drilling in section A (2 g/t gold over 22 m, 2.13 g/t gold over 22.9 m in 
other hole incl. 4.79 g/t gold /8.65 m and 2.47 g/t gold over 10 m in another 
hole (1.63 g/t gold /18.45 m) as well as in section H located 135 m south. Hole 
BB, 105 m north of AA, hit 3.7 m with 3.23 g/t gold (true width), 1.51 g/t gold 
over 1.6 m and 1.23 g/t gold over 1.10 m and altered zones: 0.21 g/t gold /13.4 
m & 0.22 g/t gold /5.25 m. Strike extents are drill targets.

Heberto structure is N160 striking, dipping 40-50 degrees west, so next drill 
targets will be more to the west. Section D 350 m due north of A (HEBERTO) hit 
7.6 g/t gold over 0.4 m, 1 g/t gold over 0.75 m and 2 g/t gold over 0.5 m, but 
main zone is aligned more to the west, related to a strong magnetic high thus 
to be drilled.

Hole H 135 m south of A had hit 3.04 g/t gold over 4.35 m (1.884 g/t gold /7.05 
m) 50 m under surface and 3.46 g/t gold /2.20 m and 1.9 g/t gold/1.00 m then 
hole HH hit 1.94 g/t gold/ 7.75 m (incl. 3.26 g/t gold/ 3.75 m). Several gold 
targets to be drilled will check splaying that could widen or get richer near 
favourable contacts. Section 235 m south of HEBERTO will be drilled more to the 
west, due to west dipping of the zone, and hole 8 drilled east towards east 
just missed it (1.025 g/t gold /1 m at top of hole).

Stripping west of HEBERTO (5.18 g/t or /5 m in outcrop) is planned (thin 
overburden) to find surface extent of other zones cut in section A (2.47 g/t 
gold /10 m). This release was prepared by M.J. Girard, M.Sc. Geo, 43-101 
Qualified Person. See Sept. 9 & 23 and Oct. 7 releases for gold zones 
mineralogy and previous results. This wholly-owned property is held by DIOS, 
without any royalties and HEBERTO GOLD is located 12 km west of EM1 CAMP, James 
Bay, road accessible, 50 km south of GOLDCORP's gold mine.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Marie-Jose Girard, M.Sc. Geo, 43-101 QP
President & CEO
mjgirard@diosexplo.com
(514) 923-9123
www.diosexplo.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=549080685