Source	MARKET NEWS
Date	11/12/2015
Time	10:07:40 AM

Company	 Para Resources Inc.
Title	Revised 
Sampling Methods at El Limon; Assays Ove





    CDNX Symbol: PBR











Press Release	





PARA RESOURCES INC ("PBR-V")
- Revised Sampling Methods at El Limon; Assays Over 100 Grams of
- Gold per Tonne

Para Resources Inc. (the "Company" or "Para") reports that sample
preparation methods have been updated due to very high grade assays
(over 100 grams gold per tonne) at the El Limon mine in Zaragoza
Colombia.

A summary of recent grades from mining at the El Limon mine, as
reported by three different laboratories, are summarized in the table
below:

As a result of the high grade assays and variability encountered
(due to nugget effect) between the various laboratories, El Limon has
adopted the following procedure for sampling and assay analysis of high
grade material:

- All of the mineralized rock is pulverized to -1, maintaining a
moisture content at a minimum of 3%.
- From each 60 kg sample, a 600 gram sample (1%) is taken and
loaded into a cement mixer with a capacity of 0.2 cubic meters or
approximately 150 kilograms. This process is repeated until the mixer
has reached its maximum rated weight or approximately 150 kilograms.
The quantity of material to be sampled will be limited to 10 tonnes.
Ideally, the resultant sample size will be approximately 100 kilograms.

- The sum of these individual samples will be then mixed together,
for a period of 20+ minutes.
- The total sample is then fed through a riffle box (or rotary
splitter if required), to reduce the total sample size to approximately
15 kilograms.
- The 15 kilos will be coned and flattened and then quartered into
3 samples of approximately 5 kilograms.
- 1st 5kg sample will be assayed in company's laboratory
- 2nd 5kg sample will be assayed by a certified independent
laboratory
- 3rd 5kg sample will be retained for arbitration
- The 1st sample is dried and the weight precisely recorded. It is
then further pulverized to 95% -150 microns or 100 mesh.
- The 1st sample is screened and the 150 micron fraction
segregated.
- The + 150 micron fraction (approximately 250 grams) is weighed
and then completely fused in crucibles followed by cupellation in
cupels.
- The 150 micron fraction is homogenized and then coned and
quartered, 4 x 35 gram samples are extracted and analyzed.
- The resultant prills or beads are flattened and treated with
nitric acid to remove the silver.
- The weight used for the 150 micron fraction is the weight of the
complete sample less the weight of the +150 micron fraction. This is
due to possible losses, in the handling of the fines fraction.

The assay results obtained for both fractions and their respective
weights will be then used to determine a final value for the grade of
the material.

Geoff Hampson, Chairman and CEO of Para Resources, commented:

"We are very pleased to be seeing grades that are considerably
greater than our projections. The new sampling techniques ensure that
Para is accurately recording and reporting the grades of the material
mined at El Limon but are also in a position to quickly and accurately
determine the grade of the material being sold to the Mill by the local
artisanal miners. The grade analyses from October indicate that there
is great variability in the material being mined but that on average
the grades are considerably higher than projected. If this trend
continues it will have a very positive effect on the cash flow
generated by the El Limon Mine."

El Limon Overview

The El Limon property is located in the northwest part of Colombia
near the town of Zaragoza, Antioquia, Colombia and is accessible via
both paved highways and gravel roads. The Mine is situated in the wide
Zaragoza Gold District which extends south from El Bagre to Segovia and
Remedios, all towns with considerable historical alluvium mining and
large underground gold mines that have operated for generations. The El
Limon claims cover a total area of approximately 277.5 hectares,
including 86.4 hectares in RPP No. 12011 and 191.1 hectares in the
concession contract No. 620 which is located west of the currently
exploited zone. Gold grade at the El Limon mine ranges from 5 grams of
gold per tonne to more than 100 grams of gold per tonne; the expected
diluted average gold grade is 7-10 grams per tonne. Extremely
high-grade mineralization is common in the narrow-vein underground
mines in the region.

It is CML's intention to utilize a portion of any cash generated
from mining to drill the El Limon property to expand the number of
targeted areas for mining.

Mr. David Bikerman, a Member of the Australian Institute of
Geoscientists (MAIG #3558), Mining Engineer, a CP/QP under NI-43-101,
has reviewed and approved the scientific and technical information in
this press release.

ABOUT PARA RESOURCES:

Para Resources is an exploration-stage gold mining and toll
milling company. In addition to its existing properties, Para will
continue to take advantage of current market conditions to acquire and
develop additional assets that have strong exploration and development
potential.

ON BEHALF OF THE BOARD OF DIRECTORS
"C. Geoffrey Hampson"
C. Geoffrey Hampson, Chief Executive Officer and Director
For further information, please contact Andrea Laird: Telephone:
604-398-3227

Neither TSX Venture Exchange nor its regulation service provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

All statements, analysis and other information contained in this
press release about anticipated future events or results constitute
forward-looking statements. Forward-looking statements are often, but
not always, identified by the use of words such as "seek",
"anticipate", "believe", "plan", "estimate", "expect" and "intend" and
statements that an event or result "may", "will", "should", "could" or
"might" occur or be achieved and other similar expressions.
Forward-looking statements are subject to business and economic risks
and uncertainties and other factors that could cause actual results of
operations to differ materially from those contained in the
forward-looking statements. Forward-looking statements are based on
estimates and opinions of management at the date the statements are
made. The company does not undertake any obligation to update
forward-looking statements even if circumstances or management's
estimates or opinions should change except as required by applicable
laws. Investors should not place undue reliance on forward-looking
statements.
______________________________________
_______________________________________________
TSX Venture closing price for PBR-V
Date: 2015/11/06
Closing Price: 0.12
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1531500036TS11531501812-10055520151112