Source	Marketwire
Date	11/17/2015
Time	05:03:17 AM

Company	 SCORPIO GOLD CORPORATION
Title	Scorpio Gold Reports Final Results from 2015 Exploration Drilling at the 
Oromonte Satellite Deposit, Mineral Ridge Project, Nevada





    CDNX Symbol: SGN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Scorpio Gold Corporation

TSX VENTURE SYMBOL: SGN

November 17, 2015

Scorpio Gold Reports Final Results from 2015 Exploration Drilling at the 
Oromonte Satellite Deposit, Mineral Ridge Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Nov. 17, 2015) - Scorpio Gold 
Corporation ("Scorpio Gold" or the "Company") (TSX VENTURE:SGN) reports final 
results from its 2015 exploration drilling program on the Oromonte satellite 
deposit at the 70% owned Mineral Ridge project, located in Nevada.

The Oromonte target occurs over a 300 x 500 meter area situated between the 
Solberry and Wedge deposits. A small mineral resource estimate containing 
almost entirely Indicated resources was reported for Oromonte based on 53 
reverse circulation ("RC") drill holes (see July 21, 2014 news release).

Drilling in 2014-2015 has intersected significant mineralization at vertical 
depths ranging from near surface to 80 meters depth across the target area. A 
notably higher-grade zone of mineralization occurs along the western edge of 
the target area, ranging in vertical depth from 106 to 142 meters.

A geological interpretation of the mineralization at Oromonte is that it 
represents a continuation of the mineralized horizon(s) between the Solberry 
and Wedge deposits that have been offset by normal faulting. The occurrence of 
a higher-grade zone of mineralization at depth may be related to a synform 
axis, which concentrated mineralization in the Oromonte area. This mineralized 
zone was subsequently down-dropped by late-stage normal faulting. A generalized 
geological model of the mineralization is presented here: Oromonte Cross 
Section.

Although not accessible by open pit mining, the deeper mineralization at 
Oromonte may be amenable to underground extraction should further results 
support underground development. Historical underground workings occur in the 
Wedge deposit area approximately 180 meters to the east.

Highlights from the final phase of the 2015 RC drilling program on the Oromonte 
deposit include:

/T/

--  MR151671: 2.13 grams per tonne ("g/t") gold over 3.05 meters
--  MR151674: 5.18 g/t gold over 3.05 meters
--  MR151677: 8.28 g/t gold over 6.10 meters
--  MR151773: 7.58 g/t gold over 1.52 meters
--  MR151777: 8.58 g/t gold over 6.10 meters
--  MR151778: 7.95 g/t gold over 9.14 meters
--  MR151779: 2.85 g/t gold over 3.05 meters
--  MR151802: 40.40 g/t gold over 7.62 meters
--  MR151804: 2.22 g/t gold over 4.57 meters
--  MR151809: 12.29 g/t gold over 4.57 meters
--  MR151810: 2.58 g/t gold over 4.57 meters
--  MR151885: 39.15 g/t gold over 1.52 meters
--  MR151887: 2.83 g/t gold over 3.05 meters

/T/

A drill hole location map is available at: DH Plan

Table 1. Oromonte Deposit - Significant Drill Results

/T/

----------------------------------------------------------------------------
Hole               Azm   Dip From   To Width   From     To Width  Gold  Gold
No.              (deg) (deg) (ft) (ft)  (ft)    (m)    (m)   (m) (OPT) (g/t)
----------------------------------------------------------------------------
MR151671             0   -90  220  230    10  67.06  70.10  3.05 0.062  2.13
----------------------------------------------------------------------------
245  250     5  74.68  76.20  1.52 0.018  0.60
----------------------------------------------------------------------------
255  260     5  77.72  79.25  1.52 0.022  0.77
----------------------------------------------------------------------------
MR151672-673         0   -90              No Significant Results
----------------------------------------------------------------------------
MR151674             0   -90    5   10     5   1.52   3.05  1.52 0.018  0.62
----------------------------------------------------------------------------
165  175    10  50.29  53.34  3.05 0.151  5.18
----------------------------------------------------------------------------
200  205     5  60.96  62.48  1.52 0.022  0.76
----------------------------------------------------------------------------
245  250     5  74.68  76.20  1.52 0.030  1.03
----------------------------------------------------------------------------
MR151675             0   -90   20   35    15   6.10  10.67  4.57 0.050  1.70
----------------------------------------------------------------------------
110  130    20  33.53  39.62  6.10 0.033  1.14
----------------------------------------------------------------------------
MR151676             0   -90  100  105     5  30.48  32.00  1.52 0.035  1.19
----------------------------------------------------------------------------
MR151677             0   -90   30   35     5   9.14  10.67  1.52 0.031  1.06
----------------------------------------------------------------------------
65   85    20  19.81  25.91  6.10 0.242  8.28
----------------------------------------------------------------------------
incl               70   75     5  21.34  22.86  1.52 0.888 30.45
----------------------------------------------------------------------------
MR151679             0   -90    5   10     5   1.52   3.05  1.52 0.028  0.96
----------------------------------------------------------------------------
MR151680             0   -90  160  165     5  48.77  50.29  1.52 0.015  0.51
----------------------------------------------------------------------------
MR151771             0   -90  290  295     5  88.39  89.92  1.52 0.131  4.49
----------------------------------------------------------------------------
325  330     5  99.06 100.58  1.52 0.018  0.62
----------------------------------------------------------------------------
MR151772             0   -90  215  225    10  65.53  68.58  3.05 0.036  1.22
----------------------------------------------------------------------------
320  325     5  97.54  99.06  1.52 0.045  1.54
----------------------------------------------------------------------------
MR151773             0   -90  245  250     5  74.68  76.20  1.52 0.221  7.58
----------------------------------------------------------------------------
375  380     5 114.30 115.82  1.52 0.016  0.55
----------------------------------------------------------------------------
MR151774             0   -90   10   15     5   3.05   4.57  1.52 0.015  0.51
----------------------------------------------------------------------------
MR151775             0   -90   35   40     5  10.67  12.19  1.52 0.100  3.43
----------------------------------------------------------------------------
130  135     5  39.62  41.15  1.52 0.018  0.62
----------------------------------------------------------------------------
230  235     5  70.10  71.63  1.52 0.032  1.10
----------------------------------------------------------------------------
260  265     5  79.25  80.77  1.52 0.030  1.03
----------------------------------------------------------------------------
MR151776             0   -90  305  315    10  92.96  96.01  3.05 0.016  0.53
----------------------------------------------------------------------------
MR151777             0   -90  380  385     5 115.82 117.35  1.52 0.022  0.75
----------------------------------------------------------------------------
400  410    10 121.92 124.97  3.05 0.062  2.11
----------------------------------------------------------------------------
445  465    20 135.64 141.73  6.10 0.250  8.58
----------------------------------------------------------------------------
incl              445  450     5 135.64 137.16  1.52 0.503 17.25
----------------------------------------------------------------------------
480  485     5 146.30 147.83  1.52 0.019  0.65
----------------------------------------------------------------------------
MR151778             0   -90  190  200    10  57.91  60.96  3.05 0.025  0.86
----------------------------------------------------------------------------
330  340    10 100.58 103.63  3.05 0.260  8.90
----------------------------------------------------------------------------
385  400    15 117.35 121.92  4.57 0.022  0.74
----------------------------------------------------------------------------
405  435    30 123.44 132.59  9.14 0.232  7.95
----------------------------------------------------------------------------
incl              410  420    10 124.97 128.02  3.05 0.582 19.95
----------------------------------------------------------------------------
495  500     5 150.88 152.40  1.52 0.017  0.58
----------------------------------------------------------------------------
MR151779             0   -90   80   85     5  24.38  25.91  1.52 0.020  0.69
----------------------------------------------------------------------------
190  195     5  57.91  59.44  1.52 0.045  1.54
----------------------------------------------------------------------------
440  450    10 134.11 137.16  3.05 0.083  2.85
----------------------------------------------------------------------------
MR151780             0   -90  185  190     5  56.39  57.91  1.52 0.032  1.10
----------------------------------------------------------------------------
275  285    10  83.82  86.87  3.05 0.031  1.05
----------------------------------------------------------------------------
300  305     5  91.44  92.96  1.52 0.020  0.69
----------------------------------------------------------------------------
MR151801             0   -90   95  100     5  28.96  30.48  1.52 0.034  1.17
----------------------------------------------------------------------------
200  225    25  60.96  68.58  7.62 0.014  0.49
----------------------------------------------------------------------------
255  260     5  77.72  79.25  1.52 0.019  0.65
----------------------------------------------------------------------------
335  340     5 102.11 103.63  1.52 0.033  1.13
----------------------------------------------------------------------------
350  360    10 106.68 109.73  3.05 0.016  0.53
----------------------------------------------------------------------------
375  395    20 114.30 120.40  6.10 0.052  1.77
----------------------------------------------------------------------------
MR151802             0   -90  205  215    10  62.48  65.53  3.05 0.024  0.82
----------------------------------------------------------------------------
270  275     5  82.30  83.82  1.52 0.016  0.55
----------------------------------------------------------------------------
310  315     5  94.49  96.01  1.52 0.068  2.33
----------------------------------------------------------------------------
370  375     5 112.78 114.30  1.52 0.038  1.30
----------------------------------------------------------------------------
420  445    25 128.02 135.64  7.62 1.178 40.40
----------------------------------------------------------------------------
incl              420  430    10 128.02 131.06  3.05 2.799 95.97
----------------------------------------------------------------------------
MR151803             0   -90   55   60     5  16.76  18.29  1.52 0.024  0.82
----------------------------------------------------------------------------
365  370     5 111.25 112.78  1.52 0.024  0.82
----------------------------------------------------------------------------
400  405     5 121.92 123.44  1.52 0.019  0.65
----------------------------------------------------------------------------
MR151804             0   -90   60   65     5  18.29  19.81  1.52 0.033  1.13
----------------------------------------------------------------------------
250  265    15  76.20  80.77  4.57 0.065  2.22
----------------------------------------------------------------------------
MR151806             0   -90  255  260     5  77.72  79.25  1.52 0.030  1.03
----------------------------------------------------------------------------
MR151807             0   -90   50   55     5  15.24  16.76  1.52 0.130  4.46
----------------------------------------------------------------------------
120  125     5  36.58  38.10  1.52 0.016  0.55
----------------------------------------------------------------------------
205  210     5  62.48  64.01  1.52 0.049  1.68
----------------------------------------------------------------------------
220  230    10  67.06  70.10  3.05 0.015  0.50
----------------------------------------------------------------------------
MR151809             0   -90    5   20    15   1.52   6.10  4.57 0.015  0.51
----------------------------------------------------------------------------
145  160    15  44.20  48.77  4.57 0.358 12.29
----------------------------------------------------------------------------
incl              145  150     5  44.20  45.72  1.52 1.034 35.45
----------------------------------------------------------------------------
MR151810             0   -90  155  170    15  47.24  51.82  4.57 0.075  2.58
----------------------------------------------------------------------------
180  190    10  54.86  57.91  3.05 0.021  0.72
----------------------------------------------------------------------------
MR151864             0   -90              No Significant Results
----------------------------------------------------------------------------
MR151865             0   -90   15   25    10   4.57   7.62  3.05 0.034  1.15
----------------------------------------------------------------------------
85  100    15  25.91  30.48  4.57 0.027  0.94
----------------------------------------------------------------------------
120  135    15  36.58  41.15  4.57 0.057  1.95
----------------------------------------------------------------------------
MR151867             0   -90              No Significant Results
----------------------------------------------------------------------------
MR151870             0   -90   20   25     5   6.10   7.62  1.52 0.015  0.51
----------------------------------------------------------------------------55  
 65    10  16.76  19.81  3.05 0.018  0.63
----------------------------------------------------------------------------
MR151871             0   -90   65   70     5  19.81  21.34  1.52 0.017  0.58
----------------------------------------------------------------------------
MR151874             0   -90   75   85    10  22.86  25.91  3.05 0.023  0.77
----------------------------------------------------------------------------
100  120    20  30.48  36.58  6.10 0.022  0.74
----------------------------------------------------------------------------
MR151876             0   -90  150  155     5  45.72  47.24  1.52 0.108  3.70
----------------------------------------------------------------------------
190  195     5  57.91  59.44  1.52 0.028  0.96
----------------------------------------------------------------------------
MR151877             0   -90   75   80     5  22.86  24.38  1.52 0.020  0.69
----------------------------------------------------------------------------
135  140     5  41.15  42.67  1.52 0.016  0.55
----------------------------------------------------------------------------
230  235     5  70.10  71.63  1.52 0.056  1.92
----------------------------------------------------------------------------
MR151878             0   -90  195  200     5  59.44  60.96  1.52 0.039  1.34
----------------------------------------------------------------------------
205  210     5  62.48  64.01  1.52 0.017  0.58
----------------------------------------------------------------------------
MR151880             0   -90  185  190     5  56.39  57.91  1.52 0.014  0.48
----------------------------------------------------------------------------
245  250     5  74.68  76.20  1.52 0.033  1.13
----------------------------------------------------------------------------
MR151882             0   -90   15   20     5   4.57   6.10  1.52 0.027  0.93
----------------------------------------------------------------------------
MR151885             0   -90  240  245     5  73.15  74.68  1.52 1.142 39.15
----------------------------------------------------------------------------
MR151886             0   -90  240  245     5  73.15  74.68  1.52 0.066  2.26
----------------------------------------------------------------------------
MR151887             0   -90  115  120     5  35.05  36.58  1.52 0.024  0.82
----------------------------------------------------------------------------
190  200    10  57.91  60.96  3.05 0.083  2.83
----------------------------------------------------------------------------
MR151889             0   -90   75   90    15  22.86  27.43  4.57 0.014  0.49
----------------------------------------------------------------------------
240  245     5  73.15  74.68  1.52 0.017  0.58
----------------------------------------------------------------------------
MR151892             0   -90  180  185     5  54.86  56.39  1.52 0.039  1.34
----------------------------------------------------------------------------
MR151894             0   -90  330  335     5 100.58 102.11  1.52 0.014  0.48
----------------------------------------------------------------------------

/T/

All holes presented in Table 1 were completed by reverse circulation (RC) 
drilling. True width is estimated at 80-100% of downhole width. Analytical 
results for the RC holes were performed by American Assay Laboratory Inc. in 
Sparks, Nevada, an ISO/IEC 17025:2005 accredited facility. External check 
assays to verify lab accuracy are routinely completed by ALS Chemex in Reno, 
Nevada, also an ISO/IEC 17025:2005 accredited facility. Further details are 
presented in the Company's quality assurance and quality control program for 
the Mineral Ridge project, available at: MR QAQC.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge gold mining 
operation located in Esmeralda County, Nevada with joint venture partner 
Elevon, LLC (30%). Mineral Ridge is a conventional open pit mining and heap 
leach operation. The Mineral Ridge property is host to multiple gold-bearing 
structures, veins and lenses at exploration, development and production stages. 
Scorpio Gold also holds a 100% interest in the advanced exploration-stage 
Goldwedge property in Manhattan, Nevada, with a fully permitted underground 
mine and 400 ton per day mill facility. The Goldwedge mill facility has been 
placed on a care and maintenance basis and can be restarted immediately when 
needed.

Scorpio Gold's President & CEO, Peter J. Hawley, P.Geo., is a Qualified Person 
as defined by National Instrument 43-101 and has reviewed and approved the 
content of this release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Peter J. Hawley, President & CEO

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

The Company relies on litigation protection for forward-looking statements. 
This news release contains forward-looking statements that are based on the 
Company's current expectations and estimates. Forward-looking statements are 
frequently characterized by words such as "plan", "expect", "project", 
"intend", "believe", "anticipate", "estimate", "suggest", "indicate" and other 
similar words or statements that certain events or conditions "may" or "will" 
occur, and include, without limitation, statements regarding the Company's 
plans with respect to the exploration, development and exploitation of its 
Mineral Ridge project, including potential further exploration or development 
of the Oromonte deposit. Such forward-looking statements involve known and 
unknown risks, uncertainties and other factors that could cause actual events 
or results to differ materially from estimated or anticipated events or results 
implied or expressed in such forward-looking statements, including risks 
involved in mineral exploration and development programs, risks related to 
differences between mineral reserve and resource estimates and actual operating 
results and those risk factors outlined in the Company's Management Discussion 
and Analysis as filed on SEDAR. Any forward-looking statement speaks only as of 
the date on which it is made and, except as may be required by applicable 
securities laws, the Company disclaims any intent or obligation to update any 
forward-looking statement, whether as a result of new information, future 
events or results or otherwise. Forward-looking statements are not guarantees 
of future performance and accordingly undue reliance should not be put on such 
statements due to the inherent uncertainty thereof.

- 30 -

CONTACT INFO:

Peter J. Hawley, President & CEO
Tel: (819) 825-7618
Email: phawley@scorpiogold.com

or

Investor Relations:
Jim Macdonald, Torrey Hills Capital
Tel: (858) 456-7300
Email: jm@sdthc.com
Website: www.scorpiogold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=549494717